## Slide 1: Generating Sinusoidal Signals
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 445S Real-Time Digital Signal Processing Lab Spring 2014
Lecture 1 http://www.ece.utexas.edu/~bevans/courses/rtdsp

## Slide 2: Outline
1-<number>
Bandwidth
Sinusoidal amplitude modulation
Sinusoidal generation
Design tradeoffs

## Slide 3: Bandwidth
1-<number>
Non-zero extent in positive frequencies
Applies to continuous-time & discrete-time signals
In practice, spectrum won’t be ideally bandlimited
  Thermal noise has “flat” spectrum from 0 to 1015 Hz
  Finite observation time of signal leads to infinite bandwidth
Alternatives to “non-zero extent”?
Ideal Lowpass Spectrum
fmax
-fmax
f
Bandwidth fmax
Ideal Bandpass Spectrum
f1
f2
f
–f2
–f1
Bandwidth W = f2 – f1
Bandwidth

## Slide 4: Lowpass Signal in Noise
1-<number>
How to determine fmax?
  Apply threshold and eyeball it
  OR
  Estimate fmax that captures certain percentage (say 90%) of energy In practice, (a) use large frequency in place of  and (b) integrate a measured spectrum numerically
Lowpass Spectrum in Noise
f
Idealized Lowpass Spectrum
fmax
-fmax
f
Bandwidth
approximate
Baseband signal: energy in frequency domain concentrated around DC

## Slide 5: Bandpass Signal in Noise
1-<number>
How to find f1 and f2?
  Apply threshold and eyeball it
  OR
  Assume knowledge of fc and estimate f1 = fc  W/2 and f2 = fc + W/2 that capture percentage of energy In practice, (a) use large frequency in place of  and (b) integrate a measured spectrum numerically
Idealized Bandpass Spectrum
f1
f2
f
–f2
–f1
Bandpass Spectrum In Noise
f
fc
- fc
Bandwidth

## Slide 6: Amplitude Modulation by Cosine
1-<number>
y1(t) = x1(t) cos(c t)
  Assume x1(t) is an ideal lowpass signal with bandwidth 1
  Assume 1 << c
  Y1() has (transmission) bandwidth of 21
  Y1() is real-valued if X1() is real-valued
Demodulation: modulation then lowpass filtering

0
1

-
X1()

0
Y1()
½
-c - 
-c + 
c
c - 
c + 
c
½X1c
½X1c
lower sidebands
Amplitude Modulation

## Slide 7: Amplitude Modulation by Sine
1-<number>
y2(t) = x2(t) sin(c t)
  Assume x2(t) is an ideal lowpass signal with bandwidth 2
  Assume 2 << c
  Y2() has (transmission) bandwidth of 22
  Y2() is imaginary-valued if X2() is real-valued
Demodulation: modulation then lowpass filtering

Y2()
j ½
-c – 
-c + 
c
c – 
c + 
c
-j ½X2c
j ½X2c
-j ½

0
1

-
X2()
lower sidebands
Amplitude Modulation

## Slide 8: How to Use Bandwidth Efficiently?
Send lowpass signals x1(t) and x2(t) with 1 = 2 over same transmission bandwidth
  Called Quadrature Amplitude Modulation (QAM)
  Used in DSL, cable, Wi-Fi, and LTE cellular communications
Cosine modulated signal is orthogonal to sine modulated signal at transmitter
  Receiver separates x1(t) and x2(t) through demodulation
1-<number>
+
cos(c t)
sin(c t)
x1(t)
x2(t)
s(t)
Amplitude Modulation

## Slide 9: Lab 2: Sinusoidal Generation
1-<number>
Compute sinusoidal waveform
  Function call
  Lookup table
  Difference equation
Output waveform off chip
  Polling data transmit register
  Software interrupts
  Quantization effects in digital-to-analog (D/A) converter
Expected outcomes are to understand
  Signal quality vs. implementation complexity tradeoff
  Interrupt mechanisms
Sinusoidal Generation

## Slide 10: Sinusoidal Waveforms
1-<number>
One-sided discrete-time cosine (or sine) signal with fixed-frequency 0 in rad/sample has form
  cos(0 n) u[n]
Consider one-sided continuous-time analog-amplitude cosine of frequency f0 in Hz
  cos(2  f0 t) u(t)
  Sample at rate of fs by substituting t = n Ts = n / fs
  (1/Ts) cos(2  (f0 / fs) n) u[n]
  Discrete-time frequency 0 = 2  f0 / fs in units of rad/sample
  Example: f0 = 1200 Hz and fs = 8000 Hz, 0 = 3/10 
How to determine gain for D/A conversion?
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 11: Math Library Call in C
1-<number>
Uses double-precision floating-point arithmetic
No standard in C for internal implementation
Appropriate for desktop computing
  On desktop computer, accuracy is a primary concern, so additional computation is often used in C math libraries
  In embedded scenarios, implementation resources generally at premium, so alternate methods are typically employed
GNU Scientific Library (GSL) cosine function
  Function gsl_sf_cos_e in file specfunc/trig.c
  Version 1.8 uses 11th order polynomial over 1/8 of period
  20 multiply, 30 add, 2 divide and 2 power calculations per output value (additional operations to estimate error)
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 12: Efficient Polynomial Implementation
1-<number>
Use 11th-order polynomial
  Direct form a11 x11 + a10 x10 + a9 x9 + ... + a0
  Horner's form minimizes number of multiplications
  a11 x11 + a10 x10 + a9 x9 + ... + a0 = ( ... (((a11 x + a10) x + a9) x ... ) + a0
Comparison
Realization | Multiply Operations | Addition Operations | Memory Usage
Direct form | 66 | 10 | 13
Horner’s form | 11 | 10 | 12
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 13: Difference Equation
1-<number>
Difference equation with input x[n] and output y[n]
  y[n] = (2 cos 0) y[n-1] - y[n-2] + x[n] - (cos 0) x[n-1]
  From inverse z-transform of z-transform of cos(0 n) u[n]
  Impulse response gives cos(0 n) u[n]
  Similar difference equation for sin(0 n) u[n]
Implementation complexity
  Computation: 2 multiplications and 3 additions per cosine value
  Memory Usage: 2 coefficients, 2 previous values of y[n] and 1 previous value of x[n]
Drawbacks
  Buildup in error as n increases due to feedback
  Fixed value for 0
Initial conditions are all zero
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 14: Difference Equation
1-<number>
If implemented with exact precision coefficients and arithmetic, output would have perfect quality
Accuracy loss as n increases due to feedback from
  Coefficients cos(0) and 2 cos(0) are irrational, except when cos(0) is equal to -1, -1/2, 0, 1/2, and 1
  Truncation/rounding of multiplication-addition results
Reboot filter after each period of samples by resetting filter to its initial state
  Reduce loss from truncating/rounding multiplication-addition
  Adapt/update 0 if desired by changing cos(0) and 2 cos(0)
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 15: Lookup Table
1-<number>
Precompute samples offline and store them in table
Cosine frequency 0 = 2  N / L
  Remove all common factors between integers N and L
  Continuous-time period for cos(2  f0 t) is T0 = 1 / f0
  Discrete-time period for cos(2  (N / L) n) is L samples
  Store L samples in lookup table (N continuous-time periods)
Built-in lookup tables in read-only memory (ROM)
  Samples of cos() and sin() at uniformly spaced values for 
  Interpolate values to generate sinusoids of various frequencies
  Allows adaptation of 0 if desired
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 16: Design Tradeoffs
1-<number>
Signal quality vs. implementation complexity in generating cos(0 n) u[n] with 0 = 2  N / L
Method | MACs/ sample | ROM (words) | RAM (words) | Quality in floating pt. | Quality in fixed point
C math library call | 30 | 22 | 1 | Second Best | N/A
Difference equation | 2 | 2 | 3 | Worst | Second Best
Lookup table | 0 | L | 0 | Best | Best
MAC Multiplication-accumulation RAM Random Access Memory (writeable) ROM Read-Only Memory
Design Tradeoffs in Generating Sinusoidal Signals