## Slide 1: Signals and Systems

## Slide 2: Outline
3 - <number>
Signals
  Continuous-time vs. discrete-time
  Analog vs. digital
  Unit impulse
Continuous-Time System Properties
Sampling
Discrete-Time System Properties
Conclusion

## Slide 3: Many Faces of Signals
3 - <number>
Function, e.g. cos(t) in continuous time or cos(n) in discrete time, useful in analysis
Sequence of numbers, e.g. {1,2,3,2,1} or a sampled triangle function, useful in simulation
Set of properties, e.g. even and causal, useful in reasoning about behavior
A piecewise representation, e.g. useful in analysis
A generalized function, e.g. (t), useful in analysis
Review

## Slide 4: Continuous-Time vs. Discrete-Time
3 - <number>
Continuous-time signals can be modeled as functions of a real argument
  x(t) where time, t, can take any real value
  x(t) may be 0 for a given range of values of t
Discrete-time signals can be modeled as functions of argument that takes values from a discrete set
  x[n] where n  {...-3,-2,-1,0,1,2,3...}
  Integer time index, e.g. n, for discrete-time systems
Values for x may be real-valued or complex-valued
Review

## Slide 5: Analog vs. Digital
3 - <number>
1
-1
Amplitude of analog signal can take any real or complex value at each time/sample
Amplitude of digital signal takes values from a discrete set
Review

## Slide 6: Unit Impulse
3 - <number>
Mathematical idealism for an instantaneous event
Dirac delta as generalized function (a.k.a. functional)
Selected properties
  Unit area:
  Sifting
  provided g(t) is defined at t = 0
  Scaling:
We will leave (0) undefined


t
Unit Area
Review


t
Unit Area

## Slide 7: Unit Impulse
3 - <number>
We will leave (0) undefined
  Some signals and systems textbooks assign (0) = ∞
Plot Dirac delta as arrow at origin
  Undefined amplitude at origin
  Denote area at origin as (area)
  Height of arrow is irrelevant
  Direction of arrow indicates sign of area
With (t) = 0 for t  0, it is tempting to think
  (t) (t) = (0) (t)
  (t) (t-T) = (T) (t-T)
t
(1)
0
Unit Area
Simplify unit impulse under integration only
No!

## Slide 8: Unit Impulse
3 - <number>
Simplifying (t) under integration
  Assuming (t) is defined at t=0
What about?
What about?
  By substitution of variables,
Other examples
What about at origin?
Before Impulse
After Impulse
Review

## Slide 9: Unit Impulse
3 - <number>
Relationship between unit impulse and unit step
What happens at the origin for u(t)?
  u(0-) = 0 and u(0+) = 1, but u(0) can take any value
  Common values for u(0) are 0, ½, and 1
  u(0) = ½ is used in impulse invariance filter design:
L. B. Jackson, “A correction to impulse invariance,” IEEE Signal Processing Letters, vol. 7, no. 10, Oct. 2000, pp. 273-275.

## Slide 10: Systems
3 - <number>
Systems operate on signals to produce new signals or new signal representations
Continuous-time system examples
  y(t) = ½ x(t) + ½ x(t-1)
  y(t) = x2(t)
Discrete-time system examples
  y[n] = ½ x[n] + ½ x[n-1]
  y[n] = x2[n]
Review
Squaring function can be used in sinusoidal demodulation
Average of current input and delayed input is a simple filter
T{•}
y(t)
x(t)
T{•}
y[n]
x[n]

## Slide 11: Continuous-Time System Properties
3 - <number>
Let x(t), x1(t), and x2(t) be inputs to a continuous-time linear system and let y(t), y1(t), and y2(t) be their corresponding outputs
A linear system satisfies
  Additivity: x1(t) + x2(t)  y1(t) + y2(t)
  Homogeneity: a x(t)  a y(t) for any real/complex constant a
For time-invariant system, shift of input signal by any real-valued  causes same shift in output signal, i.e. x(t - )  y(t - ), for all 
Example: Squaring block
Review
Quick test to identify some nonlinear systems?
()2
y(t)
x(t)

## Slide 12: Role of Initial Conditions
3 - <number>
Observe a system starting at time t0
  Often use t0 = 0 without loss of generality
Integrator
Integrator observed for t  t0
  Linear system if initial conditions are zero (C0 = 0)
  Time-invariant system if initial conditions are zero (C0 = 0)
x(t)
y(t)
x(t)
y(t)
C0 is due to initial conditions

## Slide 13: Continuous-Time System Properties
3 - <number>
Ideal delay by T seconds. Linear?
Scale by a constant (a.k.a. gain block)
  Two different ways to express it in a block diagram
  Linear? Time-invariant?
x(t)
y(t)
x(t)
y(t)
x(t)
y(t)
Review
Role of initial conditions?

## Slide 14: Continuous-Time System Properties
3 - <number>
Each T represents a delay of T time units
Tapped delay line
  Linear? Time-invariant?
There are M-1 delays

…
…
Coefficients (or taps) are a0, a1, …aM-1
Role of initial conditions?

## Slide 15: Continuous-Time System Properties
3 - <number>
Amplitude Modulation (AM)
  y(t) = A x(t) cos(2fc t)
  fc is the carrier frequency (frequency of radio station)
  A is a constant
  Linear? Time-invariant?
AM modulation is AM radio if x(t) = 1 + ka m(t) where m(t) is message (audio) to be broadcast and | ka m(t) | < 1 (see lecture 19 for more info)
A
x(t)
cos(2 fc t)
y(t)

## Slide 16: Generating Discrete-Time Signals
3 - <number>
Many signals originate in continuous time
  Example: Talking on cell phone
Sample continuous-time signal at equally-spaced points in time to obtain a sequence of numbers
  s[n] = s(n Ts) for n  {…, -1, 0, 1, …}
  How to choose sampling period Ts ?
Using a formula
  x[n] = n2 – 5n + 3 on right for 0 ≤ n ≤ 5
  How does x[n] look in continuous time?
Sampled analog waveform
s(t)
t
Ts
Ts
Review
n

## Slide 17: Discrete-Time System Properties
3 - <number>
Let x[n], x1[n] and x2[n] be inputs to a linear system
Let y[n], y1[n] and y2[n] be corresponding outputs
A linear system satisfies
  Additivity: x1[n] + x2[n]  y1[n] + y2[n]
  Homogeneity: a x[n]  a y[n] for any real/complex constant a
For a time-invariant system, a shift of input signal by any integer-valued m causes same shift in output signal, i.e. x[n - m]  y[n - m], for all m
Role of initial conditions?
Review

## Slide 18: Discrete-Time System Properties
3 - <number>
Each z-1 represents a delay of 1 sample
Tapped delay line in discrete time
Linear? Time-invariant?
There are M-1 delays

…
…
See also slide 5-4
Coefficients (or taps) are a0, a1, …aM-1
Role of initial conditions?

## Slide 19: Discrete-Time System Properties
3 - <number>
Let [n] be a discrete-time impulse function, a.k.a. Kronecker delta function:
Impulse response is response of discrete-time LTI system to discrete impulse function
  Example: delay by one sample
Finite impulse response filter
  Non-zero extent of impulse response is finite
  Can be in continuous time or discrete time
  Also called tapped delay line (slides 3-14, 3-18, 5-4)
[n]
h[n]
n
[n]
1
1
-1
2
3
-2
-3

## Slide 20: Discrete-Time System Properties
3 - <number>
Continuous time
  Linear?
  Time-invariant?
Discrete time
  Linear?
  Time-invariant?
f(t)
y(t)
f[n]
y[n]
See also slide 5-18

## Slide 21: Conclusion
3 - <number>
Continuous-time versus discrete-time: discrete means quantized in time
Analog versus digital: digital means quantized in amplitude
Digital signal processor
  Discrete-time and digital system
  Well-suited for implementing LTI digital filters
Example of discrete-time analog system?
Example of continuous-time digital system?