## Slide 1: Sampling and Aliasing
Notes: <number>

## Slide 2: Outline
4 - <number>
Data conversion
Sampling
  Time and frequency domains
  Sampling theorem
Aliasing
Bandpass sampling
Rolling shutter artifacts
Conclusion

## Slide 3: Data Conversion
Analog-to-Digital Conversion
  Lowpass filter has stopband frequency less than ½ fs to reduce aliasing due to sampling (enforce sampling theorem)
Digital-to-Analog Conversion
  Discrete-to-continuous conversion could be as simple as sample and hold
  Lowpass filter has stopband frequency less than ½ fs reduce artificial high frequencies
Analog Lowpass Filter
Discrete to Continuous Conversion
fs
Lecture 7
Analog Lowpass Filter
Quantizer
Sampler at sampling rate of fs
Lecture 8
Lecture 4
4 - <number>
Data Conversion

## Slide 4: Sampling: Time Domain
4 - <number>
Many signals originate in continuous-time
  Talking on cell phone, or playing acoustic music
By sampling a continuous-time signal at isolated, equally-spaced points in time, we obtain a sequence of numbers
  n  {…, -2, -1, 0, 1, 2,…}
  Ts is the sampling period.
Sampled analog waveform
impulse train
f(t)
t
Ts
Ts
Sampling - Review

## Slide 5: Sampling: Frequency Domain
4 - <number>
Sampling replicates spectrum of continuous-time signal at integer multiples of sampling frequency
Fourier series of impulse train where s = 2  fs

G()
s
s
s
s

F()
2fmax
-2fmax
Modulation by cos(2 s t)
Modulation by cos(s t)
How to recover F()?
Sampling - Review

## Slide 6: Sampling Theorem
4 - <number>
Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed from its samples x(n Ts) if samples taken at rate fs > 2 fmax
  Nyquist rate = 2 fmax
  Nyquist frequency = fs / 2
Example: Sampling audio signals
  Normal human hearing is from about 20 Hz to 20 kHz
  Apply lowpass filter before sampling to pass low frequencies up to 20 kHz and reject high frequencies
  Lowpass filter needs 10% of maximum passband frequency to roll off to zero (2 kHz rolloff in this case)
What happens if fs = 2 fmax?
Sampling - Review

## Slide 7: Sampling Theorem
4 - <number>
Assumption
Continuous-time signal has absolutely no frequency content above fmax
Sampling time is exactly the same between any two samples
Sequence of numbers obtained by sampling is represented in exact precision
Conversion of sequence to continuous time is ideal
In Practice
Sampling

## Slide 8: Sampling and Oversampling
4 - <number>
As sampling rate increases above Nyquist rate, sampled waveform looks more like original
Zero crossings: frequency content of a sinusoid
  Distance between two zero crossings: one half period
  With sampling theorem satisfied, sampled sinusoid crosses zero right number of times per period
  In some applications, frequency content matters not time-domain waveform shape
DSP First, Ch. 4, Sampling/Interpolation demo
  For username/password help
Sampling
link
link

## Slide 9: Aliasing
4 - <number>
Continuous-time sinusoid
  x(t) = A cos(2f0 t + )
Sample at Ts = 1/fs
  x[n] = x(Tsn) = A cos(2f0 Ts n + )
Keeping the sampling period same, sample
  y(t) = A cos(2(f0 + l fs) t + )
where l is an integer
  y[n] = y(Tsn) = A cos(2(f0 + lfs)Tsn + ) = A cos(2f0Tsn + 2lfsTsn + ) = A cos(2f0Tsn + 2ln + ) = A cos(2f0Tsn + ) = x[n]
  Here, fsTs = 1
  Since l is an integer, cos(x + 2 l) = cos(x)
y[n] indistinguishable from x[n]
Aliasing

## Slide 10: Aliasing
4 - <number>
Since l is any integer, a countable but infinite number of sinusoids give same sampled sequence
Frequencies f0 + l fs for l  0
  Called aliases of frequency f0 with respect to fs
  All aliased frequencies appear same as f0 due to sampling
Signal Processing First, Continuous to Discrete Sampling demo (con2dis)
Aliasing
link

## Slide 11: Aliasing
4 - <number>
Sinusoid sin(2  finput t) sampled at fs = 2000 samples/s with finput varied
Mirror image effect about finput = ½ fs gives rise to name of folding
Apparent frequency (Hz)
Input frequency, finput (Hz)
1000
1000
2000
3000
4000
fs = 2000 samples/s
Aliasing

## Slide 12: Bandpass Sampling
4 - <number>
Reduce sampling rate
  Bandwidth: f2 – f1
  Sampling rate fs must be greater than analog bandwidth fs > f2 – f1
  For replica to be centered at origin after sampling fcenter = ½(f1 + f2) = k fs
Practical issues
  Sampling clock tolerance: fcenter = k fs
  Effects of noise
Ideal Bandpass Spectrum
f1
f2
f
–f2
–f1
Sample at fs
Sampled Ideal Bandpass Spectrum
f1
f2
f
–f2
–f1
Lowpass filter to extract baseband
Bandpass Sampling

## Slide 13: Sampling for Up/Downconversion
Upconversion method
  Sampling plus bandpass filtering to extract intermediate frequency (IF) band with fIF = kIF fs
Downconversion method
  Bandpass sampling plus bandpass filtering to extract intermediate frequency (IF) band with fIF = kIF fs
f
fmax
-fmax
f
fs
fIF
fIF
fs
f1
f2
f
–f2
–f1
Sample at fs
f
–f2
–f1
-fIF
fIF
Bandpass Sampling

## Slide 14: Rolling Shutter Cameras
Smart phone and point-and-shoot cameras
  No (global) hardware shutter to reduce cost, size, weight
  Light continuously impinges on sensor array
  Artifacts due to relative motion between objects and camera
Rolling Shutter Artifacts
Figure from tutorial by Forssen et al. at 2012 IEEE Conf. on Computer Vision & Pattern Recognition

## Slide 15: Rolling Shutter Artifacts
Plucked guitar strings – global shutter camera
  String vibration is (correctly) damped sinusoid vs. time
“Guitar Oscillations Captured with iPhone 4”
  Rolling shutter (sampling) artifacts but not aliasing effects
Fast camera motion
  Pan camera fast left/right
  Pole wobbles and bends
  Building skewed
Rolling Shutter Artifacts
C. Jia and B. L. Evans, “Probabilistic 3-D Motion Estimation for Rolling Shutter Video Rectification from Visual and Inertial Measurements,” IEEE Multimedia Signal Proc. Workshop, 2012. Link to article.
Warped frame
Compensated using gyroscope readings (i.e. camera rotation) and video features
video
video

## Slide 16: Conclusion
4 - <number>
Sampling replicates spectrum of continuous-time signal at offsets that are integer multiples of sampling frequency
Sampling theorem gives necessary condition to reconstruct the continuous-time signal from its samples, but does not say how to do it
Aliasing occurs due to sampling
  Noise present at all frequencies
  A/D converter design tradeoffs to control impact of aliasing
Bandpass sampling reduces sampling rate significantly by using aliasing to our benefit
Conclusion