## Slide 1: Finite Impulse Response Filters

## Slide 2: Outline
5 - <number>
Many Roles for Filters
Convolution
Z-transforms
Linear time-invariant systems
  Transfer functions
  Frequency responses
Finite impulse response (FIR) filters
  Filter design with demonstration
  Cascading FIR filters demonstration
  Linear phase

## Slide 3: Many Roles for Filters
5 - <number>
Noise removal
  Signal and noise spectrally separated
  Example: bandpass filtering to suppress out-of-band noise
Analysis, synthesis, and compression
  Spectral analysis
  Examples: calculating power spectra (slides 14-10 and 14-11) and polyphase filter banks for pulse shaping (lecture 13)
Spectral shaping
  Data conversion (lectures 10 and 11)
  Channel equalization (slides 16-8 to 16-10)
  Symbol timing recovery (slides 13-17 to 13-20 and slide 16-7)
  Carrier frequency and phase recovery

## Slide 4: Finite Impulse Response (FIR) Filter
5 - <number>
Same as discrete-time tapped delay line (slide 3-18)
Impulse response h[n] has finite extent n = 0,…, M-1
z-1
z-1
z-1
…
…
x[n]

y[n]
h[0]
h[1]
h[2]
h[M-1]
x[n-1]
Discrete-time convolution

## Slide 5: Discrete-time Convolution Derivation
5 - <number>
Output y[n] for input x[n]
Any signal can be decomposed into sum of discrete impulses
Apply linear properties
Apply shift-invariance
Apply change of variables
y[n] = h[0] x[n] + h[1] x[n-1]
= ( x[n] + x[n-1] ) / 2
n
h[n]
Averaging filter impulse response
0
1
2
3
Review

## Slide 6: Convolution Comparison
5 - <number>
Continuous-time convolution of x(t) and h(t)
  For each t, compute different (possibly) infinite integral
In discrete-time, replace integral with summation
  For each n, compute different (possibly) infinite summation
LTI system
  Characterized uniquely by its impulse response
  Its output is convolution of input and impulse response
Review

## Slide 7: Convolution Demos
5 - <number>
The Johns Hopkins University Demonstrations
  http://www.jhu.edu/~signals
  Convolution applet to animate convolution of simple signals and hand-sketched signals
  Convolving two rectangular pulses of same width gives triangle with width of twice the width of rectangular pulses (see Appendix E in course reader for intermediate work)
t
1
x(t)
0
Ts
2Ts
Ts
t
1
h(t)
0
Ts
*
=
y(t)
Ts
t
What about convolving two pulses of different lengths?

## Slide 8: Z-transform Definition
5 - <number>
For discrete-time systems, z-transforms play same role as Laplace transforms do in continuous-time
  Inverse transform requires contour integration over closed contour (region) R
  Contour integration covered in a Complex Analysis course
Compute forward and inverse transforms using transform pairs and properties
Bilateral Forward z-transform
Bilateral Inverse z-transform
Review

## Slide 9: Three Common Z-transform Pairs
5 - <number>
h[n] = [n]
  Region of convergence: entire z-plane
h[n] = [n-1]
  Region of convergence: entire z-plane except z = 0
  h[n-1]  z-1 H(z)
h[n] = an u[n]
  Region of convergence for summation: |z| > |a|
  |z| > |a| is the complement of a disk
Finite extent sequences
Infinite extent sequence
Review

## Slide 10: Region of Convergence
5 - <number>
Region of the complex z-plane for which forward z-transform converges
Im{z}
Re{z}
Entire plane
Im{z}
Re{z}
Complement of a disk
Im{z}
Re{z}
Disk
Im{z}
Re{z}
Intersection of a disk and complement of a disk
Four possibilities (z = 0 is special case that may or may not be included)
Review

## Slide 11: System Transfer Function
5 - <number>
Z-transform of system’s impulse response
  Impulse response uniquely represents an LTI system
Example: FIR filter with M taps (slide 5-4)
  Transfer function H(z) is polynomial in powers of z -1
  Region of convergence (ROC) is entire z-plane except z = 0
Since ROC includes unit circle, substitute z = e j  into transfer function to obtain frequency response
Review

## Slide 12: Example: Ideal Delay
5 - <number>
Continuous Time
  Delay by T seconds
  Impulse response
  Frequency response
Discrete Time
  Delay by 1 sample
  Impulse response
  Frequency response
x(t)
y(t)
x[n]
y[n]
Linear Phase
Allpass Filter
w = W T
Conditions
Zero Initial

## Slide 13: Linear Time-Invariant Systems
5 - <number>
Fundamental Theorem of Linear Systems
  If a complex sinusoid were input into an LTI system, then output would be input scaled by frequency response of LTI system (evaluated at complex sinusoidal frequency)
  Scaling may attenuate input signal and shift it in phase
  Example in continuous time: see handout F
  Example in discrete time. Let x[n] = e j n,
  H() is discrete-time Fourier transform of h[n] H() is also called the frequency response
H()
x[n] * h[n]

## Slide 14: Frequency Response
5 - <number>
Continuous-time LTI system
Discrete-time LTI system
For real-valued impulse response H(e -j ω) = H*(e j ω)
  Input
  Output

## Slide 15: Frequency Response
5 - <number>
System response to complex sinusoid e j  n for all possible frequencies  in radians per sample:
  Lowpass filter: passes low and attenuates high frequencies
  Linear phase: must be FIR filter with impulse response that is symmetric or anti-symmetric about its midpoint
Not all FIR filters exhibit linear phase

|H()|

|H()|
p
stop
stop
p
passband
stopband
stopband
Linear phase

## Slide 16: Filter Design
5 - <number>
Specify a desired piecewise constant magnitude response
Lowpass filter example
   [0, p], mag  [1-p, 1]
   [s, ], mag  [0, s]
  Transition band unspecified
Symmetric FIR filter design methods
  Windowing
  Least squares
  Remez (Parks-McClellan)
1
s
p

p
s
Desired Magnitude Response
Passband
Stopband
Transition band

Red region is forbidden
Lowpass Filter Example
p passband ripple s stopband ripple
forbidden
forbidden
forbidden
Achtung!

## Slide 17: Example: Two-Tap Averaging Filter
5 - <number>
Linear Phase
Input-output relationship
Impulse response
Frequency response
n
h[n]
Two-tap averaging filter
½
2
3
1
z-1
x[n]

y[n]
h[0]
h[1]
x[n-1]

## Slide 18: Example: First-Order Difference
5 - <number>
Linear Phase
Input-output relationship
Impulse response
Frequency response
n
h[n]
First-order difference
½
2
3
- ½
Generalized

## Slide 19: Cascading FIR Filters Demo
5 - <number>
Five-tap discrete-time averaging FIR filter with input x[n] and output y[n]
  Standard averaging filtering scaled by 5
  Lowpass filter (smooth/blur input signal)
  Impulse response is {1, 1, 1, 1, 1}
First-order difference FIR filter
  Highpass filter (sharpens input signal)
  Impulse response is {1, -1}
n
h[n]
First-order difference impulse response
1
-1
2
3

## Slide 20: Cascading FIR Filters Demo
5 - <number>
DSP First, Ch. 6, Freq. Response of FIR Filters
  http://www.ece.gatech.edu/research/DSP/DSPFirstCD/visible/chapters/6firfreq/demos/blockd/index.htm
  For username/password help
From lowpass filter to highpass filter
  original image  blurred image  sharpened/blurred image
From highpass to lowpass filter
  original image  sharpened image  blurred/sharpened image
Frequencies that are zeroed out can never be recovered (e.g. DC is zeroed out by highpass filter)
Order of two LTI systems in cascade can be switched under the assumption that computations are performed in exact precision

## Slide 21: Cascading FIR Filters Demo
5 - <number>
Input image is 256 x 256 matrix
  Each pixel represented by eight-bit number in [0, 255]
  0 is black and 255 is white for monitor display
Each filter applied along row then column
  Averaging filter adds five numbers to create output pixel
  Difference filter subtracts two numbers to create output pixel
Full output precision is 16 bits per pixel
  Demonstration uses double-precision floating-point data and arithmetic (53 bits of mantissa + sign; 11 bits for exponent)
  No output precision was harmed in the making of this demo 

## Slide 22: Importance of Linear Phase
5 - <number>
Speech signals
  Use phase differences in arrival to locate speaker
  Once speaker is located, ears are relatively insensitive to phase distortion in speech from that speaker
  Used in speech compression in cell phones)
Linear phase crucial
  Audio
  Images
  Communication systems
Linear phase response
  Need FIR filters
  Realizable IIR filters cannot achieve linear phase response over all frequencies
d = c t

## Slide 23: Importance of Linear Phase
For images, vital visual information in phase
Original image is from Matlab
5 - <number>
Take FFT of image
Set phase to zero
Take inverse FFT
Take FFT of image
Set magnitude to one
Take inverse FFT
Keep imaginary part
Take FFT of image
Set magnitude to one
Take inverse FFT
Keep real part
code
http://users.ece.utexas.edu/~bevans/courses/rtdsp/lectures/05_FIR_Filters/Original%20Image.tif
Notes: %%% ImagePhaseDemo.m
%%%
%%% Programmer: Prof. Brian L. Evans
%%% Organization: The University of Texas at Austin
%%% Created: February 21, 2008
%%%
%%% Requires the image processing toolbox in Matlab
aerialview = imread('westconcordorthophoto.png', 'PNG');
grayramp = 0 : 1/255 : 1;
graymap = [grayramp; grayramp; grayramp]';
figure(1);
imshow(aerialview);
colormap(graymap);
title('Original image');
aerialviewfft = fft2(single(aerialview));
aerialviewfftmag = abs(aerialviewfft);
aerialview2fp = ifft2(aerialviewfftmag);
%%% Show the contribution in the spatial domain of the magnitude of the FFT
%%% of the original image
figure(2);
<number>

## Slide 24: Finite Impulse Response Filters
5 - <number>
Duration of impulse response h[n] is finite, i.e. zero-valued for n outside interval [0, M-1]:
  Output depends on current input and previous M-1 inputs
  Summation to compute y[k] reduces to a vector dot product between M input samples in the vector
  and M values of the impulse response in vector
What instruction set architecture features would you add to accelerate FIR filtering?