## Slide 1: Quantization

## Slide 2: Outline
8 - <number>
Introduction
Uniform amplitude quantization
Audio
Quantization error (noise) analysis
Noise immunity in communication systems
Conclusion
Digital vs. analog audio (optional)

## Slide 3: Resolution
8 - <number>
Human eyes
  Sample received light on 2-D grid
  Photoreceptor density in retina falls off exponentially away from fovea (point of focus)
  Respond logarithmically to intensity (amplitude) of light
Human ears
  Respond to frequencies in 20 Hz to 20 kHz range
  Respond logarithmically in both intensity (amplitude) of sound (pressure waves) and frequency (octaves)
  Log-log plot for hearing response vs. frequency
Foveated grid: point of focus in middle

## Slide 4: Data Conversion
Analog-to-Digital Conversion
  Lowpass filter has stopband frequency less than ½ fs to reduce aliasing due to sampling (enforce sampling theorem)
  System properties: Linearity
  Time-Invariance
  Causality
  Memory
Quantization is an interpretation of a continuous quantity by a finite set of discrete values
Analog Lowpass Filter
Quantizer
Sampler at sampling rate of fs
Lecture 8
Lecture 4
8 - <number>

## Slide 5: Uniform Amplitude Quantization
8 - <number>
Round to nearest integer (midtread)
  Quantize amplitude to levels {-2, -1, 0, 1}
  Step size  for linear region of operation
  Represent levels by {00, 01, 10, 11} or {10, 11, 00, 01} …
  Latter is two's complement representation
Rounding with offset (midrise)
  Quantize to levels {-3/2, -1/2, 1/2, 3/2}
  Represent levels by {11, 10, 00, 01} …
  Step size
x
Q[x]
1
-2
-2
1
x
Q[x]
1
-2
-1
1
2
Used in slide 8-10

## Slide 6: Handling Overflow
8 - <number>
Example: Consider set of integers {-2, -1, 0, 1}
  Represented in two's complement system {10, 11, 00, 01}.
  Add (–1) + (–1) + (–1) + 1 + 1
  Intermediate computations are – 2, 1, –2, –1 for wraparound arithmetic and –2, –2, –1, 0 for saturation arithmetic
Saturation: When to use it?
  If input value greater than maximum, set it to maximum; if less than minimum, set it to minimum
  Used in quantizers, filtering, other signal processing operators
Wraparound: When to use it?
  Addition performed modulo set of integers
  Used in address calculations, array indexing
Native support in MMX and DSPs
Standard two’s complement behavior

## Slide 7: Audio Compact Discs (CDs)
8 - <number>
Analog lowpass filter
  Passband 0–20 kHz
  Transition band 20–22 kHz
  Stopband frequency at 22 kHz (i.e. 10% rolloff)
  Designed to control amount of aliasing that occurs (and hence called an anti-aliasing filter)
Signal-to-noise ratio when quantizing to B bits
  1.76 dB + 6.02 dB/bit * B = 98.08 dB
  This loose upper bound is derived later in slides 8-10 to 8-14
  In practice, audio CDs have dynamic range of about 95 dB
Analog Lowpass Filter
Quantizer
Sample at 44.1 kHz
16

## Slide 8: Dynamic Range
8 - <number>
Signal-to-noise ratio in dB
For linear systems, dynamic range equals SNR
Lowpass anti-aliasing filter for audio CD format
  Ideal magnitude response of 0 dB over passband
  Astopband = 0 dB  Noise Power in dB = -98.08 dB
Why 10 log10 ?
For amplitude A,
|A|dB = 20 log10 |A|
With power P  |A|2 ,
PdB = 10 log10 |A|2
PdB = 20 log10 |A|

## Slide 9: Dynamic Range in Audio
8 - <number>
Sound Pressure Level (SPL)
  Reference in dB SPL is 20 Pa (threshold of hearing)
  40 dB SPL noise in typical living room
  120 dB SPL threshold of pain
  80 dB SPL resulting dynamic range
Estimating dynamic range
  Find maximum RMS output of the linear system with some specified amount of distortion, typically 1%
  Find RMS output of system with small input signal (e.g. -60 dB of full scale) with input signal removed from output
  Divide (b) into (a) to find the dynamic range
Anechoic room 10 dB
Whisper 30 dB
Rainfall 50 dB
Dishwasher 60 dB
City Traffic 85 dB
Leaf Blower 110 dB
Siren 120 dB
Slide by Dr. Thomas D. Kite, Audio Precision

## Slide 10: Quantization Error (Noise) Analysis
8 - <number>
Quantization output
  Input signal plus noise
  Noise is difference of output and input signals
Signal-to-noise ratio (SNR) derivation
  Quantize to B bits
  Quantization error
Assumptions
  m  (-mmax, mmax)
  Uniform midrise quantizer
  Input does not overload quantizer
  Quantization error (noise) is uniformly distributed
  Number of quantization levels L = 2B is large enough so that
QB[ · ]
m
v

## Slide 11: Quantization Error (Noise) Analysis
8 - <number>
Deterministic signal x(t) w/ Fourier transform X(f)
  Power spectrum is square of absolute value of magnitude response (phase is ignored)
  Multiplication in Fourier domain is convolution in time domain
  Conjugation in Fourier domain is reversal & conjugation in time
Autocorrelation of x(t)
  Maximum value (when it exists) is at Rx(0)
  Rx() is even symmetric, i.e. Rx() = Rx(-)
t
1
x(t)
0
Ts

Rx()
-Ts
Ts
Ts

## Slide 12: Quantization Error (Noise) Analysis
8 - <number>
Two-sided random signal n(t)
  Fourier transform may not exist, but power spectrum exists
  For zero-mean Gaussian random process n(t) with variance 2
Estimate noise power spectrum in Matlab
N = 16384; % finite no. of samples gaussianNoise = randn(N,1); plot( abs(fft(gaussianNoise)) .^ 2 );
approximate noise floor

## Slide 13: Quantization Error (Noise) Analysis
8 - <number>
Quantizer step size
Quantization error
  q is sample of zero-mean random process Q
  q is uniformly distributed
Input power: Paverage,m
  SNR exponential in B
  Adding 1 bit increases SNR by factor of 4
Derivation of SNR in deciBels on next slide

## Slide 14: Quantization Error (Noise) Analysis
8 - <number>
SNR in dB = constant + 6.02 dB/bit * B
What is maximum number of bits of resolution for
  Audio CD signal with SNR of 95 dB
  TI TLV320AIC23B stereo codec used on TI DSP board
  ADC 90 dB SNR (14.6 bits) and 80 dB THD (13 bits) page 2-2
  DAC has 100 dB SNR (16 bits) and 88 dB THD (14.3 bits) page 2-3
1.76 and 1.17 are common constants used in audio
Loose upper bound

## Slide 15: Total Harmonic Distortion (THD)
A measure of nonlinear distortion in a system
  Input is a sinusoidal signal of a single fixed frequency
  From output of system, the input sinusoid signal is subtracted
  SNR measure is then taken
In audio, sinusoidal signal is often at 1 kHz
  “Sweet spot” for human hearing – strongest response
Example
  “System” is ADC
  Calibrated DAC
  Signal is x(t)
  “Noise” is n(t)
A/D Converter
~
1 kHz
D/A Converter
~
fs
+
−
Delay
x(t)
n(t)
+

## Slide 16: Noise Immunity at Receiver Output
8 - <number>
Depends on modulation, average transmit power, transmission bandwidth and channel noise
Analog communications (receiver output SNR)
  “When the carrier to noise ratio is high, an increase in the transmission bandwidth BT provides a corresponding quadratic increase in the output signal-to-noise ratio or figure of merit of the [wideband] FM system.” – Simon Haykin, Communication Systems, 4th ed., p. 147.
Digital communications (receiver symbol error rate)
  “For code division multiple access (CDMA) spread spectrum communications, probability of symbol error decreases exponentially with transmission bandwidth BT” – Andrew Viterbi, CDMA: Principles of Spread Spectrum Communications, 1995, pp. 34-36.

## Slide 17: Conclusion
8 - <number>
Amplitude quantization approximates its input by a discrete amplitude taken from finite set of values
Loose upper bound in signal-to-noise ratio of a uniform amplitude quantizer with output of B bits
  Best case: 6 dB of SNR gained for each bit added to quantizer
  Key limitation: assumes large number of levels L = 2B
Best case improvement in noise immunity for communication systems
  Analog: improvement quadratic in transmission bandwidth
  Digital: improvement exponential in transmission bandwidth

## Slide 18: Digital vs. Analog Audio
8 - <number>
An audio engineer claims to notice differences between analog vinyl master recording and the remixed CD version. Is this possible?
  When digitizing an analog recording, the maximum voltage level for the quantizer is the maximum volume in the track
  Samples are uniformly quantized (to 216 levels in this case although early CDs circa 1982 were recorded at 14 bits)
  Problem on a track with both loud and quiet portions, which occurs often in classical pieces
  When track is quiet, relative error in quantizing samples grows
  Contrast this with analog media such as vinyl which responds linearly to quiet portions
Optional

## Slide 19: Digital vs. Analog Audio
8 - <number>
Analog and digital media response to voltage v
For a large dynamic range
  Analog media: records voltages above V0 with distortion
  Digital media: clips voltages above V0 to V0
Audio CDs use delta-sigma modulation
  Effective dynamic range of 19 bits for lower frequencies but lower than 16 bits for higher frequencies
  Human hearing is more sensitive at lower frequencies
Optional