## Slide 1: Channel Impairments

## Slide 2: Outline
Analog communication systems
Channel impairments
Hybrid communication systems
Analog pulse amplitude modulation

## Slide 3: Communication System Structure
Information sources
  Voice, music, images, video, and data (baseband signals)
Transmitter
  Signal processing block lowpass filters message signal
  Carrier circuits block upconverts baseband signal and bandpass filters to enforce transmission band
m(t)
Signal Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Signal Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Communication Systems
baseband
baseband
bandpass
bandpass
baseband
baseband

## Slide 4: Communication Channel
Transmission medium
  Wireline (twisted pair, coaxial, fiber optics)
  Wireless (indoor/air, outdoor/air, underwater, space)
Propagating signals degrade over distance
Repeaters can strengthen signal and reduce noise
m(t)
Signal Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Signal Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Review
baseband
baseband
bandpass
bandpass
baseband
baseband

## Slide 5: Wireline Channel Impairments
Linear time-invariant effects
  Attenuation: dependent on channel frequency response
  Spreading: finite extent of each transmitted pulse increases
Th
t
1
Tb
t
A
Tb
-A
Model channel as LTI system with impulse response h(t)
Communication Channel
input
output
x(t)
y(t)
t
-A Th
t
Th+Tb
Th
Assume that Th < Tb
t
Th+Tb
Th
A Th
Bit of ‘0’ or ‘1’

## Slide 6: Wireline Channel Impairments
Linear time-varying effects
  Phase jitter: sinusoid at same fixed frequency experiences different phase shifts when passing through channel
  Visualize phase jitter in periodic waveform by plotting it over one period, superimposing second period on the first, etc.
Nonlinear effects
  Harmonics: due to quantization, voltage rectifiers, squaring devices, power amplifiers, etc.
  Additive noise: arises from many sources in transmitter, channel, and receiver (e.g. thermal noise)
  Additive interference: arises from other systems operating in transmission band (e.g. microwave oven in 2.4 GHz band)

## Slide 7
Home Power Line Noise/Interference
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011

## Slide 8
Spectrally-Shaped Background Noise
Home Power Line Noise/Interference
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011

## Slide 9
Spectrally-Shaped Background Noise
Narrowband Interference
Home Power Line Noise/Interference
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011

## Slide 10
Spectrally-Shaped Background Noise
Narrowband Interference
Periodic and
Asynchronous Interference
Home Power Line Noise/Interference
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011

## Slide 11: Wireless Channel Impairments
Same as wireline channel impairments plus others
Fading: multiplicative noise
  Talking on a mobile phone and reception fades in and out
  Represented as time-varying gain that follows a particular probability distribution
Simplified channel model for fading, LTI effects and additive noise
FIR
+
noise

## Slide 12: Hybrid Communication Systems
Mixed analog and digital signal processing in the transmitter and receiver
  Example: message signal is digital but broadcast over an analog channel (compressed speech in digital cell phones)
Signal processing in the transmitter
Signal processing in the receiver
m(t)
A/D Converter
Error Correcting Codes
Digital Signaling
Decoder
Waveform Generator
Equalizer
Detection
digital sequence
digital sequence
code
baseband signal
D/A Converter
A/D
D/A

## Slide 13: Pulse Amplitude Modulation (PAM)
Amplitude of periodic pulse train is varied with a sampled message signal m(t)
  Digital PAM: coded pulses of the sampled and quantized message signal are transmitted (lectures 13 and 14)
  Analog PAM: periodic pulse train with period Ts is the carrier (below)
t
Ts
T
T+Ts
2Ts
p(t)
m(t)
s(t) = p(t) m(t)
Optional

## Slide 14: Analog PAM
Pulse amplitude varied with amplitude of sampled message
  Sample message every Ts
  Hold sample for T seconds (T < Ts)
  Bandwidth  1/T
Transmitted signal
  h(t) is a rectangular pulse of duration T units
t
m(t)
Ts
T
T+Ts
2Ts
s(t)
m(0)
m(Ts)
T
t
h(t)
1
sample
hold
Optional

## Slide 15: Analog PAM
Transmitted signal
Fourier transform
Equalization of sample and hold distortion added in transmitter
  H(f) causes amplitude distortion and delay of T/2
  Equalize amplitude distortion by post-filtering with magnitude response
  Negligible distortion (less than 0.5%) if
msampled(t)
Optional

## Slide 16: Analog PAM
Requires transmitted pulses to
  Not be significantly corrupted in amplitude
  Experience roughly uniform delay
Useful in time-division multiplexing
  public switched telephone network T1 (E1) line time-division multiplexes 24 (32) voice channels
  Bit rate of 1.544 (2.048) Mbps for duty cycle < 10%
Other analog pulse modulation methods
  Pulse-duration modulation (PDM), a.k.a. pulse width modulation (PWM)
  Pulse-position modulation (PPM): used in some optical pulse modulation systems.
Optional