## Slide 1: Digital Pulse Amplitude Modulation (PAM)

## Slide 2: Outline
13 - <number>
Introduction
Pulse shaping
Pulse shaping filter bank
Design tradeoffs
Symbol recovery

## Slide 3: Introduction
13 - <number>
Convert bit stream into pulse stream
  Group stream of bits into symbols of J bits
  Represent symbol of bits by unique amplitude
  Scale pulse shape by amplitude
M-level PAM or simply M-PAM (M = 2J)
  Symbol period is Tsym and bit rate is J fsym
  Impulse train has impulses separated by Tsym
  Pulse shape may last one or more symbol periods
4-PAM Constellation Map
d
d
3 d
3 d
00
01
10
11
input
output
Serial/ Parallel
Map to PAM
constellation
an
1
J
bit stream
J bits per symbol
Pulse shaper gTsym(t)
s*(t)
symbol amplitude
baseband waveform
Impulse modulator
impulse train
Notes: <number>

## Slide 4: Pulse Shaping
13 - <number>
Without pulse shaping
  One impulse per symbol period
  Infinite bandwidth used (not practical)
Limit bandwidth by pulse shaping (FIR filtering)
  Convolution of discrete-time signal ak and continuous-time pulse shape
  For a pulse shape lasting Ng Tsym seconds, Ng pulses overlap in each symbol period
k is a symbol index
Serial/ Parallel
Map to PAM
constellation
an
1
J
bit stream
J bits per symbol
Pulse shaper gTsym(t)
s*(t)
symbol amplitude
baseband waveform
Impulse modulator
impulse train

## Slide 5: 2-PAM Transmission
2-PAM example (right)
  Raised cosine pulse with peak value of 1
  What are d and Tsym ?
  How does maximum amplitude relate to d?
Highest frequency ½ fsym
  Alternating symbol amplitudes +d, -d, +d, …
13 - <number>
Serial/ Parallel
Map to PAM
constellation
an
1
J
bit stream
J bits per symbol
Pulse shaper gTsym(t)
s*(t)
symbol amplitude
baseband waveform
Impulse modulator
impulse train
time (ms)

## Slide 6: PAM Transmission
Transmitted signal
Sample at sampling time Ts : let t = (n L + m) Ts
  L samples per symbol period Tsym i.e. Tsym = L Ts
  n is the index of the current symbol period being transmitted
  m is a sample index within nth symbol (i.e., m = 0, 1, …, L-1)
L
Serial/ Parallel
Map to PAM
constellation
an
1
J
bit stream
J bits per symbol
Pulse shaper gTsym[m]
s*(t)
symbol amplitude
baseband waveform
impulse train
D/A
baseband waveform

## Slide 7: Pulse Shaping Block Diagram
13 - <number>
Upsampling by L denoted as L
  Outputs input sample followed by L-1 zeros
  Upsampling by L converts symbol rate to sampling rate
Pulse shaping (FIR) filter gTsym[m]
  Fills in zero values generated by upsampler
  Multiplies by zero most of time (L-1 out of every L times)
D/A
Transmit
Filter
an
gTsym[m]
L
symbol rate
sampling rate
sampling rate
cont. time
cont. time
s*(t)

## Slide 8: Digital Interpolation Example
13 - <number>
Upsampling by 4 (denoted by 4)
  Output input sample followed by 3 zeros
  Four times the samples on output as input
  Increases sampling rate by factor of 4
FIR filter performs interpolation
  Lowpass filter with stopband frequency stopband   / 4
  For fsampling = 176.4 kHz, =  / 4 corresponds to 22.05 kHz
Digital 4x Oversampling Filter
16 bits 44.1 kHz
28 bits 176.4 kHz
4
FIR Filter
16 bits 176.4 kHz
1
2
Input to Upsampler by 4
n
0
n’
Output of Upsampler by 4
1
2
3
4
5
6
7
8
0
1
2
Output of FIR Filter
3
4
5
6
7
8
n’
0

## Slide 9: Pulse Shaping Filter Bank Example
13 - <number>
L = 4 samples per symbol
Pulse shape g[m] lasts for 2 symbols (8 samples)
encoding
↑4
g[m]
bits
…a2a1a0
…000a1000a0
s[m]
x[m]
s[m] = x[m] * g[m]
s[0] = a0 g[0] s[1] = a0 g[1] s[2] = a0 g[2] s[3] = a0 g[3]
s[4] = a0 g[4] + a1 g[0] s[5] = a0 g[5] + a1 g[1] s[6] = a0 g[6] + a1 g[2] s[7] = a0 g[7] + a1 g[3]
L polyphase filters
{g[0],g[4]}
{g[1],g[5]}
{g[2],g[6]}
{g[3],g[7]}
s[m]
…,s[4],s[0]
…,s[5],s[1]
…,s[6],s[2]
…,s[7],s[3]
…,a1,a0
m=0
Commutator (Periodic)
Filter Bank

## Slide 10: Pulse Shaping Filter Bank
13 - <number>
Simplify by avoiding multiplication by zero
  Split long pulse shaping filter into L short polyphase filters operating at symbol rate
gTsym,0[n]
gTsym,1[n]
gTsym,L-1[n]
an
D/A
Transmit
Filter
s(Ln)
s(Ln+1)
s(Ln+(L-1))
Filter Bank Implementation
D/A
Transmit
Filter
an
gTsym[m]
L
symbol rate
sampling rate
sampling rate
cont. time
cont. time

## Slide 11: Pulse Shaping Filter Bank Example
13 - <number>
Pulse length 24 samples and L = 4 samples/symbol
Derivation: let t = (n + m/L) Tsym
Define mth polyphase filter
Four six-tap polyphase filters (next slide)
Six pulses contribute to each output sample

## Slide 12: Pulse Shaping Filter Bank Example
13 - <number>
24 samples in pulse
x marks samples of polyphase filter
4 samples per symbol
Polyphase filter 0 response is the first sample of the pulse shape plus every fourth sample after that
Polyphase filter 0 has only one non-zero sample.
gTsym,0[n]

## Slide 13: Pulse Shaping Filter Bank Example
13 - <number>
24 samples in pulse
x marks samples of polyphase filter
4 samples per symbol
Polyphase filter 1 response is the second sample of the pulse shape plus every fourth sample after that
gTsym,1[n]

## Slide 14: Pulse Shaping Filter Bank Example
13 - <number>
24 samples in pulse
x marks samples of polyphase filter
4 samples per symbol
Polyphase filter 2 response is the third sample of the pulse shape plus every fourth sample after that
gTsym,2[n]

## Slide 15: Pulse Shaping Filter Bank Example
13 - <number>
24 samples in pulse
x marks samples of polyphase filter
4 samples per symbol
Polyphase filter 3 response is the fourth sample of the pulse shape plus every fourth sample after that
gTsym,3[n]

## Slide 16: Pulse Shaping Design Tradeoffs
13 - <number>
 | Computation in MACs/s | Memory size in words | Memory reads in words/s | Memory writes in words/s
Direct structure (slide 13-7) | (L Ng)(L fsym) |  |  | 
Filter bank structure (slide 13-10) | L Ng fsym |  |  | 
fsym symbol rate L samples/symbol Ng duration of pulse shape in symbol periods

## Slide 17: Symbol Clock Recovery
13 - <number>
Transmitter and receiver normally have different oscillator circuits
Critical for receiver to sample at correct time instances to have max signal power and min ISI
Receiver should try to synchronize with transmitter clock (symbol frequency and phase)
  First extract clock information from received signal
  Then either adjust analog-to-digital converter or interpolate
Next slides develop adjustment to A/D converter
Also, see Handout M in the reader
Optional

## Slide 18: Symbol Clock Recovery
13 - <number>
g1(t) is impulse response of LTI composite channel of pulse shaper, noise-free channel, receive filter
Optional
Receive
B()
Squarer
BPF
H()
PLL
x(t)
q(t)
q2(t)
p(t)
z(t)
E{ak am} = a2 [k-m]
g1(t) is deterministic
s*(t) is transmitted signal
Periodic with period Tsym

## Slide 19: Symbol Clock Recovery
13 - <number>
Fourier series representation of E{ p(t) }
In terms of g1(t) and using Parseval’s relation
Fourier series representation of E{ z(t) }
where
Optional
Receive
B()
Squarer
BPF
H()
PLL
x(t)
q(t)
q2(t)
p(t)
z(t)

## Slide 20: Symbol Clock Recovery
13 - <number>
With G1() = X() B()
  Choose B() to pass  ½sym  pk = 0 except k = -1, 0, 1
  Choose H() to pass sym  Zk = 0 except k = -1, 1
B() is lowpass filter with passband = ½ sym
H() is bandpass filter with center frequency sym
Optional
Receive
B()
Squarer
BPF
H()
PLL
x(t)
q(t)
q2(t)
p(t)
z(t)