## Slide 1: Matched Filtering and Digital Pulse Amplitude Modulation (PAM)

## Slide 2: Outline
14 - <number>
Transmitting one bit at a time
Matched filtering
PAM system
Intersymbol interference
Communication performance
  Bit error probability for binary signals
  Symbol error probability for M-ary (multilevel) signals
Eye diagram
Part I
Part II

## Slide 3: Transmitting One Bit
14 - <number>
Transmission on communication channels is analog
One way to transmit digital information is called 2-level digital pulse amplitude modulation (PAM)
b
t
A
‘1’ bit
Additive Noise Channel
input
output
x(t)
y(t)
b
-A
‘0’ bit
t
How does the receiver decide which bit was sent?
receive‘1’ bit
b
t
A
receive ‘0’ bit
b
-A
t

## Slide 4: Transmitting One Bit
14 - <number>
Two-level digital pulse amplitude modulation over channel that has memory but does not add noise
h
t
1
b
t
A
‘1’ bit
b
-A
‘0’ bit
Model channel as LTI system with impulse response c(t)
LTI Channel
input
output
x(t)
y(t)
t
-A Th
receive ‘0’ bit
t
h+b
h
Assume that Th < Tb
t
receive‘1’ bit
h+b
h
A Th

## Slide 5: Transmitting Two Bits (Interference)
14 - <number>
Transmitting two bits (pulses) back-to-back will cause overlap (interference) at the receiver
Sample y(t) at Tb, 2 Tb, …, and threshold with threshold of zero
How do we prevent intersymbol interference (ISI) at the receiver?
h
t
1
Assume that Th < Tb
t
b
A
‘1’ bit
‘0’ bit
b
*
=
-A Th
t
b
‘1’ bit
‘0’ bit
h+b
Intersymbol interference

## Slide 6: Preventing ISI at Receiver
14 - <number>
Option #1: wait Th seconds between pulses in transmitter (called guard period or guard interval)
  Disadvantages?
Option #2: use channel equalizer in receiver
  FIR filter designed via training sequences sent by transmitter
  Design goal: cascade of channel memory and channel equalizer should give all-pass frequency response
h
t
1
Assume that Th < Tb
*
=
t
b
A
‘1’ bit
‘0’ bit
h+b
t
-A Th
b
‘1’ bit
‘0’ bit
h+b
h

## Slide 7: Digital 2-level PAM System
14 - <number>
Transmitted signal
Requires synchronization of clocks between transmitter and receiver
Transmitter
Channel
Receiver
bi
Clock Tb
PAM
g(t)
c(t)
h(t)
1
0
ak{-A,A}
s(t)
x(t)
y(t)
y(ti)
AWGN
w(t)
Decision
Maker
Threshold 
Sample at
t=iTb
bits
Clock Tb
pulse shaper
matched filter
N(0, N0/2)
p0 is the probability bit ‘0’ sent
bits

## Slide 8: Matched Filter
14 - <number>
Detection of pulse in presence of additive noise
  Receiver knows what pulse shape it is looking for
  Channel memory ignored (assumed compensated by other means, e.g. channel equalizer in receiver)
Additive white Gaussian noise (AWGN) with zero mean and variance N0 /2
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
T is the symbol period

## Slide 9: Matched Filter Derivation
14 - <number>
Design of matched filter
  Maximize signal power i.e. power of at t = T
  Minimize noise i.e. power of
Combine design criteria
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
T is the symbol period

## Slide 10: Power Spectra
14 - <number>
Deterministic signal x(t) w/ Fourier transform X(f)
  Power spectrum is square of absolute value of magnitude response (phase is ignored)
  Multiplication in Fourier domain is convolution in time domain
  Conjugation in Fourier domain is reversal & conjugation in time
Autocorrelation of x(t)
  Maximum value (when it exists) is at Rx(0)
  Rx() is even symmetric, i.e. Rx() = Rx(-)
t
1
x(t)
0
Ts

Rx()
-Ts
Ts
Ts

## Slide 11: Power Spectra
Two-sided random signal n(t)
  Fourier transform may not exist, but power spectrum exists
  For zero-mean Gaussian random process n(t) with variance 2
Estimate noise power spectrum in Matlab
N = 16384; % finite no. of samples gaussianNoise = randn(N,1); plot( abs(fft(gaussianNoise)) .^ 2 );
approximate noise floor
14 - <number>

## Slide 12: Matched Filter Derivation
14 - <number>
Noise
Signal
f
Noise power spectrum SW(f)
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
AWGN
Matched filter
T is the symbol period

## Slide 13: Matched Filter Derivation
14 - <number>
Find h(t) that maximizes pulse peak SNR 
Schwartz’s inequality
  For vectors:
  For functions: upper bound reached iff

a
b

## Slide 14: Matched Filter Derivation
14 - <number>
T is the symbol period

## Slide 15: Matched Filter
14 - <number>
Impulse response is hopt(t) = k g*(T - t)
  Symbol period T, transmitter pulse shape g(t) and gain k
  Scaled, conjugated, time-reversed, and shifted version of g(t)
  Duration and shape determined by pulse shape g(t)
Maximizes peak pulse SNR
  Does not depend on pulse shape g(t)
  Proportional to signal energy (energy per bit) Eb
  Inversely proportional to power spectral density of noise

## Slide 16: Matched Filter for Rectangular Pulse
14 - <number>
t=nT
T
Matched filter for causal rectangular pulse shape
  Impulse response is causal rectangular pulse of same duration
Convolve input with rectangular pulse of duration T sec and sample result at T sec is same as
  First, integrate for T sec
  Second, sample at symbol period T sec
  Third, reset integration for next time period
Integrate and dump circuit
Sample and dump
h(t) = ___

## Slide 17: Digital 2-level PAM System
14 - <number>
Transmitted signal
Requires synchronization of clocks between transmitter and receiver
Transmitter
Channel
Receiver
bi
Clock Tb
PAM
g(t)
c(t)
h(t)
1
0
ak{-A,A}
s(t)
x(t)
y(t)
y(ti)
AWGN
w(t)
Decision
Maker
Threshold 
Sample at
t=iTb
bits
Clock Tb
pulse shaper
matched filter
N(0, N0/2)
p0 is the probability bit ‘0’ sent
bits

## Slide 18: Digital 2-level PAM System
14 - <number>
Why is g(t) a pulse and not an impulse?
  Otherwise, s(t) would require infinite bandwidth
  We limit its bandwidth by using a pulse shaping filter
Neglecting noise, would like y(t) = g(t) * c(t) * h(t) to be a pulse, i.e. y(t) =  p(t) , to eliminate ISI
actual value (note that ti = i Tb)
intersymbol interference (ISI)
noise
p(t) is centered at origin

## Slide 19: Eliminating ISI in PAM
14 - <number>
One choice for P(f) is a rectangular pulse
  W is the bandwidth of the system
  Inverse Fourier transform of a rectangular pulse is is a sinc function
This is called the Ideal Nyquist Channel
It is not realizable because pulse shape is not causal and is infinite in duration

## Slide 20: Eliminating ISI in PAM
14 - <number>
Another choice for P(f) is a raised cosine spectrum
Roll-off factor gives bandwidth in excess of bandwidth W for ideal Nyquist channel
Raised cosine pulse has zero ISI when sampled correctly
Let g(t) and h(t) be square root raised cosine pulses
ideal Nyquist channel impulse response
dampening adjusted by rolloff factor 

## Slide 21: Bit Error Probability for 2-PAM
14 - <number>
Tb is bit period (bit rate is fb = 1/Tb)
  w(t) is AWGN with zero mean and variance 2
Lowpass filtering a Gaussian random process produces another Gaussian random process
  Mean scaled by H(0)
  Variance scaled by twice lowpass filter’s bandwidth
Matched filter’s bandwidth is ½ fb
h(t)
s(t)
Sample at
t = nTb
Matched filter
w(t)
r(t)
r(t)
rn
r(t) = h(t) * r(t)

## Slide 22: Bit Error Probability for 2-PAM
Noise power at matched filter output
14 - <number>
Noise power
T = Tsym
Filtered noise
2 (1–2)

## Slide 23: Bit Error Probability for 2-PAM
14 - <number>
Symbol amplitudes of +A and -A
Rectangular pulse shape with amplitude 1
Bit duration (Tb) of 1 second
Matched filtering with gain of one (see slide 14-15)
  Integrate received signal over nth bit period and sample
0
-
Probability density function (PDF)

## Slide 24: Bit Error Probability for 2-PAM
14 - <number>
Probability of error given that transmitted pulse has amplitude –A
Random variable is Gaussian with zero mean and variance of one
Q function on next slide
PDF for N(0, 1)
0
Tb = 1

## Slide 25: Q Function
14 - <number>
Q function
Complementary error function erfc
Relationship
Erfc[x] in Mathematica
erfc(x) in Matlab

## Slide 26: Bit Error Probability for 2-PAM
14 - <number>
Probability of error given that transmitted pulse has amplitude A
Assume that 0 and 1 are equally likely bits
Probability of error exponentially decreases with SNR (see slide 8-16)
Tb = 1

## Slide 27: PAM Symbol Error Probability
14 - <number>
Set symbol time (Tsym) to 1 second
Average transmitted signal power
  GT() square root raised cosine spectrum
M-level PAM symbol amplitudes
With each symbol equally likely
2-PAM
d
-d
4-PAM
Constellation points with receiver decision boundaries
d
d
3 d
3 d

## Slide 28: PAM Symbol Error Probability
14 - <number>
Noise power and SNR
Assume ideal channel, i.e. one without ISI
Consider M-2 inner levels in constellation
  Error only if
  where
  Probability of error is
Consider two outer levels in constellation
two-sided power spectral density of AWGN
channel noise after matched filtering and sampling

## Slide 29: PAM Symbol Error Probability
14 - <number>
Assuming that each symbol is equally likely, symbol error probability for M-level PAM
Symbol error probability in terms of SNR
M-2 interior points
2 exterior points

## Slide 30: Visualizing ISI
14 - <number>
Eye diagram is empirical measure of signal quality
Intersymbol interference (ISI):
  Raised cosine filter has zero ISI when correctly sampled

## Slide 31: Eye Diagram for 2-PAM
14 - <number>
Useful for PAM transmitter and receiver analysis and troubleshooting
The more open the eye, the better the reception
M=2
t - Tsym
Sampling instant
Interval over which it can be sampled
Slope indicates sensitivity to timing error
Distortion over zero crossing
Margin over noise
t + Tsym
t

## Slide 32: Eye Diagram for 4-PAM
14 - <number>
3d
d
-d
-3d
Due to startup transients.
Fix is to discard first few symbols equal to number of symbol periods in pulse shape.