## Slide 1: Quadrature Amplitude Modulation (QAM) Receiver
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin

## Slide 2: Outline
16 - <number>
Introduction
Automatic gain control
Carrier detection
Symbol clock recovery
Channel equalization
QAM demodulation

## Slide 3: Introduction
16 - <number>
Channel impairments
  Linear and nonlinear distortion of transmitted signal
  Additive noise (often assumed to be Gaussian)
Mismatch in transmitter/receiver analog front ends
Receiver subsystems to compensate for impairments
  Fading Automatic gain control (AGC)
  Additive noise Matched filters
  Linear distortion Channel equalizer
  Carrier mismatch Carrier recovery
  Symbol timing mismatch Symbol clock recovery

## Slide 4: Baseband QAM
16 - <number>
Receive
Filter
A/D
Symbol
Clock
Recovery
LPF
LPF
Carrier Detect
AGC
X
X
r0(t)
r1(t)
r(t)
r[m]
Channel Equalizer
L
L
L samples/symbol m sample index n symbol index
QAM Demodulation
c(t)
2 cos(c m)
-2 sin(c m)
Receiver
i[n]
gT[m]
L
+
cos(c m)
q[n]
gT[m]
L
sin(c m)
Serial/ parallel converter
1
Bits
Map to 2-D
constellation
J
Pulse shapers (FIR filters)
Index
s[m]
D/A
s(t)
Transmitter
fs
Carrier recovery is not shown
i[m]
q[m]

## Slide 5: Automatic Gain Control
Scales input voltage to A/D converter
  Increase gain for low signal level
  Decrease gain for high signal level
Consider A/D converter with 8-bit signed output
  When c(t) is zero, A/D output is 0
  When c(t) is infinity, A/D output is -128 or 127
  Let f-128, f0 and f127 represent how frequently outputs -128, 0 and 127 occur over a window of previous samples
  Each frequency value is between 0 and 1, inclusive
  Update: c(t) = (1 + 2 f0 – f-128 – f127) c(t – )
  Initial values: f-128 = f0 = f127 = 1 / 256. Zero also works.
16 - <number>
A/D
AGC
r1(t)
r(t)
r[m]
c(t)

## Slide 6: Carrier Detection
16 - <number>
Detect energy of received signal (always running)
  c is a constant where 0 < c < 1 and r[m] is received signal
  Let x[m] = r2[m]. What is the transfer function?
  What values of c to use?
If receiver is not currently receiving a signal
  If energy detector output is larger than a large threshold, assume receiving transmission
If receiver is currently receiving signal, then it detects when transmission has stopped
  If energy detector output is smaller than a smaller threshold, assume transmission has stopped

## Slide 7: Symbol Clock Recovery
16 - <number>
Two single-pole bandpass filters in parallel
  One tuned to upper Nyquist frequency u = c + 0.5 sym
  Other tuned to lower Nyquist frequency l = c – 0.5 sym
  Bandwidth is B/2 (100 Hz for 2400 baud modem)
A recovery method
  Multiply upper bandpass filter output with conjugate of lower bandpass filter output and take the imaginary value
  Sample at symbol rate to estimate timing error 
  Smooth timing error estimate to compute phase advancement
when
Lowpass IIR filter
Pole locations?
See Reader handout M

## Slide 8: Channel Equalizer
Mitigates linear distortion in channel
When placed after A/D converter
  Time domain: shortens channel impulse response
  Frequency domain: compensates channel distortion over entire discrete-time frequency band instead of transmission band
Ideal channel
  Cascade of delay  and gain g
  Impulse response: impulse delayed by with amplitude g
  Frequency response: allpass and linear phase (no distortion)
  Undo effects by discarding  samples and scaling by 1/g
16 - <number>
z-
g

## Slide 9: Channel Equalizer
IIR equalizer
  Ignore noise nm
  Set error em to zero
  H(z) W(z) = g z-
  W(z) = g z-/ H(z)
  Issues?
FIR equalizer
  Adapt equalizer coefficients when transmitter sends training sequence to reduce measure of error, e.g. square of em
16 - <number>
Discrete-Time Baseband System
z-
h
+
w
-
xm
ym
em
rm
nm
+
Equalizer
Channel
g
Ideal Channel
+
Receiver generates xm
Training sequence

## Slide 10: Adaptive FIR Channel Equalizer
Simplest case: w[m] = [m] + w1 [m-1]
  Two real-valued coefficients w/ first coefficient fixed at one
Derive update equation for w1 during training
  Using least mean squares (LMS)
  Step size 0 <  < 1
z-
h
+
w
-
xm
ym
em
rm
nm
+
Equalizer
Channel
g
Ideal Channel
+
Receiver generates xm
Training sequence
sm

## Slide 11: Baseband QAM Demodulation
  Recovers baseband in-phase/quadrature signals
  Assumes perfect AGC, equalizer, symbol recovery
QAM modulation followed by lowpass filtering
  Receiver fmax = 2 fc + B and fs > 2 fmax
Lowpass filter has other roles
  Matched filter
  Anti-aliasing filter
Matched filters
  Maximize SNR at downsampler output
  Hence minimize symbol error at downsampler output
16 - <number>
LPF
LPF
X
X
2 cos(c m)
-2 sin(c m)
x[m]

## Slide 12: Baseband QAM Demodulation
16 - <number>
QAM baseband signal
QAM demodulation
  Modulate and lowpass filter to obtain baseband signals
baseband
high frequency component centered at 2 c
baseband
high frequency component centered at 2 c