## Slide 1: Fast Fourier Transform
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin

## Slide 2: Discrete-Time Fourier Transform
17 - <number>
Forward transform of discrete-time signal x[n]
  Assumes that x[n] is two-sided and infinite in duration
  Produces X() that is periodic in  (in units of rad/sample) with period 2 due to exponential term
Inverse discrete-time Fourier transform
Basic transform pairs

## Slide 3: Discrete Fourier Transform (DFT)
17 - <number>
Discrete Fourier transform (DFT) of a discrete-time signal x[n] with finite extent n  [0, N-1]
  X[k] periodic with period N due to exponential
  Also assumes x[n] periodic with period N
Inverse discrete Fourier transform
Twiddle factor
for k = 0, 1, …, N-1
Two-Point DFT

## Slide 4: Discrete Fourier Transform (con’t)
17 - <number>
Forward transform
  for k = 0, 1, …, N-1
  Exponent of WN has period N
Memory usage
  x[n]: N complex words of RAM
  X[k]: N complex words of RAM
  WN : N complex words of ROM
Halve memory usage
  Allow output array X[k] to write over input array x[n]
  Exploit twiddle factors symmetry
Computation
  N2 complex multiplications
  N (N –1) complex additions
  N2 integer multiplications
  N2 modulo indexes into lookup table of twiddle factors
Inverse transform
  for n = 0, 1, …, N-1
  Memory usage?
  Computational complexity?

## Slide 5: Fast Fourier Transform Algorithms
17 - <number>
Communication system application: multicarrier modulation using harmonically related carriers
  Discrete multitone modulation in ADSL & VDSL modems
  OFDM in IEEE 802.11a/g Wi-Fi and cellular LTE
Efficient divide-and-conquer algorithm
  Compute discrete Fourier transform of length N = 2
  ½ N log2 N complex multiplications and additions
  How many real complex multiplications and additions?
Derivation: Assume N is even and power of two

## Slide 6: Fast Fourier Transform (cont’d)
17 - <number>
Substitute n = 2r for n even and n = 2r+1 for odd
Using the property
  One FFT length N => two FFTs length N/2
  Repeat process until two-point FFTs remain
  Computational complexity of two-point FFT?
Two-Point FFT

## Slide 7: Linear Convolution by FFT
17 - <number>
Linear convolution
  x[n] has length Nx and h[n] has length Nh
  y[n] has length Nx+Nh-1
Linear convolution requires NxNh real-valued multiplications and 2Nx + 2Nh - 1 words of memory
Linear convolution by FFT of length N = Nx+Nh - 1
  Zero pad x[n] and h[n] to make each N samples long
  Compute forward DFTs of length N to obtain X[k] and H[k]
  Y[k] = H[k] X[k] for k = 0…N-1: may overwrite X[k] with Y[k]
  Take inverse DFT of length N of Y[k] to obtain y[n]
If h[n] is fixed, then precompute and store H[k]

## Slide 8: Linear Convolution by FFT
17 - <number>
Implementation complexity using N-length FFTs
  3 N log2 N complex multiplications and additions
  2 N complex words of memory if Y[k] overwrites X[k]
FFT approach requires fewer computations if
Disadvantages of FFT approach
  Uses twice the memory: 2(Nx +Nh -1) complex words vs. 2Nx + 2Nh - 1 words
  Often requires floating-point arithmetic
  Adds delay of Nx samples to buffer x[n] whereas linear convolution is computed sample-by-sample
  Creates discontinuities at boundaries of blocks of input data: use overlapping blocks and windowing
FFT under fixed-point arithmetic?