## Slide 1: Equalizer Design to Maximize Bit Rate in ADSL Transceivers
Prof. Brian L. Evans Dept. of Electrical and Comp. Eng. The University of Texas at Austin http://signal.ece.utexas.edu
UT graduate students: Mr. Aditya Chopra, Mr. Yousof Mortazavi
UT MS/PhD grads: Dr. Güner Arslan (ST-Ericcson), Dr. Biao Lu (OpenSpirit), Dr. Ming Ding (Broadcom), Dr. Milos Milosevic (Schlumberger), Mr. Alex Olson (Schlumberger), Dr. Zukang Shen (Datang Mobile), and Dr. Ian Wong (Nat. Inst.)
UT senior design students: Mr. Wade Berglund, Mr. Jerel Canales, Mr. David J. Love, Mr. Ketan Mandke, Mr. Scott Margo, Ms. Esther Resendiz, Mr. Jeff Wu
Other collaborators: Dr. Lloyd D. Clark, Prof. C. Richard Johnson, Jr. (Cornell), Prof. Sayfe Kiaei (ASU), Prof. Rick Martin (AFIT), Prof. Marc Moonen (KU Leuven), Dr. Lucio F. C. Pessoa (Freescale), Dr. Arthur J. Redfern (TI)
Last modified November 30, 2009

## Slide 2: Digital Subscriber Line (DSL) Broadband Access
Customer Premises
Downstream (higher data rate)
Upstream
Voice Switch
Service
Provider
DSLAM
DSL modem
DSL modem
LPF
LPF
Internet
DSLAM - Digital Subscriber Line Access Multiplexer
LPF – Lowpass Filter (passes voiceband frequencies)
Telephone Network
Introduction

## Slide 3: Discrete Multitone (DMT) DSL Standards
ADSL – Asymmetric DSL
  Maximum data rates supported in G.DMT standard (ideal case)
    Echo cancelled: 14.94 Mbps downstream, 1.56 Mbps upstream
    Frequency division multiplexing (FDM): 13.38 Mbps downstream, 1.56 Mbps upstream
  Widespread deployment in US, Canada, Western Europe, and Hong Kong
    Central office providers only installing frequency-division multiplexed (FDM)
    ADSL:cable modem market 1:2 in US & 2:1 worldwide
  ADSL+ 8 Mbps downstream min.
  ADSL2 doubles analog bandwidth
VDSL – Very High Rate DSL
  Asymmetric
    Faster G.DMT FDM ADSL
    2m subcarriers m  [8, 12]
  Symmetric: 13, 9, or 6 Mbps
  Optional 12-17 MHz band
2003
2003
2003
1997
Introduction
2005

## Slide 4: Outline
Multicarrier modulation
Conventional equalizer training methods
  Minimum Mean Squared Error design [Stanford]
  Maximum Shortening Signal-to-Noise Ratio design [Tellabs]
  Maximum Bit Rate design (optimal) [UT Austin]
  Minimum Inter-symbol Interference design (near-optimal) [UT Austin]
Per-tone equalizer [Catholic University, Leuven, Belgium]
Dual-path equalizer [UT Austin]
Conclusion
Transmitter
Channel
Receiver
Equalizer
Message bit stream
Received bit stream

## Slide 5: Single Carrier Modulation
Ideal (non-distorting) channel over transmission band
  Flat magnitude response
  Linear phase response: delay is constant for all spectral components
  No intersymbol interference
Impulse response for ideal channel over all frequencies
  Continuous time:
  Discrete time:
Equalizer
  Shortens channel impulse response (time domain)
  Compensates for frequency distortion (frequency domain)
g[k-
Discretized Baseband System
g(t-
Multicarrier Modulation
z-
h
+
w
-
xk
yk
ek
rk
nk
+
Equalizer
Channel
g
Ideal Channel
+
Receiver generates xk
Training sequence

## Slide 6: Multicarrier Modulation
Divide channel into narrowband subchannels
  No inter-symbol interference (ISI) in subchannels if constant gain within every subchannel and if ideal sampling
Discrete multitone modulation
  Baseband transmission
  Based on fast Fourier transform (FFT)
  Standardized for ADSL and VDSL
subchannel
frequency
magnitude
carrier
DTFT-1
pulse
sampled sinc

k
c
c
channel
Subchannels are 4.3 kHz wide in ADSL and VDSL
Multicarrier Modulation

## Slide 7: Multicarrier Modulation by Inverse FFT Filter Bank
x
x
x
+
g(t)
g(t)
g(t)
x
x
x
+
Discrete
time
g(t) : pulse shaping filter Xi : ith subsymbol from encoder
Multicarrier Modulation
real-valued
complex-valued
complex-valued

## Slide 8: Discrete Multitone Modulation Symbol
N/2 subsymbols are in general complex-valued
  ADSL uses 4-level Quadrature Amplitude Modulation (QAM) during training
  ADSL uses QAM of 22, 23, 24, …, 215 levels during data transmission
Multicarrier modulation using inverse FFT
In-phase
Quadrature
QAM
N-point
Inverse
Fast Fourier Transform
X1
X2
X1*
x0
x1
x2
xN-1
X2*
XN/2
X0
Multicarrier Modulation
Xi
Mirror and conjugate N/2–1 complex subsymbols
Yields one symbol of N real-valued samples

## Slide 9: Discrete Multitone Modulation Frame
Frame is sent through D/A converter and transmitted
  Frame is the symbol with cyclic prefix prepended
  Cyclic prefix (CP) consists of last  samples of the symbol
  CP reduces throughput by factor of
Linear convolution of frame with channel impulse response
  Is circular convolution if channel length is CP length plus one or shorter
  Circular convolution frequency-domain equalization in FFT domain
  Time-domain equalization to reduce effective channel length and ISI
N samples
v samples
CP
CP
s y m b o l i
s y m b o l i+1
copy
copy
Multicarrier Modulation

## Slide 10: Eliminating ISI in Discrete Multitone Modulation
Time domain equalizer (TEQ)
  Finite impulse response (FIR) filter
  Effective channel impulse response: convolution of TEQ impulse response with channel impulse response
Frequency domain equalizer (FEQ)
  Compensates magnitude/phase distortion of equalized channel by dividing each FFT coefficient by complex number
  Generally updated during data transmission
ADSL G.DMT equalizer training
  Reverb: same symbol sent 1,024 to 1,536 times
  Medley: aperiodic pseudo-noise sequence of 16,384 symbols for subchannel SNR estimation
  Receiver returns number of bits (0-15) to transmit each subchannel i
Multicarrier Modulation
channel impulse response
effective channel impulse response

: transmission delay : cyclic prefix length

## Slide 11: ADSL Transceiver: Data Transmission
P/S
QAM decoder
invert channel
=
frequency
domain
equalizer
S/P
quadrature amplitude modulation (QAM) encoder
mirror
data
and
N-IFFT
add cyclic prefix
P/S
D/A +
transmit filter
N-FFT
and
remove
mirrored
data
S/P
remove cyclic prefix
TRANSMITTER
RECEIVER
N/2 subchannels
N real samples
N real samples
N/2 subchannels
time domain equalizer (FIR filter)
receive filter
+
A/D
channel
Bits
00110
each block programmed in lab and covered in one full lecture
each block covered in one full lecture
2.208 MHz
Multicarrier Transceivers
conventional ADSL equalizer structure

## Slide 12: Outline
Multicarrier modulation
Conventional equalizer training methods
  Minimum Mean Squared Error design [Stanford]
  Maximum Shortening Signal-to-Noise Ratio design [Tellabs]
  Maximum Bit Rate design (optimal) [UT Austin]
  Minimum Inter-symbol Interference design (near-optimal) [UT Austin]
Per-tone equalizer
Dual-path equalizer
Conclusion
Transmitter
Channel
Receiver
Equalizer
Message bit stream
Received bit stream

## Slide 13: Minimum Mean Squared Error TEQ Design
Minimize E{ek2} [Chow & Cioffi, 1992]
  Chose length of b (e.g. +1) to shorten length of h * w
  b is eigenvector of minimum eigenvalue of symmetric channel-dependent matrix
  Minimum MSE when where
Disadvantages
  Does not consider bit rate
  Deep notches in equalized frequency response
z-
h
+
w
b
-
xk
yk
ek
rk
nk
+
bk-
TEQ
Channel
Conventional Equalizer
Why?
Rxy is cross correlation matrix

## Slide 14: Infinite Length MMSE TEQ Analysis
As TEQ length goes to infinity, R becomes Toeplitz [Martin et al. 2003]
  Eigenvector of minimum eigenvalue of symmetric Toeplitz matrix has zeros on unit circle [Makhoul 1981]
  Zeros of target impulse response b on unit circle kills  subchannels
Finite length TEQ plot
  Each trace is a different zero of b
  Distance of 32 zeros of b to unit circle averaged over 8 ADSL test channels for each TEQ length
  Zeros cluster at 0.01 and 10-4 from UC for TEQ lengths 32 and 100
Longer MMSE TEQ may be worse
Conventional Equalizer
[Martin et al., 2004]

## Slide 15: Maximum Shortening SNR TEQ Design
Minimize energy leakage outside shortened channel length
For each possible position of window [Melsa, Younce & Rohrs, 1996]
Equivalent to noise-free MMSE TEQ
Disadvantages
  Does not consider channel noise
  Does not consider bit rate
  Deep notches in equalized frequency response (zeros of target impulse response near unit circle kill subchannels)
  Requires Cholesky decomposition, which is computationally-intensive and does not allow TEQ lengths longer than cyclic prefix
h
w
channel impulse response
effective channel impulse response

Conventional Equalizer

## Slide 16: Maximum Shortening SNR TEQ Design
hwin, hwall : equalized channel within and outside the window
Objective function is shortening SNR (SSNR)
h
+
w
xk
yk
rk
nk
Choose w to minimize energy outside window of desired length
  Locate window to capture maximum channel impulse response energy
Cholesky decomposition of B to find eigenvector for minimum generalized eigenvalue of A and B
Conventional Equalizer

## Slide 17: Modeling Achievable Bit Rate
Bit allocation bounded by subchannel SNRs: log(1 + SNRi / i)
Model ith subchannel SNR [Arslan, Evans & Kiaei, 2001]
Divide numerator and denominator of SNRi by noise power spectral density Sn,i
Conventional subchannel SNRi
Used in Maximum Bit Rate Method
Used in Minimum ISI Method
Conventional Equalizer

## Slide 18: Maximum Bit Rate (MBR) TEQ Design
Subchannel SNR as nonlinear function of equalizer taps w
Maximize nonlinear function of bits/symbol with respect to w
  Good performance measure for comparison of TEQ design methods
  Not an efficient TEQ design method in computational sense
H
HT
=
Ai
G
GT
qiH
Sx,i
qi
D
H
HT
=
Bi
qiH
Sx,i
qi
DT
Sn,i
FT
F
+
qiH
qi
qi is ith row of DFT matrix
Fractional bits for optimization
Conventional Equalizer

## Slide 19: Minimum-ISI (Min-ISI) TEQ Design
Rewrite subchannel SNR [Arslan, Evans & Kiaei, 2001]
Generalize MSSNR method by weighting ISI in frequency
  Minimize frequency weighted sum of subchannel ISI power
  Penalize ISI power in high conventional SNR subchannels:
  Constrain signal path gain to one to prevent all-zero solution for w
  Solution is eigenvector of minimum generalized eigenvalue of X and Y
Iterative Min-ISI method [Ding et al. 2003]
  Avoids Cholesky decomposition by using adaptive filter theory
  Designs arbitrary length TEQs without loss in bit rate
  Overcomes disadvantages of Maximum SSNR method
ISI power weighted in frequency domain by inverse of noise spectrum
Conventional Equalizer

## Slide 20: Outline
Multicarrier modulation
Conventional equalizer training methods
  Minimum Mean Squared Error design
  Maximum Shortening Signal-to-Noise Ratio design
  Maximum Bit Rate design (optimal)
  Minimum Inter-symbol Interference design (near-optimal)
Per-tone equalizer [Catholic University, Leuven, Belgium]
Dual-path equalizer
Conclusion
Transmitter
Channel
Receiver
Equalizer
Message bit stream
Received bit stream

## Slide 21: Drawbacks to Using Single FIR Filter for TEQ
Conventional equalizer
Equalizes all tones in combined fashion: may limit bit rate
Output of conventional equalizer for tone i computed using sequence of linear operations
  Zi = Di rowi(QN ) Y w
  Di is the complex scalar value of one-tap FEQ for tone i
  QN is the N  N complex-valued FFT matrix
  Y is an N  Lw real-valued Toeplitz matrix of received samples
  w is a Lw  1 column vector of real-valued TEQ taps
Y w represents convolution
Per-Tone Equalizer
invert channel
=
frequency
domain
equalizer
N-FFT
and
remove
mirrored
data
S/P
remove cyclic prefix
N real samples
time domain equalizer (FIR filter)
N/2 complex samples

## Slide 22: Frequency-Domain Per Tone Equalizer
Rewrite equalized FFT coefficient for each of N/2 tones [Van Acker, Leus, Moonen, van de Wiel, Pollet, 2001]
  Zi = Di rowi(QN ) Y w = rowi(QN Y) ( w Di ) = rowi(QN Y) wi
  Take sliding FFT to produce N  Lw matrix product QN Y
  Design wi for each tone
Sliding
N-Point
FFT
(Lw-frame)
N+
N+
N+
z-1
z-1
z-1
y
N + Lw – 1 channels
W1,1
W1,0
W1,2
W1,Lw-1
WN/2,0
WN/2,1
WN/2,2
WN/2,Lw-1
FEQ is a linear combiner of up to N/2 Lw-tap FEQs
Per-Tone Equalizer

## Slide 23: Outline
Multicarrier modulation
Conventional equalizer training methods
  Minimum Mean Squared Error design
  Maximum Shortening Signal-to-Noise Ratio design
  Maximum Bit Rate design (optimal)
  Minimum Inter-symbol Interference design (near-optimal)
Per-tone equalizer
Dual-path equalizer [UT Austin]
Conclusion
Transmitter
Channel
Receiver
Equalizer
Message bit stream
Received bit stream

## Slide 24: Dual-Path Time Domain Equalizer (DP-TEQ) [Ding, Redfern & Evans, 2002]
First FIR TEQ equalizes entire available bandwidth
Second FIR TEQ tailored for subset of subchannels
  Subchannels with higher SNR
  Subchannels difficult to equalize, e.g. at boundary of upstream and downstream channels in frequency-division multiplexed ADSL
Minimum ISI method is good match for second FIR TEQ
Path selection for each subchannel is fixed during training
Up to 20% improvement in bit rate over MMSE TEQs
Enables reuse of VLSI designs of conventional equalizers
Dual-Path Equalizer
TEQ 1
TEQ 2
FFT
FFT
Path
Selection
for each
Subchannel
FEQ

## Slide 25: Simulation Results for 17-Tap Equalizers
Parameters
Cyclic prefix length 32
FFT size (N) 512
Coding gain (dB) 4.2
Margin (dB) 6
Input power (dBm) 23
Noise power (dBm/Hz)
-140
Crosstalk noise 24 ISDN disturbers
Figure 1 in [Martin, Vanbleu, Ding, Ysebaert, Milosevic, Evans, Moonen & Johnson, Oct. 2005]
Downstream transmission
Simulation Results
UNC(b) means unit norm constraint on target impulse response b, i.e. || b || = 1
MDS is Maximum Delay Spread design method [Schur & Speidel, 2001]
Carrier serving area (CSA) test loop
Bit rate (Mbps)

## Slide 26: Simulation Results for 17-Tap Equalizers
Parameters
Cyclic prefix length 32
FFT size (N) 512
Coding gain (dB) 4.2
Margin (dB) 6
Input power (dBm) 23
Noise power (dBm/Hz)
-140
Crosstalk noise 24 ISDN disturbers
Figure 3 in [Martin, Vanbleu, Ding, Ysebaert, Milosevic, Evans, Moonen & Johnson, Oct. 2005]
Downstream transmission
MDR is Maximum Data Rate design method [Milosevic et al., 2002]
BM-TEQ is Bit Rate Maximizing design method [Vanbleu et al., 2003]
PTEQ is Per Tone Equalizer structure and design method [Acker et al., 2001]
Simulation Results
Carrier Serving Area (CSA) Test Loop
Bit Rate (Mbps)

## Slide 27: Estimated Computational Complexity
Simulation Results
Equalizer Design Algorithm
Computational Complexity in 10 log10(MACs)
MAC means a multiplication-accumulation operation

## Slide 28: Bit Rate vs. Training Complexity Tradeoffs
Simulation Results
Training Complexity in log10(MACs)
Bit Rate (Mbps)
MAC means a multiplication-accumulation operation

## Slide 29: Achievable Bit Rate vs. Delay Parameter
Simulation Results
Large plateau of near-optimal delays (optimal choice requires search) One choice is to set the delay parameter equal to cyclic prefix length
Delay Parameter for CSA Test Loop 4
Bit rate (Mbps)

## Slide 30: Contributions by Research Group
New methods for single-path time-domain equalizer design
  Maximum Bit Rate method maximizes bit rate (upper bound)
  Minimum Inter-Symbol Interference method (real-time, fixed-point)
Minimum Inter-Symbol Interference TEQ design method
  Generalizes Maximum Shortening SNR by frequency weighting ISI
  Improve bit rate in an ADSL transceiver by change of software only
  Implemented in real-time on three fixed-point digital signal processors: Motorola 56000, TI TMS320C6200 and TI TMS320C5000
New dual-path time-domain equalizer
  Achieves bit rates between conventional and per tone equalizers
  Lower implementation complexity in training than per tone equalizers
  Enables reuse of ASIC designs
http://www.ece.utexas.edu/~bevans/projects/adsl
Conclusion

## Slide 31: UT Austin Matlab DMTTEQ Toolbox 3.1
Single-path, dual-path, per-tone & TEQ filter bank equalizers
  Available at http://www.ece.utexas.edu/~bevans/projects/adsl/dmtteq/
various performance measures
default parameters from G.DMT ADSL standard
different graphical views
-140
23
Conclusion
18 design methods

## Slide 32: UT Austin ADSL2 Simulator 1.1
Simulation controls
Simulation state indicator
Description window
Simulation parameters
Performance indicators
http://users.ece.utexas.edu/~bevans/projects/adsl/simulator/index.html
Conclusion

## Slide 33: Backup Slides

## Slide 34: Applications of Broadband Access
Residential
Business
Introduction

## Slide 35: Selected DSL Standards
Courtesy of Shawn McCaslin (National Instruments, Austin, TX)
Introduction

## Slide 36
A Digital Communications System
Encoder maps a group of message bits to data symbols
Modulator maps these symbols to analog waveforms
Demodulator maps received waveforms back to symbols
Decoder maps the symbols back to binary message bits
Message
Source
Modulator
Encoder
Channel
Demodulator
Decoder
Message
Sink
Noise
Transmitter
Receiver
Introduction

## Slide 37: Intersymbol Interference (ISI)
1
1
1
-1
1
.7
.4
.1
1
1.7
2.1
1
1
1
1
Transmitted signal
Channel impulse response
Receivedsignal
Threshold
at zero
Detected signal
*
=
1
.7
1
Ideal channel
  Impulse response is impulse
  Flat frequency response
Non-ideal channel
  Causes ISI
  Channel memory
  Magnitude and phase variation
Received symbol is weighted sum of neighboring symbols
  Weights are determined by channel impulse response
Introduction

## Slide 38: Combat ISI with Equalization
Equalization because channel response is not flat
Zero-forcing equalizer
  Inverts channel
  Flattens freq. response
  Amplifies noise
MMSE equalizer
  Optimizes trade-off between noise amplification and ISI
Decision-feedback equalizer
  Increases complexity
  Propagates error
Channel frequency response
Zero-forcing equalizer frequency response
MMSE
equalizer frequency response
Introduction
Notes: to show the idea behind equalization
in practice DFE would be used

## Slide 39: Cyclic Prefix
cyclic prefix
equal
to be removed
Repeated symbol
*
=
Introduction

## Slide 40: Open Issues for Multicarrier Modulation
Advantages
  Efficient use of bandwidth without full channel equalization
  Robust against impulsive noise and narrowband interference
  Dynamic rate adaptation
Disadvantages
  Transmitter: High signal peak-to-average power ratio
  Receiver: Sensitive to frequency and phase offset in carriers
Open issues
  Pulse shapes of subchannels (orthogonal, efficient realization)
  Channel equalizer design (increase bit rate, reduce complexity)
  Synchronization (timing recovery, symbol synchronization)
  Bit loading (allocation of bits in each subchannel)
  Echo cancellation
Multicarrier Modulation
Notes: Simple linear equalizers are easy to implement but enhance noise
Complex equalizers such as the DFE is required (how many taps has an DFE ?)
The computational complexity of DFE increases very fast with bit rate

## Slide 41: TEQ Algorithm
ADSL standards
  Set aside 1024 frames (~.25s) for TEQ estimation
  Reserved ~16,000 frames for channel and noise estimation for the purpose of SNR calculation
TEQ is estimated before the SNR calculations
Noise power and channel impulse response can be estimated before time slot reserved for TEQ if the TEQ algorithm needs that information
Conventional Equalizer

## Slide 42: Single-FIR Time-Domain Equalizer Design Methods
All methods below perform optimization at TEQ output
Minimizing the mean squared error
  Minimize mean squared error (MMSE) method [Chow & Cioffi, 1992]
  Geometric SNR method [Al-Dhahir & Cioffi, 1996]
Minimizing energy outside of shortened (equalized) channel impulse response
  Maximum Shortening SNR method [Melsa, Younce & Rohrs, 1996]
  Divide-and-conquer methods [Lu, Evans, Clark, 2000]
  Minimum ISI method [Arslan, Evans & Kiaei, 2000]
Maximizing bit rate [Arslan, Evans & Kiaei, 2000]
Implementation
  Geometric SNR is difficult to automate (requires human intervention)
  Maximum bit rate method needs nonlinear optimization solver
  Other methods implemented on fixed-point digital signal processors
Conventional Equalizer
Notes: The frequency domain equalizer is just a complex division per subchannel
Channel shortening equalizer is an 20-30 tap FIR filter
My focus is on channel shortening

## Slide 43: Minimum Mean Squared Error (MMSE) TEQ
O selects the proper part out of Rx|y corresponding to the delay 
z-
h
+
w
b
-
xk
yk
ek
rk
nk
+
bk-
Conventional Equalizer

## Slide 44: Near-optimal Minimum-ISI (Min-ISI) TEQ Design
Generalizes MSSNR method by frequency weighting ISI
  ISI power in ith subchannel is
  Minimize ISI power as a frequency weighted sum of subchannel ISI
  Constrain signal path gain to one to prevent all-zero solution
  Solution is a generalized eigenvector of X and Y
Possible weightings
  Amplify ISI objective function in subchannels with low noise power (high SNR) to put ISI in low SNR bins:
  Set weighting equal to input power spectrum:
  Set weighting to be constant in all subchannels (MSSNR):
Performance virtually equal to MBR (optimal) method
Conventional Equalizer

## Slide 45: Efficient Implementations of Min-ISI Method
Generalized eigenvalue problem can solved with generalized power iteration:
Recursively calculate diagonal elements of X and Y from first column [Wu, Arslan, Evans, 2000]
Conventional Equalizer

## Slide 46: Motivation for Divide-and-Conquer Methods
Fast methods for implementing Maximum SSNR method
Maximum SSNR Method
  For each , maximum SSNR method requires
    Multiplications:
    Additions:
    Divisions:
  Exhaustive search for the optimal delay 
Divide Lw TEQ taps into (Lw - 1) two-tap filters in cascade
  Design first two-tap filter then second and so forth (greedy approach)
Develop heuristic to estimate the optimal delay
Conventional Equalizer

## Slide 47: Divide-and-Conquer Approach
The ith two-tap filter is initialized as either
  Unit tap constraint (UTC)
  Unit norm constraint (UNC)
Calculate best gi or i by using a greedy approach either by
  Minimizing (Divide-and-conquer TEQ minimization)
  Minimizing energy in hwall (Divide-and conquer TEQ cancellation)
Convolve two-tap filters to obtain TEQ
Conventional Equalizer

## Slide 48: Divide-and-Conquer TEQ Minimization (UTC)
At ith iteration, minimize Ji over gi
Closed-form solution
Conventional Equalizer

## Slide 49: Divide-and-Conquer TEQ Minimization (UNC)
At ith iteration, minimize Ji over i
where
Calculate i in the same way as gi for UTC version of this method
Conventional Equalizer

## Slide 50: Divide-and-Conquer TEQ Cancellation (UTC)
At ith iteration, minimize Ji over gi
Closed-form solution for the ith two-tap FIR filter
Conventional Equalizer

## Slide 51: Divide-and-Conquer TEQ Cancellation (UNC)
At ith iteration, minimize Ji over I
Closed-form solution
Conventional Equalizer

## Slide 52: Computational Complexity
Computational complexity for each candidate 
Divide-and-conquer methods vs. maximum SSNR method
  Reduces multiplications, additions, divisions, and memory
  No matrix calculations (saves on memory accesses)
  Avoids matrix inversion, and eigenvalue and Cholesky decompositions
G.DMT ADSL Lh = 512  = 32 Lw = 21
Conventional Equalizer

## Slide 53: Heuristic Search for the Optimal Delay
Estimate optimal delay  before computing TEQ taps
Total computational cost
  Multiplications:
  Additions:
  Divisions:
Performance of heuristic vs. exhaustive search
  Reduce computational complexity by factor of 500
  2% loss in SSNR for TEQ with four taps or more
  8% loss in SSNR for two-tap TEQ
Conventional Equalizer

## Slide 54: Comparison of Earlier Methods
Conventional Equalizer

## Slide 55: MBR TEQ vs. Geometric TEQ
Conventional Equalizer

## Slide 56: Min-ISI TEQ vs. MSSNR TEQ
Min-ISI weights ISI power with the SNR
  Residual ISI power should be placed in high noise frequency bands
Conventional Equalizer

## Slide 57: Bit Rate vs. Cyclic Prefix (CP) Size
Matched filter bound decreases because CP has no new information
Min-ISI and MBR achieve bound with 16-sample CP
Other design methods are erratic
MGSNR better for 15-28 sample CPs
input power 23 dBm
noise power -140 dBm/Hz
crosstalk noise 8 ADSL disturbers
TEQ taps (Lw) 17
FFT size (N) 512
coding gain 4.2 dB
margin 6 dB
Conventional Equalizer

## Slide 58: Simulation Results
Min-ISI, MBR, and MSSNR achieve matched filter bound owith CP of 27 samples
Min-ISI with 13-sample CP beats MMSE with 32-sample CP
MMSE is worst
input power 23 dBm
noise power -140 dBm/Hz
crosstalk noise 8 ADSL disturbers
TEQ taps (Lw) 3
FFT size (N) 512
coding gain 4.2 dB
margin 6 dB
Conventional Equalizer

## Slide 59: Bit Allocation Comparison
AWG 26 Loop: 12000 ft + AWGN
Simulation
  NEXT from 24 DSL disturbers
  32-tap equalizers: least squares training used for per-tone equalizer
Per-Tone Equalizer

## Slide 60: Subchannel SNR
Per-Tone Equalizer

## Slide 61: Frequency-Domain Per-Tone Equalizer
Rearrange computation of FFT coefficient for tone i [Van Acker, Leus, Moonen, van de Wiel, Pollet, 2001]
  Zi = Di rowi(QN ) Y w = rowi(QN Y) ( w Di )
  QN Y produces N  Lw complex-valued matrix produced by sliding FFT
  Zi is inner product of ith row of QN Y (complex) and w Di (complex)
  TEQ has been moved into FEQ to create multi-tap FEQ as linear combiner
After FFT demodulation, each tone equalized separately
  Equalize each carrier independently of other carriers (N/2 carriers)
  Maximize bit rate at output of FEQ by maximizing subchannel SNR
Sliding FFT to produce N  Lw matrix product QN Y
  Receive one ADSL frame (symbol + cyclic prefix) of N +  samples
  Take FFT of first N samples to form the first column
  Advance one sample
  Take FFT of N samples to form the second column, etc.
Per-Tone Equalizer

## Slide 62: Per-Tone Equalizer: Implementation Complexity
Per-Tone Equalizer

## Slide 63: Dual-Path TEQ (Simulated Channel)
Optimized for subchannel 2-250
Optimized for subchannel 2-30
Dual-Path Equalizer

## Slide 64: Motorola CopperGold ADSL Chip
Announced in March 1998
5 million transistors, 144 pins, clocked at 55 MHz
1.5 W power consumption
DMT processor consists
  Motorola MC56300 DSP core
  Several application specific ICs
    512-point FFT
    17-tap FIR filter for time-domain channel equalization based on MMSE method (20 bits precision per tap)
DSP core and memory occupies about 1/3 of chip area