## Slide 1: Analog Sinusoidal Modulation

## Slide 2: Outline
Introduction
Amplitude sinusoidal modulation
  Double-sideband large carrier
  Quadrature amplitude modulation
  Other amplitude modulation types
Frequency modulation
Conclusion

## Slide 3: Example: Radio Frequency Modem
Message signal: stream of bits
Digital sinusoidal modulation in digital signaling
Analog sinusoidal modulation in carrier circuits for upconversion to radio frequencies (RF)
Error Correction
Digital Signaling
D/A Converter
Signal Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Signal Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 4: Modulation
Some characteristic of a carrier signal is varied in accordance with a modulating signal
For amplitude, frequency, and phase modulation, modulated signals can be expressed as
  f(t) is real-valued amplitude function
  fc is carrier frequency
  (t) is real-valued phase function
See Modulation handout (Appendix I)

## Slide 5: Amplitude Modulation
By cosine
Fourier property
Spectrum F() is
  Shifted left by c and scaled by ½ and
  Shifted right by c and scaled by ½
By sine
Fourier property
Spectrum F() is
  Shifted left by c and scaled by j/2 and
  Shifted right by c and scaled by –j/2

## Slide 6: Amplitude Modulation by Cosine
Example: y(t) = f(t) cos(c t)
  Assume f(t) is an ideal lowpass signal with bandwidth 1
  Assume 1 << c
  Y() is real-valued if F() is real-valued
Demodulation: modulation then lowpass filtering
Similar derivation for modulation with sin(c t)

0
1

-
F()

0
Y()
½
-c - 
-c + 
c
c - 
c + 
c
½Fc
½Fc
lower sidebands

## Slide 7: Amplitude Modulation by Sine
Example: y(t) = f(t) sin(c t)
  Assume f(t) is an ideal lowpass signal with bandwidth 1
  Assume 1 << c
  Y() is imaginary-valued if F() is real-valued
Demodulation: modulation then lowpass filtering

Y()
j ½
-c - 
-c + 
c
c - 
c + 
c
-j ½Fc
j ½Fc
-j ½

0
1

-
F()
lower sidebands

## Slide 8: Amplitude Modulated (AM) Radio
Double sideband large carrier (DSC-LC)
  Carrier wave varied about mean value linearly with baseband message signal m(t)
  ka is the amplitude sensitivity, ka > 0
  Modulation factor is  = ka Am where Am is maximum amplitude of m(t)
Envelope of s(t) has about same shape as m(t) if
  | ka m(t) | < 1 for all t
  fc >> W where W is bandwidth of m(t)

## Slide 9: Amplitude Modulated (AM) Radio
Disadvantages
  Redundant bandwidth is used
  Carrier consumes most of the transmitted power
Advantage
  Simple detectors (e.g. AM radio receivers for cars)
Receiver uses a simple envelope detector
  Diode (with forward resistance Rf ) in series
  Parallel connection of capacitor C and load resistor Rl
+
–
vs(t)
Rf
Rs
Rl
C

## Slide 10: Amplitude Modulated (AM) Radio
Let Rs be source resistance
Charging time constant (Rf + Rs) C must be short when compared to 1/ fc, so (Rf +Rs) C << 1/ fc
Discharging time constant Rl C
  Long enough so that capacitor discharges slowly through load resistor Rl between positive peaks of carrier wave
  Not so long that capacitor voltage will not discharge at max rate of change of modulating wave 1/fc << Rl C << 1/W

## Slide 11: Quadrature Amplitude Modulation
Allows DSB-SC signals to occupy same channel bandwidth provided that the two message signals are from independent sources
Two message signals m1(t) and m2(t) are sent
  Ac m1(t) is in-phase component of s(t)
  Ac m2(t) is quadrature component of s(t)

## Slide 12: Other Amplitude Modulation Types
Double sideband suppressed carrier (DSB-SC)
Double sideband variable carrier (DSB-VC)
Single sideband (SSB) removes either lower sideband or upper sideband by
  Extremely sharp bandpass or highpass filter, or
  Phase shifters using Hilbert transformer (slides 15-7 to 15-10)

## Slide 13: Frequency Modulated (FM) Radio
Message signal: analog audio signal
Transmitter
  Signal processing: lowpass filter to reject above 15 kHz
  Carrier circuits: sinusoidal modulatation from baseband to FM station frequency (often in two modulation steps)
Receiver
  Carrier circuits: sinusoidal demodulation from FM station frequency to baseband (often in two demodulation steps)
  Signal processing: lowpass filter to reject above 15 kHz
Signal Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Signal Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 14: Frequency Modulation
Non-linear, time-varying, has memory, non-causal
For single tone message m(t) = Am cos(2  fm t)
Modulation index is  = f / fm
   << 1 => Narrowband FM (looks like double-sideband AM)
   >> 1 => Broadband FM
Instantaneous frequency

## Slide 15: Carson's Rule
Bandwidth of FM for single-tone message at fm
  Narrowband:
  Wideband:
Carson’s rule for single-tone FM:
For message signal of bandwidth W, let fm = W
 |  | FM Radio | TV Audio
f fm  | Peak freq. deviation (F) Peak message freq. (W) Deviation ratio (D) Bandwidth BT = 2 fm (1+ ) Station Spacing | 75 kHz 15 kHz 5 180 kHz 200 kHz | 25 kHz 15 kHz 1.66 80 kHz 6 MHz

## Slide 16: Conclusion
Amplitude modulation
  Digital and analog versions may be used in same system
  Analog amplitude modulation is one method for upconversion
Double sideband amplitude modulation
  Transmission bandwidth is twice message bandwidth (wasteful)
Quadrature amplitude modulation
  Uses cosine and sine to modulate two different message signals and subtracts resulting waveforms
  Two messages in same transmission bandwidth (efficient)