## Slide 1: Wireless Broadband with WiMAX: Hype and Reality Dr. Jeffrey G. Andrews Wireless Networking and Communications Group (WNCG) Dept. of Electrical and Computer Engineering The University of Texas at Austin Collaborators: Dr. Arunabha Ghosh (AT&T Labs) Dr. Runhua Chen (UT Austin, Now with TI) Rias Muhamed (AT&T Labs)

## Slide 2: Questions Addressed by This Talk
What is WiMAX?
Why is WiMAX necessary?
How is WiMAX different from cellular and Wi-Fi?
Does WiMAX deliver on its promise?
Where is WiMAX headed in the future?

## Slide 3: What is WiMAX?
WiMAX is an emerging industry consortium standard for wireless broadband networking
Based on the IEEE 802.16e standard
  Modes and enhancements clearly defined
  Infrastructure and network layer support specified
  Interoperability testing
  Frequency bands specified (2.5-2.7 GHz most promising in USA)
Notes: Cite: http://www.alvarion-usa.com/RunTime/materials/KnowledgePoolFiles/WiMAX.pdf
WiMAX is a non-profit industry trade organization formed by leading communications
component and equipment companies to promote and certify compatibility and interoperability
of broadband wireless access equipment that conforms to the IEEE* 802.16 and
ETSI* HIPERMAN standards.
• The 802.16a standard is a wireless metropolitan area network (MAN) technology that will
connect 802.11 hot spots to the Internet and provide a wireless alternative to cable and
DSL for last mile broadband access, thus accelerating last-mile broadband deployment.
• WiMAX will accelerate and increase the success of future interoperability testing by
providing tools for conformance testing now. Tools can be used during the equipment
maker's system development process today to ensure conformance with the current
standards-based product roadmap as it evolves.
• Members include leading Operators, Equipment and Component makers (see list at end)
• WiMAX was formed in April 2001, in anticipation of the publication of the original 10-66
GHz IEEE 802.16 specifications. WiMAX is to 802.16 as the Wi-Fi Alliance is to 802.11.

## Slide 4: Some History
July 1999 First working group meeting of IEEE 802.16
June 2001 WiMAX Forum established
Dec. 2001 IEEE 802.16 standards completed for > 11 GHz.
Jan. 2003 IEEE 802.16a standard completed
June 2004 IEEE 802.16-2004 standard completed
Sept. 2004 Intel begins shipping its first WiMAX chipset
Jan. 2006 WiBro commercial services launched in Korea
Feb. 2006 IEEE 802.16e standard completed (supports mobility)
June 2006 WiBro launched in Korea
Aug. 2006 Sprint-Nextel announces plans to deploy WiMAX
Apr. 2007 50th WiMAX commercial product announced
Mid 2008 Substantial coverage available nationwide (US)

## Slide 5: The Hype
From the WiMAX forum webpage:
In a typical cell radius deployment of three to ten kilometers, WiMAX Forum Certified™ systems can be expected to deliver capacity of up to 40 Mbps per channel... This is enough bandwidth to simultaneously support hundreds of businesses with T-1 speed connectivity and thousands of residences with DSL speed connectivity. Mobile network deployments are expected to provide up to 15 Mbps of capacity within a typical cell radius deployment of up to three kilometers.

## Slide 6: Why is WiMAX Necessary?
DSL and Cable Modems
  No mobility support
  Huge infrastructure investment necessary outside of developed world
Cellular systems
  Fundamentally designed for voice. (Circuit switched, small bandwidth) .
  Poor spectral efficiency (0.3 – 0.8 bps/Hz for HSDPA/HSUPA and EVDO)
Wi-Fi/802.11
  No mobility support
  Short range
  Not a broadband technique on its own
  Mesh Wi-Fi has debatable throughput (and still will require backhaul/wired connection)

## Slide 7: WiMAX Enablers
Variable and potentially large bandwidth
Efficient exploitation of diversity
  Time (scheduling, adaptive modulation)
  Frequency (scheduling, adaptive modulation, coding/interleaving)
  Space (space-time codes, MIMO)
Packet-switched architecture
Open standard allows more room for innovation, lower consumer costs from competition
Key Point: WiMAX provides a 21st century platform for wireless broadband access.

## Slide 8: WiMAX: Key Technical Features (1)
Orthogonal frequency division multiplexing (OFDM)
  Divide wideband channel into flat-fading subcarriers
  Inter-symbol interference (ISI) is mitigated
  Low-complexity, proven architecture (compare to cellular)
OFDMA: Orth. Freq. Division Multiple Access
  Smart allocation of subcarrier blocks to users
  Improved frequency and time diversity
  Reduced peak power and PAR in uplink

## Slide 9: WiMAX: Key Technical Features (2)
Very Scalable Bandwidth and Data Rates
  Bandwidths vary from 1.5 – 20 MHz
  Data rates vary from 1 – 75 Mbps
  Allows for flexible range, quality of service, bandwidth allocations
Adaptive Modulation and Coding
  Similar to Wi-Fi in this respect
  Modulation types: QPSK, 16QAM, 64QAM
  Coding types: variable rate Conv. codes, turbo codes, LDPCs
  In theory, 52 different modulation/coding “burst profiles”. In practice, only a fraction supported by WiMAX (turbo codes)

## Slide 10: WiMAX: Key Technical Features (3)
Flexible Quality of Service (QoS) support
  Flexible support of real-time traffic (voice), multimedia, data
  Even a single user can have different QoS flows
ARQ and Hybrid ARQ
FDD and TDD both supported, TDD seems to have upper hand
  Flexible uplink-to-downlink data rate ratios
  Channel reciprocity
  Simpler transceiver design.

## Slide 11: WiMAX: Key Technical Features (4)
Support for powerful multiple antenna (MIMO) technology
  OFDM is a natural partner for MIMO
  Pilot symbols, channel estimation, feedback channels
  Space-time codes
  Spatial Multiplexing
We will demonstrate the power (even the need) for MIMO shortly

## Slide 12: MIMO in 2 slides: Space-time coding
Transmit Diversity
  Space-time Code (STC): Redundant data sent over time and space domains (antennas)
  Receive SNR increases about linearly with Nr
  Receive SNR hardens about linearly with Nt
Capacity (max data rate):
c b a
Space
Time
Code
c b a
c’ b’ a’
MOD
MOD
Space
Time
Decoder
c b a

## Slide 13: MIMO in 2 slides: Spatial Multiplexing
MIMO Multiplexing
  Data is not redundant – less diversity but less repetition
  Provides multiplexing gain to increase data-rate
  Low (no) diversity compared with STC
Capacity (at high SNR):
f e d c b a
e c a
f d b
MOD
MOD
Space
Time
Decoder
f e d c b a

## Slide 14: Does WiMAX deliver on its promise?
WiMAX has promised a lot:
  Long ranges: 3 km (mobile) to 8 km (fixed)
  High data rates: 75 Mbps in 20 MHz
  Reasonable cost, power consumption, complexity
Clearly, these are not achievable simultaneously
In conjunction with AT&T labs, we have developed extensive, accurate simulations over the past 3 years to model WiMAX performance
  These results are widely used in the WiMAX forum
  Disclosure: I did not personally write any of this code

## Slide 15: WiMAX in Additive WG Noise
3 dB

## Slide 16: DL Throughput for 5 MHz Channel
This led to adoption of 2x2 system as the basic profile for WiMAX (in DL)
Notes: modes are the rate/ecc pairs. so simulation slightly optimistic since assumes optimum choice.

## Slide 17: The Benefit of Increased Diversity
Link (not system-level) performance
2 streams of data Tx’d when 4 antennas available at Tx or Rx
Data rate is per subchannel (16 subchannels in 10 MHz of BW)

## Slide 18: DL Throughput for 5 MHz Channel Bandwidth

## Slide 19: System Level Modeling
Link level simulation only characterized the performance of an 802.16 link under different conditions
A multi-cellular deployment requires system level modeling
Static Simulation:
  Two tiers of interference considered
  The SNR at any given location is determined by the Tx power of the serving and interfering cells and their respective path losses
  Power control can be integrated if desired
In TDD, 28 OFDM symbols are for the DL, and 9 are for the UL (asymmetric by about a factor of 3)
Notes: RLC = Radio Link Control
Using static calculations, determine the SINR distribution throughout the cell.
Did not due the dynamic simulation – far too complex

## Slide 20: Average Throughput: Freq. reuse, MIMO, channel model
Basic Profile (2x2 OL MIMO)
Enhanced Profiles for (1,1,3)
DL is better than UL by much more than a factor of 3
Freq. reuse helps the average data rate, but not nearly enough to justify factor of 3 hit in bandwidth
MIMO gains, especially closed loop, are very significant

## Slide 21: Coverage and Throughput: Freq. reuse & MIMO
Basic Profile (2x2 OL MIMO)
Enhanced Profiles for (1,1,3)
Frequency reuse has a significant affect at the system level
MIMO at least doubles or triples the data rate at most any outage point

## Slide 22: Key Takeaways from Simulation Results
Spectral efficiencies/data rates still obey the laws of physics and information theory
Unavoidable tradeoff between throughput and coverage: can’t excel at both
Currently, a likely incremental increase in (normalized) throughput and coverage over 3G, but more room to grow
  MIMO is key to helping capacity (also helps coverage)
  Freq. reuse/sectoring are key to coverage (freq. reuse hurts capacity)

## Slide 23: Where is WiMAX headed in the future?
Increased development and eventual deployment of aggressive MIMO techniques
  This is one key area where WiMAX has an advantage over single-carrier (cellular) systems
Range extension through relaying/multi-hopping
  802.16j committee on “Mobile Multihop Relay” (MMR)
  Extends coverage at cost of capacity
Improved Network Design and Management
  Base station cooperation (handoff, scheduling, interference reduction)
  Distributed Antenna architectures
Co-existence/synergies with 802.11n (dual mode devices)

## Slide 24: Conclusions
802.16/WiMax is the beginning of a good wireless broadband standard
  Based on reasonably cutting edge technology
  Very flexible, should prove evolvable and scalable
But don’t believe the hype
  Spectral efficiencies/data rates still obey the laws of physics and information theory, esp. at finite power and cost
  An incremental increase in throughput and coverage over 1xEV-DO/HSDPA
Do get truly impressive rates, a suite of improvements needed
  MIMO, and required technologies to support MIMO
  Advanced Signal Processing (Interference cancellation, etc)
  ARQ, Adaptive Multiuser OFDM, Power Control

## Slide 25: More Information
J. G. Andrews, A. Ghosh, R. Muhamed, Fundamentals of WiMAX, Prentice-Hall, Feb. 2007.
A. Ghosh, J. G. Andrews, R. Chen, and D. R. Wolter, "Broadband wireless access with WiMax/802.16: current performance benchmarks and future potential, " IEEE Communications Magazine, pp. 129-136, Feb. 2005.
WiMAX Forum Overview Whitepapers
  www.wimaxforum.org
Wimax.com (Austin-based)