## Slide 1: Wireless OFDM Systems
Prof. Robert W. Heath Jr.
Wireless Systems Innovations Laboratory
Wireless Networking and Communications Group
Department of Electrical and Computer Engineering
The University of Texas at Austin
rheath@ece.utexas.edu
http://www.ece.utexas.edu/~rheath/research

## Slide 2: OFDM Systems & Applications
Orthogonal Frequency Division Multiplexing (OFDM)
Digital modulation scheme
Wireless counterpart to discrete multitone transmission
Used in a variety of applications
  Broadcast
  High-speed internet access

## Slide 3: Wireless Digital Communication System
Message
Source
Encoder
Pulseshape
exp(j 2 fc t)
Modulator
Carrier frequency fc examples
FM radio 88.5-107.7 MHz (0.2 MHz station spacing)
Analog cellular 900 MHz
Digital cellular 1.8 GHz
Raised cosine pulse shaping filter
Transmitter

## Slide 4: Wireless Digital Communication System
Message
Sink
Demodulator
Pulseshape
exp(-j2 fc t)
Decoder
hc(t)
TX
RX
noise
Propagation
Receiver
Remove carrier

## Slide 5: Multipath Propagation – Simple Model
hc(t) = k k (t - k) where k = 0, …, K-1
  k : path gain (complex)
  0 = 0 normalize relative delay of first path
  k = k - 0 difference in time-of-flight
0
1
2
1
2
0
1
2

## Slide 6: Equivalent Propagation Channel
heff(t) = gtr(t) ­ hc(t) ­ grx(t)
transmit filters
receive filters
multipath channel
convolution
Effective channel at receiver
  Propagation channel
  Transmit / receive filters
hc(t) typically random & changes with time
  Must estimate and re-estimate channel

## Slide 7: Impact of Multipath: Delay Spread & ISI
2Ts
4Ts
Ts
Max delay spread = effective number of symbol periods occupied by channel
Requires equalization to remove resulting ISI

## Slide 8: Effective Delay Spread
Delay spread depends on difference in path lengths
Effective delay spread: function of the maximum difference
Sampling period Ts determines effect of delay spread
 | Cell size | Max Delay Spread
Pico cell | 0.1 km | 300 ns
Micro cell | 5 km | 15 us
Macro cell | 20 km | 40 us
 | Sampling Period | Channel taps | Application
802.11a | 50 ns | 6 | WLAN
DVB-T | 160 ns | 90 | TV broadcast
DAB | 600 ns | 60 | Audio
Radio waves travel ~ 1 ns / ft

## Slide 9
Multicarrier Modulation
Divide broadband channel into narrowband subchannels
  No ISI in subchannels if constant gain in every subchannel and if ideal sampling
Orthogonal Frequency Division Multiplexing
  Based on the fast Fourier transform
  Standardized for DAB, DVB-T, IEEE 802.11a, 802.16a, HyperLAN II
  Considered for fourth-generation mobile communication systems
subchannel
frequency
magnitude
carrier
channel
Subchannels are 312 kHz wide in 802.11a and HyperLAN II

## Slide 10: An OFDM Symbol
N-point
Inverse
FFT
X1
X2
x0
x2
x3
xN-1
XN-1
X0
N subsymbols
one symbol
N complex samples
N samples
v samples
CP: Cyclic Prefix
CP
CP
s y m b o l i
s y m b o l ( i+1)
copy
copy
Key difference with DMT N input symbols! Why?
Bandpass transmission allows for complex waveforms
  Transmit: y(t) = Re{(I(t)+j Q(t)) exp(j2 fc t)}
  = I(t) cos(2 fc t) – Q(t) sin(2  fc t)

## Slide 11: An OFDM Modem
P/S
QAM decoder
invert channel
=
frequency
domain
equalizer
S/P
quadrature amplitude modulation (QAM) encoder
N-IFFT
add cyclic prefix
P/S
D/A +
transmit filter
N-FFT
S/P
remove cyclic prefix
TRANSMITTER
RECEIVER
N subchannels
N complex samples
N complex samples
N subchannels
Receive filter
+
A/D
multipath channel
Bits
00110

## Slide 12: Frequency Domain Equalization
For the kth carrier:
xk = Hk sk + vk
where Hk = n hk(nTs) exp(j2 k n / N) where n = 0, …,. N-1
Frequency domain equalizer
xk
Hk-1
sk
Noise enhancement factor
k
|Hk|2
|Hk-1|2
k
good
bad

## Slide 13: DMT vs. OFDM
DMT
  Channel changes very slowly ~ 1 s
  Subchannel gains known at transmitter
  Bitloading (sending more bits on good channels) increases throughput
OFDM
  Channel may change quickly ~ 10 ms
  Not enough time to convey gains to transmitter
  Forward error correction mitigates problems on bad channels
frequency
magnitude
DMT: Send more data here
OFDM: Try to code so bad subchannels can be ignored

## Slide 14: Coded OFDM (COFDM)
Error correction is necessary in OFDM systems
Forward error correction (FEC)
  Adds redundancy to data stream
  Examples: convolutional codes, block codes
  Mitigates the effects of bad channels
  Reduces overall throughput according to the coding rate k/n
Automatic repeat request (ARQ)
  Adds error detecting ability to data stream
  Examples: 16-bit cyclic redundancy code
  Used to detect errors in an OFDM symbol
  Bad packets are retransmitted (hopefully the channel changes)
  Usually used with FEC
  Minus: Ineffective in broadcast systems

## Slide 15: Typical Coded OFDM Encoder
FEC
Bitwise
Interleaving
Symbol
Mapping
Reed-Solomon and/or convolutional code
Intersperse coded and uncoded bits
Data bits
Parity bits
Rate 1/2
Map bits to symbols

## Slide 16: Example: IEEE 802.11a
IEEE 802.11 employs adaptive modulation
  Code rate & modulation depends on distance from base station
  Overall data rate varies from 6 Mbps to 54 Mbps
Reference: IEEE Std 802.11a-1999

## Slide 17: Typical Coded OFDM Decoder
Frequency-domain
equalization
Symbol
Demapping
Deinterleaving
Decoding
Symbol demapping
  Produce soft estimate of each bit
  Improves decoding

## Slide 18: Spectrum Shaping
FCC manages spectrum
Specifies power spectral density mask
  Adjacent channel interference
  Roll-off requirements
Implications to OFDM
  Zero tones on edge of band
  Time domain windowing ‘smoothes’ adjacent symbols
IEEE 802.11a
Inband
Adjacent channel
Reference: Std 802.11a
frequency
Zero tones
Ofdm symbol

## Slide 19: Ideal Channel Estimation
Wireless channels change frequently ~ 10 ms
Require frequent channel estimation
Many systems use pilot tones – known symbols
  Given sk, for k = k1, k2, k3, … solve xk = l=0L hl e-j2 k l/N sk for hl
  Find Hk = l=0L hl e-j2 k l / N (significant computation)
More pilot tones
  Better noise resiliance
  Lower throughput (pilots are not informative)
frequency
magnitude
Pilot tones

## Slide 20: Channel Estimation Via Interpolation
More efficient approach is interpolation
Algorithm
  For each pilot ki find Hki = xki / ski
  Interpolate unknown values using interpolation filter
  Hm = m,1 Hk1 + m,2 Hk2 + …
Comments
  Longer interpolation filter: more computation, timing sensitivity
  Typical 1dB loss in performance in practical implementation
frequency
magnitude

## Slide 21: OFDM and Antenna Diversity
Wireless channels suffer from multipath fading
Antenna diversity is a means of compensating for fading
Example Transmit Delay Diversity
OFDM Modulator
Delay
h1(t)
h2(t)
Equivalent channel is h(t) = h1(t) + h2(t -D)
More channel taps = more diversity
  Choose D large enough

## Slide 22: OFDM and MIMO Systems
Multiple-input multiple-output (MIMO) systems
  Use multiple transmit and multiple receive antennas
  Creates a matrix channel
Equivalent system for kth tone
  xk = Hk sk + vk
Vector inputs & outputs!
See Wireless Sys. Innovations Lab Web page for more info
OFDM Modulator
OFDM Modulator
Joint
Demodulator
H(t)

## Slide 23: Why OFDM in Broadcast?
Enables Single Frequency Network (SFN)
  Multiple transmit antennas geographically separated
  Enables same radio/TV channel frequency throughout a country
  Creates artificially large delay spread – OFDM has no problems!
20km

## Slide 24: Why OFDM for High-Speed Internet Access?
High-speed data transmission
  Large bandwidths -> high rate, many computations
  Small sampling periods -> delay spread becomes a serious impairment
  Requires much lower BER than voice systems
OFDM pros
  Takes advantage of multipath through simple equalization
OFDM cons
  Synchronization requirements are much more strict
    Requires more complex algorithms for time / frequency synch
  Peak-to-average ratio
    Approximately 10 log N (in dB)
    Large signal peaks require higher power amplifiers
    Amplifier cost grows nonlinearly with required power

## Slide 25: Case Study: IEEE 802.11a Wireless LAN
System parameters
  FFT size: 64
  Number of tones used 52 (12 zero tones)
  Number of pilots 4 (data tones = 52-4 = 48 tones)
  Bandwidth: 20MHz
  Subcarrier spacing : f = 20 MHz / 64 = 312.5 kHz
  OFDM symbol duration: TFFT = 1/f = 3.2us
  Cyclic prefix duration: TGI = 0.8us
  Signal duration: Tsignal = TFFT + TGI
TFFT
TGI
CP
s y m b o l i

## Slide 26: Case Study: IEEE 802.11a WLAN
Frequency Band (GHz) | Maximum Output Power (6dBi antenna gain) mW
5.15 – 5.25 | 40
5.25 – 5.35 | 200
5.725-5.825 | 800
Modulation: BPSK, QPSK, 16-QAM, 64-QAM
Coding rate: 1 / 2, 2 / 3, 3 / 4
FEC: K=7 (64 states) convolutional code