## Slide 1: Modern Digital Signal Processors

## Slide 2: Digital Signal Processor Market
Most rapidly expanding sector of semiconductor market (30% growth rate 1990-2001)
600 million cell phone subscribers worldwide (June 2001)
  DSPs in more than 60% of existing cell phones
  51.7 million cell phone subscribers in 1Q00 in China, the single largest market (30%) in Asia/Pacific (Dataquest)
How many digital signal processors (DSPs) are in each PC? Where are they?

## Slide 3: DSPs on the Market Today
Berkeley Design Tech. Inc. Pocket Guide to DSPs
  http://www.bdti.com/pocket/pocket.htm (see handout)
Texas Inst. | www.ti.com/sc/docs/dsps/dsphome.htm www.ti.com/sc/docs/dsps/develop/3party.htm | Dallas/ Houston | 45
Agere Systems | www.lucent.com/micro/dsp/ no third-party support listed | Allen-town | 25
Moto-rola | www.mot.com/SPS/DSP/ www.mot.com/SPS/DSP/developers/thirdparty.html | Austin | 10
Analog Devices | www.analog.com/SHARC_2154 www.analog.com/publications/press/products/3rd_party/ | Boston/ Austin | 8
Market Share %
Big Four Producers of DSPs
DSP Information / Third-Party Support
Agere Systems was formerly the Lucent Tech. Microelectronics Group

## Slide 4: Texas Instruments
First commercially successful DSP
  Texas Instruments TMS32010 in 1982
  Harvey Cragon (UT Austin) was a key part of design team
DSP processors shipped
  More than 250 million in 1999 (estimated)
DSP processor revenue
  $2.1 Billion of $4.4 Billion total (48% share) in 1999
  $2.7 Billion of $6.1 Billion total (44% share) in 2000
Modern DSP family is TMS 320C6000
  256-bit instructions: Very Long Instruction Word (VLIW)
  ADSL modems, 3G basestations, video codecs

## Slide 5: C6000 Instruction Set Architecture
Program RAM
Data RAM
or Cache
Internal Buses
Control Regs
Regs (B0-B15)
Regs (A0-A15)
.D1
.M1
.L1
.S1
.D2
.M2
.L2
.S2
CPU
Addr
Data
External
Memory
-Sync
-Async
DMA
Serial Port
Host Port
Boot Load
Timers
Pwr Down
Simplified Architecture
C6200 fixed point
C6400 fixed point
C6700 floating point

## Slide 6: C6000 Instruction Set Architecture
Address 8/16/32 bit data + 64 bit data on C67x
Load-store RISC architecture with 2 data paths
  16 32-bit registers per data path (A0-15 and B0-15)
  48 instructions (C62x) and 79 instructions (C67x)
Two parallel data paths with 32-bit RISC units
  Data unit - 32-bit address calculations (modulo, linear)
  Multiplier unit - 16 bit x 16 bit with 32-bit result
  Logical unit - 40-bit (saturation) arithmetic & compares
  Shifter unit - 32-bit integer ALU and 40-bit shifter
  Conditionally executed based on registers A1-2 & B0-2
  Work with two 16-bit halfwords packed into 32 bits

## Slide 7: C6000 Functional Units
.M multiplication unit
  16 bit x 16 bit signed/unsigned packed/unpacked
.L arithmetic logic unit
  Comparisons and logic operations (and, or, and xor)
  Saturation arithmetic and absolute value
.S shifter unit
  Bit manipulation (set, get, shift, rotate) and branching
  Addition and packed addition
.D data unit
  Load/store to memory
  Addition and pointer arithmetic

## Slide 8: C6000 Register Accesses Restrictions
Each function unit has read/write ports
  Data path 1 (2) units read/write A (B) registers
  Data path 2 (1) can read one A (B) register per cycle
40 bit words stored in adjacent even/odd registers
  Used in extended precision accumulation
  One 40-bit result can be written per cycle
  A 40-bit read cannot occur in same cycle as 40-bit write
Two simultaneous memory accesses cannot use registers of same register file as address pointers
No more than four reads per register per cycle

## Slide 9: C6000 Disadvantages
No acceleration for variable length decoding
  50% of computation for MPEG-2 decoding on C6x in C
  Acceleration available in C6400 family
Very deep pipeline
  If a branch is in the pipeline, interrupts are disabled: avoid branches by using conditional execution
  No hardware protection against pipeline hazards: programmer and software tools must guard against it
No hardware looping or bit-reversed addressing
40-bit accumulation incurs performance penalty
No status register: must emulate status bits other than saturation bit (.L unit)

## Slide 10: C6700 Floating Point VLIW DSP
32-bit floating-point VLIW DSP
  Introduced in 1997
  Extends C6000 instruction set for floating point arithmetic
Eight functional units: single cycle throughput
  Two ALUs are fixed-point
  Four ALUs support fixed-point and floating-point
  Two multipliers support fixed-point and floating-point
Applications include professional audio, home entertainment, wireless base stations, medical imaging, sonar imaging, and robotics

## Slide 11: C6712 vs. C6713
C6712
150 MHz clock, 900 MFLOPS
4 kB/4kB of L1 program/data memory
64 kB of L2 cache
1200 MB/s on-chip data bus bandwidth
$13.50 each in volume
C6713
225 MHz clock, 1350 MFLOPS
4 kB/4kB of L1 program/data memory
256 kB of L2 cache
1800 MB/s on-chip data bus bandwidth
$26.85 each in volume
Information as of December 3, 2001

## Slide 12: TMS320C6200 vs. Pentium
BDTImarks: Berkeley Design Technology Inc. DSP benchmark results (larger means better) http://www.bdti.com/bdtimark/results.htm
http://www.ece.utexas.edu/~bevans/courses/ee382c/lectures/processors.html

## Slide 13: Starcore
Startup company with two major investors
  Motorola (Semiconductor Product Sector, Austin, TX)
  Agere Systems (formerly Lucent Technologies Microelectronics Group, Allentown, PA)
Has developed 16-bit VLIW DSPs
  SC140: 300 MHz, 1200 MMACS or 3000 RISC MIPS at 0.2mW/ MMAC at 1.5V or 0.07 mW/MMAC at 0.9V (Jan. 2001 figures)
  SC110: 300 MHz, 300 MMACs or 1200 RISC MIPS, one-half of the peak power consumption of SC140. (Jan. 2001 figures)

## Slide 14: TMS320C6200 vs. StarCore S140
* Does not count equivalent RISC operations for modulo addressing ** On the C62x, there is a performance penalty for 40-bit accumulation

## Slide 15: Starcore
Lucent StarPro2000 | 3 SC140 cores | servers and cellular infrastructure
Motorola MSC8101 | 1 SC140 core | third-generation wireless systems, IP telephony, modem banks, multi-channel DSL modems
Motorola MSC8102 | 4 SC140 cores | high-density multi-channel multi-standard applications, e.g. in central offices of telephone companies and third-generation wireless basestations
What does Motorola’s DigitalDNA slogan mean?

## Slide 16: Analog Devices ADSP-21161
32-bit floating-point Super Harvard Architecture (SHARC) DSP based on SIMD core (Sept. 6, 2000)
Single-cycle throughput for fixed-point and floating-point arithmetic
100 MHz clock, 600 MFLOPS
1 Mbit dual-ported memory
800 Mbyte/s of on-chip data bus bandwidth
$35 each in volumes of 1,000
Applications include high-end audio systems, wireless basestations, medical imaging, sonar imaging, and robotics

## Slide 17: Intel/Analog Devices Blackfin DSP
Collaboration begun in Dec. 1999 in Austin, TX
First member ADSP-21535 (June 20, 2001, Webcast)
16-bit fixed-point core
  High performance: 1.5V, 300 MHz, 350 mW
  Low power: 0.9V, 100 MHz, 50 mW
2.4 GB on-chip I/O bandwidth at 300 MHz
Dual multiply-accumulate units
  16-bit x 16-bit multiplier
  32-bit accumulation
  600 million MACs/second at 300 MHz

## Slide 18: Intel/Analog Devices Blackfin DSP
8 video ALUs
16-bit and 32-bit instructions
Registers
  8 32-bit address registers
  8 32-bit data registers
Addressability: 8, 16, and 32 bit data
On-core peripherals: PCI, USB, 2 UARTs (one IrDA), A/D and LCD drivers, 3 timers, etc.
Interlocked, eight-stage pipeline

## Slide 19: LSI Logic (Dallas, TX)
LSI Logic LSI401Z (Formerly ZSP164xx)
  Four-way, in-order superscalar processor
  16-bit DSP (16-bit instructions, 16-bit or 32-bit data)

## Slide 20: Benchmarking
Berkeley Design Technology Inc. BDTImark2000
  12 DSP kernels in hand-optimized assembly language
  Returns single number (higher means faster) per processor
  Use only on-chip memory (memory bandwidth is the major bottleneck in performance of embedded applications)
EDN Embedded Microprocessor Benchmark Consortium (EEMBC pronounced “embassy”)
  30 companies formed by Electronic Data News (EDN)
  Benchmark evaluates compiled C code on a variety of embedded processors (microcontrollers, DSPs, etc.)
  Application domains: automotive-industrial, consumer, office automation, networking and telecommunications

## Slide 21: Battery Technology
Key limiting factor in handheld embedded systems
  NiMH is Nickel/metal-hydroxide. Used in electric vehicles (see IEEE Spectrum, Dec. 1997, p. 69)
  NiCd, NiMH, and Li+ used in cellular phones
  Source: Larry Hayes, Motorola Semiconductor Product Sector in Phoenix, Arizona, 1998.