## Slide 1: Native Signal Processing
Ravi Bhargava
Laboratory of Computer Architecture
Electrical and Computer Engineering Department
The University of Texas at Austin
November 22, 1999

## Slide 2: Motivation
Need new ways to support emerging applications
  Multimedia
  Signal processing
  3D graphics
Many applications have similar properties
  Large streams of data
  Data parallelism
  Small data types
  Tight loops
  High percentage of computations
  Common computations (e.g. MAC)

## Slide 3: Target Applications
IP telephony gateways
Multi-channel modems
Speech processing systems
Echo cancelers
Image and video processing systems
Scientific array processing systems
Internet routers
Virtual private network servers

## Slide 4: Basic Idea
Extend capabilities of general-purpose processor
  Additions to the instruction set architecture
  Additions to the CPU state
Exploit Data Parallelism
  Single Instruction Multiple Data (SIMD)
  Multiple operations using one functional unit

## Slide 5: SIMD
Use one register to store many pieces of data

## Slide 6: Packed Arithmetic
Unsigned Packed Add with Saturation

## Slide 7: Packed Arithmetic
Multiply Accumulate

## Slide 8: MMX Example
16-bit Vector Dot-Product

## Slide 9: Dot-Product (cont.)

## Slide 10: Alternative Dot-Product
Useful in certain cases

## Slide 11: Alternative Dot-Product (cont.)
Interleaving the Data

## Slide 12: Support for NSP
Libraries
  Most common type of support
  Tradeoff speed for robustness
Compiler
  Can’t do too much, but getting better
  Can use macros, annotations, and “intrinsics”
Operating System
  Needs to know about any new registers and states
  Needs to know about any new exceptions

## Slide 13: Common Concerns
Organizing SIMD data
  Packing and unpacking SIMD registers
  Shuffling data within the register
  “swizzling”, “scatter and gather”
  Permute units
Aligning data
  Special load and store instructions
  New data types in compilers
  Padding data types

## Slide 14: New Instructions
Packed Comparisons
Packed maximum, minimum
Packed Average
Packed Sum of absolute differences
Multiply-accumulate
Conversion: signed, data length, data type
Approximations: reciprocal, reciprocal square root
Prefetch
Store fence

## Slide 15: Evolution of NSP
Visual Instruction Set (VIS)
  First NSP extension found on Sun’s UltraSPARC
MMX
  First x86 NSP extensions, created for Intel’s Pentium
3DNow!
  Addition of FP SIMD instructions on AMD’s K6-2
Altivec
  Adds new CPU State for Motorola’s G4 PowerPC
Streaming SIMD Extensions
  New x86 FP SIMD for Intel’s Pentium III

## Slide 16: VIS
Uses 64-bit floating point registers
Data formats “tailored for graphics”
No saturation arithmetic
Only 8-bit x 16-bit multiplication
Implicit assumptions about rounding & number of significant bits
3% increase in die area
C Macros and “MediaLib” for development

## Slide 17: VIS Tailored for Graphics
Assumes pixels will be most common data

## Slide 18: UltraSPARC with VIS

## Slide 19: 3DNow! on K6-II
21 new SIMD instructions
  Including floating point SIMD instructions
  PREFETCH instruction
  Approximation and intra-element instructions
Two 32-bit FP instructions in one register
  Two 3DNow! instructions possible per cycle
  Latency of two cycles, throughput of one cycle
Aliased to the FP registers (like MMX)

## Slide 20: 3DNow! on the K6-II

## Slide 21: Streaming SIMD Extension
70 new instructions
8 new 128-bit SSE registers (OS support)
Execute two SSE instructions simultaneously
  Double-cycle through existing 64-bit hardware
  2 micro-ops per SSE instruction
  Latency often two cycles or greater
Explicit scalar SSE instructions
Prefetch to various levels of cache
Non-allocating stores
10% increase in die area

## Slide 22: Pentium III

## Slide 23: 3DNow! on the Athlon
Zero switching overhead back to FP!
Most instructions have one cycle latency
24 more instructions
  12 more integer SIMD instructions
  7 more data manipulation instructions
  5 “unique” DSP instructions
    Packed FP to Integer word conversion with sign extend
    Packed FP negative accumulate
    Packed FP mixed negative-positive accumulate
    Packed integer word to FP conversion
    Packed swap double-word

## Slide 24: Athlon

## Slide 25: Altivec
162 new instructions
  Intra-element: rotate, shift, max, min, sum across
  Approximations: log2, 2 raised to an exponent
  No explicit SAD instruction
Separate 32-entry, 128-bit vector register file
Floating-point and fixed-point data types
Instructions have three source operands

## Slide 26: Altivec (cont.)
Permute Unit
  Shuffle data from any of the 32 byte locations in two operands to any of 16 byte locations in the destination
  Permute instructions - one cycle
Vector Unit
  Three sub-units
  Simple fixed-point - one cycle
  Complex fixed-point - three cycles
  Floating-point - four cycles

## Slide 27: Applications using 3DNow!
3D games and engines
  Descent 4, Diablo 2, Quake III, Unreal 2
3D video card drivers
  Matrox, Diamond, ATI, nVidia, 3DLabs, 3dfx
Graphics APIs
  OpenGL, DirectX, Glide
Other apps
  Naturally Speaking, LiveArt98, WinAMP, PicVideo, PC-Doctor, QuickTech, XingMP3

## Slide 28: Additional Information
MMX talk and additional references
  http://www.ece.utexas.edu/~ravib/mmxdsp/
NSP talk outline and links
  http://www.ece.utexas.edu/~ravib/nsp/