## Slide 1
Ravi Bhargava *
Lizy K. John *
Brian L. Evans
Ramesh Radhakrishnan *
The University of Texas at Austin
Department of Electrical and Computer Engineering
* Laboratory of Computer Architecture
Evaluating MMX Technology
Using DSP and Multimedia Applications
November 22, 1999

## Slide 2
This talk is a condensed version of a presentation given at:
The 31st International Symposium on Microarchitecture
(MICRO-31)
Dallas, Texas
November 30, 1998
http://www.ece.utexas.edu/~ravib/mmxdsp/
Evaluating MMX Technology
Using DSP and Multimedia Applications

## Slide 3
57 New assembly instructions
64-bit registers
Aliased to FP registers
EMMS Instruction
No compiler support
MMX

## Slide 4
8, 16, 32, 64-bit fixed-point data
Packing, unpacking of data
Packed moves
16-bit multiply-accumulate
Saturation arithmetic
MMX

## Slide 5
Independent evaluation of MMX
How much speedup is possible?
What tradeoffs are involved?
  Time, complexity, performance, precision
Characterization of MMX workloads
  Instruction mix, memory accesses, etc.
Motivation

## Slide 6
Finite Impulse Response Filter
  Speech, general filtering
Fast Fourier Transform
  MPEG, spectral analysis
Matrix &Vector Multiplication
  Image processing
Infinite Impulse Response Filter
  Audio, LPC
Kernels

## Slide 7
JPEG Image Compression
  Bitmap Image to JPEG Image
  2D DCT
G.722 Speech Encoding
  Compression, Encoding of Speech
  ADPCM
Image Processing
  Uniform Color Manipulation
  Vector Arithmetic
Doppler Radar Processing
  Vector Arithmetic, FFT
Applications

## Slide 8
Adjust non-MMX benchmark
  DSP environment
Create MMX version
  Setup like non-MMX
  Use Intel Assembly Libraries
Microsoft Visual C++ 5.0
Simulate with VTune 2.5.1
Methodology

## Slide 9
Not just function swapping
Different input data types
  Fixed-point versus floating-point
  16-bit versus 32-bit
Reordering of data
  Ex: Arrangement of filter coefficients
  Row-order versus column-order
Creating MMX Benchmarks

## Slide 10
Intel performance profiling tool
  Designed for “hot spots”
Simulate sections of code
  Pentium with MMX
  CPU penalties
  Instruction mix
  Library calls
Hardware performance counters
VTune 2.5.1

## Slide 11
Ratio of non-MMX to MMX Programs
Overall Results

## Slide 12
JPEG and G722 show slowdowns
Superlinear speedup in MatVec
  16-bit data, 6.6X speedup
  Free unrolling
MMX related overhead
  FIR, Radar, JPEG, G722
MMX multiplication
  Fewer cycles
  Requires unpacking
Overall Results

## Slide 13
% MMX Instructions and MMX Instruction Mix. Speedup increasing from left to right
MMX Instruction Mix

## Slide 14
Input set size
  Small: FIR, Radar, G722, JPEG
  Large: IIR, Image, MatVec, FFT
  Affects MMX %, speedup
“Automatic” Packing
Less than 50% MMX arithmetic
FFT
  Converts to FP
  Old version: 40% MMX, less speedup
MMX Instruction Mix

## Slide 15
Ratio of Non-MMX Assembly to MMX
Versus Optimized Code

## Slide 16
Non-MMX version 1.98X faster
But... inserted MMX code 1.6X faster
Function call overhead
  8.8X more in MMX version
MMX Maintenance Instructions
  Accounting for precision
  Non-sequential data accesses
Closer Look at JPEG

## Slide 17
Slowdown possible
  JPEG and G722
Parallel, contiguous data
  Hard to find
Precision
  Obtainable at a price
Library function call overhead
  Hand-coded assembly, inlining
Some Problems

## Slide 18
Speedup available with libraries
  Kernels: 1.25 to 6.6
  Applications: 1.21 to 5.5
  Versus optimized FP: 1.25 to 1.71
General Characteristics of MMX
  More static instructions used
  Fewer dynamic instructions
  Fewer memory references
  Less than 50% of MMX is arithmetic
Summary of Results

## Slide 19
This concludes this portion of the talk.
The following slides provide further information on: methodology, benchmarks, results, and additional work.

## Slide 20: Unreal 1.0
Doom-like game
Command-line MMX switch
Hardware Performance Counters
48% MMX Instructions
Real-time. What is speedup?
1.34X more frame/second
Same trends as benchmarks

## Slide 21
Focus on “Important” Code
Buffer Inputs and Outputs
No OS Effects Measured
Real-time Atmosphere
DSP-like Environment

## Slide 22
Some functions use MMX
  8-bit and 16-bit data
  Scale factors
  Vector inputs
  Library-specific structures
Signal Processing Library 4.0
Recognition Primitives Library 3.1
Image Processing Library 2.0
Intel Assembly Libraries

## Slide 23: Precision
JPEG
  Non-MMX SNR: 31.05 dB
  MMX SNR: 31.04 dB
Image: No Change
G722
  Non-MMX SNR: 5.46 dB
  MMX SNR: 5.18 dB
Doppler Radar
  Less than 1%

## Slide 24
Profiled Program
  2D DCT
  Quantization
  Color Conversion
  74% of execution time
Small Block Size
  8x8 blocks of pixels
An Example: JPEG

## Slide 25
2D DCT
  Library only has 1D DCT
  Data in different order
Quantization
  Not enough data parallelism
Color conversion
  Create and fill vectors
JPEG: Inserting MMX

## Slide 26: FIR Filter
Finite Impulse Response Filter
Moving averages filter
Process one input at a time
Non-MMX: 32-bit FP
MMX: 16-bit fixed-point
Filter length is 35

## Slide 27: FFT
Fast Fourier Transform
Computes discrete Fourier Transform
4096-point
In-place
Whole FFT to MMX function
Non-MMX: 32-bit FP
MMX: 16-bit fixed-point

## Slide 28: MatVec
Matrix & Vector Multiplication
  512x512 matrix times 512-entry vector
  Dot product of two 512-entry vectors
Both versions: 16-bit data

## Slide 29: IIR
Infinite Impulse Response Filter
  Butterworth coefficients
  Direct form, Bandpass
  Filter length of 8, 17 coefficients
Requires high precision
  Feedback
  Our versions unstable

## Slide 30: Doppler Radar Processing
Subtract complex echo signals
Removing stationary targets
Estimates power spectrum
Dominant frequency from peak of FFT
16-point, in-place FFT

## Slide 31: G.722 Speech Encoding
Input signal: 16-bit, 16 kHz
Output signal: 8-bit, 8 kHz
6 kb speech file