## Slide 1: Texas Instruments ExpressDSP Algorithm Standard
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
August 7, 2001

## Slide 2: Outline
Introduction
ExpressDSP requirements and rules
Source code
Algorithm performance characterization
C6000-specific guidelines
Direct memory access (DMA) resource rules
Conclusion
Reference: http://www-s.ti.com/sc/techlit/spru352

## Slide 3: Introduction: Algorithm Model
Transformation of inputs into outputs
Interoperate (play well) with other algorithms
Decoupled from scheduling and resource allocation (e.g. dynamic memory allocation)
object code (function)
…
inputs
outputs
algorithm performance
…
source code (function)

## Slide 4: Introduction: Abstraction
Maurice Wilkes: “There is no problem in computer programming that cannot be solved by an added level of indirection.”
  Achieve device independence by decoupling algorithms and physical peripherals
  Achieve algorithm interchangeability by using function pointers
Maurice Wilkes is a hardware designer and the father of microcoding. He is from England and is 88 years old. He is one of the few foreign members of the US National Academy of Engineering.

## Slide 5: Introduction: Abstraction
Jim Gray: “There is no performance problem that cannot be solved by eliminating a level of indirection.”
Jim Gray is software designer who is an expert in transaction processing and databases. He is in his early 50s and works at Microsoft Research in the San Francisco Bay Area. Jim is a member of the US National Academy of Engineering.

## Slide 6: ExpressDSP Requirements
Algorithms from multiple vendors can be integrated into a single system
Algorithms are framework agnostic
Algorithms can be deployed in statically scheduled and dynamically scheduled run-time environments
Algorithms can be distributed in binary form (e.g. Hyperception’s Hypersignal approach)
Algorithm integration does not require compilation but may require reconfiguration and relinking

## Slide 7: ExpressDSP Rules
Source code (levels 1 and 2)
  Programming guidelines: C callable, reentrant, etc.
  Component model: modules, naming conventions, etc.
Algorithm performance characterization (level 2)
  Data and program memory
  Interrupt latency (delay upon invocation)
  Execution time (throughput)
DMA resource rules (level 2)
DSP-specific (level 3)

## Slide 8: Programming Guidelines (level 1)
R1 Algorithms must follow run-time conventions imposed by TI’s implementation of the C language
  Only externally visible functions must be C callable
  All functions must be careful in use of the stack
R2 Algorithms must be reentrant
  Only modify data on stack or in instance “object”
  Treat global and static variables as read-only data
  Do not employ self-modifying code
  Disable interrupts (disabling all thread scheduling) around sections of code that violate these rules

## Slide 9: Reentrant Example
/* previous input values */
int iz0 = 0, iz1 = 0;
void PRE_filter(int piInput[], int iLength) {
int i;
for (i = 0; i < iLength; i++) {
int tmp = piInput[i] – iz0 + (13*iz1 + 16) / 32;
iz1 = iz0;
iz0 = piInput[i];
piInput[i] = tmp;
}
}
void PRE_filter(int piInput[], int iLength, int piPrevInput[]) {
int i;
for (i = 0; i < iLength; i++) {
int iTmp = piInput[i] – piPrevInput[0] + (13*piPrevInput[1] + 16) / 32;
piPrevInput[1] = piPrevInput[0];
piPrevInput[0] = piInput[i];
piInput[i] = iTmp;
}
}
Not reentrant
Reentrant
state

## Slide 10: Component Model (level 2)
R7 All header files must support multiple inclusions within a single source file
R8 All external definitions must be API identifiers or API and vendor prefixed (e.g. H263_UT)
R11 All modules must supply an initialization (e.g. FIR_init) and finalization (e.g. FIR_exit) method
  Init function: initialize global data
  Exit function: run-time debugging assertions for sanity checks (usually empty in production code)

## Slide 11: Component Model (level 2)
Convention | Description | Example
Variables and functions | Begin with lower case (after prefix) | LOG_printf()
Constants | All uppercase | G729_FRAMELEN
Data types | Title case after prefix | LOG_Obj or int
Structure fields | Lowercase | buffer
Macros | Same as constants or functions as appropriate | LOG_getbuf()
R10 Naming Conventions

## Slide 12: FIR Module
typedef struct FIR_Params {
int iFrameLen;
int *piCoeff;
} FIR_Params;
const FIR_Params FIR_PARAMS = { 64, NULL };
typedef struct FIR_Obj {
int iHist[16];
int iFrameLen;
int *piCoeff;
} FIR_Obj;
void FIR_init(void) { }
void FIR_exit(void) { }
typedef struct FIR_Obj* FIR_Handle;
FIR_Handle FIR_create( FIR_Obj *pFir, const FIR_Params *pParams) {
if (pFir) {
if (pParams == NULL) {
pParams = &FIR_PARAMS;
}
pFir->iFrameLen =
pParams->iFrameLen;
pFir->piCoeff = pParams->piCoeff;
memset(pFir->iHist, 0,
sizeof(pFir->iHist));
}
return(pFir);
}
void FIR_delete(FIR_Handle fir) { }

## Slide 13: Algorithm Performance (level 2)
Algorithms declare memory usage in bytes
  R19 Worst-case heap data memory (inc. alignment)
  R20 Worst-case stack space data memory
  R21 Worst-case static data memory
  R22 Program memory
Algorithms declare
  R23 Worst-case interrupt latency
  R24 Typical period and worst case execution time
Include this information in the comment header

## Slide 14: Example: Worst-case Heap Usage
 | Size | Align | Size | Align | Size | Align
Scratch | 0 | 0 | 1920 | 0 | 0 | 0
Persistent | 0 | 0 | 0 | 0 | 1440 | 0
DARAM
SARAM
External
Example requires 960 16-bit words of single-access on-chip memory, 720 16-bit words of external persistent memory.
Entries in table may be functions of algorithm parameters.

## Slide 15: C6000-specific Rules
R25 All C6000 algorithms must be supplied in little endian format.
  Guideline 13 All C6000 algorithms should be supplied in both little and big endian formats
R26 All C6000 algorithms must access all static and global data as far data.
R27 C6000 algorithms must never assume placement in on-chip memory; they must properly operate with program memory operated in cache mode.

## Slide 16: C6000 Register Usage
Register | Usage | Type
A0-A9 | General purpose | Scratch
A10-A14 | General purpose | Preserve
A15 | Frame pointer | Preserve
A16-A31 (C64x) | General purpose | Scratch
Register | Usage | Type
B0-B9 | General purpose | Scratch
B10-B13 | General purpose | Preserve
B14 | Data page pointer | Preserve
B15 | Stack pointer | Preserve
B16-B31 (C64x) | General purpose | Scratch
Preserve: function must restore its value on exit

## Slide 17: DMA Resource Rules
DMA is used to move large blocks of memory on and off chip
Algorithms cannot access DMA registers directly
Algorithms cannot assume a particular physical DMA channel
Algorithms must access the DMA resources through a handle using the specific asynchronous copy (ACPY) APIs.
IDMA R1 All data transfer must be completed before return to caller

## Slide 18: DMA Resource Rules
IDMA R2 All algorithms using the DMA resource must implement the IDMA interface
IDMA R3 Each of the IDMA methods implemented must be independently relocateable.
IDMA R4 All algorithms must state the maximum number of concurrent DMA transfers for each logical channel
IDMA R5 All algorithms must characterize the average and maximum size of the data transfers per logical channel for each operation.

## Slide 19: Top 10 XDAIS Rules
All global and static variables must be constants
Must use C calling conventions
All include (.h) files must have an #ifdef structure to prevent it from being evaluated twice
All visible (external) variables, functions, and constants must be prefixed by PACKAGE_ORG, e.g. H263_UT.
Never use absolute (hardcoded) addresses (allows data to be relocated and properly aligned)

## Slide 20: Top 10 XDAIS Rules
Must use IDMA instead of regular DMA (i.e. DAT_copy)
Never allocate or deallocate dynamic memory (no use of malloc, calloc, or free)
Disable interrupts (disables all thread scheduling) around sections of code that are not reentrant
Always check to see if a DSP/BIOS, chipset library, or I/O function is allowed (most are not)
Compile in far mode, e.g. in Code Composer

## Slide 21: Issues for Future Standards
Version control
Licensing, encryption, and IP protection
Installation and verification (digital signatures)
Documentation and online help