## Slide 1: Review for Midterm #2
Wireless Networking and Communications Group
July 30, 2026
Prof. Brian L. Evans
EE 445S Real-Time Digital Signal Processing Laboratory

## Slide 2: Outline
Introduction
Signal processing building blocks
  Filters
  Data conversion
  Rate changers
Communication systems
Design tradeoffs in signal quality vs. implementation complexity

## Slide 3: Introduction
Signal processing algorithms
  Multirate processing: e.g. interpolation
  Local feedback: e.g. IIR filters
  Iteration: e.g. phase locked loops
Signal representations
  Bits, symbols
  Real-valued symbol amplitudes
  Complex-valued symbol amplitudes (I-Q)
  Vectors/matrices of scalar data types
Algorithm implementation
  Dominated by multiplication/addition
  High-throughput input/output
Do not need recursion
Often iterative
Bit error rate vs. Signal-to-noise ratio (Eb/No)
Communication signal quality plot

## Slide 4: Finite Impulse Response Filters
Pointwise arithmetic operations (addition, etc.)
Delay by m samples
Finite impulse response filter
  Always stable
  Each input sample produces one output sample
  DSP processor architecture
op

…
…
FIR

## Slide 5: Infinite Impulse Response Filters

x[k]
y[k]
y[k-M]
x[k-1]
x[k-2]
b2
b1
b0
Unit Delay
Unit Delay
Unit Delay
x[k-N]
bN
Feed-forward
a1
a2
y[k-1]
y[k-2]
Unit Delay
Unit Delay
Unit Delay
aM
Feedback
IIR
Each input sample produces one output sample
Pole locations perturbed when expanding transfer function into unfactored form
20+ filter structures
  Direct form
  Cascade biquads
  Lattice

## Slide 6: Data Conversion
Analog-to-Digital
Quantize to B bits
  Quantization error = noise
  SNRdB  C0 + 6.02 B
  Dynamic range  SNR
Digital-to-Analog
A/D and D/A lowpass filter
  fstop < ½ fs fpass  0.9 fstop
  Astop = SNRdB Apass = dB
  dB = 20 log10 (2mmax / (2B-1))
   is quantization step size
  mmax is max quantizer voltage
Analog Lowpass Filter
Discrete to Continuous Conversion
fs
Analog Lowpass Filter
Quantizer
Sample at rate of fs
B
B

## Slide 7
<number>
Increasing Sampling Rate
Upsampling by L denoted as L
  Outputs input sample followed by L-1 zeros
  Increases sampling rate by factor of L
Finite impulse response (FIR) filter g[m]
  Fills in zero values generated by upsampler
  Multiplies by zero most of time (L-1 out of every L times)
Sometimes combined into rate changing FIR block
m
Output of Upsampler by 4
1
2
3
4
5
6
7
8
0
1
2
Output of FIR Filter
3
4
5
6
7
8
m
0
1
2
Input to Upsampler by 4
n
0
g[m]
4
1
4
1
1
FIR
1
4

## Slide 8
<number>
Polyphase Filter Bank Form
Filter bank (right) avoids multiplication by zero
  Split filter g[m] into L shorter polyphase filters operating at the lower sampling rate (no loss in output precision)
  Saves factor of L in multiplications and previous inputs stored and increases parallelism by factor of L
g0[n]
g1[n]
gL-1[n]
s(Ln)
s(Ln+1)
s(Ln+(L-1))
g[m]
L
Oversampling filter a.k.a. sampler + pulse shaper a.k.a. linear interpolator
Multiplies by zero (L-1)/L of the time
1
L
L
1

## Slide 9: Decreasing Sampling Rate
Finite impulse response (FIR) filter g[m]
  Typically a lowpass filter
  Enforces sampling theorem
Downsampling by L denoted as L
  Inputs L samples
  Outputs first sample and discards L-1 samples
  Decreases sampling rate by factor of L
Sometimes combined into rate changing FIR block
4
4
1
g[m]
1
1
1
2
Input to Downsampler
3
4
5
6
7
8
m
0
1
2
Output of Downsampler
n
0
FIR
4
1

## Slide 10
<number>
Polyphase Filter Bank Form
  y[1] = v[L] = h[0] s[L] + h[1] s[L-1] + … + h[L-1] s[1] + h[L] s[0]
Filter bank only computes values output by downsampler
  Split filter h[m] into L shorter polyphase filters operating at the lower sampling rate (no loss in output precision)
  Reduces multiplications and increases parallelism by factor of L
h0[n]
h1[n]
hL-1[n]
h[m]
L
s(Ln)
s(Ln+1)
s(Ln+(L-1))
Undersampling filter a.k.a. Matched filter + sampling a.k.a. linear decimator
Outputs discarded (L-1)/L of the time
1
1
L
M
s[m]
s[m]
y[n]
y[n]
v[m]

## Slide 11
<number>
Communication Systems
Message signal m[k] is information to be sent
  Information may be voice, music, images, video, data
  Low frequency (baseband) signal centered at DC
Transmitter baseband processing includes lowpass filtering to enforce transmission band
Transmitter carrier circuits include digital-to-analog converter, analog/RF upconverter, and transmit filter
Baseband Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 12
<number>
Communication Systems
Propagating signals experience attenuation & spreading w/ distance
Receiver carrier circuits include receive filter, carrier recovery, analog/RF downconverter, automatic gain control and analog-to-digital converter
Receiver baseband processing extracts/enhances baseband signal
Baseband Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Model the environment

## Slide 13
<number>
Quadrature Amplitude Modulation
i[n]
gT[m]
L
+
cos(0 m)
q[n]
gT[m]
L
sin(0 m)
Serial/ parallel converter
1
Bits
Map to 2-D
constellation
J
L samples per symbol (upsampling)
Transmitter Baseband Processing
Pulse shaper (FIR filter)
Index
Baseband Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 14
<number>
Quad. Amplitude Demodulation
iest[n]
hopt[m]
L
cos(0 m)
hopt[m]
L
sin(0 m)
L samples per symbol (downsampling)
Matched filter (FIR filter)
qest[n]
Parallel/ serial converter
J
Bits
Decision Device
1
Symbol
Baseband Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
heq[m]
Channel equalizer (FIR filter)
Receiver Baseband Processing

## Slide 15: Modeling of Points In-Between
Baseband discrete-time channel model
  Combines transmitter carrier circuits, physical channel and receiver carrier circuits
  One model uses cascade of gain, FIR filter, and additive noise
Baseband Processing
Carrier Circuits
Transmission Medium
Carrier Circuits
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
FIR
+
noise

## Slide 16: QAM Signal Quality
Assumptions
  Each symbol is equally likely
  Channel only consists of additive noise
    White Gaussian noise with zero mean and variance 2 in in-phase and quadrature components
    Total noise power of 22
  Carrier frequency and phase recovery
  Symbol timing recovery
Probability of symbol error
  Constellation spacing of 2d
  Symbol duration of Tsym
3
3
3
3
2
2
2
2
2
2
2
2
1
1
1
1
I
Q
16-QAM