## Slide 1
EE 445S Real-Time Digital Signal Processing Lab Spring 2012
Lab #3.1 Digital Filters
Some contents are from the book
“Real-Time Digital Signal Processing from MATLAB to C with the TMS320C6x DSPs”
Notes: 1

## Slide 2
2
Outline
Frame-based DSP
Frame-based FIR filter
Code Optimization
Notes: 2

## Slide 3
3
Sample-based DSP
Easier to understand and program
Minimize the system latency (act on each sample as soon as it is available)
Insufficient cycles (codec transfers; memory access; instruction and data cache latency)
Input one sample
Process one sample by DSP
Output one sample
Reconstructed analog signal
Analog signal
Notes: 3

## Slide 4
4
Frame-based DSP
Input one sample
Process N samples by DSP
Output N samples
Reconstructed analog signal
Analog signal
Collected N samles?
Start assembling the next frame
No
Yes
Notes: 4

## Slide 5
Triple Buffering
Initial Condition (all three buffers filled with zeros)
Pointer pInput
Pointer pProcess
Pointer pOutput
Buffer A
Buffer B
Buffer C
Time Progression
pointer | T0 | T1 | T2 | T3 | T4 | and so on …
pInput | Buffer A | Buffer C | Buffer B | Buffer A | Buffer C | and so on …
pProcess | Buffer B | Buffer A | Buffer C | Buffer B | Buffer A | and so on …
pOutput | Buffer C | Buffer B | Buffer A | Buffer C | Buffer B | and so on …
1. Each time block is the amount of time needed to fill one frame with samples.
2. Time T0: Buffer A is filling, Buffer B and C are still filled with zeros.
3. Time T1: Buffer C is filling, Buffer A is being processed, Buffer B is all zeros.
4. Time T2: the first actual output appears when Buffer A is sent to the DAC.
5. The same pattern repeats as shown above for as long as the program runs.
Notes: 5

## Slide 6
Frame-based convolution (FIR filter)
x[N-2] | x[N-1] | x[0] | x[1] | x[2] | … | x[N-2] | x[N-1] | x[0] | x[1] | x[2] | … | x[N-2] | x[N-1]
From previous frame
Frame 1
Frame 2
b[0] | b[1] | b[2]
b[0] | b[1] | b[2]
b[0] | b[1] | b[2]
b[0] | b[1] | b[2]
b[0] | b[1] | b[2]
b[0] | b[1] | b[2]
Last allowable position for B
Can’t do this
Can’t do this
Can’t do this
Second-order FIR filter implementation
Notes: 6

## Slide 7: Code Optimization
A typical goal of any system’s algorithm is to meet real-time
You might also want to approach or achieve “CPU Min” in order to maximize #channels processed
The minimum # cycles the algorithm takes based on architectural limits (e.g. data size, #loads, math operations req’d)
Goals:
CPU Min (the “limit”):
Often, meeting real-time only requires setting a few compiler options
However, achieving “CPU Min” often requires extensive knowledge of the architecture (harder, requires more time)
Real-time vs. CPU Min

## Slide 8
8
“Debug” vs “Optimized” Benchmarks
for (j = 0; j < nr; j++) {
sum = 0;
for (i = 0; i < nh; i++)
sum += x[i + j] * h[i];
r[j] = sum >> 15;
}
Debug – get your code LOGICALLY correct first (no optimization)
“Opt” – increase performance using compiler options (easier)
“CPU Min” – it depends. Could require extensive time
Optimization | Machine Cycles
Debug (no opt, –g) | 817K
“Release” (-o3, no -g) | 18K
CPU Min | 6650
Notes: 8

## Slide 9: Levels of Optimization
FILE1.C
{
{
}
{
. . .
}
}
{
. . .
}
FILE2.C
-o0, -o1 -o2 -o3 -pm -o3
LOCAL
single block
FUNCTION
Across blocks
FILE
Across
functions
PROGRAM
Across files
{
. . .
}