## Slide 1: Discrete-Time Convolution
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 8 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
Discrete-Time Convolution – SPFirst Sec. 5-4 to 5-7
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

✔
✔
✔
✔
✔
✔

## Slide 3: Linear Time Invariant Systems
Have rich set of mathematical tools for analysis
Discrete-Time Convolution – SPFirst Sec. 5-5 Intro & Sec. 5-5.1
T{•}
y[n]
x[n]
T{•}
yshifted[n]
x[n-n0]
Characterize properties of system as a closed box
Time-Invariance
  When input delayed by n0, output delayed by same amount
  For y[n] = x2[n],
  yshifted[n] = (x[n-n0])2
  = x2[n-n0]
  = y[n-n0]
  YES
  For y[n] = n x[n],
  yshifted[n] = n x[n-n0]
  NO
  Try input x[n-n0] and see if response yshifted[n] = y[n-n0]

## Slide 4: Linear Time Invariant Systems
Consider a system
Discrete-Time Convolution – SPFirst Sec. 5-5.2
T{•}
y1[n]
x1[n]
T{•}
y2[n]
x2[n]
  For y[n] = x2[n],
  yscaled[n] = (a x[n])2
  = a2 x2 [n].
  Is it a y[n]?
  NO
  For y[n] = n x[n],
  yscaled[n] = n (a x[n])
  YES
  = a (n x[n])
  = a y[n]
  yadditive[n] = n (x1[n] + x2[n])
  = n x1[n] + n x2[n]
  = y1[n] + y2[n]
  YES
Linearity means additivity and homogeneity hold
Additivity
  Input x1[n] + x2[n] gives additive output y1[n] + y2[n]
Homogeneity
    Input a x1[n] gives scaled output a y1[n] for all constant a

## Slide 5: Role of Initial Conditions
Unit delay system
  Observe system with y[n] = x[n-1] for time n ≥ 0
  First input value is x[0] and first output value is y[0]
  What is the value of y[0]?
  For input a x[n], what is the output yscaled[n]?
  For input x1[n] + x2[n], what is the output yadditive[n]?
  For input x[n-n0], what is the output yshifted[n]?
Discrete-Time Convolution – SPFirst Sec. 5-4.1 & 5-5.3 & 8-2
Linearity and time-invariance system properties
  System must be “at rest” (i.e. initial conditions are zero)
  Necessary but not sufficient condition

## Slide 6: FIR Filters
Time-invariance for input x[n-n0], is output y[n-n0]?
Additivity for input x1[n]+x2[n], is output y1[n]+y2[n]?
Homogeneity: for input a x[n], is output a y[n]?
Discrete-Time Convolution – SPFirst Sec. 5-5.3
  YES
  YES
  YES

## Slide 7: FIR Filters
What happens when observing FIR filter for n ≥ 0?
  First input value is x[0] and first output value is y[0]
  What is the value of y[0]?
  What are the initial conditions?
Discrete-Time Convolution – SPFirst Sec. 5-4 & 5-5.3
h[0]
h[1]
h[2]
h[3]
FIR filter block diagram
  Where are the initial conditions?

## Slide 8: Convolution and LTI Systems
Output y[n] for input x[n]
Discrete-Time Convolution – SPFirst Sec. 5-6.1
Decompose x[n] into weighted sum of delayed impulses
Apply additivity
Apply homogeneity
Apply time-invariance
Apply change of variables

## Slide 9: FIR Convolution
Impulse response h[n] has extent 0 ≤ n ≤ M
y[n] = h[0] x[n] + h[1] x[n-1]
= ( x[n] + x[n-1] ) / 2
n
h[n]
Averaging filter impulse response
0
1
2
3
Example: Two-point averaging filter M = 1
Discrete-time convolution demos
  http://dspfirst.gatech.edu/matlab/#dconvdemo
  http://pages.jh.edu/~signals/discreteconv2/index.html
Discrete-Time Convolution – SPFirst Sec. 5-6.1
h = [1/2 1/2];
x = [0 1 2 3 2 1 0];
y = conv(h, x);

## Slide 10: Convolution Properties
Convolution with impulse
Commutative property
  Showed earlier on slide 8-8
Associative property
Discrete-Time Convolution – SPFirst Sec. 5-6.2
Non-zero when m = n – n0

## Slide 11: Cascaded LTI Systems
Switching the order of cascaded LTI systems
  Application of associative property of convolution
Discrete-Time Convolution – SPFirst Sec. 5-7
©2003-2016, JH McClellan & RW Schafer

## Slide 12: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
8-12