## Slide 1: Z-Transforms
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 10 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Z-Transforms – SPFirst Ch. 7 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12
✔
✔
✔
✔
✔
✔
✔


✔
** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔

## Slide 3: Z-Transforms
Analysis tool for discrete-time signals and systems
  Converts convolution & difference equations into polynomials
  Describes LTI system transfer of input to output frequencies
Z-Transforms – SPFirst Ch. 7 Intro & Sec. 7-1
z
z
time domain
z-domain
Adds third domain to time and frequency domains
  Hopefully pick domain in which analysis is the easiest
General definition: z is complex variable
Simplified definition for finite-length signal x[n]

## Slide 4: Z-Transform Pairs
Z-transform for finite length signal x[n]
Z-Transforms – SPFirst Sec. 7-1
z
z
valid for all z
z
valid for all z ≠ 0
z
valid for all z ≠ 0
Unit impulse
Delayed unit impulse
Two-point impulse response
polynomial in z -1

## Slide 5: Z-Transform Pairs
x[n] | X(z) | Valid
 |  | all z
 |  | z ≠ 0
 |  | z ≠ 0
Z-Transforms – SPFirst Sec. 7-2
FIR filter of Mth order
  Impulse response h[n]
  Let x[n] = zn for –∞ < n < ∞
h[n]
  H(z) is system function, a.k.a. transfer function in z-domain
  H(z) is z-transform of impulse response h[n]
z
Review
polynomial in z -1
  If H(z) = 1 + 2z-1 + z-2, what is h[n]?

## Slide 6: Z-Transform Properties
Superposition property
Z-Transforms – SPFirst Sec. 7-3 & 7-4
z
  When viewed as system, z-transform has linearity
Time-delay property
  z-1 in z-domain corresponds to time shift of 1 sample
z
x[n]
y[n]
initial condition
z-1
if x[-1] = 0 system is LTI

## Slide 7: Convolution and the z-Transform
Unit delay
Z-Transforms – SPFirst Sec. 7-5
y[n] | Y(z) | Valid
 |  | all z
 |  | z ≠ 0
 |  | z ≠ 0
 |  | z ≠ 0
 |  | **
 |  | z ≠ 0
Review
if x[-1] = 0 system is LTI
x[n]
y[n]
z-1
z
Convolution property
  h[n] = d[n-1]
  y[n] = x[n] * d[n-1] = x[n-1]
  Y(z) = z-1 X(z) = H(z) X(z)
Assuming causal x[n] i.e. x[n] = 0 for n < 0

## Slide 8: Cascading LTI Systems
Based on convolution property
Z-Transforms – SPFirst Sec. 7-5.1
X(z)
W(z)
Y(z)
W(z) = H1(z) X(z)
Y(z) = H2(z) W(z) = H2(z) H1(z) X(z)
X(z)
Y(z)
H(z) = H2(z) H1(z) = H1(z) H2(z)

## Slide 9: z-Domain and Frequency Domain
Z-Transforms – SPFirst Sec. 7-6
Make connection directly from their definitions
How does look in z-domain?
Circle of radius 1 (a.k.a. unit circle)
Basis for freqz(h) command

## Slide 10: L-Point Averaging Filter
Impulse response:
Z-Transforms – SPFirst Sec. 7-6 & 7.7
Z-transform
n
h[n]
1
L-1
L
0
-1
2
  Roots of denominator (poles):
  Roots of numerator (zeros):
h = (1/10)*ones(1,10);
zplane(h);
  Zero at z = 1 cancels pole at z = 1
L=10

## Slide 11: L-Point Averaging Filter
Z-Transforms – SPFirst Sec. 7-6 & 7.7
Zeros in magnitude response at
h = (1/3)*ones(1,3);
freqz(h);
h = (1/7)*ones(1,7);
freqz(h);
h = (1/10)*ones(1,10);
freqz(h);
L = 3
L = 7
L = 11

## Slide 12: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
10-12