## Slide 1: Sampling and Reconstruction
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 16 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Continuous-Time Fourier Transform – SPFirst Ch. 12 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔

## Slide 3: Sampling: Time Domain
Many signals originate in continuous-time
Sampled analog waveform
impulse train
f(t)
t
Ts
Ts
Sampler at sampling rate of fs
f(t)
Sampling & Reconstruction – SPFirst Sec.12-3.1
By sampling continuous-time signal at isolated, equally-spaced points in time, we obtain a sequence of numbers
  Talking on cell phone, or playing acoustic music
  Ts is sampling period (Ts = 1 / fs)

## Slide 4: Sampling: Frequency Domain
Sampling replicates spectrum of continuous-time signal at integer multiples of sampling frequency
w
G(jw)
2ws
-2ws
ws
-ws
Modulation by cos(2st)
Modulation by cos(st)
How to recover F(j)?
Sampling & Reconstruction – SPFirst Sec.12-3.2
Fourier series of impulse train ws = 2 p fs
SPFirst Ex. 11-4 p. 321
w
F(jw)
2pfmax
-2pfmax
1

## Slide 5: Reconstruction
Revisiting bandlimited example on previous slide
Sampling & Reconstruction – SPFirst Sec.12-3.3
Sampler at sampling rate of fs
f(t)
g(t)
w
F(jw)
2pfmax
-2pfmax
1
Apply lowpass filter H(jw) to G(jw) to recover F(jw)
w
G(jw)
2ws
-2ws
ws
-ws
w
H(jw)
2ws
-2ws
ws
-ws
  sin(pt/Ts) / (pt/Ts)  Ts rect(w/ws)
0
t
h(t)
Ts
1
2Ts
3Ts
-Ts
-2Ts
F
Impulse response lasts for –∞ < t < ∞

## Slide 6: Sampling Theorem
Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed from its samples x(n Ts) if samples taken at rate fs > 2 fmax
Sampling & Reconstruction – SPFirst Sec.4-1, 4-2 & 12-3
Example: Sampling audio signals
  Nyquist rate = 2 fmax
  Nyquist frequency = fs / 2
  Normal human hearing is from about 20 Hz to 20 kHz
  Apply lowpass filter before sampling to pass low frequencies up to 20 kHz and reject high frequencies
  Lowpass filter needs 10% of maximum passband frequency to roll off to zero (2 kHz rolloff in this case)

## Slide 7: Discrete-to-Continuous Conversion
General form of interpolation is sum of weighted pulses
Sampling & Reconstruction – SPFirst Sec. 4-4.1, 12-3.3 & 12-3.4
Pulse function p(t)
  Input: discrete-time sequence y[n]
  Unit amplitude and/or unit area
  Rectangular, triangular, sinc, truncated sinc, etc.
  Overlaps in time with other pulses when duration > Ts
  Output: continuous-time signal that is an approximation of y(t)

## Slide 8: Ideal Bandlimited Interpolation
Sinc pulse
  In time, infinite overlap with other sinc pulses
Plot of pulse p(t)
Sampling & Reconstruction – SPFirst Sec. 4-4.6, 11-4.2, 12-3.3 & 12-3.4
Interpolate in time w/ infinite extent pulse?
  Make it finite in extent
  Truncate sinc pulse by multiplying it by rectangular pulse
Ts = 1;
t = -5 : 0.01 : 5;
p = sinc(t/Ts);
plot(t, p)
Interpolation

## Slide 9: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
16-9