## Slide 1: Common Signals in MATLAB
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
Fall 2024

## Slide 2: Outline
MATLAB
Mathematical Representations of Signals
Continuous-Time Signals
  Sinusoids
  Exponentials
  Infinite and finite length
  Sinc pulse
  Chirps
Spectrograms
Discrete-Time Signals

## Slide 3: MATLAB
Matrix Laboratory (MATLAB)
  Released in 1984 to universities
  First toolboxes in control systems and signal processing (1987)
  Semicolon prevents printing result
Scalar variables
Generating vectors
  start : inc : end generate values from start to end at increments of inc
  1 : 0.5 : 3 gives vector [1.0 1.5 2.0 2.5 3.0]
Plot vector x vs. vector t
% Scalar variables
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
% Generate four periods % of time samples
t = 0 : Ts : 4/f0;
% Apply cosine to every
% element of 2 pi f0 t
x = cos(2*pi*f0*t);
plot(t, x);
MATLAB

## Slide 4: MATLAB
Plot individual samples as stems
Sound card on platform
  Supports specific sampling rates, such as
  8000 Hz for speech and audio
    44100 Hz for CD audio
Playing sound in MATLAB
  sound(vector, rate) will play values of vector at sampling rate and clip values lying outside [-1, 1]
  soundsc(vector, rate) will scale values of vector to be in range [-1, 1] and play scaled values at sampling rate
MATLAB
stem(x);
f0 = 440;
fs = 8000; % rate
Ts = 1/fs;
t = 0 : Ts : 3; % 3 sec
x = cos(2*pi*f0*t);
sound(x, fs);

## Slide 5: Signals As Functions
Function of independent variable
  High temperature vs. day
  Audio signal vs. time
Mathematical Representations of Signals
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
t = 0 : Ts : 4/f0;
x = cos(2*pi*f0*t); plot(t, x);
Continuous-time signals
  x(t) where t can take any real value
  x(t) may be 0 for range of values of t
Discrete-time signals
  x[n] where n  {...-3,-2,-1,0,1,2,3...}
  Unitless sample index n (e.g. day)
Amplitude value may be real or complex
sep2016hightemp = [ 96, 92, 92, 93, 94, 95, 96, 95, 95, 93, 93, 93, 94, 92, 94, 95, 96, 98, 99, 99, 96, 94, 93, 97, 88, 73, 80, 89, 86, 83 ];
stem(sep2016hightemp);
title('High Temp. in Austin, TX, Sept. 2016');
xlabel('Day');
ylabel('Degrees F');
ylim( [70 100] );

## Slide 6: Signals As Functions
Mathematical Representations of Signals
Analog amplitude
1
-1
flipnumber = 1:10;
y = sign(randn(10,1));
stem(flipnumber, y);
Digital amplitude
  From a discrete set of values
Random amplitudes
  Cannot be predicted exactly or described by a formula
  Distribution of amplitude values can be defined
  Example: Flipping coin 10x
flip
-1
1
Trial #1
flip
-1
1
Trial #2
Deterministic amplitudes
  Mathematically described, e.g. x(t) = cos(2 p f0 t)

## Slide 7: Sinusoidal Signal
Mathematical form: A cos(w0 t + f)
  A is amplitude/magnitude
  w0 is frequency in rad/s where w0 = 2 p f0 and f0 is in cycles/s or Hz
  f is phase shift in radians
f0 = 440;
fs = 8000;
Ts = 1/fs;
t = 0 : Ts : 3;
x = cos(2*pi*f0*t);
sound(x, fs);
Play As Audio
Smallest period: T = 1 / f0
  Signal x(t) has period T if x(t+T) = x(t) for all t
  Using property cos(x + 2p) = cos(x),
    cos(2p f0 (t + T)) = cos(2p f0 t + 2p f0 T) = cos(2p f0 t)
    when 2p f0 T = 2p or when f0 T = 1 or when T = 1 / f0
  When f0 = 440 Hz, T = 2.27 ms
Continuous-Time Signals

## Slide 8: Exponential Signals
Real-valued exponential signals
  Amplitude values are always non-negative
  Might decay or not as t goes to infinity
t = -1 : 0.01 : 1;
e1 = exp(t);
plot(t, e1)
et
t
t = -1 : 0.01 : 1;
e2 = exp(-t);
plot(t, e2)
e-t
t
Continuous-Time Signals

## Slide 9: Exponential Signals
Complex numbers
  Cartesian form x + j y for real x and y
  Polar form r e jq = r cos(q) + j r sin(q)
  Polar-to-Cartesian: x = r cos(q) and y = r sin(q)
  Cartesian-to-Polar: and
t
Complex sinusoid: Euler’s formula
Complex sinusoidal signal
t = 0 : 1/100 : 1;
plot(t, cos(2*pi*t));
hold;
plot(t, sin(2*pi*t));
“inverse” Euler formula
Continuous-Time Signals

## Slide 10: Two-Sided Signals
Continuous-Time Signals
t
t
t
Square wave f0 = 3 Hz
t = -2 : 0.01 : 2;
% Cosine
w0 = 3*pi;
x1 = 10*cos(w0*t);
figure;
plot(t, x1);
ylim( [-11 11] );
t = -2 : 0.01 : 2;
% Square Wave
f0 = 3;
v = cos(2*pi*f0*t);
x2 = 0.5*sign(v) + 0.5;
figure;
plot(t, x2);
ylim( [-0.1, 1.1] );
t = -2 : 0.01 : 2;
% Two-Sided Exponential
x3 = 5*exp(-abs(t));
figure;
plot(t, x3);

## Slide 11: One-Sided Infinite-Length Signals
Continuous-Time Signals
t = -2 : 0.01 : 2;
% Cosine
w0 = 3*pi;
x1 = 10*cos(w0*t).*stepfun(t,0);
figure;
plot(t, x1);
ylim( [-11 11] );
t = -2 : 0.01 : 2;
% Two-Sided Exponential
x3 = 5*exp(-t).*stepfun(t,0);
figure;
plot(t, x3);
ylim( [-0.5, 5.5] );
t
t = -2 : 0.01 : 2;
% Unit Step
x1 = stepfun(t, 0);
figure;
plot(t, x1);
ylim( [-0.1 1.1] );
t
t
stepfun(t, 0) can also be implemented as ( t >= 0 )
Pointwise multiplication: vector1 .* vector2

## Slide 12: Finite-Length Signals
Continuous-Time Signals
Rectangular pulse
  Value of p(0)?
  p(0.5)?
  p(1)?
t = -1 : 0.01 : 4;
rp = rectpuls(t-1/2);
plot(t, rp);
ylim( [-0.1 1.1] );
Sinusoidal signal
t = -1 : 0.01 : 4;
rp = rectpuls(t-1/2);
w0 = 3*pi;
x4 = 10*cos(w0*t).*rp;
plot(t, x4);
ylim( [-11 11] );

## Slide 13: Sinc Pulse
Sinc pulse
  In time, infinite overlap with other sinc pulses
Plot of pulse p(t)
Finite-length version
  Truncate sinc pulse by multiplying it by rectangular pulse
  Symmetry about origin?
Ts = 1;
t = -5 : 0.01 : 5;
p = sinc(t/Ts);
plot(t, p)
  Where are the zero crossings?
  Amplitude decrease vs. time?
  Why is sinc(0) = 1?
Continuous-Time Signals

## Slide 14: Chirp Signals
Sinusoid with rising or falling frequency vs. time
  Change in frequency occurs continuously
  Linear sweep over range of frequencies (e.g. audio test signal)
Revisit sinusoidal signal model
  Assumes constant amplitude, frequency and phase over time
  Angle in right term y(t) = 2 p f0 t + f varies linearly with time
  Derivative of y(t) w/r to t is constant frequency 2 p f0 in rad/s
Continuous-Time Signals

## Slide 15: Chirp Signals
Chirp x(t) = A cos(y(t))
  where
Instantaneous freq. (Hz)
  Scaled slope of angle y(t)
  For x(t) over 0 ≤ t ≤ tmax, instantaneous frequency from f0 to f0 + 2 m tmax
Linear frequency sweep
  For 0 ≤ t ≤ tmax, sweep f1 to f2
  f0 = f1 and m = (f2 – f1) / (2 tmax)
x(t)
t
Spectrogram
Linear sweep 261-3951 Hz
Continuous-Time Signals

## Slide 16: Music – Western Scale – Intro
Piano with 88 keys
  Key frequencies increase from left to right (27.5 to 4186 Hz)
  Middle C at 262 Hz (C4) in cyan & A at 440 Hz (A4) in yellow
  Octave has 12 keys and doubles frequencies of previous octave
4
4
♯
B
F
E
D
G
Frequency
Time
Sheet music
Time-Frequency Spectrum – SPFirst Sec. 3-7
https://en.wikipedia.org/wiki/File:Piano_Frequencies.svg
C D E F G A B
Octave
Octave
How fast notes are played depends on time signature and beats per minute (bpm)
Music Note Graphics by Vecteezy
Lyrics
A
B
C
eas - y
as
1
2
3
ah
sim-ple
as

## Slide 17: Music – Western Scale – Intro
C major scale
  Stepped frequencies
  Constant frequency for each note
Ideal Analysis
C4 = 261.626;
D4 = 293.665;
E4 = 329.628;
F4 = 349.228;
G4 = 391.995;
A4 = 440.000;
B4 = 493.883;
C5 = 523.251;
bpm = 60; % 300
beattime = 60/bpm;
fs = 48000;
Ts = 1/fs;
N = beattime/Ts;
t = Ts : Ts : N*Ts;
f = [C4,D4,E4,F4,G4,A4,B4,C5];
vec = zeros(1, length(f)*N);
for i = 1:length(f)
note = cos(2*pi*f(i)*t);
vec((i-1)*N+1 : i*N) = note;
end
sound(vec, fs);
Time-Frequency Spectrum – SPFirst Sec. 3-7
60 bpm
300 bpm
300 bpm

## Slide 18: Music – Western Scale – Intro
Analysis of audio clip for C major scale
N = beattime * fs; % number of samples in one note
spectrogram(vec, N, 100, N, fs, 'yaxis');
ylim( [0 0.7] ); % focus on 0 to 700 Hz
colormap bone % grayscale mapping
Time-Frequency Spectrum – SPFirst Sec. 3-7
Grayscale map
300 bpm
Artifacts at transitions in notes (more on slide 4-9)

## Slide 19: Music – Western Scale – Intro
Analysis of audio clip for C major scale (repeated)
Time-Frequency Spectrum – SPFirst Sec. 3-7
300 bpm
Artifacts at transitions in notes (more on slide 4-9)
N = beattime * fs; % number of samples in one note
spectrogram(vec, N, 100, N, fs, 'yaxis');
ylim( [0 0.7] ); % focus on 0 to 700 Hz
Default map

## Slide 20: Spectrogram: Time-Frequency Plot
Breaks signal x(t) into segments of N samples
Segment 1
Segment 2
Segment 3
FFT Segment 1
FFT Segment 2
FFT Segment 3
Shift start of segment
Shift start of segment
t
f
Spectrogram
t
x(t)
Time-Domain Plot
  MATLAB: spectrogram(x, N, overlap, N, fs, ‘yaxis’)
Time-Frequency Spectrum – SPFirst Sec. 3-7
Computes Fourier series for each segment using FFT
  Fourier series fundamental period T0 = N Ts is time resolution
  N Fourier series frequencies due to sampling
  Fourier series fundamental frequency is frequency resolution

## Slide 21: Discrete-Time Signals & Systems
Discrete-time signals (see slide 2-9)
  Formula: x[n] = cos((p/2) n) useful in analysis
  Samples: xvec = [1 0 -1 0 1 0 -1 0] useful in simulation
  Properties: even symmetric useful in reasoning
  Piecewise: v[n] = rectpuls(n/10)
n = -7 : 7;
v = rectpuls(n/10);
stem(n, v);
T{•}
y[n]
x[n]
Discrete-time systems
  Produce output signal from input signal
  Squaring: y[n] = x2[n]
  Averaging: y[n] = ½ x[n] + ½ x[n-1]
Discrete-Time Signals
Width is 10 samples

## Slide 22: Unit Impulse Response
Discrete-time unit impulse signal d[n]
n
d[n]
1
1
-1
2
3
-2
-3
0
n
d[n-2]
1
1
-1
2
3
-2
-3
0
Expressing finite-length signals using unit impulses
d[n+2]
1
0
2
3
n
1
-1
2
3
-2
-3
x[n]
2 d[n+1]
3 d[n]
2 d[n-1]
d[n-2]
n = -3 : 3;
x = [0 1 2 3 2 1 0];
stem(n, x);
n = -3 : 3;
x = 3*tripuls(n/6);
stem(n, x);
- OR -
No MATLAB function for d[n]
Could use rectpuls(n) but awkward
Discrete-Time Signals

## Slide 23: Periodicity of Discrete-Time Sinusoids
Key idea
  Continuous-time period may not align w/ discrete-time grid
  Example
  f0 = 1200 Hz and fs = 8000 Hz
Three continuous-time periods
Discrete-time period of 20 samples
Discrete-Time Signals

## Slide 24: Periodicity of Discrete-Time Sinusoids
Continuous-time
  Continuous-time period T0 = 1 / f0
Discrete-time cosine
  Sample x(t) at rate fs by substituting t = n Ts :
Discrete-time frequency
  Remove common factors between integers N & L
  cos(2  (N / L) n) has discrete-time period of L samples that contains N continuous-time periods
  See handout on Discrete-Time Periodicity
f0 = 1200;
fs = 8000;
% w0 = 2 pi (3 / 20)
N = 3;
L = 20;
% Time extent
Ts = 1/fs;
nmax = L;
tmax = nmax*Ts;
% x(t) = cos(2 pi f0 t)
fp = fs*24;
Tp = 1 / fp;
t = 0 : Tp : tmax;
xt = cos(2*pi*f0*t);
% x[n] = cos(w0 n)
w0 = 2*pi*N/L;
n = 0 : nmax;
xn = cos(w0*n);
tn = 0 : Ts : tmax;
% Plots
plot(t, xt);
figure; stem(n, xn);
figure; plot(t, xt);
hold; stem(tn, xn);
Discrete-Time Signals