## Slide 1: Introduction & Sinusoids
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2025
Lecture 1 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Instructional Staff
Welcome
Support learning & growth to reach goals
Mr. Dan Jacobellis, Teaching Assistant
  M 2:00-3:30pm and W 3:30-5:00pm, EER 6.882
  Lecture discussions and assignments
  Friday 12-2pm coffee/advising hours EER O’s cafe
  In-class and Canvas announcements
  Immediately after TTH 11:00am-12:30pm lecture
Prof. Evans’ Office hours
  Office hours: TBA

## Slide 3: Destress Course to Improve Learning
  In-lecture assignments to help you on that week’s assignment
  Balanced workload week-to-week (one major deliverable)
  Drop lowest homework and in-lecture assignment to help in balancing course workload with other commitments
  Always know equivalent letter grade: 90+ A, 86.67-89.99 A-, 83.34-86.66 B+, 80.00-83.33 B, 76.67-79.99 B-, etc.
  No relative grading – each student is in their own lane
Review pre-requisite course info first two weeks
Predictable weekly schedule and workload
Feedback on assignments by next class meeting
Access to previous homework & midterm solutions
Welcome

## Slide 4: Getting the Most Out of This Course
Student advice (during Friday coffee/advising hours)
  Remove distractions that prevent you from being efficient in your work and in your play
  Write down questions in a journal when they arise & ask them
  Find mutually beneficial study group of 2-3 persons
Welcome
** D. Brewer-Deluce, "3 ways to study better, according to cognitive research", The Conversation, Aug. 2020
Professor advice
  When choosing courses, check workload ratings (see slide 1-12)
  Attend instructor and TA office hours as you can
  Attend/view lectures: it will save you time & give new insights
  Start assignments when assigned and make progress each day: having more calendar time will allow you to learn info better **

## Slide 5: Prof. Evans’ Research Projects
DSP Digital Signal Processor FPGA Field Programmable Gate Array
Course Overview
System | Contribution | SW release | Prototype | Funding
Cellular (LTE) | full duplex commun. | Matlab |  | 6G@UT
 | satellite commun. | Python |  | AT&T Labs
 | reconfigurable surface | Matlab+Py |  | Tektronix
Smart grid commun. | interference reduction real-time testbeds | Matlab | Freescale & TI modems | IBM, NXP, TI
Wi-Fi | interference reduction | Matlab | NI FPGA | Intel, NI
Underwater | large receive array | Matlab | Lake testbed | ARL:UT
Camera | image acquisition | Matlab | DSP/C | Intel,Ricoh
 | video acquisition | Matlab | Android | TI
Display | image halftoning | Matlab | C | HP, Xerox
 | video halftoning | Matlab | C | Qualcomm
Design tools | distributed computing | Linux/C++ | Navy sonar | Navy, NI
33 PhD, 13 MS and 215 BS alumni

## Slide 6: Linear Systems & Signals
Audio mixing board
IP camera
Wi-Fi access point
Signal
  Carries information
  Patterns of variations in physical quantity
Course Overview – SPFirst Ch. 1 Intro
Signal processing signalprocessingsociety.org
  Generation, transformation and extraction of information
  Algorithms with associated architectures and implementations
  Applications related to processing information
System
  Manipulates, changes, records or transmits signals
  Converts a signal into another

## Slide 7: IEEE Signal Processing Society Videos
Course Overview

## Slide 8: Course Overview
Objectives
  Understand mathematical descriptions of signal processing algorithms
  Express those algorithms as software implementations in MATLAB
Course Overview
James McClellan (Georgia Tech)
Ronald Schafer (Georgia Tech)
Mark Yoder (Rose-Hulman Inst. of Tech.)
dspfirst.gatech.edu
x(t) = cos(2 p (440 Hz) t)
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
t = 0 : Ts : 4/f0;
x = cos(2*pi*f0*t); plot(t, x);
Your objectives?
Required textbook

## Slide 9: Grading
Calculation of numeric grades
  17% midterm #1 exam
  17% midterm #2 exam
  26% final exam
  20% homework (drop lowest grade of 9)
  10% tune-up Tuesdays (drop lowest grade of 9)
  10% mini-projects
Cutoffs 90.00 A 86.67 A- 83.34 B+ 80.00 B 76.67 B- 73.34 C+ 70.00 C etc.
Course Overview
Midterm and final exams (in person)
  Based on in-lecture discussions and assignments
  Open books, notes & computer (but no networking or AI tools)
  Dozens of old exams on course site (most with solutions)
  Dates are October 2, November 13, and December 12

## Slide 10: Grading
By Beth Hayden
from www.studentum.no
Homework (drop lowest of 9)
  Model signals/systems using mathematics
  Translate mathematics into Matlab simulations
  Submit your own independent solutions
  Submitted on Fridays by 11:59pm on Canvas
Course Overview
Two mini-projects
  Deeper dive into material from Signal Processing First online
Tune-up Tuesdays (drop lowest of 7)
  Hands-on work in lecture, submitted by 6pm
  Related to that week’s homework assignment
  Keeping up-to-date reduces Thursday night panic

## Slide 11: Pre-requisite for 15 ECE Courses
Energy Systems and Renewable Energy
ECE 341 Electric Drives and Motors
ECE 362R Renewable Energy
Computer Architecture & Embedded Systems
ECE 445L Embedded Systems Design Lab ECE 445S Real-Time Dig. Sig. Proc. Lab
Data Science & Machine Learning
Communications, Networks, Signal Processing, Systems
ECE 445S Real-Time Dig. Sig. Proc. Lab ECE 351M Digital Signal Processing ECE 360K Digital Communications
ECE 460J Data Science Laboratory
ECE 461P Data Science Principles
ECE 361E Machine Learning / Data
Analytics / Edge AI
ECE 362K Intro to Automatic Control
ECE 371R Digital Image Processing ECE 471C Wireless Communications Lab
ECE 372N Telecommunication Networks
ECE 379K Computer Vision
ECE 313 Linear Systems and Signals at The University of Texas at Austin
Clouds represent ECE specializations (tech cores/components)
Courses in blue fulfill a requirement for one or more technical cores/components

## Slide 12: Course Workloads
Undergrad ECE courses with highest workload ratings?
4.70 460N Computer Arch F21
4.47 445L Emb Sys Des Lab Sp22
4.13 445L Emb Sys Des Lab F21
4.05 461S Operating Systems F21
3.88 460N Computer Arch Sp22
3.88 461S Operating Systems Sp22
3.80 325 Electromagnetic Eng. Sp22
3.78 422C SW Des & Impl II ** F21
3.77 460R Intro to VLSI Design F21
** Averaged across all sections that semester. **
Workload rating
(1-5 with 5 highest)
Course Overview

## Slide 13: Signals As Functions
Function of independent variable
  High temperature vs. day
  Audio signal vs. time
Mathematical Representations of Signals – SPFirst Sec. 1-1
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
t = 0 : Ts : 4/f0;
x = cos(2*pi*f0*t); plot(t, x);
Continuous-time signals
  x(t) where t can take any real value
  x(t) may be 0 for range of values of t
Discrete-time signals
  x[n] where n  {...-3,-2,-1,0,1,2,3...}
  Unitless sample index n (e.g. day)
Amplitude value may be real or complex
sep2016hightemp = [ 96, 92, 92, 93, 94, 95, 96, 95, 95, 93, 93, 93, 94, 92, 94, 95, 96, 98, 99, 99, 96, 94, 93, 97, 88, 73, 80, 89, 86, 83 ];
stem(sep2016hightemp);
title('High Temp. in Austin, TX, Sept. 2016');
xlabel('Day');
ylabel('Degrees F');
ylim( [70 100] );

## Slide 14: Signals As Functions
Mathematical Representations of Signals – SPFirst Sec. 1-1
Analog amplitude
1
-1
flipnumber = 1:10;
y = sign(randn(10,1));
stem(flipnumber, y);
Digital amplitude
  From a discrete set of values
Random amplitudes
  Cannot be predicted exactly or described by a formula
  Distribution of amplitude values can be defined
  Example: Flipping coin 10x
flip
-1
1
Trial #1
flip
-1
1
Trial #2
Deterministic amplitudes
  Mathematically described, e.g. x(t) = cos(2 p f0 t)

## Slide 15: Sinusoidal Signal
Mathematical form: A cos(w0 t + f)
  A is amplitude/magnitude
  w0 is frequency in rad/s where w0 = 2 p f0 and f0 is in cycles/s or Hz
  f is phase shift in radians
Sinusoids – SPFirst Ch. 2 Intro & Sec. 2-3
f0 = 440;
fs = 8000;
Ts = 1/fs;
t = 0 : Ts : 3;
x = cos(2*pi*f0*t);
sound(x, fs);
Play As Audio
Smallest period: T = 1 / f0
  Signal x(t) has period T if x(t+T) = x(t) for all t
  Using property cos(x + 2p) = cos(x),
    cos(2p f0 (t + T)) = cos(2p f0 t + 2p f0 T) = cos(2p f0 t)
    when 2p f0 T = 2p or when f0 T = 1 or when T = 1 / f0
  When f0 = 440 Hz, T = 2.27 ms

## Slide 16: Tuning Fork Example A-440 Hz
©2003-2016, JH McClellan & RW Schafer
Sinusoids – SPFirst Sec 2-1
Estimate Period
Middle plot below gives T ≈ 8.15ms – 5.85ms = 2.3ms
Bottom plot below gives
T ≈ (2 + 2/7) ms = 2.28ms
Estimate Frequency
f0 = 1 / T = 1 / (2.3ms) = 435 Hz
f0 = 1 / T = 1 / (2.28ms) = 438 Hz

## Slide 17: MATLAB Interlude
Matrix Laboratory (MATLAB)
  Released in 1984 to universities
  First toolboxes in control systems and signal processing (1987)
  Semicolon prevents printing result
Scalar variables
Generating vectors
  start : inc : end generate values from start to end at increments of inc
  1 : 0.5 : 3 gives vector [1.0 1.5 2.0 2.5 3.0]
Plot vector x vs. vector t
% Scalar variables
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
% Generate four periods % of time samples
t = 0 : Ts : 4/f0;
% Apply cosine to every
% element of 2 pi f0 t
x = cos(2*pi*f0*t);
plot(t, x);
Sinusoids – SPFirst Sec. 2-4

## Slide 18: MATLAB Interlude
Plot individual samples as stems
Sound playback on platform
  Supports specific sampling rates, such as
  8000 Hz for speech and audio
    44100 Hz for CD audio
Playing sound in MATLAB
  sound(vector, rate) will play values of vector at sampling rate and clip values lying outside [-1, 1]
  soundsc(vector, rate) will scale values of vector to be in range [-1, 1] and play scaled values at sampling rate
Sinusoids – SPFirst Sec. 2-4
stem(x);
f0 = 440;
fs = 8000; % rate
Ts = 1/fs;
t = 0 : Ts : 3; % 3 sec
x = cos(2*pi*f0*t);
sound(x, fs);

## Slide 19: Systems
Systems operate on signals to produce new signals or new signal representations
Continuous-time system examples
  y(t) = ½ x(t) + ½ x(t-1)
  y(t) = x2(t)
Discrete-time system examples
  y[n] = ½ x[n] + ½ x[n-1]
  y[n] = x2[n]
T{•}
y(t)
x(t)
T{•}
y[n]
x[n]
Audio, image and communication applications for squaring block
Average of current input and delayed input is a simple filter
Mathematical Representations of Systems – SPFirst Sec. 1-2 & 1-3

## Slide 20: Squaring Block
Applications
  AM radio receiver
  Displayed pixels on screen undergo ()2.2 nonlinearity
  Increase musical note by one octave on Western scale
Input ‘A’ note at 440 Hz
  x(t) = cos(2 p 440 t)
  y(t) = cos2(2 p 440 t) = ½ (1 + cos(2 (2 p 440 t)) ) = ½ + ½ cos(2 p 880 t)
(•)2
y(t)
x(t)
f0 = 440;
fs = 8000;
Ts = 1/fs;
tmax = 3;
t = 0 : Ts : tmax;
x = cos(2*pi*f0*t);
sound(x, fs);
pause(tmax+1);
y = x .^ 2;
sound(y, fs);
Play As Audio
What frequency does a constant value have?
What frequency does the second term have?
Uses trig identity cos2(q) = ½ + ½ cos(2q)
Mathematical Representations of Systems – SPFirst Sec. 1-2, 1-3 & 2-2

## Slide 21: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
1-21