## Slide 1: Periodic Signals
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2025
Lecture 2 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Periodic Signals
A signal has period T if x(t + T) = x(t) for all t
  Also periodic with periods 2T, 3T, etc., and –T, –2T, etc.
  Smallest positive period is called the fundamental period
Signal cos(2 p f0 t + f) has period T0 = 1 / f0
  Using cosine property cos(x + 2p) = cos(x),
    cos(2p f0 (t + T0) + f) = cos(2p f0 t + 2p f0 T0 + f) = cos(2p f0 t + f)
    when 2p f0 T0 = 2p or when f0 T0 = 1 or when T0 = 1 / f0
Periodic Signals – SPFirst Sec. 2-3.1
f0 = 100 Hz
0
5
ms
10
15
20
-5
-10
0
5
ms
10
15
20
-5
-10
0
5
ms
10
15
20
-5
-10
f0 = 200 Hz
f0 = 0 Hz
5 cos(2p f0 t)

## Slide 3: Time Shift
Unit area rectangular pulse
  Symmetric about origin
  Matlab command rectpuls(t)
Periodic Signals – SPFirst Sec. 2-3.2
0
1
1/2
-1/2
t
rect(t)
1
-1
3/2
0
1
1/2
-1/2
t
rect(t-1)
1
-1
3/2
Ts = 1/100;
t = -1.5 : Ts : 2.5;
x = rectpuls(t-1);
plot(t, x);
ylim( [-0.5 1.5] );
Shift to the right
0
1
1/2
-1/2
t
rect(t+1/2)
1
-1
3/2
Shift to the left

## Slide 4: Phase Shift
For sinusoidal signals, time shift causes phase shift
  x0(t) = A cos(2 p f0 t)
  x0(t - t1) = A cos(2 p f0 (t – t1)) = A cos(2 p f0 t – 2 p f0 t1)
  Time shift of t1 causes phase shift of f = –2 p f0 t1
Initial interpretation of this phase shift
  Positive time shift causes negative phase shift
  Negative time shift causes positive phase shift
Phase shift: ambiguity of multiples of 2p
  Due to cosine property cos(x + 2p) = cos(x)
  Each multiple of 2p corresponds to picking different peak
Periodic Signals – SPFirst Sec. 2-3.2
= cos(2p 440 t)
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
t = 0 : Ts : 4/f0;
x = cos(2*pi*f0*t); plot(t, x);
cos(2p 440 t + 2p)

## Slide 5: Sampling
Many signals originate as continuous-time signals, e.g. voice or conventional music
Sample continuous-time signal at equally-spaced points in time to obtain discrete-time signal
  y[n] = y(n Ts)
  n  {…, -2, -1, 0, 1, 2,…}
  Ts is sampling period
Sinusoidal signal
n
1
2
4
5
6
7
3
y(t)
Ts
Sampling Sinusoids – SPFirst Sec. 2-4

## Slide 6: Plotting Signals
Sample signals before plotting them in Matlab
  x(t) = 20 cos(2p 40 t – 0.4p)
  Uniformly sample at points in continuous time t = n Ts :
  x(nTs) = 20 cos(80p nTs – 0.4p)
How small does Ts have to be to produce an accurate plot?
Sampling Sinusoids – SPFirst Sec. 2-4
Ts = 0.0050s fs = 200Hz = 5f0
5 samples/cycle
Ts = 0.0025s
fs = 400Hz = 10f0
10 samples/cycle
Ts = 0.0001s
fs = 10kHz = 250f0 250 samples/cycle
f0 = 40; Ts = 0.0001;
t = -0.03 : Ts : 0.045;
x = 20*cos(2*pi*f0*t - 0.4*pi);
figure; plot(t, x);
hold; stem(t, x);

## Slide 7: Exponential Signals
Real-valued exponential signals
  Amplitude values are always non-negative
  Might decay or not as t goes to infinity
Complex Exponentials– SPFirst Sec. 2-5
t = -1 : 0.01 : 1;
e1 = exp(t);
plot(t, e1)
et
t
t = -1 : 0.01 : 1;
e2 = exp(-t);
plot(t, e2)
e-t
t

## Slide 8: Exponential Signals
Complex numbers
  Cartesian form x + j y for real x and y
  Polar form r e jq = r cos(q) + j r sin(q)
  Polar-to-Cartesian: x = r cos(q) and y = r sin(q)
  Cartesian-to-Polar: and
Complex Exponentials– SPFirst Sec. 2-5.1
x
y
q
r
SPFirst Fig. 2.4
t
Complex sinusoid: Euler’s formula
Complex sinusoidal signal
t = 0 : 1/100 : 1;
plot(t, cos(2*pi*t));
hold;
plot(t, sin(2*pi*t));
“inverse” Euler formula

## Slide 9: Many Faces of Signals
Function, e.g. cos(t) in continuous time or cos(p n) in discrete time, useful in analysis
Complex Exponentials– SPFirst Sec. 2-8
0
1
1/2
-1/2
t
rect(t)
Above mathematical models can be used to approximate measured/observed signals
0
1
1/2
-1/2
t
Sequence of numbers, e.g. {1,2,3,2,1} or a sampled triangle function, useful in simulation
Set of properties, e.g. even symmetric, useful in reasoning about behavior
A piecewise representation, e.g. rect(t) below, useful in analysis

## Slide 10: Spectrum Representation
Sinusoidal waveforms
Spectrum Representation – SPFirst Ch. 3 Intro
A0 |  |  | 
A1 |  | A2 | 
f1 | 440 Hz | f2 | 880 Hz
f1 |  | f2 | 
Example (slide 1-16)
  y(t) = x2(t) = cos2(2 p 440 t) = ½ (1 + cos(2 (2 p 440 t)) ) = ½ + ½ cos(2 p 880 t)
Spectrum is collection of amplitude, phase and frequency info to express more complicated signals
  where A0 is real-valued and

## Slide 11: Two-Sided Spectrum
Expanding cosine terms with inverse Euler formula
Spectrum Representation – SPFirst Sec. 3-1
Two-sided spectrum
  2N+1 frequencies and 2N+1 complex amplitudes
  { (0, X0), (f1, ½ X1), (-f1, ½ X1*), …, (fk, ½ Xk), (-fk, ½ Xk*), … }
  Frequency-domain representation of signal x(t)
  where

## Slide 12: Two-Sided Spectrum Example
x(t) = 10 + 14 cos(200p t – p/3) + 8 cos(500p t + p/2)
Spectrum Representation – SPFirst Sec. 3-1
0
100
250
–100
–250
f (in Hz)
Complex amplitude
Spectral line
©2003-2016, JH McClellan & RW Schafer
t
Two periods of x(t)
Spectrum plot
  Constant term has zero frequency: 10 e j 0 t = 10
  Expanding cosine terms using (inverse) Euler formula

## Slide 13: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
2-13