## Slide 1: Time-Frequency Spectrum
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 4 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Waveform Synthesis
Time-Frequency Spectrum – SPFirst Sec. 3-7
Synthesize many kinds of waveforms using
  Constant, cosine and general periodic signals when fk = k f0
  Non-periodic signals, e.g.
©2003-2016, JH McClellan & RW Schafer

## Slide 3: Waveform Synthesis
Figure 3-10: Sum of three cosine waves of harmonic frequencies. Fundamental frequency of xh(t) is 10 Hz.
Figure 3-11: Sum of three cosine waves with nonharmonic frequencies, x2(t). No exact repetition appears in this signal.
©2003-2016, JH McClellan & RW Schafer
We’ve been assuming spectrum (set of amplitudes, frequencies, and phases) does not change with time
Time-Frequency Spectrum – SPFirst Sec. 3-7

## Slide 4: Music – Western Scale – Intro
Piano with 88 keys
  Key frequencies increase from left to right (27.5 to 4186 Hz)
  Middle C at 262 Hz (C4) in cyan & A at 440 Hz (A4) in yellow
  Octave has 12 keys and doubles frequencies of previous octave
4
4
♯
B
F
E
D
G
Frequency
Time
Sheet music
Time-Frequency Spectrum – SPFirst Sec. 3-7
https://en.wikipedia.org/wiki/File:Piano_Frequencies.svg
C D E F G A B
Octave
Octave
How fast notes are played depends on time signature and beats per minute (bpm)
Music Note Graphics by Vecteezy
Lyrics
A
B
C
eas - y
as
1
2
3
ah
sim-ple
as

## Slide 5: Music – Western Scale – Intro
C major scale
  Stepped frequencies
  Constant frequency for each note
Ideal Analysis
C4 = 261.626;
D4 = 293.665;
E4 = 329.628;
F4 = 349.228;
G4 = 391.995;
A4 = 440.000;
B4 = 493.883;
C5 = 523.251;
bpm = 60; % 300
beattime = 60/bpm;
fs = 8000;
Ts = 1/fs;
N = beattime/Ts;
t = Ts : Ts : N*Ts;
f = [C4,D4,E4,F4,G4,A4,B4,C5];
vec = zeros(1, length(f)*N);
for i = 1:length(f)
note = cos(2*pi*f(i)*t);
vec((i-1)*N+1 : i*N) = note;
end
sound(vec, fs);
Time-Frequency Spectrum – SPFirst Sec. 3-7
60 bpm
300 bpm
300 bpm

## Slide 6: Music – Western Scale – Intro
Analysis of audio clip for C major scale
N = beattime * fs; % number of samples in one note
spectrogram(vec, N, 100, N, fs, 'yaxis');
ylim( [0 0.7] ); % focus on 0 to 700 Hz
colormap bone % grayscale mapping
Time-Frequency Spectrum – SPFirst Sec. 3-7
Grayscale map
300 bpm
Artifacts at transitions in notes (more on slide 4-9)

## Slide 7: Music – Western Scale – Intro
Analysis of audio clip for C major scale (repeated)
Time-Frequency Spectrum – SPFirst Sec. 3-7
300 bpm
Artifacts at transitions in notes (more on slide 4-9)
N = beattime * fs; % number of samples in one note
spectrogram(vec, N, 100, N, fs, 'yaxis');
ylim( [0 0.7] ); % focus on 0 to 700 Hz
Default map

## Slide 8: Spectrogram: Time-Frequency Plot
Breaks signal x(t) into segments of N samples
Segment 1
Segment 2
Segment 3
FFT Segment 1
FFT Segment 2
FFT Segment 3
Shift start of segment
Shift start of segment
t
f
Spectrogram
t
x(t)
Time-Domain Plot
  MATLAB: spectrogram(x, N, overlap, N, fs, ‘yaxis’)
Time-Frequency Spectrum – SPFirst Sec. 3-7
Computes Fourier series for each segment using FFT
  Fourier series fundamental period T0 = N Ts is time resolution
  N Fourier series frequencies due to sampling
  Fourier series fundamental frequency is frequency resolution

## Slide 9: Spectrogram
50% overlap between adjacent segments common
Consider “edge” effects in analyzing short sinusoid
SECTION
LOCATIONS
MIDDLE of SECTION
is REFERENCE TIME
©2003-2016, JH McClellan & RW Schafer
Time-Frequency Spectrum – SPFirst Sec. 3-7
SPFirst adds plotspec (above) and spectgr functions

## Slide 10: Chirp Signals
Sinusoid with rising or falling frequency vs. time
  Change in frequency occurs continuously
  Linear sweep over range of frequencies (e.g. audio test signal)
Revisit sinusoidal signal model
  Assumes constant amplitude, frequency and phase over time
  Angle in right term y(t) = 2 p f0 t + f varies linearly with time
  Derivative of y(t) w/r to t is constant frequency 2 p f0 in rad/s
Time-Frequency Spectrum – SPFirst Sec. 3-8

## Slide 11: Chirp Signals
Chirp x(t) = A cos(y(t))
  where
Time-Frequency Spectrum – SPFirst Sec. 3-8
x(t)
t
Spectrogram
Linear sweep 261-3951 Hz
Instantaneous freq. (Hz)
  Scaled slope of angle y(t)
  For x(t) over 0 ≤ t ≤ tmax, instantaneous frequency from f0 to f0 + 2 m tmax
Linear frequency sweep
  For 0 ≤ t ≤ tmax, sweep f1 to f2
  f0 = f1 and m = (f2 – f1) / (2 tmax)

## Slide 12: Chirp Signals
MATLAB code for previous slide
fs = 8000;
Ts = 1 / fs;
tmax = 5;
t = 0 : Ts : tmax;
f1 = 261; % note C4
f2 = 3951; % note B7
f0 = f1;
mu = (f2 - f1) / (2*tmax);
phi = 0;
angle = 2*pi*mu*t.^2 + 2*pi*f0*t + phi;
x = cos(angle);
sound(x, fs);
figure;
plot(t(1:800), x(1:800));
figure;
spectrogram(x, 1024, 512, 1024, fs, 'yaxis');

## Slide 13: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
4-13