## Slide 1: Sampling and Aliasing
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 5 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Introduction
Conversion of signals
  Sampling: Continuous-Time to Discrete-Time
  Reconstruction: Discrete-Time to Continuous-Time
Sampling and Reconstruction– SPFirst Ch. 4 Intro
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
tmax = 1/f0;
t = 0 : Ts : tmax;
x = cos(2*pi*f0*t);
plot(t, x);
figure;
stem(t, x);
cosine at 440 Hz
t
sampling rate: 10560 Hz sampling period: 94.7 ms
sampling
reconstruction

## Slide 3: Sampling and Reconstruction
Sampling Theorem
  Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed exactly from its samples x(n Ts) if samples taken at sampling rate of fs > 2 fmax
Sampling audio CD signals
  Normal human hearing is from about 20 Hz to 20 kHz
  Filter analog continuous-time signal to pass frequencies up to 20 kHz and reject frequencies above 22 kHz
  Sample filtered signal at sampling rate of 44100 Hz
Reconstruction fills in missing values between sampling times (e.g. interpolation)
Sampling and Reconstruction– SPFirst Ch. 4 Intro and Sec. 4-1.4

## Slide 4: Discrete-Time Signals
Many signals originate in continuous time
  Example: Talking on smart phone or playing live music
Sample continuous-time signal at equally-spaced points in time to obtain a sequence of numbers
  s[n] = s(n Ts) for n  {…, -1, 0, 1, …}
  How to choose sampling period Ts ?
Sampled analog waveform
s(t)
t
Ts
Ts
Sampling– SPFirst Sec. 4-1
n = 0 : 7;
x = n.^2 - 5*n + 3;
stem(n, x);
x[n]
n
Using a formula
  x[n] = n2 – 5n + 3
  How does it look in continuous time?
See also SPFirst Fig. 4-2

## Slide 5: Sampling Sinusoidal Signals
Analog continuous-time signals
  Sinusoids model physical quantities such as musical tones
  Sums of sinusoids can represent general continuous-time signals
Sampling– SPFirst Sec. 4-1.1
Sampling sinusoidal signal x(t) = A cos(w t + f)
  where the normalized radian frequency is
  Discrete time n abstracts away continuous time information
  Discrete-time frequency abstracts away continuous-time frequency information

## Slide 6: Discrete-Time Frequency
Examples
Sampling– SPFirst Sec. 4-1.1
Application | Sampling Rate | Continuous-Time Frequency | Discrete-Time Frequency
Speech | 8000 Hz | 220 Hz | 2 p 11/400 = 0.1728
Audio | 44100 Hz | 441 Hz | 2 p 1/100 = 0.0628
Audio | 48000 Hz | 1320 Hz | 2 p 11/400 = 0.1728
n = 1 : 48000;
wHat = 0.1728;
x = cos(wHat*n);
sound(x, 8000);
pause(3);
sound(x, 48000);
Comparing first and third rows
  Same gives same discrete-time signal x[n]
  Different tone when x[n] is played at sampling rate 8000 Hz vs. 48000 Hz

## Slide 7: How to Pick a Sampling Rate?
  Sampling theorem
    Sampling rate fs > 2 fmax
  Larger fs tracks waveform shape better in time
  fs = 5 fmax = 2.5 (2 fmax) is 2.5 times oversampling
Sampling– SPFirst Sec. 4-1.1
Used 10x oversampling to generate continuous-time plot
fs =500 Hz
fs =2000 Hz
Cosine at f0 =100 Hz
2.5x oversampling
10x oversampling
See also SPFirst Fig. 4-3

## Slide 8: How to Pick a Sampling Rate?
  MATLAB code
    For previous slide
Sampling– SPFirst Sec. 4-1.1
f0 = 100;
tmin = -0.01; tmax = 0.02;
fs = 5*f0; Ts = 1/fs;
wHat = 2*pi*f0/fs;
nmin = round(tmin / Ts);
nmax = round(tmax / Ts);
n = nmin : nmax;
x2 = cos(wHat*n);
figure; stem(n, x2);
xlabel('Sample Index n');
title('100-Hz Sinusoid Sampled at 500 Hz');
f0 = 100;
tmin = -0.01; tmax = 0.02;
fs = 20*f0; Ts = 1/fs;
wHat = 2*pi*f0/fs;
nmin = round(tmin / Ts);
nmax = round(tmax / Ts);
n = nmin : nmax;
x1 = cos(wHat*n);
figure; stem(n, x1);
xlabel('Sample Index n');
title('100-Hz Sinusoid Sampled at 2000 Hz');
f0 = 100;
tmin = -0.01; tmax = 0.02;
fs = 20*f0; Ts = 1/fs;
t = tmin : Ts : tmax;
x = cos(2*pi*f0*t);
figure;
plot(t, x);
xlabel('Time (s)');
title('Continuous-Time Sinusoid at 100 Hz');
Used 10x oversampling to generate continuous-time plot
Cosine at f0 =100 Hz
fs =500 Hz
2.5x oversampling
fs =2000 Hz
10x oversampling

## Slide 9: Aliasing
f2 = 1.2 Hz
Definition for “alias” [dictionary.com]
  “a false name used to conceal one's identity; an assumed name”
Is x2[n]=cos(2.4pn) an alias for x1[n]=cos(0.4pn)?
  x2[n] = cos(2.4pn) = cos(0.4pn + 2pn) = cos(0.4pn) = x1[n]
Sampling– SPFirst Sec. 4-1.2
Sample at fs = 1 Hz
f1 = 0.2 Hz
See also SPFirst Fig. 4-4

## Slide 10: Aliasing
MATLAB code from previous slide
Sampling– SPFirst Sec. 4-1.2
%% Part 1: Define Signals
wHat = 0.4*pi;
nmax = 12;
n = 0:nmax;
x1 = cos(wHat*n);
x2 = cos(2.4*pi*n);
fs = 1;
f1 = 0.2;
w1Hat = 2*pi*f1/fs;
period = round(fs/f1);
f2 = 1.2;
w2Hat = 2*pi*f2/fs;
Ts = 1/fs;
tmax = (nmax/period)*(1/f1);
t = 0 : (Ts/100) : tmax;
x1cont = cos(2*pi*f1*t);
x2cont = cos(2*pi*f2*t);
%% Part 2: Generate Plots
figure;
plot(t, x2cont, 'm-', 'LineWidth', 1);
figure;
plot(t, x2cont, 'm-', 'LineWidth', 1);
hold;
stem(n, x1, 'Linewidth', 2, 'MarkerEdgeColor', 'black');
stem(n, x2, 'Linewidth', 2, 'MarkerEdgeColor', 'black');
figure;
plot(t, x2cont, 'm-', 'LineWidth', 1);
hold;
stem(n, x1, 'Linewidth', 2, 'MarkerEdgeColor', 'black');
stem(n, x2, 'Linewidth', 2, 'MarkerEdgeColor', 'black');
plot(t, x1cont, 'b-', 'LineWidth', 2);

## Slide 11: Aliasing
Continuous-time sinusoid
  x(t) = A cos(2p f0 t + f)
Sample at Ts = 1/fs
  x[n] = x(Tsn) = A cos(2p f0 Ts n + f)
Keeping the sampling period same, sample
  y(t) = A cos(2p (f0 + l fs) t + f)
where l is an integer
  y[n] = y(Tsn) = A cos(2p(f0 + lfs)Tsn + f) = A cos(2pf0Tsn + 2plfsTsn + f) = A cos(2pf0Tsn + 2pln + f) = A cos(2pf0Tsn + f) = x[n]
  Here, fsTs = 1
  Since l is an integer, cos(x + 2 p l) = cos(x)
y[n] indistinguishable from x[n]
Sampling– SPFirst Sec. 4-1.2

## Slide 12: Another Kind of Aliasing (Folding)
Continuous-time sinusoid
  x(t) = A cos(-2p f0 t + f)
Sample at Ts = 1/fs
  x[n] = x(Tsn) = A cos(-2p f0 Ts n + f)
Keeping the sampling period same, sample
  y(t) = A cos(2p (-f0 + l fs) t + f)
where l is an integer
  y[n] = y(Tsn) = A cos(2p(-f0 + lfs)Tsn + f) = A cos(-2pf0Tsn + 2plfsTsn + f) = A cos(-2pf0Tsn + 2pln + f) = A cos(-2pf0Tsn + f) = x[n]
  Here, fsTs = 1
  Since l is an integer, cos(x + 2 p l) = cos(x)
y[n] indistinguishable from x[n]
Sampling– SPFirst Sec. 4-1.2

## Slide 13: Spectrum of a Discrete-Time Signal
Spectrum of a sinusoidal signal
Sampling– SPFirst Sec. 4-1.3
½
0.4p
-0.4p
1.6p
2.4p
-1.6p
-2.4p
Example: Two of the aliases for x1[n] = cos(0.4pn)
  x2[n] = cos(2.4pn) = cos(0.4pn + 2pn) = cos(0.4pn) = x1[n]
  x3[n] = cos(-1.6pn) = cos(0.4pn − 2pn) = cos(0.4pn) = x1[n]
  Only need to add principal frequency components for synthesis
Principal Components
Aliases
Aliases
½
  Frequency components at and

## Slide 14: Ideal Reconstruction
Sampling theorem
  Possible to reconstruct continuous-time signal from samples
  Does not say how to do it
Sampling– SPFirst Sec. 4-1.5
Practical?
Reconstruction: Ideal case
  Need a formula for signal of one or more sinusoids
  Consider y[n] = A cos(2 p f0 n Ts + f) where fs > 2 f0
Reconstruction: Practical case
  Interpolation fills in values between samples
  There are other approaches to “undo” sampling process

## Slide 15: Discrete-to-Continuous Conversion
Input: sequence of samples y[n]
Output: continuous-time signal y(t) via interpolation (“connecting the dots”)
Example: Cosine of frequency f0
  From sampling theorem, fs > 2 f0 or f0 < ½ fs
Sampling– SPFirst Sec. 4-1.5
%% y[n] is sinusoid w/
%% period of 8 samples
f0 = 0.125;
fs = 1;
wHat = 2*pi*f0/fs;
n = 0 : 8;
yofn = cos(wHat*n);
fs = 20*f0;
Ts = 1/fs;
t = 0 : Ts : (1/f0);
yoft = cos(2*pi*f0*t);
figure;
stem(n, yofn);
figure;
stem(n, yofn);
hold
plot(t, yoft);

## Slide 16: Interpolation From Tables
Using mathematical tables to estimate a function value
x | f(x)
0 | 0.0
1 | 1.0
2 | 4.0
3 | 9.0
Estimate f(1.5) from table
  Zero-order hold: take value to be f(1) to make f(1.5) = 1.0 (“stairsteps”) No multiplications or additions
  Linear interpolation: average values of nearest two neighbors: f(1.5) = 2.5 2 multiplications and 3 additions per value
  Curve fitting: fit four points to cubic polynomial: f(1.5) = x2 = 2.25 43 multiplications to find polynomial coefficients + 1 multiplication per value
x
f(x)
Sampling– SPFirst Sec. 4-1.5
Notes: xmin = 0;
xmax = 3;
xoffset = 0.1;
yoffset = 0.3;
%%% Samples
xsamples = xmin : xmax;
ysamples = xsamples .^ 2;
figure;
hold on;
stem(xsamples, ysamples, 'LineWidth', 2);
xlim( [xmin-xoffset xmax+xoffset] );
ymax = max(ysamples);
ylim( [-yoffset ymax+yoffset] );
pause;
%%% Interpolation
N = 1000;
xstep = 1/N;
x = [ xmin : xstep : xmax ];
yzoh = floor(x) .^ 2;
plot(x, yzoh, 'LineWidth', 2);
pause;
y1 = x;
y2 = 3*x - 2;
y3 = 5*x - 6;
ylinear = [ y1(1:N) y2(N+1:2*N) y3(2*N+1:3*N+1) ];
plot(x, ylinear, 'LineWidth', 2);
pause;
yspline = x .^ 2;
plot(x, yspline, 'LineWidth', 2);
hold off;

## Slide 17: Curve Fitting
Interpolate over 1 < x < 2 using cubic polynomial
  f(x) = a0 + a1 x + a2 x2 + a3 x3
  f(0) = 0 = a0
  f(1) = 1 = a0 + a1 + a2 + a3
  f(2) = 4 = a0 + 2 a1 + 4 a2 + 8 a3
  f(3) = 9 = a0 + 3 a1 + 9 a2 + 27 a3
A
Matlab code to solve for
  A = [ 1 0 0 0; 1 1 1 1; 1 2 4 8; 1 3 9 27 ]; b = [ 0; 1; 4; 9 ]; a = A \ b;
a2 = 1 and a0 = a1 = a3 = 0 to give f(x) = x2
(2/3)n3 operations to solve system of n equations
Sampling– SPFirst Sec. 4-1.5

## Slide 18: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
5-18