## Slide 1: Sampling Theorem
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 6 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
Sampling Theorem – SPFirst Ch. 4
✔
✔
✔
✔

## Slide 3: Sampling Theorem
Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed from its samples x(n Ts) if samples taken at rate fs > 2 fmax
  Nyquist rate = 2 fmax
  Nyquist frequency = fs / 2
What happens if fs = 2 fmax?
Sampling Theorem – SPFirst Sec.4-1.4 and 4.2 Intro
link
SPFirst sampling and interpolation demo
  Distance between two zero crossings: one half period
  How to compute sinusoidal frequency from zero crossings?
  Is frequency content of sinusoid preserved after sampling?
  What is the quality of sampled vs. original signal in time domain as sampling rate increases above Nyquist rate?

## Slide 4: Spectrum of Discrete-Time Signal
Sampling a sinusoidal signal x(t) = A cos(w0 t + f)
  Frequency of discrete-time signal is
Spectrum Due to Sampling – SPFirst Sec.4-1.5 and 4-2.1
Including aliased frequencies
  Has two spectral lines at
  Also contains all aliases due to periodicity of exp(j q):

## Slide 5: Case #1: Oversampling
Sampling rate fs > 2 fmax to avoid aliasing & folding
Example: f0 = 100 Hz and fs = 1000 Hz
Oversampling – SPFirst Sec. 4-2.2
where
1.8p
–1.8p
0.2p
–0.2p
See also SPFirst Fig. 4-8
©2003-2016, JH McClellan & RW Schafer

## Slide 6: Case #2: Aliasing by Undersampling
Sampling rate fs ≤ 2 fmax
Example: f0 = 100 Hz and fs = 80 Hz
Aliasing – SPFirst Sec. 4-2.3
where
–0.5p
–1.5p
0.5p
1.5p
2.5p
–2.5p
See also SPFirst Fig. 4-9
©2003-2016, JH McClellan & RW Schafer

## Slide 7: Case #3: Folding by Undersampling
Sampling rate fmax < fs ≤ 2 fmax as special case of #2
Example: f0 = 100 Hz and fs = 125 Hz
Folding – SPFirst Sec. 4-2.4
where
0.4p
–0.4p
1.6p
–1.6p
See also SPFirst Fig. 4-11
©2003-2016, JH McClellan & RW Schafer

## Slide 8: Folding Due to Undersampling
Sinusoid sin(2  finput t) sampled at fs = 2000 samples/s with finput varied
Apparent frequency (Hz)
Input frequency, finput (Hz)
1000
1000
2000
3000
4000
fs = 2000 samples/s
See also SPFirst Fig. 4-12
Folding – SPFirst Sec. 4-2.4
Mirror image effect about finput = ½ fs gives rise to name of folding (see next slide)

## Slide 9: Folding Due to Undersampling

## Slide 10: Aliasing & Folding Demonstrations
Case #1 Oversampling
    Third demo: f0 = 600 Hz and fs = 2000 Hz
Case #2 Aliasing
  First demo: f0 = 600 Hz and fs = 500 Hz
Case #3 Folding
    Second demo: f0 = 600 Hz and fs = 750 Hz
Reconstructed signal
  Has frequencies between –½ fs and ½ fs
Sampling Theorem – SPFirst Sec. 4-2
link
  http://dspfirst.gatech.edu/chapters/04samplin/demos/aliasing/index.html

## Slide 11: Strobe Demonstrations
Strobe Demonstrations – SPFirst Sec. 4-3
link
©2003-2016, JH McClellan & RW Schafer

## Slide 12: Discrete-to-Continuous Conversion
General form of interpolation is sum of weighted pulses
Sampling & Reconstruction – SPFirst Sec. 4-4.1
Pulse function p(t)
  Input: discrete-time sequence y[n]
  Unit amplitude and/or unit area
  Rectangular, triangular, sinc, truncated sinc, etc.
  Overlaps in time with other pulses when duration > Ts
  Output: continuous-time signal that is an approximation of y(t)

## Slide 13: Zero-Order Hold
Rectangular pulse
  Easy to implement in hardware or software
  In time, no overlap between p(t) and adjacent pulses p(t - Ts) and p(t + Ts)
Plot of pulse p(t)
D-to-C Conversion– SPFirst Sec. 4-4.2
  Symmetry about origin?
Ts = 1;
t = -5 : 0.01 : 5;
p = rectpuls(t/Ts);
plot(t, p)
  Value of p(0)?
  Value of p(-0.5*Ts)?
  Value of p(0.5*Ts)?

## Slide 14: Linear Interpolation
Triangular pulse
  Easy to implement in hardware or software
  Zero-order hold even easier
  Overlap between p(t) and its adjacent pulses p(t - Ts) and p(t + Ts)
  No overlap with others
Plot of pulse p(t)
D-to-C Conversion– SPFirst Sec. 4-4.3
Ts = 1;
t = -5 : 0.01 : 5;
p = tripuls(t/(2*Ts));
plot(t, p)
  Symmetry about origin?
  Value of p(0)?
  Value of p(-Ts)?
  Value of p(Ts)?

## Slide 15: Ideal Bandlimited Interpolation
Sinc pulse
  In time, infinite overlap with other sinc pulses
Plot of pulse p(t)
D-to-C Conversion– SPFirst Sec. 4-4.6 and 11-4.2
Interpolate in time w/ infinite extent pulse?
  Make it finite in extent
  Truncate sinc pulse by multiplying it by rectangular pulse
  Symmetry about origin?
Ts = 1;
t = -5 : 0.01 : 5;
p = sinc(t/Ts);
plot(t, p)
  Where are the zero crossings?
  Amplitude decrease vs. time?
  Why is sinc(0) = 1?

## Slide 16: Sampling and Interpolation Demo
Sampling and interpolation demo (revisited) http://dspfirst.gatech.edu/chapters/04samplin/demos/recon/index.html/
D-to-C Conversion– SPFirst Sec. 4-4.6
  Does the rectangular, triangular, or truncated sinc pulse shape give the best reconstruction?
  Sinc pulse is truncated to be four sampling periods long. Why is the sinc pulse truncated?
  What happens as the sampling rate is increased?
Discrete to Continuous Time Conv.
fs
Continuous to Discrete Time Conv.
fs
Sampling
Reconstruction

## Slide 17: Sampling & Reconstruction
Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed from its samples x(n Ts) if samples taken at rate fs > 2 fmax
  x(t) bandlimited: limited to band of frequencies -fmax ≤ f ≤ fmax
  Represent
  Can represent periodic & non-periodic signals (slides 4-2/4-3)
Sampling Theorem– SPFirst Sec. 4-5
Sampling
Reconstruction

## Slide 18: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
6-18