## Slide 1: Discrete-Time Systems
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 7 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
Discrete-Time Systems – SPFirst Sections 5-1 to 5-4
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12
✔
✔
✔
✔
✔


## Slide 3: Discrete-Time Signals & Systems
Discrete-time signals (see slide 2-9)
  Formula: x[n] = cos((p/2) n) useful in analysis
  Samples: xvec = [1 0 -1 0 1 0 -1 0] useful in simulation
  Properties: even symmetric useful in reasoning
  Piecewise: v[n] = rectpuls(n/10)
n = -7 : 7;
v = rectpuls(n/10);
stem(n, v);
T{•}
y[n]
x[n]
Discrete-time systems
  Produce output signal from input signal
  Squaring: y[n] = x2[n]
  Averaging: y[n] = ½ x[n] + ½ x[n-1]
see slide 1-18
Discrete-Time Systems – SPFirst Ch. 5 Intro & Sec. 5-1
Width is 10 samples

## Slide 4: Running-Average Filter
Filter alters input
  Removes component or modifies characteristic
The Running Average Filter – SPFirst Sec. 5-2
n
coffee filter [Wikipedia]
Finite impulse response (FIR) filter
  Each output sample is finite sum of weighted input samples
Running-average (a.k.a. moving average) filter
  Each output sample is average of finite number of input samples
  Example: y[n] = ( x[n] + x[n+1] + x[n+2] ) / 3
n
0
1
2
3
4
5
6
7
-1
-2
-3
x[n]
2
4
6
0
1
2
3
4
5
6
7
-1
-2
-3
y[n]
4
6
sliding window
See also SPFirst Figs. 5-2 & 5-3

## Slide 5: Running-Average Filter
Noncausal filter
  Uses future input values (as in example on previous slide)
  Buffer input signal before computing nth output sample
The Running Average Filter – SPFirst Sec. 5-2
n
n
0
1
2
3
4
5
6
7
-1
-2
-3
x[n]
2
4
6
0
1
2
3
4
5
6
7
-1
-2
-3
y[n]
4
6
sliding window
Causal filter
  Only uses present and past input values
  Compute nth output sample when nth input sample arrives
  Example: y[n] = ( x[n] + x[n-1] + x[n-2] ) / 3

## Slide 6: General FIR Filter
Causal FIR filter
  Sliding window of M+1 samples
  M+1 filter coefficients b0, b1, …, bM
  Vector dot product of [b0 b1 … bM] and [x[n] x[n-1] … x[n-M]]
The Running Average Filter – SPFirst Sec. 5-3
Averaging filter
  Three terms: filter order M = 2 and bk = 1/3 for k = 0, 1, 2
  General case: bk = 1/(M+1) for k = 0, 1, …, M
Coefficients completely define filter
  Example: { bk } = { 1, -1 } gives y[n] = x[n] – x[n-1]
  Example: { bk } = { 1, 0, -1 } gives y[n] = x[n] – x[n-2]

## Slide 7: FIR Filtering
Signal is sum of increasing exponential & sinusoid
  x[n] = (1.02)n + ½ cos((2 p / 8) n + p / 4) for 0 ≤ n ≤ 40
Apply causal 3-point and 7-point averaging filters
  b = { bk } = { 1/3, 1/3, 1/3 } where M = 2
  b = { bk } = { 1/7, 1/7, 1/7, 1/7, 1/7, 1/7, 1/7 } where M = 6
The Running Average Filter – SPFirst Sec. 5-3.1
See also SPFirst Fig. 5-6
n
n
n

## Slide 8: FIR Filtering (MATLAB Code)
Note: filter(b, 1, x) command
% Define x[n] for 0<=n<=40
n = 0 : 40;
x1 = (1.02).^n;
x2 = 0.5*cos((2*pi/8)*n + pi/4);
x = x1 + x2;
% Save n and x1 for plotting trend
t = n;
x1t = x1;
% Define x[n] for -6<=n<=50
n0 = 6;
n = [ (-n0:-1) n (41:50) ];
x = [ zeros(1,n0) x zeros(1,10) ];
x1 = [ zeros(1,n0) x1 zeros(1,10) ];
% Define filter coefficients
b3coeff = (1/3)*ones(1,3);
b7coeff = (1/7)*ones(1,7);
% Filter data
y3 = filter(b3coeff, 1, x);
y7 = filter(b7coeff, 1, x);
% Plot results
figure;
stem(n, x);
title('x[n]'); ylim([0 3]);
hold on; plot(t, x1t); hold off;
figure;
stem(n, y3);
title('Output of 3-Point Filter'); ylim([0 3]);
hold on; plot(t, x1t); hold off;
figure;
stem(n, y7);
title('Output of 7-Point Filter'); ylim([0 3]);
hold on; plot(t, x1t); hold off;
The Running Average Filter – SPFirst Sec. 5-3.1
Filter coefficients
Input signal

## Slide 9: Audio Example
Signal is sum of three ‘B’ notes on Western scale
  Where fB3 = 246.9416 Hz, fB4 = 493.8833 Hz, fB5 = 987.7666 Hz
  With sampling rate fs = 8000 Hz and
  Note: fB4 = 2 fB3 and fB5 = 4 fB3 due to octave spacing
The Running Average Filter – SPFirst Sec. 5-3.1
Filter signal with 4-point averaging filter
  b = { bk } = { 1/4, 1/4, 1/4, 1/4 } where M = 3
Filter signal with 16-point averaging filter
  b = { bk } = { 1/16, 1/16, 1/16, …, 1/16 } where M = 15
What differences do you hear?

## Slide 10: Audio Example (MATLAB code)
% Set sampling rate and duration
fs = 8000;
tmax = 3;
nmax = round(fs * tmax);
n = 1 : nmax;
% B note in three different octaves
B1 = 61.73541; % Hz
B3 = 4*B1
B4 = 2*B3;
B5 = 2*B4;
f = [ B3 B4 B5 ];
wHat = 2*pi*f/fs;
a = [ 1 1 1 ];
x = zeros(1, length(n));
for i = 1 : length(wHat)
x = x + a(i)*cos(wHat(i)*n);
end
Note: filter(b, 1, x) command
The Running Average Filter – SPFirst Sec. 5-3.1
% Scale amplitude to be in [-1, 1]
x = x / max(abs(x));
% Filter signal of 3 notes
average4 = (1/4)*ones(1,4);
y4 = filter(average4, 1, x);
average16 = (1/16)*ones(1,16);
y16 = filter(average16, 1, x);
% Play sounds to keep same volume level
sound(x, fs);
pause(tmax+1);
sound(y4, fs);
pause(tmax+1);
sound(y16, fs);
Filter coefficients
Input signal

## Slide 11: Unit Impulse Response
Discrete-time unit impulse signal d[n]
The Running Average Filter – SPFirst Sec. 5-3.2
n
d[n]
1
1
-1
2
3
-2
-3
0
n
d[n-2]
1
1
-1
2
3
-2
-3
0
Expressing finite-length signals using unit impulses
d[n+2]
1
0
2
3
n
1
-1
2
3
-2
-3
x[n]
2 d[n+1]
3 d[n]
2 d[n-1]
d[n-2]
n = -3 : 3;
x = [0 1 2 3 2 1 0];
stem(n, x);
n = -3 : 3;
x = 3*tripuls(n/6);
stem(n, x);
- OR -
No MATLAB function for d[n]
Could use rectpuls(n) but awkward

## Slide 12: Unit Impulse Response
Output of system when unit impulse d[n] is input
The Running Average Filter – SPFirst Sec. 5-3.2
T{•}
h[n]
d[n]
M = 2;
n = -2 : 10;
h = rectpuls((n-1) / 3);
h = h / (M+1);
stem(n, h);
ylim( [0, 0.5] );
M = 6;
n = -2 : 10;
h = rectpuls((n-M/2) / (M+1));
h = h / (M+1);
stem(n, h);
ylim( [0, 0.5] );
n
n
  When system is a finite impulse response filter, let x[n] = d[n],
  Impulse responses for 3-point and 7-point averaging filters

## Slide 13: Convolution and FIR Filters
FIR filters of order M
  Input-output relationship (slide 7-6):
The Running Average Filter – SPFirst Sec. 5-3.3
Convolution
  Input-output algorithm for large class of filters including FIR
  Applies to infinite-length signals
  More on general case later
  Impulse response h[n] = bn for 0 ≤ n ≤ M (see slide 7-11)
  Called a finite convolution sum
  Output y[n] obtained by convolving x[n] and h[n]

## Slide 14: Computing Finite Convolution Sums
Expand finite convolution sum
The Running Average Filter – SPFirst Sec. 5-3.3
0
1
2
3
4
5
-1
-2
-3
x[n]
1
2
3
n
2
3
4
h[n]
1
n
-1
n | -1 | 0 | 1 | 2 | 3 | 4
x[n] | 0 | 1 | 2 | 3 | 0 | 0
h[n] | 0 | 1 | -1 | 0 | 0 | 0
h[0] x[n] | 0 | 1 | 2 | 3 | 0 | 0
h[1] x[n-1] | 0 | 0 | -1 | -2 | -3 | 0
y[n] | 0 | 1 | 1 | 1 | -3 | 0
x = [1 2 3];
h = [1 -1];
y = conv(x, h);
x = [1 2 3 0];
h = [1 -1];
y = filter(h, 1, x);
- OR -
y[n] is one sample longer than x[n]

## Slide 15: Block Diagram Representations
The Running Average Filter – SPFirst Sec. 5-4
©2003-2016, JH McClellan & RW Schafer

## Slide 16: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
7-16