## Slide 1: Frequency Response of FIR Filters
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 9 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
Frequency Response of FIR Filters – SPFirst Sec. 6-1 to 6-7
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12
✔
✔
✔
✔
✔
✔
✔



## Slide 3: Linear Time Invariant System
Uniquely defined by its impulse response h[n]
Frequency Response of FIR Filters – SPFirst Ch. 6 Intro
h[n]
y[n]
x[n]
Sinusoidal response
  When input is sinusoid, output is sinusoid of same frequency
  The output sinusoid may have different magnitude/phase
Frequency response
  Indicates how input frequencies are transferred to output
  Directly connected to impulse response (next slide)
Output frequencies are only those present in input

## Slide 4: Sinusoidal Response of FIR Filters
Input complex-valued sinusoid
Frequency Response of FIR Filters – SPFirst Sec. 6-1
Output is due to convolution
h[n]
y[n]
x[n]
Frequency response
  Directly related to impulse response
  Response to complex sinusoid signal of any frequency
  Describes how frequencies are transferred from input to output

## Slide 5: Sinusoidal Response of FIR Filters
Frequency response
  Powers of :
  Polar form (magnitude-phase form):
Frequency Response of FIR Filters – SPFirst Sec. 6-1
Response to complex-valued sinusoid revisited
Change in magnitude (gain)
Change in phase (phase shift)

## Slide 6: Sinusoidal Response of FIR Filters
Example
Frequency Response of FIR Filters – SPFirst Sec. 6-1 & 6-5
n
h[n]
0
1
2
magnitude
wHat = -pi : 0.01 : pi;
Hmag = 2 + 2*cos(wHat);
Hphase = -wHat;
figure;
plot(wHat, Hmag);
title('Magnitude Response');
xlim( [-pi pi] );
figure;
plot(wHat, Hphase);
title('Phase Response');
xlim( [-pi pi] );
Sinusoidal Response
h = [ 0 1 2 1 0 0];
n = [-1 0 1 2 3 4];
stem(n, h);
ylim( [-0.5 2.5] );
phase
gain of 3
phase shift -p/3
Lowpass filter

## Slide 7: Sinusoidal Response of FIR Filters
Frequency Response of FIR Filters – SPFirst Sec. 6-2 & 6-4.3
Derivation
Frequencies in output are only those in input
Output:
Input:
For real-valued h[n]

## Slide 8: Ideal Delay
Delay by 1 Sample
x[n]
y[n]
Linear Phase
Allpass Filter
Condition
Zero Initial
Frequency Response of FIR Filters – SPFirst Sec. 6-5.1
  Impulse response
  Frequency response
h[n]
n
h = [ 0 0 0 1 0 0 0];
n = [-2 -1 0 1 2 3 4];
stem(n, h);
ylim( [-0.5 1.5] );
freqz( [ 0 1 ] );

## Slide 9: Two-Point Averaging Filter
Input-output relationship
n
h[n]
Two-tap averaging filter
½
2
3
1
Delay
x[n]
S
y[n]
h[0]
h[1]
x[n-1]
Frequency Response of FIR Filters
Impulse response
Frequency response
magnitude
phase (linear)

## Slide 10: First-Order Difference
n
h[n]
First-order difference
½
2
3
- ½
Linear Phase
Generalized
Frequency Response of FIR Filters – SPFirst Sec. 6-5.2
Input-output relationship
Impulse response
Frequency response
amplitude
phase

## Slide 11: Cascading FIR Filters Demo
DSP First, 2nd ed, ch. 6, cascading FIR Filters
  http://dspfirst.gatech.edu/chapters/06firfreq/demos/blockd/index.html
From lowpass filter to highpass filter
  original image  blurred image  sharpened/blurred image
From highpass to lowpass filter
  original image  sharpened image  blurred/sharpened image
Frequencies that are zeroed out can never be recovered (e.g. DC is zeroed out by highpass filter)
Two LTI systems in cascade
  Order can be switched and cascade output would remain same
  Assumes computations are performed in exact precision
Frequency Response of FIR Filters – SPFirst Sec. 6-6

## Slide 12: Periodicity of Discrete-Time Sinusoids
Key idea
  Continuous-time period may not align w/ discrete-time grid
Frequency Response of FIR Filters – Not in SPFirst
  Example
  f0 = 1200 Hz and fs = 8000 Hz
Three continuous-time periods
Discrete-time period of 20 samples

## Slide 13: Periodicity of Discrete-Time Sinusoids
Continuous-time
  Continuous-time period T0 = 1 / f0
Frequency Response of FIR Filters – Not in SPFirst
Discrete-time cosine
  Sample x(t) at rate fs by substituting t = n Ts :
Discrete-time frequency
  Remove common factors between integers N & L
  cos(2  (N / L) n) has discrete-time period of L samples that contains N continuous-time periods
  See handout on Discrete-Time Periodicity
f0 = 1200;
fs = 8000;
% w0 = 2 pi (3 / 20)
N = 3;
L = 20;
% Time extent
Ts = 1/fs;
nmax = L;
tmax = nmax*Ts;
% x(t) = cos(2 pi f0 t)
fp = fs*24;
Tp = 1 / fp;
t = 0 : Tp : tmax;
xt = cos(2*pi*f0*t);
% x[n] = cos(w0 n)
w0 = 2*pi*N/L;
n = 0 : nmax;
xn = cos(w0*n);
tn = 0 : Ts : tmax;
% Plots
plot(t, xt);
figure; stem(n, xn);
figure; plot(t, xt);
hold; stem(tn, xn);

## Slide 14: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
9-14