## Slide 1: Infinite Impulse Response Filters
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 11 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Infinite Impulse Response (IIR) Filters– SPFirst Ch. 8 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12


✔
✔
✔
✔
✔
✔
✔
✔
** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔


## Slide 3: Infinite Impulse Response (IIR) Filter
IIR Filter
Infinitely long impulse response
First-order example #1:
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-2
  Compute first output value:
  Initial condition y[-1]. What value to use? Why? p. 198/201
  Depends on current/previous input values (like an FIR filter)
  Depends on previous output values (unlike an FIR filter)
  Given y[-1] and x[n], we can compute y[n] iteratively
  Consists of modes of form an u[n] where u[n] is unit step
  Amplitude decays or remains bounded or explodes as n  ∞
etc.

## Slide 4: Infinite Impulse Response (IIR) Filter
First-order example #2:
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-2
Closed-form impulse response using time domain
n | -1 | 0 | 1 | 2 | 3 | …
d[n] |  |  |  |  |  | 
h[n-1] |  |  |  |  |  | 
h[n] | 0 |  |  |  |  | 
First-order example #3:
LTI #2
  Input
  into LTI #2 to get impulse response
  Using LTI properties,

## Slide 5: Three Common Z-Transform Pairs
h[n] = d[n]
h[n] = an u[n]
h[n] = d[n-1]
  Region of convergence for summation: |z| > |a|
  |z| > |a| is the complement of a disk in z-domain
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-3.3
  Region of convergence: entire z-plane
  Region of convergence: entire z-plane except z = 0
  h[n-1]  z-1 H(z)

## Slide 6: First-Order LTI IIR Filter
Find impulse response h[n] in z-domain
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-3.1
Take z-transform of both sides of difference equation
z
Take inverse z-transform of transfer function H(z)
pole at z = a

## Slide 7: First-Order LTI IIR Filter Freq. Resp.
Pole p0 = 0.9 and zero z0 = 0
  Angle of pole near unit circle indicates frequency at which peak occurs in magnitude response
  Angle of zero on or near unit circle indicates frequency at which valley occurs in magnitude response
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-5 & 8-9
Since |z| > 0.9, region of convergence includes the unit circle
)|
)|

## Slide 8: Demonstrations
Time/frequency/z domain movies for IIR Filters
  http://dspfirst.gatech.edu/chapters/08feedbac/demos/3_domain/index.html
IIR filter with one pole and a zero at the origin
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-6
link

## Slide 9: Second-Order LTI IIR Filter
Input-output relationship in time domain
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-4 & 8-9
  MATLAB : filter([b0 b1 b2], [1 -a1 -a2], x);
Transfer function in z-domain
Factor transfer function in z-domain
Zeros z0 and z1
Poles p0 and p1
|z| > |p0| and |z| > |p1|
Valid z values

## Slide 10: Magnitude Response
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-5 & 8-9
lowpass highpass bandpass bandstop allpass notch?
Re(z)
Im(z)
X
O
O
X
Zeros are on the unit circle
% zero locations on unit circle
zeroAngle = 15*pi/16;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
% pole locations inside unit circle
r = 0.9; poleAngle = pi/16;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
% Set DC response at H(1) to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
  Zeros z0 & z1 and poles p0 & p1
  |a – b| is distance between complex numbers a and b
  Poles inside unit circle:
  is valid
  is distance from point on unit circle and pole p0

## Slide 11: Demonstrations
Time/frequency/z domain movies for IIR Filters
  http://dspfirst.gatech.edu/chapters/08feedbac/demos/3_domain/index.html
IIR filter with two poles and two zeros with poles moving towards unit circle
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-6
link

## Slide 12: Stability
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-8
A discrete-time LTI system is bounded-input bounded-output (BIBO) stable if for any bounded input x[n] such that | x[n] |  B1 < , then the filter response y[n] is also bounded | y[n] |  B2 < 
Proposition: A discrete-time filter with an impulse response of h[n] is BIBO stable if and only if
  Every finite impulse response LTI system (even after implementation) is BIBO stable
  A causal infinite impulse response LTI system is BIBO stable if and only if its poles lie inside the unit circle
  http://users.ece.utexas.edu/~bevans/courses/signals/handouts/Appendix%20H%20BIBO%20Stability.pdf

## Slide 13: BIBO Stability
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-8
Rule #1: For a causal sequence, poles are inside the unit circle (applies to z-transform functions that are ratios of two polynomials) OR
pole at z=a
Rule #2: Unit circle is in region of convergence
Example:
  Stable if |a| < 1 by rule #1 or equivalently
  Stable if |a| < 1 by rule #2 because |z|>|a| and |a|<1

## Slide 14: Block Diagram for IIR Filter
Convert difference equation to visual representation
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-3.2
  Start with input x[n] and output y[n]
x[n]
y[n]
  Generate x[n-1] and y[n-1] terms using unit delay blocks
z-1
x[n-1]
×
b0
×
b1
×
a1
+
+
z-1
y[n-1]
  Add blocks for multiplication by constants a1, b0 and b1
  Add blocks for addition
How many initial conditions?

## Slide 15: Block Diagram for IIR Filter
Infinite Impulse Response (IIR) Filters– SPFirst Sec. 8-3.2 & 8-9
Convert difference equation to visual representation
x[n]
y[n]
z-1
x[n-1]
×
b0
×
b1
×
a1
+
+
z-1
y[n-1]
z-1
x[n-2]
z-1
y[n-2]
×
b2
×
a2
+
+
How many initial conditions?
What happens if a2=0 and b2=0?

## Slide 16: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
11-16