## Slide 1: Continuous-Time Signals and LTI Systems
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 12 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Continuous-Time Signals and LTI Systems – SPFirst Ch. 9 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

✔
✔
✔
✔
✔
✔
✔
✔
** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔
✔
✔
✔

## Slide 3: Many Faces of Signals
Function, e.g. A cos(w0 t + f) in continuous time or in discrete time, useful in analysis
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-1
Sequence of numbers, e.g. {1,2,3,2,1} or a sampled triangle function, useful in simulation
Set of properties, e.g. even and causal, useful in reasoning about behavior
A piecewise representation, e.g. useful in analysis
A generalized function, e.g. the Dirac delta d(t), useful in analysis

## Slide 4: Two-Sided Signals
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-1
t
t
t
Square wave f0 = 3 Hz
t = -2 : 0.01 : 2;
% Cosine
w0 = 3*pi;
x1 = 10*cos(w0*t);
figure;
plot(t, x1);
ylim( [-11 11] );
t = -2 : 0.01 : 2;
% Square Wave
f0 = 3;
v = cos(2*pi*f0*t);
x2 = 0.5*sign(v) + 0.5;
figure;
plot(t, x2);
ylim( [-0.1, 1.1] );
t = -2 : 0.01 : 2;
% Two-Sided Exponential
x3 = 5*exp(-abs(t));
figure;
plot(t, x3);

## Slide 5: One-Sided Signals
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-1
t = -2 : 0.01 : 2;
% Cosine
w0 = 3*pi;
unitstep = (t >= 0);
x1 = 10*cos(w0*t).*unitstep;
figure;
plot(t, x1);
ylim( [-11 11] );
t = -2 : 0.01 : 2;
% Two-Sided Exponential
unitstep = (t >= 0);
x3 = 5*exp(-t).*unitstep;
figure;
plot(t, x3);
ylim( [-0.5, 5.5] );
t
t = -2 : 0.01 : 2;
% Unit Step
unitstep = (t >= 0);
x1 = unitstep;
figure;
plot(t, x1);
ylim( [-0.1 1.1] );
t
t

## Slide 6: Finite-Length Signals
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-1
Rectangular pulse
  Value of p(0)?
  p(0.5)?
  p(1)?
t = -1 : 0.01 : 4;
rp = rectpuls(t-1/2);
plot(t, rp);
ylim( [-0.1 1.1] );
Sinusoidal signal
t = -1 : 0.01 : 4;
rp = rectpuls(t-1/2);
w0 = 3*pi;
x4 = 10*cos(w0*t).*rp;
plot(t, x4);
ylim( [-11 11] );

## Slide 7: Unit Impulse (Dirac Delta)
Mathematical idealism for an instantaneous event
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-2
e
-e
t
Unit Area
e
-e
t
Unit Area
Dirac delta as generalized function (a.k.a. functional)
Note that d(0) is undefined
  Unit area:
  Sifting
  provided g(t) is defined at t = 0
  Scaling:

## Slide 8: Unit Impulse (Dirac Delta)
Generalized sifting, assuming that a > 0
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-2
t
(1)
0
Unit Area
By convention, plot Dirac delta as arrow at origin
  Undefined amplitude at origin
  Denote area at origin as (area)
  Height of arrow is irrelevant
  Direction of arrow indicates sign of area

## Slide 9: Unit Impulse (Dirac Delta)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-2
We can simplify d(t) under integration
Other examples
What about?
What about?
  Answer: 0
  By substitution of variables,
What about at origin?
L. B. Jackson, “A correction to impulse invariance,” IEEE Sig. Proc. Letters, Oct. 2000.
  u(0) can take any value
  Common values: 0, ½, 1

## Slide 10: Systems
Systems operate on signals to produce new signals or new signal representations
T{•}
y(t)
x(t)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-3
See lecture slides 1-15 and 1-16
Continuous-time system examples
Squaring block
  Screen maps pixels by ()2.2
  AM radio receiver
  Increase musical note by one octave
  x(t) = cos(2 p 440 t)
  y(t) = cos2(2 p 440 t) = ½ (1 + cos(2 (2 p 440 t)) ) = ½ + ½ cos(2 p 880 t)
  y(t) = ½ x(t) + ½ x(t-1)
(•)2
y(t)
x(t)
  y(t) = x2(t)

## Slide 11: Continuous-Time System Properties
Let x(t), x1(t), and x2(t) be inputs to a continuous-time linear system and let y(t), y1(t), and y2(t) be their corresponding outputs
Quick test to identify some nonlinear systems?
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-4
A linear system satisfies
  Additivity: x1(t) + x2(t)  y1(t) + y2(t)
  Homogeneity: a x(t)  a y(t) for any real/complex constant a
For time-invariant system, shift of input signal by any real-valued t causes same shift in output signal, i.e. x(t - t)  y(t - t), for all t
Example: Squaring block
(•)2
y(t)
x(t)
See lecture slides 8-2 and 8-3

## Slide 12: Initial Conditions for Linear Systems
Observe signals and systems starting at time t = 0
x(t)
y(t)
C0 is the initial condition w/r to observation
Example: Integrator
Observe integrator for t  0
System “at rest” is a necessary condition for linearity
x(t)
y(t)
  Homogeneity: input for output
  for all values of ?

## Slide 13: Init. Cond. for Time-Invariant Systems?
Observe system for t  0-
  Does yshifted(t) = y(t-t0) for all real-valued t0 for ?
  Notation means to include any Dirac delta signals at origin
Handouts for example systems
  Time-Invariance for a (Shift) System Under Observation
  Time-Invariance for an Integrator
link
link

## Slide 14: Continuous-Time System Properties
Ideal delay by T seconds
x(t)
y(t)
x(t)
y(t)
x(t)
y(t)
Role of initial conditions?
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-4
Scale by a constant (a.k.a. gain block)
  Linear? Time-invariant?
  Two different ways to express it in a block diagram
  Linear? Time-invariant?
See lecture slide 8-4

## Slide 15: Continuous-Time System Properties
Tapped delay line
M-1 delay blocks:
S
…
…
Coefficients (or taps) are a0, a1, …aM-1
Role of initial conditions?
Impulse response lasts for (M-1) T seconds:
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-4
  Linear? Time-invariant?
See lecture slides 8-5 and 8-6

## Slide 16: Continuous-Time System Properties
Amplitude Modulation (AM)
  y(t) = A x(t) cos(2p fc t)
  fc is the carrier frequency (frequency of radio station)
  A is a constant
  Linear? Time-invariant?
AM radio transmitter if x(t) = 1 + ka m(t)
  m(t) is audio signal to be broadcast
  | ka m(t) | < 1
A
x(t)
cos(2 p fc t)
y(t)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-4

## Slide 17: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
12-17