## Slide 1: Continuous-Time Convolution
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 13 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Continuous-Time Signals and LTI Systems – SPFirst Ch. 9-4
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔

## Slide 3: Systems
Systems operate on signals to produce new signals or new signal representations
T{•}
y(t)
x(t)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-4
Linear time-invariant system
T{•}
h(t)
d(t)
T{•}
y(t)
x(t)
  Uniquely defined by its impulse response
  Output in time domain is convolution of impulse response and input signal
Continuous-time convolution

## Slide 4: LTI System Examples
Observe signals over all time
x(t)
y(t)
Ideal delay by T seconds
x(t)
y(t)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-5
  Initial conditions must be zero for LTI properties to hold
apply sifting property
apply sifting property
Gain

## Slide 5: LTI System Examples (continued)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-5
x(t)
y(t)
Integrator
Tapped delay line
S
…
…
M-1 delay blocks
Impulse response:
1 if t ≥ t
Lasts for (M-1)T seconds

## Slide 6: Graphical Convolution Methods
From its definition, convolution is equivalent to
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-7
  Rotating one of the functions about the y axis
  Shifting it by t
  Multiplying this flipped, shifted function with other function
  Calculating the area under this product
  Assigning this value to f1(t) * f2(t) at t
Sometimes called “flip-and-slide” convolution
Convolution demo cconvdemo from SP First
  http://dspfirst.gatech.edu/matlab/ZipFiles/cconvdemo-v218.zip

## Slide 7: Graphical Convolution Example
3
t
2
f(t)
2
-2 + t
2 + t
g(t-t)
*
2
2
t
f(t)
-2
2
3
t
g(t)
Convolve two signals:
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-7
Replace t with t in f(t) and g(t)
Choose to flip and slide g(t) since it is simpler and symmetric
Functions overlap like this:

## Slide 8: Graphical Convolution Example
3
t
2
f(t)
2
-2 + t
2 + t
g(t-t)
3
t
2
f(t)
2
-2 + t
2 + t
g(t-t)
Convolution can be divided into 5 parts
  t < -2
    Two functions do not overlap
    Area under the product of the functions is zero
  -2  t < 0
    Part of g(t-t) overlaps part of f(t)
    Area under the product of the functions is
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-7

## Slide 9: Graphical Convolution Example
  0  t < 2
    Here, g(t-t) completely overlaps f(t)
    Area under the product is just
  2  t < 4
    Part of g(t-t) and f(t) overlap
    Calculated similarly to -2  t < 0
  t  4
    g(t-t) and f(t) do not overlap
    Area under their product is zero
3
t
2
f(t)
2
-2 + t
2 + t
g(t-t)
3
t
2
f(t)
2
-2 + t
2 + t
g(t-t)
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-7

## Slide 10: Graphical Convolution Example
Result of convolution (5 intervals of interest):
t
y(t)
0
2
4
-2
6
No Overlap
No Overlap
Partial Overlap
Partial Overlap
Complete Overlap
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-7
Check values at interval endpoints to validate answer

## Slide 11: Convolution Demos
Continuous-Time Convolution Demonstation
  cconvdemo from Signal Processing First
  http://dspfirst.gatech.edu/matlab/ZipFiles/cconvdemo-v218.zip
Some conclusions from the animations
  Convolution of two causal signals gives a causal result
  Convolving two finite-length signals results in a signal whose length is the sum of the lengths of tsignals being convolved
  See convolution of two rectangular pulses in handout E
Discrete-Time Convolution Demonstration
  dconvdemo from Signal Processing First
  http://dspfirst.gatech.edu/matlab/ZipFiles/dconvdemo-v318.zip
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-7

## Slide 12: Convolution Properties
Definition
Continuous-Time Signals and LTI Systems – SPFirst Sec. 9-4
Properties
  Commutative: f1(t) * f2(t) = f2(t) * f1(t)
  Distributive: f1(t) * [f2(t) + f3(t)] = f1(t) * f2(t) + f1(t) * f3(t)
  Associative: f1(t) * [f2(t) * f3(t)] = [f1(t) * f2(t)] * f3(t)
  Shift: If f1(t) * f2(t) = c(t), then f1(t) * f2(t – T) = f1(t – T) * f2(t) = c(t – T)

## Slide 13: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
13-13