## Slide 1: The Laplace Transform
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 17 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
The Laplace Transform – SPFirst Ch. 16 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔

## Slide 3: Transforms
Provide alternate signal & system representations
The Laplace Transform – SPFirst Ch. 16 Intro
  Simplifies analysis in some cases
  Reveals new properties (e.g. bandwidth)
Input-Output Physical Model
Algebra: Poles and Zeros
Passbands and Stopbands
Input-Output Physical Model
Passbands and Stopbands
SPFirst Fig. 16-1
SPFirst Fig. 8-13
Diff. Equ. {ak, bk}
Diff. Equ. {ak, bk}

## Slide 4: Laplace Transform
Decompose a signal x(t) into complex sinusoids of the form es t where s is complex: s = s + jw
The Laplace Transform – SPFirst Sec. 16-1
Forward bilateral (two-sided) Laplace transform
  x(t): complex-valued function of a real variable t
  X(s): complex-valued function of a complex variable s
Forward unilateral (one-sided) Laplace transform
  Lower limit of 0- means to include Dirac deltas at t = 0 within limits of integration and ignore x(t) for t < 0

## Slide 5: Complex Exponential Signal
The Laplace Transform – SPFirst Sec. 16-1
Ratio of two polynomials
Region of convergence

## Slide 6: Region of Convergence
The Laplace Transform – SPFirst Sec. 16-2 & 16-3
-e-a t u(-t) and e-a t u(t) have same transform function but different regions of convergence
Im{s}
Re{s} = -Re{a}
Re{s}
-1
t
x(t)
x(t) = -e- a t u(-t)
anti-causal
1
t
x(t)
x(t) = e-a t u(t)
causal
What happens to X(s) = 1/(s+a) at s = -a?
Page 11
Page 3

## Slide 7: Relationship to Fourier Transform
The Laplace Transform – SPFirst Sec. 16-2.2
Substitute s = s + jw into the Laplace transform
Bilateral Laplace transform is identical to the continuous-time Fourier transform of x(t) e –s t
Continuous-time Fourier transform is the Laplace transform X(s) after substituting s = j w
  Substitution s = j w has to be valid (in region of convergence)
Existence of Laplace and Fourier transforms
because s = 0

## Slide 8: More Transform Pairs
The Laplace Transform – SPFirst Sec. 16-3
Dirac delta
Unit step
Rect. pulse
Exponential
Integral converges when s = 0

## Slide 9: Linearity and Delay Properties
The Laplace Transform – SPFirst Sec. 16-3 & 16-6
Linearity
Delay

## Slide 10: Other Properties
The Laplace Transform – SPFirst Sec. 16-6
Freq. shifting
Convolution in time
Convolution in frequency
Scaling in time or frequency
t
x(t)
2
-2
t
x(2 t)
1
-1
Area reduced by factor 2

## Slide 11: One-Sided Sinusoids
Cosine
Sine
The Laplace Transform – SPFirst Sec. 16-3
More transform pairs in Table 16-1 on page 16 of Chapter 16

## Slide 12: Inverse Laplace Transform
Definition
The Laplace Transform – SPFirst Sec. 16-7
  is a contour integral over a complex region in s plane
  c is a real constant chosen to ensure convergence of integral
Use transform pairs and properties instead
Many Laplace transform expressions are ratios of two polynomials, a.k.a. rational functions
  Convert a rational expression to simpler forms
  Apply partial fractions decomposition
  Use transform pairs

## Slide 13: Partial Fractions Example #1
Compute y(t) = e a t u(t) * e b t u(t) , where a  b
If a = b, then we would have resonance
What form would the resonant solution take?
The Laplace Transform – SPFirst Sec. 16-7

## Slide 14: Partial Fractions Example #2
The Laplace Transform – SPFirst Sec. 16-7

## Slide 15: Partial Fractions Example #3
The Laplace Transform – SPFirst Sec. 16-7

## Slide 16: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
17-16