## Slide 1: Transfer Functions
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2024
Lecture 18 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
The Laplace Transform – SPFirst Ch. 16 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔

## Slide 3: Transforms
Provide alternate signal & system representations
The Laplace Transform – SPFirst Ch. 16 Intro
  Simplifies analysis in some cases
  Reveals new properties (e.g. bandwidth)
Input-Output Physical Model
Algebra: Poles and Zeros
Passbands and Stopbands
Input-Output Physical Model
Passbands and Stopbands
SPFirst Fig. 16-1
SPFirst Fig. 8-13
Diff. Equ. {ak, bk}
Diff. Equ. {ak, bk}

## Slide 4: Transfer Function
Laplace transform of impulse response h(t) of linear time-invariant (LTI) system
Convolution in time property:
W(s) = H1(s) X(s)
Y(s) = H2(s) W(s) = H2(s) H1(s) X(s)
H(s) = H2(s) H1(s) = H1(s) H2(s)
See lecture slide 10-8 for discrete-time analogy
X(s)
W(s)
Y(s)
x(t)
w(t)
y(t)
h1(t)
h2(t)
X(s)
Y(s)
y(t)
x(t)
h(t)

## Slide 5: Transfer Function Examples
Ideal delay by T seconds
x(t)
y(t)
x(t)
y(t)
Scale by a constant (a.k.a. gain block)
See lecture slide 12-13
  Initial conditions (initial voltages in delay buffer) are zero

## Slide 6: Transfer Function Examples
Tapped delay line
M-1 delay blocks:
S
…
…
Impulse response lasts for (M-1) T seconds:
See lecture slide 12-14
  Initial conditions (initial voltages in delay buffers) are zero

## Slide 7: Transfer Function Examples
Ideal integrator with y(0-) = 0 for LTI to hold
x(t)
y(t)
x(t)
y(t)
See lecture slide 12-12
0
0
Ideal differentiator with x(0-) = 0 for LTI to hold

## Slide 8: Transfer Function for Diff. Equation
Example: y”(t) + 5 y’(t) + 6 y(t) = x’(t) + x(t)
  For LTI, initial conditions must be zero:
  y(0-) = 0, y’(0-) =0 and x’(0-) =0
Take Laplace transform of both sides of equation
Apply partial fractions decomposition
x(t)
y(t)

## Slide 9: First-Order LTI System
One pole at s = p0
Im{s}
Re{s} > Re{p0}
Re{s}
X
Frequency response
  If ROC includes imaginary axis, i.e. when Re{p0} < 0,
  is distance from point on imaginary axis jw to pole p0
p0 = -1;
w = -10 : 0.01 : 10;
plot(w, abs(1 ./ (j*w - p0)));
Lowpass Filter
w

## Slide 10: Second-Order LTI Oscillator
Poles at s = ±jw0 & zero at s = 0
See lecture slide 17-11
Frequency response
Im{s}
Re{s} > 0
Re{s}
X
X
jw0
-jw0
O
  Since ROC does not include imaginary axis, we cannot go directly from Laplace to Continuous-time Fourier transform
  Compute continuous-time Fourier transform of h(t)
w
w0
-w0
(p)
(p)
SPFirst Table 16-1

## Slide 11: Second-Order LTI Bandpass Filter
Poles at s = -a±jw0 & zero at s = -a
Frequency response
Im{s}
Re{s} > -a
Re{s}
X
X
jw0
-jw0
O
-a
  Since ROC includes imaginary axis, i.e. when a > 0,
SPFirst Table 16-1
a = 1
w0 = 10p
w

## Slide 12: LTI Systems in Cascade and Parallel
H1(s)
X(s)
Y(s)
H2(s)
H2(s)
X(s)
Y(s)
H1(s)

G1(s) + G2(s)
X(s)
Y(s)
G1(s)
X(s)
Y(s)
G2(s)

Cascade
  W(s) = H1(s) X(s) Y(s) = H2(s)W(s)
  Y(s) = H1(s) H2(s) X(s)  Y(s)/X(s) = H1(s)H2(s) = H(s)
  One can switch order of the cascade of two LTI systems if both LTI systems represent amplitudes in exact precision
Parallel combination
  Y(s) = G1(s)X(s) + G2(s)X(s)

Use partial fractions to decompose a transfer function H(s) = G1(s) + G2(s)
  Y(s)/X(s) = G1(s) + G2(s)
Advantages of parallel vs. cascade combination?

## Slide 13: Feedback Connection of LTI Systems
G(s)
F(s)
Y(s)
H(s)

-
E(s)
Combining equations

  Choice of K controls all poles in transfer function
  Common LTI system in EE362K Introduction to Automatic Control and EE445L Microcontroller Applications/Organization
Governing equations
What happens if H(s) is a constant K?
F(s)
Y(s)

## Slide 14: Solving a Differential Equation
Example: y”(t) +5 y’(t) + 6 y(t) = x’(t) + x(t)
  With y(0-) = 2, y’(0-) =1, and f(t) = e- 4 t u(t)
  So x’(t) = -4 e-4 t u(t) + e-4 t d(t), x ’(0-) = 0 and x ’(0+) = 1
  See Course Handout S
The Laplace Transform – SPFirst Sec. 16-8

## Slide 15: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
18-15