## Slide 1
Performance of Full-Reference Algorithms
Evaluated on Dell U2412M 24-inch displays
64 subjects evaluated every image over three sessions
Single Stimulus Continuous Evaluation on a scale of [0,100]
Reference and distorted images evaluated in same session
Differential Mean Opinion Score obtained for each image
Subjective Study Methodology
Sources of graphics data
Artifacts
Multiple artifacts may occur at same time
Problem: Automate Image Quality Assessment (IQA) for synthetic scenes
Approach: Evaluate IQA algorithms for high-resolution synthetic scenes
Motivation
Synthetic Scenes
25 pristine reference images
Used less severe distortions than natural images
500 distorted images
ESPL Synthetic Image Database
Processing Artifacts
Transmission Artifacts
Overall: SR-SIM ✓
Saliency-inspired pooling strategies perform well
PSNR does reasonably well for additive noise & fast fading
Interpolation and Blur
Conclusion
  Animation studios
  Kinect, video games
  Interpolation, banding, ringing, noise, blur
  JPEG and wireless distortions
  Give designers of video games and animated films immediate feedback for rendering artifacts
  Give video game designers immediate feedback on transmission artifacts in cloud gaming
  5 distortion types
  4 distortion levels for each image and each distortion type
Fast Fading
Evaluate 23 image quality assessment algorithms
Scatter plot of DMOS scores
Histogram of DMOS scores
http://users.ece.utexas.edu/~bevans/papers/2015/imagequality/
Conduct subjective tests for larger number of graphics artifacts
Evaluate no-reference image quality measures on database
Applicability of natural video statistics in animation sequences
Future Work
Spearman’s Rank Ordered Correlation Coefficient between leading full-reference metrics and subjective opinion scores
  Interpolation: MAD ✓
  Blur and Gaussian Noise: SR-SIM ✓
Blur
Original
  Develop public database of pristine and distorted synthetic images
  Conduct subjective testing for visual quality assessment
  Correlate IQA algorithms with subjective test results
Synthetic Scenes
Spectral Residual Based Similarity (SR-SIM) | Feature Similarity Index (Color) (FSIMc)
Visual Saliency Induced Index (VSI) | Most Apparent Distortion (MAD)
Multiscale Structural Similarity Index (MS-SSIM) | Peak Signal-to-Noise Ratio (PSNR)
Interpolation
Gaussian Noise
JPEG Compression
  Less severe distortions in the database
  Result in near-threshold artifacts
  JPEG Compression : FSIMc ✓
  Fast Fading: MAD ✓
Ms. Debarati Kundu and Prof. Brian L. Evans
Embedded Signal Processing Laboratory (ESPL)
debarati@utexas.edu, bevans@ece.utexas.edu
Full-Reference Visual Quality Assessment for Synthetic Images: A Subjective Study