## Slide 1
Junmo Sung and Brian L. Evans
Wireless Networking and Communications Group and
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
May 24, 2018
Real-time testbed for diversity in powerline and wireless smart grid communications

## Slide 2: Motivation
Exploit existing heterogeneous smart grid communication technologies
Diversity of powerline and wireless communication channels
More reliable communication possible with diversity
Testbed for test and evaluation of various combining schemes

## Slide 3: Heterogeneous Link Diversity
Good performance-complexity tradeoff
Log-likelihood ratio (LLR) combining
Average | Overhead | Complexity
Instantaneous | High | High
✓ Time | Medium | Medium
Time & Freq. | Low | Low
Noise Estimator Options
Maximal Ratio Combiner (MRC)
nth OFDM symbol; kth subcarrier; s2 Gaussian noise variance

## Slide 4: Powerline/Wireless Diversity System
Diversity over heterogeneous links
Combiner at receiver
Common OFDM baseband system for both subsystems
Smart Meter (Transmitter)
Data Concentrator (Receiver)

## Slide 5: Testbed Overview: Hardware
National Instruments
Two chasses
Plug-in modules
Two subsystems
  Powerline Tx/Rx chassis
  Wireless Tx/Rx chassis
Laptop
  Command center
  Visualization
Ethernet router
Powerline
Wireless
Hardware Setup

## Slide 6: Testbed Overview: Software
3 parallel threads (PLC, wireless communications, LLR combiner)
2 processors running a real-time operating system
Displays instantaneous and average BER/SNR and constellations
Wireless Transceiver
Powerline Transceiver

## Slide 7: Baseband Parameters
IEEE P1901.2-like baseband system
Wireless carrier frequency: 920 MHz
Parameter | Value
Sample rate | 400 kHz
DFT/IDFT size | 256 samples
CP length | 64 samples
Frame duration | variable
Frame rate | 2.5 frames/s
Active subcarriers | 36
Modulation Schemes | BPSK / Differential BPSK
DBPSK: This version applies differential encoding across adjacent subcarriers in the same OFDM symbol
Frame Structure: preamble of 9 training symbols for channel estimation, noise estimation and timing synch. plus up to 491 data symbols
PLC Transmission Band: CENELEC-A band from 35.9375 to 90.6250 kHz
Coding: Convolutional encoder plus Viterbi decoder

## Slide 8: Implementation Challenges
Channel and noise power estimation
  For channel: least-squares estimation and zero-forcing equalization
  For noise power: exploitation of repeated symbols in preamble
Sample timing detection
  Cross-correlation of received and known preambles
Sampling and carrier frequency offset
  Sample synchronization using PXI chassis reference clock
  Wireless system uses same local oscillator for up/downconversion
  Transmitter sends start triggers to receiver
Frame transmission synchronization
  Determinism of real-time operating system

## Slide 9: Initial Results
Case 1: Both communications experience a similar Eb/N0
separate
combined
separate
combined
With MRC and Differential BPSK
Both communications experience a similar Eb/N0
BPSK and MRC
Differential BPSK and MRC

## Slide 10: Initial Results
With MRC and BPSK
SNR is fixed for wireless and variable for powerline
powerline
combined
powerline
combined
BPSK and MRC
Differential BPSK and MRC
Case 2: SNR is fixed for wireless and is swept for powerline

## Slide 11: Conclusion
Testbed for evaluation of diversity combining schemes
  Flexible and real-time testbed
  Powerline and wireless communication subsystems implemented
Source code and implementation details released
  http://users.ece.utexas.edu/∼bevans/projects/plc/software/testbed/
Demonstration with a simple scheme
  Similar performance to simulation achieved on testbed