## Slide 1: Modeling and Mitigation of Interference in Wireless Receivers with Multiple Antennae
Aditya Chopra
PhD Committee:
Prof. Jeffrey Andrews
Prof. Brian L. Evans (Supervisor)
Prof. Robert W. Heath, Jr.
Prof. Elmira Popova
Prof. Haris Vikalo
November 18, 2011

## Slide 2
The demand for wireless Internet data is predicted to increase 1000 over the next decade
Chart: Mobile Internet Data Demand (Petabytes)
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Mobile Video | 0.1172 | 0.287 | 0.6512 | 1.3322 | 2.3542 | 4.2263
Other Mobile Internet | 0.1151 | 0.2532 | 0.5075 | 0.9123 | 1.3563 | 2.0312
Chart: Mobile Internet Traffic as a Percentage of Overall Internet Traffic
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015
S1 | 0.015733 | 0.02683 | 0.040664 | 0.057895 | 0.076 | 0.095481
2x increase per year!
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Source: Cisco Visual Networking Index Forecast

## Slide 3
Wireless communication systems are increasingly using multiple antennae to meet demand
Benefits
Multiplexing | Diversity
Multiple data streams are transmitted simultaneously to increase data rate | Antennae with strong channels compensate for antennae with weak channels to increase reliability
Wireless Channel
Transmit Antennae
Receive Antennae
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
101110
11
10
10

## Slide 4
Adj. Channel Interference
A growing mobile user population with increasing wireless data demand leads to interference
Base Station
or
Access Point
Cell Boundary
Link
Co-channel Interference
Out-of-cell Interference

## Slide 5
Interference is also caused by non-communicating source emissions …
… and impairs wireless communication performance
Computational Platform
Clocks, amplifiers, busses
Non-communicating devices
Microwave ovens Fluorescent bulbs
Chart: Throughput (Mbps)
| Channel 1 | Channel 7
LCD ON | 18 | 2.2
LCD OFF | 22 | 22
Impact of platform interference from a laptop LCD on wireless throughput (IEEE 802.11g) [Slattery06]
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 6
Interference mitigation has been an active area of research over the past decade
Base Station
Cell Boundary
Interference Cancellation [Andrews2005]
Interference Alignment [Jafar2008]
Resource Allocation[Andrews2009]
Base Station Coordination[Heath2009]
Co-existence[Rao2002]

## Slide 7
I employ a statistical approach to the interference modeling and mitigation problem
Thesis statement
Accurate statistical modeling of interference observed by multi-antenna wireless receivers facilitates design of wireless systems with significant improvement in communication performance in interference-limited networks.
Proposed solution
  Model statistics of interference in multi-antenna receivers
  Analyze performance of conventional multi-antenna receivers
  Develop multi-antenna receiver algorithms using statistical models of interference
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Notes: Remove problem and approach… expand solution

## Slide 8
A statistical-physical model of interference generation and propagation
Key Features
  Co-located receiver antennae ( )
  Interferers are common to all antennae ( ) or exclusive to nth antenna ( )
  Interferers are stochastically distributed in space as a 2D Poisson point process with intensity ( ), or ( ) (per unit area)
  Interferer free guard-zone ( ) of radius
  Power law propagation and fast fading
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
1
1
1
1
2
2
2
3
3
A 3-antenna receiver within a Poisson field of interferers
3
n
n

## Slide 9
Non-Gaussian distributions have been used in prior work to model single antenna interference statistics
I derive joint statistics of interference observed by multi-antenna receivers
  Wireless networks with guard zones (Centralized Networks)
  Wireless networks without guard zones (De-centralized Networks)
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Guard Zone Radius () | Single Antenna Statistics | Characteristic function | Parameters | Density Distribution
 | Symmetric Alpha Stable (SAS) [Sousa92] |  | : Dispersion, : Index, | Not known except =2,1,0.5
 | Middleton Class A (MCA) [Middleton99] |  | : Impulsive index : Variance | 
 | Single Antenna Statistics | Characteristic function | Parameters | Density Distribution
 | Symmetric Alpha Stable (SAS) [Sousa92] |  |  | 
 | Middleton Class A (MCA) [Middleton99] |  |  | 
 | Gaussian distribution
 | Cauchy distribution
 | Levy distribution

## Slide 10
Using the system model, the sum interference at the nth antenna is expressed as
COMMON INTERFERERS
SOURCE EMISSION
FADING CHANNEL
PATHLOSS
EXCLUSIVE INTERFERERS
Network model | Single Ant. Statistics | Multi antenna joint statistics | 
 |  | Common interferers | Independent interferers
Decentralized | Symmetric Alpha Stable (SAS) | Isotropic SAS [Ilow98] | Independent SAS
Centralized | Middleton Class A (MCA) |  | Independent MCA
Network model | Single Ant. Statistics | Multi antenna joint statistics | 
 |  | Common interferers | Independent interferers
Decentralized | Symmetric Alpha Stable (SAS) |  | 
Centralized | Middleton Class A (MCA) |  | 
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 11
In networks with guard zones, interference from common interferers exhibits isotropic Middleton Class A statistics
Interference in decentralized networks
Interference in centralized networks
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
1
1
1
1
2
2
2
3
3
A 3-antenna receiver within a Poisson field of interferers
3
Joint characteristic function | Parameters
Joint characteristic function | Parameters
Joint characteristic function | Parameters
Joint characteristic function | Parameters

## Slide 12
Simulation results indicate a close match between proposed statistical models and simulated interference
Tail probability of simulated interference in networks without guard zones
Tail probability of simulated interference in networks with guard zones
PARAMETER VALUES |  |  | 
 | 4 | ‘Isotropic’ | (per unit area)
 | 1.2 (Distance Units) (w/ GZ) | ‘Mixture’ | (per unit area)
PARAMETER VALUES |  |  | 
 | 4 | ‘Isotropic’ | 
 | 1.2 (Distance Units) (w/ GZ) | ‘Mixture’ | 
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Tail Probability:

## Slide 13
My framework for multi-antenna interference across co-located antennae results in joint statistics that are
Spatially isotropic (common interferers)
Spatially independent (exclusive interferers)
In a continuum between isotropic and independent (mixture)
for two impulsive distributions
Middleton Class A (networks with guard zones)
Symmetric alpha stable (networks without guard zones)
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 14
In networks without guard zones, antenna separation is incorporated into the system model
Applications
  Cooperative MIMO
  Two-hop communication
  Temporal modeling of interference in mobile receivers
Sum interference expression
  +
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Two antennae ( ) and interferers ( ) in a decentralized network
1
1
1
1
2
2
2
2
1
2

## Slide 15
The extreme scenarios of antenna colocation () and antenna isolation () are readily resolved
Interference statistics move in a continuum from spatially isotropy to spatial independence as antenna separation increases!
Colocated antennae ()
Characteristic function of interference:
Interference exhibits spatial isotropy
Remote antennae ()
Characteristic function of interference:
Interference exhibits spatial independence
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 16
Interference statistics are approximated using the isotropic-independent statistical mixture framework
Weighting function for different pathloss exponents ()
Joint tail probability vs. antenna separation for ,
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 17
The framework is used to evaluate communication performance of conventional multi-antenna receivers
Prior Work
System Model
Received signal vector
Rayleigh()
Isotropic + Independent SAS
Communication performance is evaluated using outage probability
Single Transmit Antenna
Multiple Receive Antennae
Introduction | Modeling (CoLo) | Modeling (Dist) |Outage Performance | Receiver Design
Article | Wireless System | Interference | Joint Statistics | Performance Metric
[Rajan2011] | SIMO | SAS | Independent | Bit Error Rate (BPSK)
[Gao2005] | SIMO | MCA | Indp. / Isotropic | Bit Error Rate (BPSK)
[Gao2007] | MIMO | MCA | Independent | Bit Error Rate (BPSK)
SIR: Signal-to-Interference Ratio

## Slide 18
Outage probability of linear combiners
+
Receiver algorithm | Weight vector | Outage probability
Equal Gain Combiner |  | 
Maximum Ratio Combiner |  | 
Selection Combiner |  | 
Receiver algorithm | Weight vector | 
Equal Gain Combiner |  | 
Maximum Ratio Combiner |  | 
Selection Combiner |  | 
Introduction | Modeling (CoLo) | Modeling (Dist) |Outage Performance | Receiver Design
SIR: Signal-to-Interference Ratio

## Slide 19
Outage probability of a genie-aided non-linear combiner
SELECT BEST
Receiver algorithm | Outage probability
Post Detection Combining | 
Receiver algorithm | 
Post Detection Combining | 
Select antenna stream with best detection SIR
Receiver assumes knowledge of SIR at each antenna
Introduction | Modeling (CoLo) | Modeling (Dist) |Outage Performance | Receiver Design

## Slide 20
Derived expressions (‘Model’) match simulated outage (‘Sim’) for a variety of spatial dependence scenarios
PARAMETER VALUES | 
Common interferer density() (per unit area) | 
Excl. interferer density() (per unit area) | 
PARAMETER VALUES | 
Maximum ratio combining and selection combining receiver performance vs. (N=4)
Outage performance of different combiners vs. number of antennae (6)
Introduction | Modeling (CoLo) | Modeling (Dist) |Outage Performance | Receiver Design
(N)

## Slide 21
Using communication performance analysis, I design algorithms that outperform conventional receivers
Prior Work
Proposed Receiver Structures
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Receiver Type | Interference Model | Joint Statistics | Fading Channel
Filtering | Symmetric alpha stable [Gonzales98][Ambike94] | Independent | No
Sequence detection, Decision feedback | Gaussian Mixture [Blum00][Bhatia94] | Independent | No
Detection | Symmetric alpha stable[Rajan10] | Independent | Yes
Receiver Type | Interference Model | Joint Statistics | Fading Channel
Linear filtering | SAS | Independent/Isotropic | Yes
Non-linear filtering | SAS | Independent/Isotropic | Yes

## Slide 22
I investigate linear receivers in the presence of alpha stable interference
Linear receivers without channel knowledge
  Select antenna with strongest mean channel to interference power ratio
Optimal linear receivers with channel knowledge
Independent SAS interference
  Outage optimal
Isotropic SAS interference
Maximum ratio combining is outage optimal
Outage of optimal linear combiner in spatially independent interference (=1.3)
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
(N)

## Slide 23
I propose sub-optimal non-linear receivers for impulsive interference
‘Deviation’ in an antenna output is defined as
Proposed diversity combiners
  Hard-limiting combiner
  Soft-limiting combiner
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 24
Proposed diversity combiners exhibit better outage performance compared to conventional combiners
Parameter values | 
Pathloss coefficient () | 
Guard- zone radius () (Unit Distance) | 
Common interferer density() (per unit area) | 
Exclusive interferer density() (per unit area) | 
HL combiner parameter () | 
SL combiner parameter () | 
Parameter values | 
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
10x improvement in
outage probability

## Slide 25
Joint interference statistics across separate antennae can also improve cooperative reception strategies
System Model Performance-Cost tradeoff
A distant base-station transmits a signal to the destination receiver ( ) surrounded by interferers ( ) and cooperative receivers ( )
Which cooperative receiver should be selected to assist in signal reception?
Antenna Separation (Distance Units)
Outage Probability
Power Cost
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design

## Slide 26
Total cost is evaluated using a re-transmission based model
Optimal Antenna Separation
-Nearest Neighbor Selection
is the random variable describing
the location of the k-th nearest neighbor
Optimal cooperative antenna location
Cost per re-transmission
Expected re-transmissions
Optimal k-th nearest neighbor
Expected Cost of k-th re-transmission
Cooperative antenna power usage vs. separation. Power usage increases as () with 10mW fixed overhead and usage of 150mW at 50 distance units.
10% Outage probability per individual antenna.

## Slide 27
In conclusion, the contributions of my dissertation are
A framework for modeling multi-antenna interference
  Interference statistics are mix of spatial isotropy and spatial independence
Statistical modeling of multi-antenna interference
  Co-located antennae in networks without guard zones
  Two geographically separate antennae in networks with guard zones
Outage performance analysis of conventional receivers in networks without guard zones
  Accurate outage probability expressions inform receiver design
Design of receiver algorithms with improved performance in impulsive interference
  Order of magnitude reduction in outage probability compared to linear receivers
  80% reduction in power by using physically separate antennae

## Slide 28
Future work
Statistical Modeling
Non-Poisson distribution of interferer locations
>2 physically separate antennae in a field of interferers
Physically separate antennae in a centralized network
Temporal modeling of interference statistics with correlated fields of randomly distributed interferers
Performance Analysis
Performance analysis of multi-antenna wireless networks
Receiver Design
Closed form expressions and bounds on performance of non-linear receivers
Incorporate interference modeling into conventional relaying strategies

## Slide 29
Journal Papers
A. Chopra and B. L. Evans, ``Outage Probability for Diversity Combining in Interference-Limited Channels'', IEEE Transactions on Wireless Communications, submitted Sep. 14, 2011
A. Chopra and B. L. Evans, ``Joint Statistics of Radio Frequency Interference in Multi-Antenna Receivers'', IEEE Transactions on Signal Processing, accepted with minor mandatory changes.
A. Chopra and B. L. Evans, ``Design of Sparse Filters for Channel Shortening'', Journal of Signal Processing Systems, May 2011, 14 pages, DOI 10.1007/s11265-011-0591-0
Conference Papers
A. Chopra and B. L. Evans, ``Design of Sparse Filters for Channel Shortening'', Proc. IEEE Int. Conf. on Acoustics, Speech, and Signal Proc., Mar. 14-19, 2010, Dallas, Texas USA.
A. Chopra, K. Gulati, B. L. Evans, K. R. Tinsley, and C. Sreerama, ``Performance Bounds of MIMO Receivers in the Presence of Radio Frequency Interference'', Proc. IEEE Int. Conf. on Acoustics, Speech, and Signal Proc., Apr. 19-24, 2009, Taipei, Taiwan.
K. Gulati, A. Chopra, B. L. Evans, and K. R. Tinsley, ``Statistical Modeling of Co-Channel Interference'', Proc. IEEE Int. Global Communications Conf., Nov. 30-Dec. 4, 2009, Honolulu, Hawaii.
K. Gulati, A. Chopra, R. W. Heath, Jr., B. L. Evans, K. R. Tinsley, and X. E. Lin, ``MIMO Receiver Design in the Presence of Radio Frequency Interference'', Proc. IEEE Int. Global Communications Conf., Nov. 30-Dec. 4th, 2008, New Orleans, LA USA.
A. G. Olson, A. Chopra, Y. Mortazavi, I. C. Wong, and B. L. Evans, ``Real-Time MIMO Discrete Multitone Transceiver Testbed'', Proc. Asilomar Conf. on Signals, Systems, and Computers, Nov. 4-7, 2007, Pacific Grove, CA USA.
In preparation
A. Chopra and B. L. Evans, ``Joint Statistics of Interference Across Two Separate Antennae''

## Slide 30
References
RFI Modeling
D. Middleton, “Non-Gaussian noise models in signal processing for telecommunications: New methods and results for Class A and Class B noise models”, IEEE Trans. Info. Theory, vol. 45, no. 4, pp. 1129-1149, May 1999.
J. Ilow and D . Hatzinakos, “Analytic alpha-stable noise modeling in a Poisson field of interferers or scatterers”, IEEE Trans. on Signal Proc., vol. 46, no. 6, pp. 1601-1611, Jun. 1998.
E. S. Sousa, “Performance of a spread spectrum packet radio network link in a Poisson field of interferers,” IEEE Trans. on Info. Theory, vol. 38, no. 6, pp. 1743–1754, Nov. 1992.
X. Yang and A. Petropulu, “Co-channel interference modeling and analysis in a Poisson field of interferers in wireless communications,” IEEE Trans. on Signal Proc., vol. 51, no. 1, pp. 64–76, Jan. 2003.
Cisco visual networking index: Global mobile data traffic forecast update, 2010 - 2015. Technical report, Feb. 2011.
John P. Nolan. Multivariate stable densities and distribution functions: general and elliptical case. Deutsche Bundesbank’s Annual Fall Conference, 2005.

## Slide 31
Performance Analysis
Ping Gao and C. Tepedelenlioglu. Space-time coding over fading channels with impulsive noise. IEEE Transactions on Wireless Communications, 6(1):220–229, Jan. 2007.
A. Rajan and C. Tepedelenlioglu. Diversity combining over Rayleigh fading channels with symmetric alpha-stable noise. IEEE Transactions on Wireless Communications, 9(9):2968–2976, 2010.
S. Niranjayan and N. C. Beaulieu. The BER optimal linear rake receiver for signal detection in symmetric alpha-stable noise. IEEE Transactions on Communications, 57(12):3585–3588, 2009.
C. Tepedelenlioglu and Ping Gao. On diversity reception over fading channels with impulsive noise. IEEE Transactions on Vehicular Technology, 54(6):2037–2047, Nov. 2005.
G. A. Tsihrintzis and C. L. Nikias. Performance of optimum and suboptimum receivers in the presence of impulsive noise modeled as an alpha stable process. IEEE Transactions on Communications, 43(234):904–914, 1995.

## Slide 32
Receiver Design
A. Spaulding and D. Middleton, “Optimum Reception in an Impulsive Interference Environment-Part I: Coherent Detection”, IEEE Trans. Comm., vol. 25, no. 9, Sep. 1977
J.G. Gonzalez and G.R. Arce, “Optimality of the Myriad Filter in Practical Impulsive-Noise Environments”, IEEE Trans. on Signal Proc., vol. 49, no. 2, Feb 2001
S. Ambike, J. Ilow, and D. Hatzinakos, “Detection for binary transmission in a mixture of Gaussian noise and impulsive noise modelled as an alpha-stable process,” IEEE Signal Proc. Letters, vol. 1, pp. 55–57, Mar. 1994.
O. B. S. Ali, C. Cardinal, and F. Gagnon. Performance of optimum combining in a Poisson field of interferers and Rayleigh fading channels. IEEE Transactions on Wireless Communications, 9(8):2461–2467, 2010.
Andres Altieri, Leonardo Rey Vega, Cecilia G. Galarza, and Pablo Piantanida. Cooperative strategies for interference-limited wireless networks. In Proc. IEEE International Symposium on Information Theory, pages 1623–1627, 2011.
Y. Chen and R. S. Blum. Efficient algorithms for sequence detection in non-Gaussian noise with intersymbol interference. IEEE Transactions on Communications, 48(8):1249–1252, Aug. 2000.

## Slide 33
about me
Member of the Wireless Networking and Communications Group at The University of Texas at Austin since 2006.
Completed projects
Currently active projects
ADSL testbed (Oil & Gas) | 2 x 2 wired multicarrier communications testbed using PXI hardware, x86 processor, real-time operating system and LabVIEW
Spur modeling/mitigation (NI) | Detect and classify spurious signals; fixed and floating-point algorithms to mitigate spurs
Interference modeling and mitigation (Intel) | Statistical models of interference; receiver algorithms to mitigate interference; MATLAB toolbox
Impulsive noise mitigation in OFDM (NI) | Non-parametric interference mitigiation for wireless OFDM receivers using PXI hardware, FPGAs, and LabVIEW
Powerline communications (TI, Freescale, SRC) | Modeling and mitigating impulsive noise; building multichannel multicarrier communications testbed using PXI hardware, x86 processor, real-time operating system, LabVIEW

## Slide 34
Interference mitigation has been an active area of research over the past decade
INTERFERENCE MITIGATION STRATEGY | LIMITATIONS
Hardware design Receiver shielding | Does not mitigate interference from devices using same spectrum
Network planning Resource allocation Basestation coordination Partial frequency re-use | Requires user coordination Slow updates
Receiver algorithms Interference cancellation Interference alignment Statistical interference mitigation | Require user coordination and channel state information Statistical methods require accurate interference models
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
Notes: Base station coord. , statistical receiver methods..

## Slide 35
Interference Mitigation Techniques

## Slide 36
Interference alignment

## Slide 37
Interference cancellation
J. G. Andrews, ”Interference Cancellation for Cellular Systems: A Contemporary Overview”, IEEE Wireless Communications Magazine, Vol. 12, No. 2, pp. 19-29, April 2005

## Slide 38
Femtocell Networks
V. Chandrasekhar, J. G. Andrews and A. Gatherer, "Femtocell Networks: a Survey", IEEE Communications Magazine, Vol. 46, No. 9, pp. 59-67, September 2008

## Slide 39
Spectrum Occupied by Typical Standards
39
Standard | Carrier (GHz) | Wireless Networking | Interfering Clocks and Busses
Bluetooth | 2.4 | Personal Area Network | Gigabit Ethernet, PCI Express Bus, LCD clock harmonics
IEEE 802. 11 b/g/n | 2.4 | Wireless LAN (Wi-Fi) | Gigabit Ethernet, PCI Express Bus, LCD clock harmonics
IEEE 802.16e | 2.5–2.69 3.3–3.8 5.725–5.85 | Mobile Broadband (Wi-Max) | PCI Express Bus, LCD clock harmonics
IEEE 802.11a | 5.2 | Wireless LAN (Wi-Fi) | PCI Express Bus, LCD clock harmonics

## Slide 40
Impact of LCD on 802.11g
Pixel clock 65 MHz
LCD Interferers and 802.11g center frequencies
40
LCD Interferers | 802.11g Channel | Center Frequency | Difference of Interference from Center Frequencies | Impact
2.410 GHz | Channel 1 | 2.412 GHz | ~2 MHz | Significant
2.442 GHz | Channel 7 | 2.442 GHz | ~0 MHz | Severe
2.475 GHz | Channel 11 | 2.462 GHz | ~13 MHz | Just outside Ch. 11. Impact minor

## Slide 41
Measured Data
25 radiated computer platform RFI data sets from Intel each with 50,000 samples taken at 100 MSPS

## Slide 42: Single Antenna RFI Models
Model Name | Key Features
Symmetric alpha stable [Sousa,1992] [Ilow & Hatzinakos,1998] | Models wireless ad hoc networks, computational platform noise No closed form distribution function (except ) Unbounded variance (generally )
Middleton Class A [Middleton, 1979, 1999] | Models wireless networks with guard zones and interferers in a finite area around receiver [Gulati, Chopra, Evans & Tinsley, 2009] Model incorporates thermal noise present at receiver Special case of the Gaussian mixture distribution
Gaussian mixture distribution | Models wireless networks with hotspots, femtocell networks [Gulati, Evans, Andrews & Tinsley, 2009]
Model Name | Key Features
Symmetric alpha stable [Sousa,1992] [Ilow & Hatzinakos,1998] | 
Middleton Class A [Middleton, 1979, 1999] | Models wireless networks with guard zones and interferers in a finite area around receiver [Gulati, Chopra, Evans & Tinsley, 2009] Model incorporates thermal noise present at receiver Special case of the Gaussian mixture distribution
Gaussian mixture distribution | Models wireless networks with hotspots, femtocell networks [Gulati, Evans, Andrews & Tinsley, 2009]
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 43: Single Antenna RFI Models
Symmetric alpha stable distribution [Sousa,1992]
  Characteristic function:
Middleton Class A distribution [Middleton, 1977, 1999] Amplitude distribution:
Gaussian mixture distribution
  Amplitude distribution:
Parameter | Range
Parameter | Range
Parameter | Range
Parameter | Range
Parameter | Range
Parameter | Range
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 44: Two-Antenna RFI Generation Model
Key model characteristics
  Correlated interferer field observed by receive antennas
  Inter-antenna distances insignificant compared to antenna-interferer distances
Sum interference in two-antenna receiver
  denotes set of interferers observed by both antennas (intensity
  denote interferers observed at antenna and respectively (intensity
INTERFERER TO ANTENNA 2
INTERFERER TO ANTENNA 1
COMMON INTERFERER
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 45: Multi-Antenna RFI Generation Model
Spatially correlated interferer fields in -antenna receiver
  i.i.d. interferer sets
  Sum interference from sets at each antenna
Proposed model extension to -antenna receiver
  Two categories of interferers
  Sum interference from sets at each antenna
Sum interference in -antenna receiver
  is set of interferers common to all receive antennas (intensity )
  is set of interferers observed by receive antenna (intensity )
Emissions lead to RFI in all antennas | Emissions lead to RFI in one antenna
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 46: Existing Models of Multi-Antenna RFI
Model Name | Key Features
Symmetric alpha stable (isotropic) [Ilow & Hatzinakos,1998] | Models spatially dependent RFI generated from single set of interferers observed by all receive antennas No closed form distribution function (except ) Unbounded variance (generally )
Multidimensional Class A Models [Delaney, 1995] | Multidimensional extension of Middleton class A distribution, no statistical derivation Different statistical distributions required to reflect spatial dependence/independence in RFI
Bivariate class A distribution [McDonald & Blum, 1997] | Approximate distribution based on statistical-physical derivation Models RFI observed at two receive antennas only Spatially dependent RFI
Temporal second-order alpha stable model [Yang & Petropulu, 2003] | Models second-order temporal statistics of co-channel interference Assumes temporal correlation in interferer fields
Model Name | Key Features
Symmetric alpha stable (isotropic) [Ilow & Hatzinakos,1998] | 
 | Multidimensional extension of Middleton class A distribution, no statistical derivation Different statistical distributions required to reflect spatial dependence/independence in RFI
Bivariate class A distribution [McDonald & Blum, 1997] | Approximate distribution based on statistical-physical derivation Models RFI observed at two receive antennas only Spatially dependent RFI
Temporal second-order alpha stable model [Yang & Petropulu, 2003] | Models second-order temporal statistics of co-channel interference Assumes temporal correlation in interferer fields
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 47: Statistical Models for Multi-Antenna RFI
Extension type | Amplitude distribution
Spatially independent | 
Isotropic | 
Multidimensional symmetric alpha stable distribution [Ilow & Hatzinakos, 1998]
Multidimensional Class A distribution [Delaney, 1995]
Extension type | Characteristic function
Spatially independent | 
Isotropic | 
Extension type | Characteristic function
Spatially independent | 
Isotropic | 
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 48: Statistical Models for Multi Antenna RFI
Physical model of RFI for 2 antenna systems
  Amplitude distribution [McDonald & Blum, 1997]
Parameter | Range
Parameter | Range
Introduction |RFI Modeling | Performance Analysis | Receiver Design | Summary

## Slide 49
KL divergence

## Slide 50
Interference in separate antennae

## Slide 51: Homogeneous Spatial Poisson Point Process

## Slide 52: Poisson Field of Interferers
Applied to wireless ad hoc networks, cellular networks
Closed Form Amplitude Distribution |  |  | 
Model | Interference | Region | Key Prior Work
Symmetric Alpha Stable | Spatial | Entire plane | [Sousa, 1992] [Ilow & Hatzinakos, 1998] [Yang & Petropulu, 2003]
Middleton Class A | Spatio-temporal | Finite area | [Middleton, 1977, 1999]
Other Interference Statistics – closed form amplitude distribution not derived |  |  | 
Statistics | Interference | Region | Key Prior Work
Moments | Spatial | Finite area | [Salbaroli & Zanella, 2009]
Characteristic Function | Spatial | Finite area | [Win, Pinto & Shepp,2009]
Notes: Actions:
Should mention Shot-Noise related work.
Questions:

## Slide 53
Isotropic SAS

## Slide 54
Independent SAS

## Slide 55
Mixture SAS

## Slide 56: Threshold selection with

## Slide 57: Threshold selection with

## Slide 58: Parameter Estimators for Alpha Stable
58
Return

## Slide 59: Gaussian Mixture vs. Alpha Stable
Gaussian Mixture vs. Symmetric Alpha Stable
 | Gaussian Mixture | Symmetric Alpha Stable
Modeling | Interferers distributed with Guard zone around receiver (actual or virtual due to PL) | Interferers distributed over entire plane
Pathloss Function | With GZ: singular / non-singular Entire plane: non-singular | Singular form
Thermal Noise | Easily extended (sum is Gaussian mixture) | Not easily extended (sum is Middleton Class B)
Outliers | Easily extended to include outliers | Difficult to include outliers

## Slide 60: RFI Mitigation in SISO Systems
60
Computer Platform Noise Modelling | Evaluate fit of measured RFI data to noise models Middleton Class A model Symmetric Alpha Stable
Parameter Estimation | Evaluate estimation accuracy vs complexity tradeoffs
Filtering / Detection | Evaluate communication performance vs complexity tradeoffs Middleton Class A: Correlation receiver, Wiener filtering, and Bayesian detector Symmetric Alpha Stable: Myriad filtering, hole punching, and Bayesian detector
Mitigation of computational platform noise in single carrier, single antenna systems [Nassar, Gulati, DeYoung, Evans & Tinsley, ICASSP 2008, JSPS 2009]
Return

## Slide 61: Filtering and Detection
61
Pulse
Shaping
Pre-Filtering
Matched Filter
Detection Rule
Impulsive Noise
Middleton Class A noise
Symmetric Alpha Stable noise
Filtering
Wiener Filtering (Linear)
Detection
Correlation Receiver (Linear)
Bayesian Detector [Spaulding & Middleton, 1977]
Small Signal Approximation to Bayesian detector [Spaulding & Middleton, 1977]
Filtering
Myriad Filtering
  Optimal Myriad [Gonzalez & Arce, 2001]
  Selection Myriad
Hole Punching [Ambike et al., 1994]
Detection
Correlation Receiver (Linear)
MAP approximation [Kuruoglu, 1998]
  Assumption
  Multiple samples of the received signal are available
  N Path Diversity [Miller, 1972]
  Oversampling by N [Middleton, 1977]
Return

## Slide 62: Results: Class A Detection
62
Pulse shape Raised cosine 10 samples per symbol 10 symbols per pulse | Channel A = 0.35  = 0.5 × 10-3 Memoryless
Method | Comp. Complexity | Detection Perform.
Correl. | Low | Low
Wiener | Medium | Low
Bayesian S.S. Approx. | Medium | High
Bayesian | High | High
Communication Performance
Binary Phase Shift Keying

## Slide 63: Results: Alpha Stable Detection
63
Use dispersion parameter g in place of noise variance to generalize SNR
Method | Comp. Complexity | Detection Perform.
Hole Punching | Low | Medium
Selection Myriad | Low | Medium
MAP Approx. | Medium | High
Optimal Myriad | High | Medium
Communication Performance
Same transmitter settings as previous slide
Return

## Slide 64: RFI Mitigation in 2x2 MIMO Systems
64
RFI Modeling | Evaluated fit of measured RFI data to the bivariate Middleton Class A model [McDonald & Blum, 1997] Includes noise correlation between two antennas
Parameter Estimation | Derived parameter estimation algorithm based on the method of moments (sixth order moments)
Performance Analysis | Demonstrated communication performance degradation of conventional receivers in presence of RFI Bounds on communication performance [Chopra , Gulati, Evans, Tinsley, and Sreerama, ICASSP 2009]
Receiver Design | Derived Maximum Likelihood (ML) receiver Derived two sub-optimal ML receivers with reduced complexity
2 x 2 MIMO receiver design in the presence of RFI [Gulati, Chopra, Heath, Evans, Tinsley & Lin, Globecom 2008]
Return

## Slide 65: Bivariate Middleton Class A Model
Joint spatial distribution
Parameter | Description | Typical Range
 | Overlap Index. Product of average number of emissions per second and mean duration of typical emission | 
 | Ratio of Gaussian to non-Gaussian component intensity at each of the two antennas | 
 | Correlation coefficient between antenna observations | 
Return

## Slide 67: Results on Measured RFI Data
50,000 baseband noise samples represent broadband interference
Estimated Parameters |  | 
Bivariate Middleton Class A |  | 
Overlap Index (A) | 0.313 | 2D- KL Divergence 1.004
Gaussian Factor (G1) | 0.105 | 
Gaussian Factor (G2) | 0.101 | 
Correlation (k) | -0.085 | 
Bivariate Gaussian |  | 
Mean (µ) | 0 | 2D- KL Divergence 1.6682
Variance (s1) | 1 | 
Variance (s2) | 1 | 
Correlation (k) | -0.085 | 
Marginal PDFs of measured data compared with estimated model densities

## Slide 68: System Model
2 x 2 MIMO System
Maximum Likelihood (ML) receiver
Log-likelihood function
Sub-optimal ML Receivers
approximate
Return

## Slide 69: Sub-Optimal ML Receivers
69
Two-piece linear approximation
Four-piece linear approximation
chosen to minimize
Approximation of
Return

## Slide 70: Results: Performance Degradation
Performance degradation in receivers designed assuming additive Gaussian noise in the presence of RFI
Simulation Parameters
4-QAM for Spatial Multiplexing (SM) transmission mode
16-QAM for Alamouti transmission strategy
Noise Parameters: A = 0.1, 1= 0.01, 2= 0.1, k = 0.4
Severe degradation in communication performance in high-SNR regimes
Return

## Slide 71: Results: RFI Mitigation in 2 x 2 MIMO
71
A | Noise Characteristic | Improve-ment
0.01 | Highly Impulsive | ~15 dB
0.1 | Moderately Impulsive | ~8 dB
1 | Nearly Gaussian | ~0.5 dB
Improvement in communication performance over conventional Gaussian ML receiver at symbol error rate of 10-2
Communication Performance (A = 0.1, 1= 0.01, 2= 0.1, k = 0.4)
Return

## Slide 72: Results: RFI Mitigation in 2 x 2 MIMO
72
Complexity Analysis
Receiver | Quadratic Forms | Exponential | Comparisons
Gaussian ML | M2 | 0 | 0
Optimal ML | 2M2 | 2M2 | 0
Sub-optimal ML (Four-Piece) | 2M2 | 0 | 2M2
Sub-optimal ML (Two-Piece) | 2M2 | 0 | M2
Complexity Analysis for decoding M-level QAM modulated signal
Communication Performance (A = 0.1, 1= 0.01, 2= 0.1, k = 0.4)
Return

## Slide 73
Wireless communication systems are increasingly using multiple antennae
Benefits
Multiplexing | Diversity | Interference Removal
Multiple data streams transmitted simultaneously | Antennae with strong channels can compensate for antennae with weak channels | Interference cancellation and alignment
Wireless Channel
Transmit Antennae
Receive Antennae
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
101110
11
10
10

## Slide 74
Interference statistics in networks without guard zones are a mix of isotropic and i.i.d. alpha stable …
Joint characteristic function
… and interference statistics in networks with guard zones are a mix of isotropic and i.i.d. Middleton Class A
Joint characteristic function
Introduction | Modeling (CoLo) | Modeling (Dist) | Outage Performance | Receiver Design
1
1
1
1
2
2
2
3
3
A 3-antenna receiver within a Poisson field of interferers
3