## Slide 1
Faris B. Mismar
IMPROVING NEXT-GENERATION WIRELESS NETWORK PERFORMANCE AND RELIABILITY WITH DEEP LEARNING
The University of Texas at Austin
Embedded Signal Processing Laboratory
Wireless Networking & Communications Group
November 22, 2019
Ph.D. Defense

## Slide 2: VISION FOR 5G COMMUNICATIONS
BACKGROUND
[https://www.qorvo.com/design-hub/blog/getting-to-5g-comparing-4g-and-5g-system-requirements]
NETWORK ANALYTICS
“Network Data Analytics Function”
(3gpp)

## Slide 3: VISION FOR INTELLIGENT WIRELESS NETWORK
BACKGROUND
[https://www.qualcomm.com/media/documents/files/making-ai-ubiquitous.pdf]
Hybrid approach to unleash next-generation wireless “network intelligence”
Central location to coherently train models
Trained models at the network edge
Sub-6 GHz
mmWave
Base Station (BS)
User Equipment (UE)
Notes: One of the visions

## Slide 4: MOTIVATION: DEEP LEARNING IN COMMUNICATIONS
BACKGROUND
Incremental changes in radio resource management (RRM) algorithms
Desire for fully autonomous self-organizing networks (SON)
industry standards still prefer “legacy” algorithms despite successive evolutions
operators are under constant pressure to reduce operational expenditure without impacting performance
Long training times and high implementation complexity pose significant challenges
[3gpp15] & [3gpp18]
[Zappone19]
Absence of accurate mathematical formulations
data-driven approaches using ray-tracing datasets or field-measurements
[Zappone19]

## Slide 5: CONTRIBUTIONS
How to improve next-generation wireless networks system performance?
CONTRIBUTIONS
disrupt the legacy industry standards to boost reliability and eliminate performance bottlenecks
Predictive Band Switching
Intelligent Coordinated Multipoint
Beamforming, Power Control and Interference Coordination
Contribution 2
Contribution 3
Contribution 1
PHY perspective
RRM perspective
Improve user rates
RRM: radio resource management layer
PHY: physical layer
Contributions are on the downlink (BS to UE)
BS: Base station UE: user equipment.

## Slide 6: JOINT BEAMFORMING, POWER CONTROL, AND INTERFERENCE COORDINATION
Related publications:
[1]. F. B. Mismar, B. L. Evans and A. Alkhateeb, “Deep Reinforcement Learning for 5G Networks: Joint Beamforming, Power Control, and Interference Coordination,” IEEE Transactions on Communications, submitted Jun. 28, 2019 and resubmitted Sep. 21, 2019 and Nov. 8, 2019.
[2]. F. B. Mismar and B. L. Evans, “Q-Learning Algorithm for VoLTE Closed-Loop Power Control in Indoor Small Cells,” Proceedings of the 52nd Annual Asilomar Conference on Signals, Systems, and Computers, Oct. 2018.
Contribution 1
Discussed in the PhD Qualifying Exam and Included in the PhD Dissertation

## Slide 7: BACKGROUND
User served by a base station receives interference from neighboring base station
Base station serving the user causes interference to other users
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
Problem
Parameters
Goal
Approach
Maximize the signal to interference plus noise ratio (SINR) from serving base station to user
Beamforming (BF) to create a virtual sense of a user-specific channel for data
Power Control (PC) to control the transmit power of the serving BS towards a user
Interference Coordination (IC) to control the transmit power of the neighboring BSs
User spatial coordinates
Perform binary encoding of BF, PC, and IC actions to enable joint actions
If SINR of all users improve, then reward actions. This resolves the race condition
Compare proposed solution with optimal solution
Notes: Let’s start with the background of the first contribution.

## Slide 8: SYSTEM MODEL
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
Multi-user downlink system
Multi-cell environment with single-antenna users
L total dual-band base stations
Uniform linear array (ULA) antennas (M)
Power control for all users
Codebook analog beamforming for mmWave data
More power control commands for sub-6 GHz voice
Narrow-band geometric channel model
array response vector
angle of departure
channel path p gain
Beamforming vector
[Alkhateeb14]
suitable for both sub-6 and mmWave propagation
smaller number of paths at mmWave (sparse)
Signal model for the user served by the -th BS:
Gaussian noise
Inter-cellular interference
Received SINR for the user served by the -th BS:
path loss for user served by BS l in area of BS b

## Slide 9: MOTIVATION AND PROBLEM FORMULATION
Improve SINR through joint power control, interference coordination, beam selection
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
How can we reduce the complexity?
Baseline solution for voice is obtained from fixed power allocation with adaptive coding
Optimal solution (upper bound) for data is found through a brute force over all
  beam patterns
  power commands for the BSs
Run-time complexity of for M antennas and L base stations.
Set of power (and interference coordination) commands
Set of beamforming vectors (where applicable)
Target SINR value
beamforming vector of the j-th user
received SINR of the j-th user

## Slide 10: SOLUTION
Deep Reinforcement Learning
Create an environment from the system model
Create a joint reward
Reward the agent for every time the SINR improves.
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
Use deep Q-network (DQN) as an estimator for state-action value function
  Greedy policy
  Train the DQN using minibatch samples to minimize the loss function:
state-action value function
DQN vectorized weights
estimated state-action value function
discount rate
Bearer selector
reward
Can an 𝜺-greedy policy do better?

## Slide 11: SOLUTION (L = 2)
Joint beamforming, power control, and interference coordination (JB-PCIC) encoding
Reward function
bearer selector
if any constraint in problem formulation becomes inactive.
if the target SINR is achieved.
0: step down beamforming codebook
1: step up beamforming codebook
enables up to 16 simultaneous actions for voice and 16 for data
voice
data
Bitwise AND, masking, and shifting
States
A total of 8 states
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
string of bits in a register
0
3
➔
Bearer selector
Notes: Here, I propose a compact way to jointly perform BF, PC, and IC, using a string of bits and binary logic.

## Slide 12: SIMULATION
JB-PCIC algorithm achieves upper bound on performance but without exhaustive search in action space
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
Deep Reinforcement Learning Hyperparameters
Communication System Parameters
Notes: Proposed RL algorithm outperforms industry standards. However, closer to cell center, algorithms perform similarly.
Tabular learning uses O(SA) = 16 * 8. Deep learning uses 16 * 24^2. Therefore, tabular achieves a speedup of 72x.
Tabular is guaranteed to converge. Qlearning is unstable or will diverge if nonlinear function approximator is used

## Slide 13: SUMMARY
Optimize users’ received SINR
Voice bearers
Data bearers
CONTRIBUTION 1: JOINT BEAMFORMING AND POWER CONTROL
Perform power control for the serving cell
Coordinate transmit power for the other cells
Voice uses adaptive coding
Perform power control for the serving cell
Coordinate transmit power for the other cells
Exponential in number of base stations
Uses brute force
Uses deep reinforcement learning
Encoding to facilitate joint actions
Avoids exhaustive search in the action space
Proposed
Optimal

## Slide 14: IMPROVED DOWNLINK COORDINATED MULTIPOINT PERFORMANCE
Contribution 2
Related publications:
[1]. F. B. Mismar and B. L. Evans, “Deep Learning in Downlink Coordinated Multipoint in New Radio Heterogeneous Network,” IEEE Wireless Communications Letters, vol. 8, no. 4, pp. 1040-1043, Aug. 2019.
[2]. F. B. Mismar and B. L. Evans, “Machine Learning in Downlink Coordinated Multi-point in Heterogeneous Networks,” Technical Report, Feb. 2019. [Online]. arXiv:1608.08306.

## Slide 15: BACKGROUND
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
Industry implementations trigger coordinated multipoint (CoMP) based on user SINR
This yields low user throughput
Problem
Parameters
Goal
Approach
Develop triggering function to improve the user throughput
Block Error Rate (BLER) target for codeword reception error
Channel State Information (CSI) to help derive transmission rank
Train a classifier to learn the relationship between the reported measurements and the BLER
If a user is predicted to have a BLER lower than the target, configure rank-2 transmission
Compare with SINR-based trigger
Notes: Base stations work independently to deliver data to the users. However, using low latency backhaul to small cells nearby, introducing a coordinated transmission can help further improve the user throughputs.
Explain why lower throughput: it is in the log(). Why SINR: it is standard-driven (based on CQI).

## Slide 16: SYSTEM MODEL
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
Multi-user downlink system
Multi-cell environment with multiple-antenna users
Small cells scattered in the service area
Macro cells and small cells can form a distributed MIMO channel with transmit antennas
Zero-Forcing (ZF) receiver at the user end
distributed MIMO channel (both large- and small-scale gain)
Gaussian noise
The received SNR for the -th user at the -th antenna
[Tse05]
Signal model for the -th user (narrowband):
ZF receiver enhanced noise power
energy per symbol
number of receive antennas
The received power for the -th user at the -th antenna:
The received reference symbol power (RSRP) for the -th user:
UE received power measured at the first antenna
number of subcarriers in a resource block
The codeword block error rate (BLER) for the -th user:
number of resource blocks
BLER for the codeword transmitted to the j-th antenna
Notes: Since energy is sampled every one second, it is equal to power. Hence P_BS = E_s.
BLER increases as the number of streams increase. BLER per stream also increases at low SNR.

## Slide 17: MOTIVATION AND PROBLEM FORMULATION
Industry approach is to use the users’ reported CSI to determine proper transmission rank
BLER increases as the transmission rank increases
  Throughput decreases as BLER increases
  Throughput increases as transmission rank increases, assuming decorrelated transmission streams
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
bandwidth
effective rate of the i-th UE
How to optimize this group of conflicting variables?
Can a dynamic data-driven approach help?
Answer: main idea:
  When the BLER is low, try to increase the transmission rank, if the second spatially decorrelated stream (i.e., rank-2) is possible.
  Otherwise, default to a rank-1 transmission.
Users report a “quantized” SNR value known as the channel quality indicator (CQI)
CSI: Channel State Information
BLER: Block Error Rate
Notes: The pre-log terms have bigger gains

## Slide 18: SOLUTION
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
Simplify the problem to rank-2 MIMO channel and build a binary classifier
For the binary classifier:
  Labels are a function of the BLER meeting the standard threshold
  Use standard-compliant CSI as learning features that help define the transmission rank
Invalidate the learned model after the channel coherence time passes.
Coordinated Multipoint (CoMP) trigger function:
CoMP trigger (MIMO), based on the majority of votes
a frequency function: percentage of y=0 and y=1 samples (i.e., an empirical probability):
Standards-Compliant
a machine learning function
Proposed
uses SINR as a measure of decorrelation
CSI reported by the i-th user
found from either standards-compliant or proposed CoMP “votes”

## Slide 19: SOLUTION
Construct the surrogate function from:
Train classifiers to minimize loss objective
Define the classification label based on the BLER being within target
 | Parameter | Type | Description
 | Bias term | Float | Equal to unity
 | CSI-RSRP | Float | Narrowband received power
 | CQI | Integer | Wideband received SNR on the first antenna (linear)
 | Rank | Integer | Number of received streams j
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
  fully connected deep neural network (DNN)
  support vector machine (SVM)
binary cross-entropy for DNN
hinge loss and regularization for SVM
hyperplane weights
The i-th support vector
Notes: Why not hinge loss? Hinge loss maximizes the decision boundary, cross-entropy maximizes the likelihood of the estimate.

## Slide 20: SIMULATION
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
Because CoMP decision is an “imbalanced” classification, DNN does better
CoMP: Coordinated Multipoint, DNN: Deep Neural Network, PRB: Physical Resource Block, SVM: Support Vector Machine.

## Slide 21: SUMMARY
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
More features and more complicated models lead to better performance
Optimize users’ achievable rate
Achievable rate depends on a group of features, some of which have opposing effects on the rate.
The use of a data-driven approach to find an improved achievable rate is possible.
Higher transmission rank does not always lead to better achievable rates.
Dynamic
SVM
Static
Triggers rank-2 based on reported SINR (absolute cutoff).
Triggers rank-2 based on a surrogate function based on deep learning.
The surrogate function is relearned every time the channel coherence time passes.
DNN

## Slide 22: DEEP LEARNING PREDICTIVE BAND SWITCHING IN WIRELESS NETWORKS
Contribution 3
Related publications:
[1] F. B. Mismar, A. AlAmmouri, A. Alkhateeb, J. G. Andrews, and B. L. Evans, “Deep Learning Predictive Band Switching in Wireless Networks,” IEEE Transactions on Wireless Communications, submitted Oct. 2, 2019.
[2] F. B. Mismar and B. L. Evans, “Partially Blind Handovers for mmWave New Radio Aided by Sub-6 GHz LTE Signaling,” Proceedings of IEEE International Conference on Communications Workshops, May 2018.
Discussed in the PhD Qualifying Exam and Included in the PhD Dissertation

## Slide 23: BACKGROUND
Users want to switch to a different frequency band if they expect to get higher throughput
Switching between frequency bands requires a “measurement gap” which reduces user throughput
Problem
Parameters
Goal
Approach
Improve user throughput by exploiting the spatial correlation to eliminate the measurement gap
Band switch request threshold which defines the rate below which UE requests a band switch
Band switch grant threshold which defines the rate above which the UE request is granted
Percentage of users in sub-6 GHz or mmWave vs total users
User spatial coordinates
Employ a data-driven approach using a ray-tracing dataset
Use deep learning to rank the downlink channel quality based on the users’ coordinates
Grant a band switch if predicted to improve the user throughput (no need for the gap)
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
Notes: I shift now from PHY to RRM.
Explain what a measurement gap is

## Slide 24: SYSTEM MODEL
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
Multi-user downlink system
Single-cell with multiple transmit antennas
Sub-6 GHz and mmWave bands (28 GHz)
Analog beamforming using DFT-based codebook
beamforming precoder
transmit power and large scale channel gain
Gaussian noise
The received SINR for the -th user at the -th frequency band
[Tse05]
Signal model for the -th user at the -th frequency band:
channel vector
SINR-optimal beamforming precoder
noise power
The received instantaneous rate for the -th user at the -th frequency band:
received SINR
bandwidth
channel coherence time
band switching overhead
beam training time
The received effective achievable rate for the -th user at the -th frequency band:
Here, is the band switching algorithm.
Notes: Since energy is sampled every one second, it is equal to power. Hence P_BS = E_s

## Slide 25: MOTIVATION AND PROBLEM FORMULATION
Next-generation wireless networks will use more frequency bands.
The band selection problem becomes more complicated:
  How does user choose a band to improve their rate?
Problem:
  Measurement gap reduces users’ effective achievable rates
  Blindly switching user eliminates need for gap but risks rates
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
Data-driven approach to eliminate the “measurement gap”
Solution:
  Main idea: rank bands based on their quality
  Grant switch to band with the highest rank if requested.
[3gpp18]
Legacy
Blind
Notes: Is ranking quality mathematically intractable/. Why?

## Slide 26: SOLUTION
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
Optimal solution (upper bound)
Proposed solution
  Exploit the spatial correlation between frequency bands based on the location of the user
  Define the band switch request and the band switch grant decision as follows:
  Train a machine learning algorithm using the following features
 | Parameter | Type | Description
 | Bias term | Integer | Equal to unity
 | Effective rate at sub-6 | Float | Based on (2) with j = sub-6
 | Effective rate at mmWave | Float | Based on (2) with j = mmWave
 | Source technology | Boolean | (1 = for sub-6 and 0 for mmWave)
 | Coordinates | Float | The latitude, longitude, and height of the user (from the BS)
 | Band switch requested | Boolean | Did UE request band switch?
 | Band switch decision | Boolean | Was this requested switch granted?
Use DeepMIMO ray-tracing dataset and engineer more features
[Alkhateeb19]
band switching threshold
estimated instantaneous rate based on other users

## Slide 27: SIMULATION
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
Scenarios
Confusion Matrix
DNN Confusion Matrix (Scenarios A, B, and C)
XGBoost Confusion Matrix (Scenarios A, B, and C)
Scenario | Users at Start
A | 100% sub-6 GHz
B | 100% mmWave
C | 70% sub-6 GHz and 30% mmWave
DNN requires a run-time of , while XGBoost requires a run-time of .
DNN depth
DNN width
Number of rows in the feature matrix
DNN outperforms XGBoost in receiver operator characteristic area and classification accuracy.
Parameters (DNN: deep neural networks, XGBoost: Extreme Gradient Boosting)

## Slide 28: SIMULATION
Impact of the band switching threshold on the performance
Higher band switching thresholds cause the legacy approach performance to do worse.
Higher band switching thresholds enable my proposed algorithm to do even better
Legacy approach performs better than blind in low throughput regime.
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
absence of measurement gap in optimal
… and near perfect DNN classification decisions
Scenario A: 100% users sub-6 GHz
Scenario B: 100% users mmWave
Scenario C: 30%-70% users

## Slide 29: SUMMARY
CONTRIBUTION 3: DEEP LEARNING PREDICTIVE BAND SWITCHING
I disrupt the need to use a measurement gap in band switching
Optimize users’ achievable rate
Band switching grows in importance with successive evolutions of wireless technology
The use of a data-driven approach to rank channels by their estimated quality is possible.
Using measurement gaps for the band switching procedure is a “performance overkill.”
Proposed
XGBoost
Industry
Use a gap to measure the candidate frequency band.
DNN
Blind
Legacy
Blindly switch to a different band.
Does not require a measurement gap.
Exploits the spatial and spectral correlation of frequency bands at a given location.
  Predicts the quality and ranks the bands.

## Slide 30: DISSERTATION SUMMARY AND CONCLUSION
PHY Layer Perspective
Next-generation wireless networks will require intelligent predictive and prescriptive abilities
  boost reliability and eliminate performance bottlenecks
  disrupt reactive legacy standards
CONCLUSION
Intelligent Coordinated Multipoint
Beamforming, Power Control and Interference Coordination
RRM Layer Perspective
Predictive Band Switching

## Slide 31: FUTURE WORK IN DEEP LEARNING FOR COMMUNICATIONS
FUTURE WORK
Optimal hybrid beamforming
Generalized multi-band predictive handoff
I used simple DFT-based analog beamforming, but digital beamforming generates more patterns
at mmWave, a disjoint solution exists, but may not be optimal.
Exploit powers of two in the number of antennas
Introduce mobility over multiple base stations and build a multi-class classifier
Improved Cell-Free Massive MIMO
Use coordinated BS capabilities with massive MIMO to improve joint-beamforming capabilities
Notes: Here, propose the following ideas for future work
This is the last slide.

## Slide 32: PUBLICATIONS
Faris B. Mismar, Ahmad AlAmmouri, Ahmed Alkhateeb, Jeffrey G. Andrews, and Brian L. Evans, “Predictive Band Switching in Wireless Networks,” IEEE Transactions on Wireless Communications (submitted).
Faris B. Mismar, Brian L. Evans, and Ahmed Alkhateeb, “Deep Reinforcement Learning for 5G Networks: Joint Beamforming, Power Control, and Interference Coordination,” IEEE Transactions on Communications (submitted).
Faris B. Mismar, Jinseok Choi, and Brian L. Evans, “A Framework for Automated Cellular Network Tuning with Reinforcement Learning,” IEEE Transactions on Communications, vol. 67, no. 10, pp. 7152-7167, Oct. 2019.
Faris B. Mismar and Brian L. Evans, “Deep Learning in Downlink Coordinated Multipoint in New Radio Heterogeneous Networks,” IEEE Wireless Communications Letters, vol. 8, no. 4, pp. 1040-1043, Aug. 2019.
PUBLICATIONS
Journal articles
Conference papers
Faris B. Mismar and Brian L. Evans, “Deep Q-Learning for Self-Organizing Networks Fault Management and Radio Performance Improvement,” Proceedings of the 52nd Annual Asilomar Conference on Signals, Systems, and Computers, Oct. 2018.
Faris B. Mismar and Brian L. Evans, “Q-Learning Algorithm for VoLTE Closed-Loop Power Control in Indoor Small Cells,” Proceedings of the 52nd Annual Asilomar Conference on Signals, Systems, and Computers, Oct. 2018.
Faris B. Mismar and Brian L. Evans, “Partially Blind Handovers for mmWave New Radio Aided by Sub-6 GHz LTE Signaling,” Proceedings of IEEE International Conference on Communications Workshops, May 2018.
Notes: Thank you!

## Slide 33: SOFTWARE RELEASES
Faris B. Mismar and Brian L. Evans, “Band Switching with Deep Learning,” Python 3 code to accompany a paper entitled “Predictive Band Switching in Wireless Networks,” Version 1.0 (Sep. 28, 2019). [Online]. Available: https://github.com/farismismar/Bandswitch-DeepMIMO Builds on top of the 3.5 GHz and 28 GHz ray tracing dataset from ASU.
Faris B. Mismar and Brian L. Evans, “Deep Reinforcement Learning for 5G Networks: Joint Beamforming, Power Control, and Interference Coordination,” Python 3 code to accompany a paper entitled “Deep Reinforcement Learning for 5G Networks: Joint Beamforming, Power Control, and Interference Coordination,” Version 2.0 (Nov. 6, 2019). [Online]. Available: https://github.com/farismismar/Deep-Reinforcement-Learning-for-5G-Networks
Faris B. Mismar and Brian L. Evans, “Deep Q-Learning for SON Performance Improvement,” Python 3 and MATLAB codes to accompany a paper entitled “A Framework for Automated Cellular Network Tuning with Reinforcement Learning,” IEEE Transactions on Communications, 2019. Version 2.0 (Jun. 27, 2019). [Online]. Available: https://github.com/farismismar/Deep-Q-Learning-SON-Perf-Improvement Builds on top of Vienna University of Technology (TU Wien) Vienna LTE-A Downlink System Level Simulator v1.9.
Faris B. Mismar and Brian L. Evans, “Deep Learning in Downlink Coordinated Multipoint in New Radio Heterogeneous Networks,” Python 3 and MATLAB codes to accompany a paper entitled “Deep Learning in Downlink Coordinated Multipoint in New Radio Heterogeneous Networks,” IEEE Wireless Communications Letters, 2019. Version 2.0 (Jul. 30, 2019). [Online]. Available: https://github.com/farismismar/DL-CoMP-Machine-Learning Builds on top of Vienna University of Technology (TU Wien) Vienna LTE-A Downlink System Level Simulator v1.9.
SOFTWARE RELEASES
Available at https://github.com/farismismar

## Slide 34: REFERENCES
[3gpp15] 3GPP, “LTE; Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC); Protocol specification; Protocol specification” 3rd Generation Partnership Project, TS 36.331, Sep. 2015. [Online]. Available: http://www.3gpp.org/dynareport/36331.htm
[3gpp18] 3GPP, “LTE; Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC); Protocol specification; Protocol specification” 3rd Generation Partnership Project, TS 36.331, Dec. 2018.
[Alkhateeb14] A. Alkhateeb, O. El Ayach, G. Leus, and R. W. Heath Jr., “Channel Estimation and Hybrid Precoding for Millimeter Wave Cellular Systems,” IEEE Journal of Selected Topics in Signal Processing, vol. 8, no. 5, pp. 831-846, Oct. 2014.
[Alkhateeb19] A. Alkhateeb, “DeepMIMO: A Generic Deep Learning Dataset for Millimeter Wave and Massive MIMO Applications,” Proceedings of Information Theory and Applications Workshop, Feb. 2019.
[Chen16] T. Chen and C. Guestrin, “XGBoost: A Scalable Tree Boosting System,” Proceedings of the ACM SIGKDD International Conference on Knowledge Discovery and Data Mining, Aug. 2016.
[Cortes95] C. Cortes and V. Vapnik, “Support-Vector Networks,” Machine Learning, vol. 20, no. 3, pp. 273-297, Sep. 1995.
[Goodfellow] I. Goodfellow, Y. Bengio, and A. Courville, Deep Learning, MIT Press, 2016.
[Paulraj] A. Paulraj, A. Rohit, R. Nabar, and D. Gore, Introduction to Space-Time Wireless Communications. New York, USA: Cambridge University Press, 2003.
[Silver] D. Silver, “Advanced Topics – Reinforcement Learning,” 2015. [Online]. Available: http://www0.cs.ucl.ac.uk/staff/d.silver/web/Teaching.html
[Sutton] R. Sutton and A. Barto, Reinforcement Learning. Massachusetts, USA: The MIT Press, 2002.
[Tse05] D. Tse and P. Vishwanath, Fundamentals of Wireless Communication. New York, USA: Cambridge University Press, 2005.
[Zadeh16] R. Zadeh, “The hard thing about Deep Learning,” KD Nuggets, Dec. 2016. [Online]. Available: https://www.kdnuggets.com/2016/12/hard-thing-about-deep-learning.html
[Zappone19] A. Zappone, M. Di Renzo and M. Debbah, “Wireless Networks Design in the Era of Deep Learning: Model-Based, AI-Based, or Both?,” IEEE Transactions on Communications, vol. 67, no. 10, pp. 7331-7376, Oct. 2019.
REFERENCES

## Slide 35: ACRONYMS AND ABBREVIATIONS

## Slide 36: DISSERTATION CONTRIBUTIONS
DISSERTATION CONTRIBUTIONS
 | 1. Joint BF, PC, IC | 2. Improved CoMP | 3. Band Switching
Dissertation Chapter | 2 | 3 | 4
Reference | [Mismar&Evans20a] | [Mismar&Evans19a] | [Mismar&Evans20b]
Frequency band | mmWave and sub-6 GHz | sub-6 GHz | mmWave and sub-6 GHz
Stack layer | PHY | PHY | RRM
Algorithm | DRL | DNN and SVM | DNN and XGBoost
Direction | Downlink |  | 
Users | Multi-User |  | 
BF: Beamforming, CoMP: Coordinated Multipoint, DNN: Deep Neural Network, DRL: Deep Reinforcement Learning, IC: Interference Coordination, PC: Power Control, PHY: Physical Layer, SON: Self-Organizing Network, XGBoost: Extreme Gradient Boosting.

## Slide 37: SIMULATION
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
CoMP decisions are “imbalanced” and DNN does better
CoMP: Coordinated Multipoint, DNN: Deep Neural Network, PRB: Physical Resource Block, SVM: Support Vector Machine.

## Slide 38: SOLUTION
CONTRIBUTION 2: IMPROVED DOWNLINK COORDINATED MULTIPOINT
Why DNN?
Is CoMP triggered in a balanced fashion in a cell?
Support Vector Machines
Can be faster than DNN, but suffers from bias towards majority class.
[Cortes95]
Kernel
“Box” constraint to control overfitting
Lagrangian multipliers
SVM will trigger more rank-2s than DNN, but at the wrong time!
m-th support vector
Notes: Why is SVM biased towards the majority class? Hinge loss.

## Slide 39: SIMULATION
Scenario A – DNN
Scenario A – XGBoost
DNN achieved ROC AUC = 1.0 with far less training samples than XGBoost
AUC ~ 1.0
AUC = 1.0

## Slide 40: SUPPORT VECTOR MACHINES
kernel
hinge loss
Primal
Dual
Computationally more efficient, exploits strong duality, and enables the kernel “trick”
[Cortes95]
Notes: Primal has wTx, which can be expensive for lengthy w. However, the kernel is sparse in nature, with few support vectors, leading to much less xTx computations.
Support vector are the points that are the nearest from the max separating hyperplane

## Slide 41: XGBOOST
A tree-ensemble learning technique, which minimizes this objective function
Fast and accurate hence used in many data mining contests
Uses the sub-gradient (or derivative if differentiable) for the first (gradient) and second order (Hessian) of the objective function
convex loss function (e.g., logistic loss)
regularization terms
Logistic loss function:
Using the gradient and Hessian, compute the “gain” for both the right and left subtrees. Choose the direction with the maximum gain.
[Chen16]
minimum loss reduction required to make a further partition (i.e., complexity control)
number of leaves
weight vector

## Slide 42: DEEP NEURAL NETWORKS
Perceptron
Optimizers
  Stochastic Gradient Descent
  Adaptive moments “Adam”
Deeper and wider neural networks
  Feed-forward (no loops, adjusts weights )
  Backpropagation (method of calculating the gradient with respect to the neural network weights)
bias term
Non-linear activation function
input feature vector
perceptron weights
Uses the gradient and its second moment (i.e., gradient squared). Adapts the learning rate.
learning rate
loss function
[Goodfellow]
Slower execution time compared to SVM and XGBoost

## Slide 43: DEEP Q-LEARNING
[Sutton]
Reinforcement learning
  Learns through interaction with an environment
  Seeks to maximize the expected future reward of an agent
Experience
Replay
  Samples from prior experience (i.e., the replay buffer) to remove potential correlation and improve stability of DQN
Deep Q-Network (DQN)
Bellman
current state
current action
current reward
next state
Stored in a replay buffer
future discounted reward
discount rate
Universal approximation theorem
Policy: defines a mapping from states to the actions taken
  Stochastic
Exploration vs exploitation
  Select a random action w.p.
  Find action that maximizes w.p.
∊-greedy has linear “regret”
[Silver]