## Slide 1
Jinseok Choi
OPTIMIZING COMMUNICATION PERFORMANCE
OF LOW-RESOLUTION ADC SYSTEMS
WITH HYBRID BEAMFORMING
The University of Texas at Austin
Embedded Signal Processing Laboratory
Wireless Networking & Communications Group
September 10, 2019
Ph.D. Defense
Notes: Hi, thank you all for coming.
My name is Jinseok Choi, working with Prof. Evans mostly on wireless communications
Today, I am going to present my PhD research on ~

## Slide 2: VISION FOR 5G COMMUNICATIONS
Sustainable Data Rate 100 Mb/s
Latency < 1ms
Data Traffic 50 Exabytes/Month (2021)
Peak Data Rates 20 Gb/s
Connection Density 1M Connections/km2
4G 5G
10 ms Latency
7.2 Exabytes/Month Data Traffic
1 Gb/s Peak Data Rates
10 Mb/s Sustainable Data Rate
100k Connections/km2 Connection Density
[2017 Qorvo Inc.]
+ Energy Efficiency
[https://www.qorvo.com/design-hub/blog/getting-to-5g-comparing-4g-and-5g-system-requirements]
BACKGROUND
Notes: Now, we are looking at 5G communications which requires much less latency and much larger data traffic.
It also requires higher peak data rates and about 10x sustainable data rates.
Data: 100x or 1000x increase
Latency: 15ms roundtrip -> 1ms (an order of magnitude)
Energy/cost efficiency: at least maintain on per-link basis.
MmWave
Vulnerable(susceptible) to blockage effect
Massive MIMO
Spectral efficiency [bps/Hz]
Channel smoothing - reduce randomness of small scale fading – due to law of large numbers
Quasi-orthogonal – simple tranceiver architecture

## Slide 3: OVERVIEW
propagation paths
Millimeter wave channel
User devices
Base station (BS)
High frequency: 30 – 300 GHz
Large bandwidth: 100MHz – 1GHz
Sparse in angular (beam) domain
Severe large scale fading (pathloss & shadowing)
Multiple users
Single antenna
Low-resolution ADCs
Many antennas (64+)
Hybrid analog/digital BF*
Low-resolution ADCs
User scheduling
Advanced BS design
*BF: beamforming
BACKGROUND
[Pi&Khan11, Akdeniz&Rappaport14]
[Andrews14]
Notes: Read Rappaport

## Slide 4: CHALLENGE IN MILLIMETER WAVE COMMUNICATION
Conventional MIMO receiver
Full-resolution ADC (12 – 16 bits)
Full RF chains ()
Baseband
Combiner
A
ADC
A
ADC
A
ADC
. . .
A
ADC
. . .
. . .
. . .
RF chain
RF chain
RF chain
RF chain
BACKGROUND
: caused by large number of antennas/RF components and high sampling rate of mmWave systems
Excessive power consumption
$$$$$
Low-resolution ADC (<<12bits)
Full RF chains ()
Low-resolution ADC receiver
. . .
Baseband
Combiner
A
ADC
A
ADC
A
ADC
. . .
A
ADC
. . .
. . .
Low resolution
RF chain
RF chain
RF chain
RF chain
Conventional Solution (A)
Hybrid beamforming receiver
Full-resolution ADC (12 – 16 bits)
Fewer RF chains (NRF << Nr)
Conventional Solution (B)
Baseband
Combiner
. . .
RF chain
RF chain
RF chain
. . .
Analog
Combiner
A
ADC
A
ADC
A
ADC
. . .
$$$
$$$
Notes: 5G Technologies
https://www.qorvo.com/design-hub/blog/getting-to-5g-comparing-4g-and-5g-system-requirements
Channel hardening
http://ma-mimo.ellintech.se/2017/01/25/channel-hardening-makes-fading-channels-behave-as-deterministic/
Millimeter wave antennas
https://www-03.ibm.com/press/us/en/photo/41229.wss
Massive MIMO antennas
http://www.ni.com/white-paper/52382/en/
Thank you,

## Slide 5: LOW POWER RECEIVER ARCHITECTURE
+
Hybrid beamforming receiver
Baseband
Combiner
. . .
RF chain
RF chain
RF chain
. . .
Analog
Combiner
A
ADC
A
ADC
A
ADC
. . .
. . .
BACKGROUND
Low-resolution ADC receiver
. . .
Baseband
Combiner
A
ADC
A
ADC
A
ADC
. . .
A
ADC
. . .
. . .
Low resolution
RF chain
RF chain
RF chain
RF chain
$$$
$$$
Naïve combination of low-resolution ADCs and hybrid beamforming
: applying techniques for hybrid BF with perfect quantization does not work well
Problem
Sol A
Sol B
Hybrid beamforming with low-resolution ADC receiver
Considered receiver (BS) architecture
Reduced number of RF chains
…
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
…
…
Low Resolution
…
Analog
Combiner
Reduced number of ADC bits
+
$$
[Mo&Heath17]
Notes: Blindly applying

## Slide 6: CONTRIBUTIONS
How to improve new system performance?
CONTRIBUTIONS
optimize architecture and/or technique to efficiently reduce quantization error
Antenna selection
Resolution-adaptive ADCs
User scheduling
Contribution 2
Contribution 3
Contribution 1
ADC
ADC
ADC
Two-stage analog combiner
Contribution 4
…
Analog combiner
ADC
…
MAC perspective
PHY perspective
Optimize: set of users
Optimize: ADC bits
Optimize: analog beamformer
ADC
RF chain
RF chain
RF chain
Analog combiner
. . .
. . .
. . .
Switch-based
Phase shifter-based
MAC: medium access control layer
PHY: physical layer
Notes: To improve the performance of the new system, we need to optimize the architecture and relevant techniques to efficiently reduce quantization error.
In MAC layer, I investigated USER SCHEDULING.
In PHY layer, I developed different BS designs such as RESOLUTION-ADAPTIVE ADC RECEIVER, ANTENNA SELECTION ARCHITECTURE, AND TWO-STAGE ANALOG COMBINING RECEIVER.
The user scheduling work aimed to optimize a set of users.
The resolution-adaptive ADC work considered to optimize the number of ADC bits
and antenna selection and two-stage analog combining work considered to optimize the analog beamformer for switch-based analog networks and phase-shifter-based analog networks, respectively.
In today’s presentation, I will skip the contribution 1 and present the rest of contributions with more details. If time permits, I will also come back to contribution 1.

## Slide 7: UPLINK USER SCHEDULING FOR HYBRID RECEIVERS WITH LOW-RESOLUTION ADCS
Related publications:
[1]. Jinseok Choi, Gilwon Lee, and Brian L. Evans, "Millimeter-Wave MIMO User Scheduling for Low-Resolution ADC Systems", IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2401-2414, Apr. 2019.
[2]. Jinseok Choi, and Brian L. Evans, "User Scheduling for Millimeter Wave MIMO Communications with Low-Resolution ADCs", IEEE International Conference on Communications, May 20-24, 2018, Kansas City, MO, USA.
Contribution 1
Discussed in the PhD Qualifying Exam and Included in the PhD Dissertation
Notes: I can present in the closed door if committees would like to see

## Slide 8: SYSTEM MODEL
CONTRIBUTION 1: USER SCHEDULING
Multi-user MIMO uplink system
Single cell environment with K users with single antenna
Selects users to serve
Uniform linear array (ULA) antennas
DFT-based analog combining
Zero-forcing digital equalizer
Millimeter wave channel model with limited scattering
array response vector (ARV)
angle of arrival (AoA)
channel path gain
Beam domain projection by using
path gains
DFT matrix
[Akdeniz&Rappaport14]
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
. . .
. . .
. . .
+
+
Low resolution
DFT submatrix
Considered receiver architecture
sparse in beam domain
small Lk
:
Beam domain projection:
Beam domain channel
ULA
Notations
Notes: Sharif, Masoud, and Babak Hassibi. "On the capacity of MIMO broadcast channels with partial side information." IEEE Transactions on information Theory 51.2 (2005): 506-522.
Yoo, Taesang, and Andrea Goldsmith. "On the optimality of multiantenna broadcast scheduling using zero-forcing beamforming." IEEE Journal on selected areas in communications 24.3 (2006): 528-541.
Lee, Gilwon, Youngchul Sung, and Marios Kountouris. "On the performance of random beamforming in sparse millimeter wave channels." IEEE Journal of Selected Topics in Signal Processing 10.3 (2016): 560-575.

## Slide 9: MOTIVATION & PROBLEM FORMULATION
Achievable rate of user k
AWGN
(1), (2) cannot minimize quantization error
AWGN: minimized by previous criteria
(1)
(2)
QN: requires additional condition
Quantization noise (QN)
Non-negligible quantization error
Maximum sum rate and fairness problems
Maximum sum rate user scheduling
set of scheduled users
beam domain channel of users in S
Proportional fairness (PF) scheduling
where
: first-order auto-regressive filter
weight of user k at time t
regression rate parameter in (0, 1)
indicator function
CONTRIBUTION 1: USER SCHEDULING
Notes: Sharif, Masoud, and Babak Hassibi. "On the capacity of MIMO broadcast channels with partial side information." IEEE Transactions on information Theory 51.2 (2005): 506-522.
Yoo, Taesang, and Andrea Goldsmith. "On the optimality of multiantenna broadcast scheduling using zero-forcing beamforming." IEEE Journal on selected areas in communications 24.3 (2006): 528-541.
Lee, Gilwon, Youngchul Sung, and Marios Kountouris. "On the performance of random beamforming in sparse millimeter wave channels." IEEE Journal of Selected Topics in Signal Processing 10.3 (2016): 560-575.

## Slide 10: NEW SCHEDUILNG CRITERIA & SIMULATIONS
PF scheduling
Fig. 1: Rate vs. Tx power
Fig. 2: Rate vs. User index
MS scheduling
New scheduling criteria
1. Unique *AoAs for channel paths:
2. Equal power spread within each channel:
index set of nonzero channel gains
total channel gain for user S(k)
number of nonzero channel gains for user S(k)
*AoA: angle of arrivals
Proposed user scheduling methods
Semi-orthogonality
Spatial orthogonality
Set Filtering
Selection
Update
Approximated SINR
Approximated weighted rate
Max
Sum
Prop
Fair
:
:
AR filter
where
[Lee&Sung16]
[Yoo&Goldsmith06]
CONTRIBUTION 1: USER SCHEDULING

## Slide 11: SUMMARY
Takeaway Message
Chordal distance-based scheduling
Channel structural scheduling criteria
Channel structure-based scheduling
Unique *AoAs for channel paths:
Equal power spread within each channel:
Semi-orthogonality
Spatial orthogonality
Maximum SINR scheduling
Partial
Full CSI
Sum rate analysis
Filtering
Selection
CONTRIBUTION 1: USER SCHEDULING

## Slide 12: BIT ALLOCATION FOR HYBRID BEAMFORMING RECEIVERS WITH RESOLUTION-ADAPTIVE ADCS
Contribution 2
Discussed in the PhD Qualifying Exam and Included in the PhD dissertation
Related publications:
[1]. Jinseok Choi, Brian L. Evans, and Alan Gatherer, "Resolution-Adaptive Hybrid MIMO Architectures for Millimeter Wave Communications", IEEE Transactions on Signal Processing, vol. 65, no. 23, pp. 6201-6216, Dec. 2017.
[2]. Jinseok Choi, Brian L. Evans, and Alan Gatherer, "ADC Bit Allocation under a Power Constraint for MmWave Massive MIMO Communication Receivers", Proc. IEEE Int. Conf. on Acoustics, Speech and Signal Processing, Mar. 5-9, 2017, New Orleans, LA, USA.
[3]. Jinseok Choi, Junmo Sung, Brian L. Evans, and Alan Gatherer, "ADC Bit Optimization for Spectrum- and Energy-Efficient Millimeter Wave Communications", IEEE Global Communications Conf., Dec. 4-8, 2017, Singapore.

## Slide 13: SYSTEM MODEL
CONTRIBUTION 2: ADAPTIVE ADC
Multi-user MIMO uplink system
Single cell environment
Serve users with single antenna
Uniform linear array (ULA) antennas
DFT-based analog combining
Resolution-adaptive ADCs
Millimeter wave channel model with limited scattering
array response vector (ARV)
angle of arrival (AoA)
channel path gain
large scale fading gain
Beam domain projection by using
path gains
DFT matrix
[Akdeniz&Rappaport14]
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
. . .
. . .
. . .
+
+
Resolution adaptive
DFT submatrix
Considered receiver architecture
sparse in beam domain
small Lk
:
Beam domain projection:
Beam domain channel
ULA
Notations
Notes: Sharif, Masoud, and Babak Hassibi. "On the capacity of MIMO broadcast channels with partial side information." IEEE Transactions on information Theory 51.2 (2005): 506-522.
Yoo, Taesang, and Andrea Goldsmith. "On the optimality of multiantenna broadcast scheduling using zero-forcing beamforming." IEEE Journal on selected areas in communications 24.3 (2006): 528-541.
Lee, Gilwon, Youngchul Sung, and Marios Kountouris. "On the performance of random beamforming in sparse millimeter wave channels." IEEE Journal of Selected Topics in Signal Processing 10.3 (2016): 560-575.

## Slide 14: MOTIVATION & PROBLEM FORMULATION
Selective bit allocation
Sparse beam domain mmWave channel
real number relaxation
Convex optimization
Minimizing quantization error
Mean squared quantization error (MSQE)
[Gersho&Gray12]
quantized desired signal
desired signal
quantization bits
: ADC total power constraint
Relaxed minimum MSQE problem in high SNR
more bits
less bits
ADC
ADC
ADC
ex.
1 bit
2 bits
3 bits
More quantization bits
to larger channel gain
fewer quantization bits
to smaller channel gain
maintain similar quantization error over all ADCs
CONTRIBUTION 2: ADAPTIVE ADC

## Slide 15: BIT ALLOCATION SOLUTION & SIMULATIONS
Fig. 4: Energy efficiency vs. Constraint bits
Fig. 3: Rate vs. Constraint bits
Near optimal bit allocation (solution for )
Minimizes total MSQE in high SNR
associated channel gain
channel gain for all RF chains
Minimizes generalized mutual information in low SNR
where
Worst case analysis
Approximated lower bound of achievable rate
: more bit to larger channel
System parameters
Cell radius | 200 m | Noise figure | 5 dB | # User | 8
Min. distance | 30 m | Equalizer | MRC | Tx power | 20 dBm
Carrier freq. | 28 GHz | # Antennas | 256 |  | 
Bandwidth | 1 GHz | # RF chains | 128 |  | 
[Akdeniz&Rappaport14]
CONTRIBUTION 2: ADAPTIVE ADC
Notes: In this work, I focused on optimizing the ADC resolutions.
In the following two contributions, I focus on optimizing analog beamformer: one with switch-based, the other with phase-shifter based.
Show fig 3 first and show fig 4 later.

## Slide 16: SUMMARY
ADC
ADC
ADC
ex.
1 bit
2 bits
3 bits
maintain similar quantization error over all ADCs
path gains
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
. . .
. . .
. . .
+
+
Resolution adaptive
DFT submatrix
ULA
Adaptive Bit Allocation
Selective bit allocation achieves high SE* and EE*
Main assumption
Takeaway Message
Main results
ADC changes its resolution depending on channel
High SNR: minimizes mean squared quantization error
Resolution-adaptive ADC with bit-allocation solution
Performance analysis: lower bound
Low SNR: maximizes generalized MI
*SE: spectral efficiency
*EE: energy efficiency
CONTRIBUTION 2: ADAPTIVE ADC
Notes: In this work, I focused on optimizing the ADC resolutions.
In the following two contributions, I focus on optimizing analog beamformer: one with switch-based, the other with phase-shifter based.
Show fig 3 first and show fig 4 later.

## Slide 17: BASE STATION ANTENNA-SELECTION FOR LOW-RESOLUTION ADC SYSTEMS
Contribution 3
Partially Discussed in the PhD Qualifying Exam
Related publications:
[1] Jinseok Choi, Junmo Sung, Narayan Prasad, Xiao-Feng Qi, Brian L. Evans, and Alan Gatherer, "Base Station Antenna Selection for Low-Resolution ADC Systems", IEEE Transactions on Communications (submitted).
[2] Jinseok Choi, Brian L. Evans, and Alan Gatherer, "Antenna Selection for Large-Scale MIMO Systems with Low-Resolution ADCs", IEEE Int. Conf. on Acoustics, Speech, and Signal Processing, Apr. 15-20, 2018, Calgary, Alberta, Canada,

## Slide 18: MOTIVATION & UPLINK SYSTEM MODEL
CONTRIBUTION 3: ANTENNA SELECTION
Uplink system model
Considered uplink communication
Lower implementation cost and complexity compared to phase shifters
Moderate performance in reducing the number of RF chains with small loss
Switch-based analog beamforming
RF chain
RF chain
RF chain
Analog combiner
. . .
. . .
. . .
Switch-based
ADC
…
ADC
ADC
New design/analysis is necessary due to coarse quantization
quantization error
. . .
[Méndez-Rial16]
[Gao15]
RF chain
Baseband
Processor
RF chain
Baseband
Processor
Mobile station 1
Mobile station NMS
. . .
H
NMS users are equipped with single antenna
BS selects antenna subset with known CSI
BS employs low-resolution ADCs
Narrowband channel assumption
Notes: ADD ARROWS IN MS

## Slide 19: PROBLEM FORMULATION
*BS: base station
Uplink maximum mutual-information problem
Maximum mutual-information selection for narrowband system
Challenges
(1) Large number of antennas at BS*: Exhaustive search (X) vs. Greedy search (O)
(2) Greedy is suboptimal: performance bound is necessary
set of selected antennas
quantization noise covariance matrix
Mutual information with selected antennas under additive quantization noise model (AQNM)
[Fletcher07]
CONTRIBUTION 3: ANTENNA SELECTION
Notes: Sharif, Masoud, and Babak Hassibi. "On the capacity of MIMO broadcast channels with partial side information." IEEE Transactions on information Theory 51.2 (2005): 506-522.
Yoo, Taesang, and Andrea Goldsmith. "On the optimality of multiantenna broadcast scheduling using zero-forcing beamforming." IEEE Journal on selected areas in communications 24.3 (2006): 528-541.
Lee, Gilwon, Youngchul Sung, and Marios Kountouris. "On the performance of random beamforming in sparse millimeter wave channels." IEEE Journal of Selected Topics in Signal Processing 10.3 (2016): 560-575.

## Slide 20: UPLINK BS ANTENNA SELECTION METHOD
where
Decomposition of mutual information
At th antenna selection stage
matrix determinant lemma
# Generalized greedy selection criterion
gain
tradeoff
penalty
Quantization-aware fast antenna selection (QFAS)
Matrix inversion in gain computation
Computational complexity reduction
# Simplified gain update
reuse previous gain
vector inner product
matrix inversion lemma
scalar
where
CONTRIBUTION 3: ANTENNA SELECTION

## Slide 21: PERFORMANCE ANALYSIS: LOWER BOUND
Submodular function
Definition
Theorem
Normalized nonnegative and monotone submodular function f
: set obtained by selecting one at a time with largest marginal increase
: optimal set with same size as
Function with diminishing return property :
(Lower bound)
# Lower bound of f with
[Nemhauser78]
Performance lower bound of proposed greedy selection
Proof sketch
Mutual information achieved by proposed greedy-based antenna selection is lower bounded by
Define
Use submodularity of entropy function w.r.t. selected antennas
Show submodular, normalized, nonnegative, and monotone function
optimal antenna subset
and
Corollary 1 (Lower bound of QFAS)
CONTRIBUTION 3: ANTENNA SELECTION
Notes: e: Euler's number
G. L. Nemhauser, L. A. Wolsey, and M. L. Fisher, An analysis of approximations for maximizing submodular set functions

## Slide 22: WIDEBAND UPLINK ANTENNA SELECTION
Uplink wideband OFDM* system
Quantized signal for subcarrier n under AQNM*
*OFDM: orthogonal frequency-division multiplexing
Mutual-information for subcarrier n
*AQNM: additive quantization noise model
thermal noise + quantization noise
quantization gain < 1
gain update w/o matrix inversion
Frequency domain channel
Quantization noise variance
all subcarriers share same antenna subset
Greedy antenna selection and performance bound
Maximum mutual-information problem for OFDM system
Simplified greedy antenna selection method without matrix inversion
Proof: submodularity is closed under addition
Corollary 2 (Lower bound of QFAS)
[Fletcher07]
CONTRIBUTION 3: ANTENNA SELECTION

## Slide 23: SIMULATION RESUTLS: UPLINK OFDM SYSTEM
Fig. 6: MI vs. # selected antennas
Fig. 5: MI vs. Tx power
*MCMC: Markov chain Monte Carlo
QMCMC-AS: quantization-aware adaptive-MCMC* based on MIS*
- Near numerical upper bound
- High complexity: iterations with multiple sampling (ex. 60, 120)
*MIS: metropolized independence sampler
System parameters
Simulated algorithms
QFAS: quantization-aware fast antenna selection (proposed)
FAS: fast antenna selection without quantization
NBS: norm-based selection
Cell radius | 200 m | Noise figure | 5 dB
Min. distance | 20 m | # channel paths | 3
Carrier freq. | 28 GHz | # channel delay taps | 4
Bandwidth | 100MHz | # subcarriers | 64
BS antenna gain | 15 dBi | # ADC bits | 3
Fig. 5 | Fig. 6
Fig. 5 | Fig. 6
[Akdeniz&Rappaport14]
Effective in low-resolution ADC system with high performance
CONTRIBUTION 3: ANTENNA SELECTION
Notes: M. R. Akdeniz, Y. Liu, M. K. Samimi, S. Sun, S. Rangan, T. S. Rappaport, and E. Erkip, “Millimeter wave channel modeling and cellular capacity evaluation,” IEEE Journal Sel. Areas in Comm., vol. 32, no. 6, pp. 1164–1179, 2014.

## Slide 24: DOWNLINK BS ANTENNA SELECTION
System model
Zero-forcing (ZF) precoder with CSI known at BS
Equal power allocation (EPA)
Users employ low-resolution ADCs
Achievable sum rate:
ZF Precoding
+
equal power allocation
RF chain
RF chain
RF chain
. . .
. . .
. . .
RF chain
Baseband
Processor
A
ADC
RF chain
Baseband
Processor
A
ADC
. . .
Mobile station 1
Mobile station NMS
Base station
. . .
Low resolution
Considered downlink communication
set of selected antennas
Tx symbol power
Antenna selection problem
Maximum rate antenna selection problem
total transmit power
Equivalent to antenna selection in perfect quantization system
: needs to be large and orthogonal
CONTRIBUTION 3: ANTENNA SELECTION

## Slide 25: SUM RATE ANALYSIS
How many antennas?
More antennas do not always provide higher rate due to limited transmit power
Rx
Tx
h1
h2
)
<
>
# In perfect quantization system
[Lin&Tsai12]
: higher maximum rate with more antennas for ZF precoding with equal power allocation
# In coarse quantization system
Proof sketch
Higher maximum rate with more antennas for ZF-EPA
Higher rate with more antennas for ZF-EPA*
(a) Define where and
(b) Show by using matrix inversion lemma and [Lemma 2, Lin&Tsai12]
(c) Show where and
from (a), (b)
*ZF-EPA: zero-forcing precoding and equal power allocation
Corollary 3 (Monotonicity)
Theorem 1
CONTRIBUTION 3: ANTENNA SELECTION
Notes: Less number of antennas = fewer antennas

## Slide 26: SUM RATE ANALYSIS
How much transmit power?
More power provides higher rate, but maybe less efficient
Similar analysis also holds for downlink OFDM systems
Tx power can compensate for rate loss due to using less antennas
can be good reference point
# In coarse quantization system
Rate loss converges to zero with tx power:
Maximum rate loss occurs at following tx power:
Corollary 4 (Vanishing loss)
Corollary 5 (Maximum loss)
# In perfect quantization system
matrix of channel eigenvalues
where
and
: rate loss increases with tx power and upper bounded by
[Lin&Tsai12]
CONTRIBUTION 3: ANTENNA SELECTION
Notes: .-H. Lin and S.-H. Tsai, Performance analysis and algorithm designs for transmit antenna selection in linearly precoded multiuser MIMO systems,
Why less efficient
Inter-cell-interference
Slower increase in rate
Tradeoff between tx power and # selected antennas need to be investigated (future work)

## Slide 27: SIMULATION RESUTLS: DOWNLINK OFDM SYSTEM
Cell radius | 200 m
Min. distance | 20 m
Carrier freq. | 28 GHz
Bandwidth | 100MHz
BS antenna gain | 15 dBi
Noise figure | 5 dB
# channel paths | 3
# channel delay taps | 4
# subcarriers | 64
Fig. 5 | Fig. 6
dB | 
Fig. 5 | Fig. 6
System parameters
Validations
Non-decreasing property w.r.t number of selected antennas Nt
Presence of maximum rate loss and rate convergence
More antennas vs. more tx power
Fig. 7: Rate vs. # selected antennas
Fig. 8: Rate vs. Tx power
lower rate
less gap
higher rate
less gap
[Akdeniz&Rappaport14]
CONTRIBUTION 3: ANTENNA SELECTION

## Slide 28: SUMMARY
Uplink BS antenna selection
Downlink BS antenna selection
Algorithm
Main assumption
Performance lower bound
Takeaway Message
Extension to wideband OFDM system
Main results
BS selects rx antenna subset depending on channels
More antennas always provide higher rate
Tx power can fully compensate reduced # antennas
Quantization error needs to be considered
Greedy choice is suboptimal but efficient
Main assumption
Takeaway Message
Main results
BS selects tx antenna subset depending on channels
Monotonicity
Max loss
Equivalent problem to perfect quantization
Extension to wideband OFDM system
CONTRIBUTION 3: ANTENNA SELECTION

## Slide 29: TWO-STAGE ANALOG COMBINING IN HYBRID BEAMFORMING SYSTEMS WITH LOW-RESOLUTION ADCS
Contribution 4
Related publications:
[1]. Jinseok Choi, Gilwon Lee, and Brian L. Evans, "Two-Stage Analog Combining in Hybrid Beamforming Systems with Low-Resolution ADCs", IEEE Transactions on Signal Processing, vol. 67, no. 9, pp. 2410-2425, May 1, 2019
[2]. Jinseok Choi, Gilwon Lee, and Brian L. Evans, "A Hybrid Combining Receiver with Two-Stage Analog Combiner and Low-Resolution ADCs", IEEE Int. Conf. on Communications, 2019, pp. 1-6. doi: 10.1109/ICC.2019.8761780

## Slide 30: MOTIVATION
128 Rx antennas
16 RF chains
8 users
Fig. 9: Signal power on each RF chain
noise components
desired signals
Fig. 10: Mutual information vs. SNR
SVD analog combining
SVD upper bound
Proposed analog combining
Optimal analog combining
proposed
SVD
large gap
CONTRIBUTION 4: TWO-STAGE COMBINING
Optimal analog combiner design
If feasible, is SVD* analog combiner optimal?
*SVD: singular value decomposition
# In perfect quantization system: Yes!
large gain
: collects all of the channel gains onto reduced number of RF chains
…
RF chain
RF chain
RF chain
…
SVD
combiner
A
ADC
A
ADC
A
ADC
…
# In coarse quantization system: Maybe not..
: too large signal power experiences large quantization error
quantization error
large quantization error
small quantization error
Notes: SVD: No penalty in using reduced number of RF chains in perfect quantization system

## Slide 31: SYSTEM MODEL & PROBLEM FORMULATION
Proposed two-stage analog combining architecture
Single cell environment
Phase shifter-based two-stage analog combining
Uniform linear array (ULA)
Serve users with single antenna
MmWave narrowband channel
[Akdeniz&Rappaport14]
…
+
+
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
…
…
…
…
…
…
…
+
+
…
…
…
…
…
1st Analog Combiner
2nd Analog Combiner
Low Resolution
ULA
Maximizing mutual information
Mutual information
Relaxation: no constant modulus constraint on elements of analog combiner matrix
Relaxed maximum mutual-information problem
Analog combiner
Covariance matrix of quantization noise
: key role in changing quantization distribution
array response vector (ARV)
angle of arrival
channel path gain
CONTRIBUTION 4: TWO-STAGE COMBINING

## Slide 32: OPTIMAL SCALING LAW & TWO-STAGE SOLUTION
Optimal scaling law with respect to number of RF chains NRF
Theorem 2 (Optimal scaling law)
Optimal solution to achieves following scaling law w.r.t. number of RF chains:
signals
…
1
1. project on lower dimension
2. Spread evenly
ADCs
2
RF chains
A
A
A
A
A
Intuition
Moderate and even
quantization noise distribution
Optimal scaling law can be also achieved by using following two-stage combiners:
: any NRF x NRF unitary matrix with constant modulus
: SVD combiner
CONTRIBUTION 4: TWO-STAGE COMBINING
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 33: BOUNDED MI FOR CONVENTIONAL OPTIMAL SOLUTION
Mutual information achieved by SVD analog combining
Corollary 6 (Upper bound for SVD analog combining)
MI for conventional optimal solution for perfect quantization systems is bounded by
Second analog combiner WRF2 in Theorem 2 addresses quantization noise enhancement
Proof
matrix of channel eigenvalues
collects all channel gains:
Nu eigenvalues
:
increases effective quantization noise:
large gains on a few ADCs
:
Quantization error term
CONTRIBUTION 4: TWO-STAGE COMBINING
Notes: Zhang, Wenyi. "A general framework for transmission with transceiver distortion and some applications." IEEE Transactions on Communications 60.2 (2012): 384-399.

## Slide 34: MAXIMUM MUTUAL INFORMATION – SPECIAL CASE
Maximizing MI for special case: homogeneous channel singular values
Theorem 3 (Maximum Mutual Information)
Two-stage analog combining solution in Theorem 2, , is solution for:
and achieves maximum mutual information:
Proof sketch
(a) Show is upper bounded by
(b) Then,
(c) Find upper bound of C(WRF) by using Jensen’s inequality with (b)
(d) Show upper bound of C(WRF) can be achieved with by replacing in Proof of Theorem 2
: achieves optimal scaling
CONTRIBUTION 4: TWO-STAGE COMBINING

## Slide 35: TWO-STAGE ANALOG COMBINING ALGORITHM
Implementation of two-stage analog combiner under practical constraints
Key constraints: (1) Constant modulus condition on elements of analog combining matrix
(2) Finite resolution of phase shifters
Two-stage analog combining architecture provides favorable structure for implementation
1st analog combiner
2nd analog combiner
: capture max channel gain
: null space projection (for orthogonality)
: AoA codebook
*ARV: array response vector
*TSAC: two-stage analog combiner
Closely meets first condition in Theorem 2
: left eigenvectors (channel gain aggregation)
Perfectly meets second condition in Theorem 2
: unitary with constant modulus (spreading)
First analog combiner
Second analog combiner
ARVs collect most sparse beam-domain channel gain
DFT matrix or Hadamard matrix can be used
Low cost; negligible power consumption once configured
: independent to channel condition
implemented with fixed phase shifters
CONTRIBUTION 4: TWO-STAGE COMBINING
Notes: Zhang, Wenyi. "A general framework for transmission with transceiver distortion and some applications." IEEE Transactions on Communications 60.2 (2012): 384-399.

## Slide 36: PERFORMANCE ANALYSIS
Ergodic rate of ARV-TSAC method with maximum ratio combining (MRC)
Theorem 4 (Ergodic rate of two-stage combining)
For MRC digital combining, ergodic rate of ARV-TSAC is approximated as
where
Two-stage analog combining
One-stage analog combining
Corollary 7 (Ergodic rate of one-stage combining)
For MRC digital combining, ergodic rate of one-stage analog combining is approximated as
where
Two-stage analog combining achieves optimal scaling law with linear receiver
: achieves optimal scaling
: cannot achieve optimal scaling
CONTRIBUTION 4: TWO-STAGE COMBINING
Notes: Zhang, Wenyi. "A general framework for transmission with transceiver distortion and some applications." IEEE Transactions on Communications 60.2 (2012): 384-399.

## Slide 37: SIMULATION RESULTS 1
Fig. 12: Mutual information vs. SNR
Fig. 13: Signal power on each RF chain
Fig. 11: Mutual information vs. # RF chains
ARV-TSAC: proposed two-stage analog combining
SVD+DFT:
ARV: designed from ARV-TSAC
Greedy-MI: greedy maximization based on ARVs
SVD:
Infeasible
Infeasible
and (Theorem 2)
Simulated algorithms
Two-
stage
One-
stage
Fig. 11 | Fig. 12 | Fig. 13
# paths |  | 
SNR = dB |  | SNR = dB
Fig. 11 | Fig. 12 | Fig. 13
3 ~ 6 dB gain
CONTRIBUTION 4: TWO-STAGE COMBINING

## Slide 38: SIMULATION RESULTS 2
Low resolution regime
(Figure 14) NRF/Nr = 1/3, Nu = 8, b = 2, # paths = 3, and SNR = 0 dB
Linear digital equalizer: maximum ratio combiner
Fig. 14: Rate vs. # RF chains
Fig. 15: Rate vs. Quantization bits
(Figure 15) Nr = 128, NRF = 43, Nu = 8, b = 2, # paths = 3
Two-stage analog combining is effective in low-resolution ADC regime
: due to increasing Nr
CONTRIBUTION 4: TWO-STAGE COMBINING

## Slide 39: SPECTRAL VS ENERGY EFFICIENCY TRADE-OFF
Two-stage analog combining receiver (contribution 4)
Resolution-adaptive ADC receiver (contribution 2)
Conventional one-stage analog combining receiver
Fully digital receiver
Simulated algorithms in low-resolution ADC system
*SE: spectral efficiency
*EE: energy efficiency
Bandwidth | 1 GHz | # users | 4
SNR | 10 dB | # channel paths | 2
System parameters
CONTRIBUTION 4: TWO-STAGE COMBINING

## Slide 40: SUMMARY
…
+
+
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
…
…
…
…
…
…
…
+
+
…
…
…
…
…
1st Analog Combiner
2nd Analog Combiner
Low Resolution
Proposed two-stage analog combining receiver
Optimality
Optimal scaling law
Maximum mutual information
Two-stage combining solution
: unitary
Second analog combiner is essential in reducing effective quantization error
Algorithm
ARV-TSAC algorithm
Ergodic rate analysis with MRC receiver
Sparse channel assumption
CONTRIBUTION 4: TWO-STAGE COMBINING

## Slide 41: SUMMARY AND CONCLUSION
optimize ADC resolution
optimize analog combiner
optimize set of users
MAC Layer Perspective
PHY Layer Perspective
User scheduling
Optimizations for mitigating quantization error
Considered system: hybrid beamforming with low-resolution ADC system for high energy efficiency
Antenna selection
Adaptive ADC
Two-stage combining
- switch based -
- phase shifter based -
Advanced architectures and techniques at different parts of wireless systems can significantly increase spectral and energy efficiency
CONCLUSION
Notes: Dahrouj, Hayssam, and Wei Yu. "Coordinated beamforming for the multicell multi-antenna wireless system." IEEE transactions on wireless communications 9.5 (2010).
Sanderovich, Amichai, Oren Somekh, and Shlomo Shamai. "Uplink macro diversity with limited backhaul capacity." Information Theory, 2007. ISIT 2007. IEEE International Symposium on. IEEE, 2007.
Ng, Boon Loong, et al. "Distributed downlink beamforming with cooperative base stations." IEEE Transactions on Information Theory 54.12 (2008): 5491-5499.

## Slide 42: FUTURE WORK
Channel estimation in two-stage analog combining system
FUTURE WORK
Extension of receiver design work into wideband communications
Cooperation of multiple base stations under limited total power consumption
Use estimation techniques for hybrid system after multiplying inverse matrix of second combiner
: Less performance degradation thanks to even distribution of quantization error (QE)
Develop new estimation technique by estimating quantization noise level
: Maybe easier to estimate quantization error thanks to even distribution of QE under same total QE
Base station antenna selection: similar results both in narrowband and wideband OFDM
: It is not proved for two-stage analog combining system and resolution-adaptive ADC system
Optimization of ADC resolution over multiple BSs in multiple cells
: It can be jointly optimized with user transmit power
Notes: Dahrouj, Hayssam, and Wei Yu. "Coordinated beamforming for the multicell multi-antenna wireless system." IEEE transactions on wireless communications 9.5 (2010).
Sanderovich, Amichai, Oren Somekh, and Shlomo Shamai. "Uplink macro diversity with limited backhaul capacity." Information Theory, 2007. ISIT 2007. IEEE International Symposium on. IEEE, 2007.
Ng, Boon Loong, et al. "Distributed downlink beamforming with cooperative base stations." IEEE Transactions on Information Theory 54.12 (2008): 5491-5499.

## Slide 43: PUBLICATIONS – JOURNAL ARTICLES
Jinseok Choi, Junmo Sung, Narayan Prasad, Xiao-Feng Qi, Brian L. Evans, and Alan Gatherer, "Base Station Antenna Selection for Low-Resolution ADC Systems", IEEE Transactions on Communications (under revision).
Faris B. Mismar, Jinseok Choi, and Brian L. Evans, "A Framework for Automated Cellular Network Tuning with Reinforcement Learning", IEEE Transactions on Communications accepted for publication.
Jinseok Choi, Gilwon Lee, and Brian L. Evans, "User Scheduling for Millimeter Wave Hybrid Beamforming Systems with Low-Resolution ADCs", IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2401-2414, Apr. 2019.
Jinseok Choi, Gilwon Lee, and Brian L. Evans, "Two-Stage Analog Combining in Hybrid Beamforming Systems with Low-Resolution ADCs", IEEE Transactions on Signal Processing, vol. 67, no. 9, pp. 2410-2425, May 1, 2019.
Jinseok Choi and Brian L. Evans, "Analysis of Ergodic Rate for Transmit Antenna Selection in Low-Resolution ADC Systems", IEEE Transactions on Vehicular Technology, vol. 68, no. 1, pp. 952-956, Jan. 2019.
Jinseok Choi, Brian L. Evans, and Alan Gatherer, "Resolution-Adaptive Hybrid MIMO Architectures for Millimeter Wave Communications", IEEE Transactions on Signal Processing, vol. 65, no. 23, pp. 6201-6216, Dec. 2017.
Jinseok Choi, Jeonghun Park, and Brian L. Evans, "Spectral Efficiency Bounds for Interference-Limited SVD-MIMO Cellular Communication Systems", IEEE Wireless Communications Letters, vol. 6, no. 1, pp. 46-49, Feb. 2017.
PUBLICATIONS

## Slide 44: PUBLICATIONS – CONFERENCE PAPERS
Jinseok Choi, Yunseong Cho, Brian L. Evans, and Alan Gatherer, "Robust Learning-Base ML Detection for Massive MIMO Systems with One-Bit Quantized Signals", IEEE Global Communications Conf. Dec. 9-13, 2019, Waikoloa, HI, USA.
Jinseok Choi, Gilwon Lee, and Brian L. Evans, "A Hybrid Beamforming Receiver with Two-Stage Analog Combiner and Low-Resolution ADCs", IEEE Int. Conf. on Communications, 2019, May 2019, Shanghai, China.
Jinseok Choi, Brian L. Evans, and Alan Gatherer, "Antenna Selection for Large-Scale MIMO Systems with Low-Resolution ADCs", Proc. IEEE Int. Conf. on Acoustics, Speech, and Signal Processing, Apr. 15-20, 2018, Calgary, Alberta, Canada, accepted.
Junmo Sung, Jinseok Choi, and Brian L. Evans, "Narrowband Channel Estimation for Hybrid Beamforming Millimeter Wave Communication Systems with One-bit Quantization", Proc. IEEE Int. Conf. on Acoustics, Speech, and Signal Processing, Apr. 15-20, 2018.
Jinseok Choi, and Brian L. Evans, "User Scheduling for Millimeter Wave MIMO Communications with Low-Resolution ADCs", Proc. IEEE Int. Conf. on Communications, May 20-24, 2018, Kansas City, MO, USA.
Jinseok Choi, Junmo Sung, Brian L. Evans, and Alan Gatherer, "ADC Bit Optimization for Spectrum- and Energy-Efficient Millimeter Wave Communications”, Proc. IEEE Global Communications Conf., Dec. 4-8, 2017, Singapore.
Jinseok Choi, Brian L. Evans, and Alan Gatherer, "ADC Bit Allocation under a Power Constraint for MmWave Massive MIMO Communication Receivers", Proc. IEEE Int. Conf. on Acoustics, Speech and Signal Processing, Mar. 5-9, 2017, New Orleans, LA, USA.
Jinseok Choi, Brian L. Evans, and Alan Gatherer, "Space-­Time Fronthaul Compression of Complex Baseband Uplink LTE Signals'', Proc. IEEE Int. Conf. on Communications, May 23-27, 2016, Kuala Lumpur, Malaysia.
PUBLICATIONS

## Slide 45: SOFTWARE RELEASES
Jinseok Choi and Brian L. Evans, "Two-Stage Analog Beamforming", MATLAB code to accompany a paper entitled "Two-Stage Analog Combining in Hybrid Beamforming Systems with Low-Resolution ADCs" in the IEEE Transactions on Signal Processing, vol. 67, no. 9, May 1, 2019, pp. 2410-2425, DOI 10.1109/TSP.2019.2904931. Version 1.0 (July 27, 2019)
Jinseok Choi and Brian L. Evans, "Antenna Selection for Large-Scale MIMO Systems with Low-Resolution ADCs", MATLAB code to accompany a paper of the same title in the 2018 IEEE International Conference on Acoustics, Speech and Signal Processing. Version 1.0 (October 27, 2017).
Jinseok Choi and Brian L. Evans, "User Scheduling Algorithms for Millimeter Wave MIMO Systems", MATLAB code to accompany a paper of the same title in the 2018 IEEE International Conference on Communications. Version 1.0 (October 13, 2017).
Jinseok Choi and Brian L. Evans, "Resolution-Adaptive Hybrid MIMO Architectures for Millimeter Wave Communications", MATLAB code to accompany a paper of the same title in the IEEE Transactions on Signal Processing, vol. 65, no. 23, pp. 6201-6216, Dec. 2017, DOI 10.1109/TSP.2017.2745440. Software release is version 1.0 (Nov. 15, 2018).
Jinseok Choi and Brian L. Evans, "Space-Time Baseband LTE Compression Software", copyright © 2016 by The University of Texas. This MATLAB release implements algorithms to compress uplink baseband cellular LTE signals received by an antenna array. Software release accompanies the paper "Space-Time Fronthaul Compression of Complex Baseband Uplink LTE Signals" in the 2016 IEEE International Conference on Communications. Version 1.0 (April 4, 2016).
SOFTWARE RELEASE
Available at http://users.ece.utexas.edu/~bevans/projects/mimo/software.html

## Slide 46: REFERENCES
[Akdeniz&Rappaport14] M. R. Akdeniz, Y. Liu, M. K. Samimi. S. Sun, S. Rangan, T. S. Rappaport, E. Erkip, "Millimeter wave channel modeling and cellular capacity evaluation." IEEE Journal on Sel. Areas in Comm. 32.6 (2014): 1164-1179.
[Andrews14] J. G. Andrews, S. Buzzi, W. Choi, S. V. Hanly, A. Lozano, A. C. K. Soong, J. C. Zhang, "What will 5G be?." IEEE Journal on Sel. Areas in Comm. 32.6 (2014): 1065-1082.
[Fletcher ] A. K. Fletcher, S. Rangan, V. K. Goyal, and K. Ramchandran, “Robust predictive quantization: Analysis and design via convex optimization,” IEEE Journal of Sel. Topics in Signal Process., vol. 1, no. 4, pp. 618–632, Dec. 2007.
[Gersho&Gray12] Gersho, Allen, and Robert M. Gray. ”Vector quantization and signal compression”. Vol. 159. Springer Science & Business Media, 2012.
[Lee&Sung16] Gilwon Lee, Youngchul Sung, and Marios Kountouris. "On the performance of random beamforming in sparse millimeter wave channels." IEEE Journal of Sel. Topics in Signal Processing 10.3 (2016): 560-575.
[Lin&Tsai] Lin, Pu-Hsuan, and Shang-Ho Tsai. "Performance analysis and algorithm designs for transmit antenna selection in linearly precoded multiuser MIMO systems." IEEE Trans. on Veh. Tech. 61.4 (2012): 1698-1708.
[Méndez-Rial16], R. Méndez-Rial, C. Rusu, N. González-Prelcic, A. Alkhateeb, and R. W. Heath, “Hybrid MIMO architectures for millimeter wave Communications: Phase shifters or switches?” IEEE Access, vol. 4, pp. 247–267, Jan. 2016.
[Mo&Heath17] J. Mo, A. Alkhateeb, S. Abu-Surra and R. W. Heath, "Hybrid Architectures With Few-Bit ADC Receivers: Achievable Rates and Energy-Rate Tradeoffs," in IEEE Transactions on Wireless Communications, vol. 16, no. 4, pp. 2274-2287, April 2017
[Nemhauser78] G. L. Nemhauser, L. A. Wolsey, and M. L. Fisher, “An analysis of approximations for maximizing submodular set functions–I,” Math. Programming, vol. 14, no. 1, pp. 265–294, 1978
[Pi&Khan11] Pi, Zhouyue, and Farooq Khan. "An introduction to millimeter-wave mobile broadband systems." IEEE Comm. Mag. 49.6 (2011).
[Yoo&Goldsmith06] Yoo, Taesang, and Andrea Goldsmith. "On the optimality of multiantenna broadcast scheduling using zero-forcing beamforming." IEEE Journal on Sel. Areas in Comm. 24.3 (2006): 528-541.
REFERENCES

## Slide 47: OUTLINE
1 | User scheduling in low-resolution ADC systems
2 | Resolution-adaptive ADC receiver architecture
3 | Base station antenna selection in low-resolution ADC systems
4 | Two-stage analog combining receiver architecture in low-resolution ADC systems
Millimeter wave communications with a large number of antennas
Motivation of my PhD dissertation
OUTLINE
Contributions
Future work
Summary
Background
Conclusion & Future work

## Slide 48: MILLIMETER WAVE SPECTRUM
[Pi&Khan11] Pi, Zhouyue, and Farooq Khan. "An introduction to millimeter-wave mobile broadband systems." IEEE Comm. Mag. 49.6 (2011).

## Slide 49: ADC POWER CONSUMPTION
Svensson, Christer, Stefan Andersson, and Peter Bogner. "On the power consumption of analog to digital converters." 2006 NORCHIP. IEEE, 2006.
n: quantization bits
fs: sampling rate

## Slide 50: SYSTEM ASSUMPTIONS
3GPP TR 36.931 V12.0.0 (2014-09)

## Slide 51: CONTRIBUTION 1 USER SCHEDULING
APPENDIX

## Slide 52: NEW USER SCHEDULING CRITERIA
For total # of channel paths
Solution of : structural scheduling criteria
Unique *AoAs at receiver for channel paths of each scheduled user:
Equal power spread across beamspace complex gains within each channel:
+
+
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
Aggregated channel gain at ADC
Unique AoAs
Equal power spread
minimize error here
Theorem A-1
Channel Hb
*Angle of arrivals
CONTRIBUTION 1

## Slide 53: PROOF OF THEOREM A-1
(a-c): sufficient conditions for maximizing sum rate
Two-stage maximization approach
1. Minimize
: channels have to be orthogonal
II. Maximize under orthogonal condition
: max rate for single user case
Non-overlap of channel gains
KKT condition: equal power spread
Case: total # of channel paths NRF
CONTRIBUTION 1

## Slide 54: PARTIAL CSI-BASED USER SCHEDULING
3. Max # of AoAs (+ max. chordal distance)
2. Chordal distance filtering
1. RF chain angle filtering
Alternative to instantaneous full CSI
*Angles of arrival (AoA): slowly-varying channel characteristics
  : reduces burden of estimating instantaneous full CSI at every channel coherence time
Chordal distance-based user scheduling
Steps
Filter users:
no AoAs in reduced range of angles of RF chains
Filter users:
Select user with max. # of AoAs.
If many:
measure separation between channel subspaces
Key idea
Channel
Vector
Chordal
Distance
CONTRIBUTION 1

## Slide 55: PERFORMANCE ANALYSIS – PARTIAL CSI
Remark
Ergodic sum rate analysis for single path
Exact AoA alignment
Arbitrary AoA
Proposition 1
Ergodic rate without quantization
rate loss due to quantization error
Proposition 2
As both converge to
CONTRIBUTION 1

## Slide 56: SIMULATION – PERFORMANCE VALIDATION
Sub-optimality
More beneficial
when SNR is high
Quantization error dominates thermal noise
: CSS is effective under coarse quantization
Why?
As NRF increases, channels become more orthogonal
: quantization error becomes major bottleneck
Why?
Marginal gain
Sub-optimality
Sum Rate vs. Transmit power
Sum Rate vs. # of RF chains
(40 RF chains)
(6 dB Tx power)
128 antennas, 200 candidate users, 12 scheduled users, 3 ADC bits, 3 average channel paths
Settings
Greedy: schedules user who provides maximum sum rate (sub-optimal performance with prohibitively high complexity)
NRF
Figure 1
Figure 2
CONTRIBUTION 1

## Slide 57: SIMULATION – ANALYSIS VALIDATION
Sum Rate vs. Transmit power
Sum Rate vs. # of ADC bits
128 antennas, 128 RF chains, 200 candidate users, 12 scheduled users, single channel path
Settings
Sum rate gap
Converges to
Channel leakage reduces quantization error
: equal power spread in Theorem 1
Why?
Figure 3
Figure 4
CONTRIBUTION 1

## Slide 58: CONTRIBUTION 2 ADAPTIVE ADC
APPENDIX

## Slide 59: EXTENSION TO RECEIVER POWER CONSTRAINT
Joint binary search algorithm
: solves total power constrained MMSQE bit allocation problem
Total receiver power constraint
# of active RF chains
: function of ADC bits (0-bit: inactive)
Resolution-switching power consumption
: function of previous bits and current bits
3. Total MSQE computation & comparison
2. BA solution for fixed Nact
1. Offline PSW estimation
Training and modeling
avg. PSW as function of power constraint
Challenges in total receiver power
Steps
Case:
(Nact + 1)
(Nact )
(Nact - 1)
Joint binary search for Nact & b
MSQE:
vs
vs
Go to smaller half
*Channel gains are sorted in descending order
CONTRIBUTION 2

## Slide 60: SUMMARY
CONTRIBUTION 2
Proposed resolution-adaptive ADC receiver
Near optimal bit-allocation
Selective bit allocation works for sparse channel with limited power consumption
Worst case analysis
RF chain
RF chain
Baseband
Combiner
RF chain
A
ADC
A
ADC
A
ADC
. . .
. . .
. . .
+
+
Resolution adaptive
ULA
. . .
High SNR: minimizes mean squared quantization error
Low SNR: maximizes generalized mutual information
Lower bound of Ergodic rate for proposed receiver architecture

## Slide 61: SYMBOL ERROR RATE (SER)
Achieves SER comparable to infinite-resolution case at around Ptot = 120 W
30 % total receiver power saving from 4~5-bit ADC system
80 % total receiver power saving from *infinite-bit (b = 12) ADC system
Proposed Method
*Power consumption of infinite-bit ADC system = 689 W
CONTRIBUTION 2

## Slide 62: CONTRIBUTION 3 ANTENNA SELECTION
APPENDIX

## Slide 63: GREEDY MI-MAXIMIZING ANTENNA SELECTION
Here, (a) comes from matrix determinant lemma
Decomposition of mutual information
where
(n+1) th row of Hn+1
Diagonal entry of D corresponding to fK(n+1)
At (n+1)th selection stage
(a)
Mutual information
quantization noise covariance
where
CONTRIBUTION 3

## Slide 64: COMPLEXITY OF QFAS ALGORITHM
Quantization-Aware Fast Antenna Selection (QAFAS)
Complexity
O(K Nr Nu)
Complexity for step 5: O()
  iterations x Inner product
Complexity for step 6: O()
  iterations x updates x Inner product
Large antenna arrays ()
Complexity analysis
  Overall complexity becomes O(K Nr Nu)
same as FAS
[Gharavi-Alkhansari04]
Proposed algorithm
CONTRIBUTION 3

## Slide 65: CONTRIBUTION 4 TWO-STAGE ANALOG COMBINING
APPENDIX

## Slide 66: PROOF OF THEOREM 2 - SCALING LAW
CONTRIBUTION 4
Rewrite mutual information
Define and rewrite mutual information
Jensen’s inequality
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 67: PROOF OF THEOREM 2 – TWO-STAGE SOLUTION
CONTRIBUTION 4
With two-stage solution in Theorem 2:
: NRF x NRF unitary matrix with constant modulus
Condition (i) and (ii)
Recall channel model:
As , we have:
and
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 68: SIMULATION RESULTS 3
Nr = 128, NRF = 43, Nu = 8, b = 2, and # paths = 3
CONTRIBUTION 4
Linear digital equalizers
Fig. 14: Rate vs. SNR
Proposed algorithm provides higher rates than one-stage algorithms
Proposed algorithm achieves MMSE performance with ZF whereas one-stage algorithms cannot achieve it
– one-stage algorithms suffer from large quantization errors
Simple equalizer can achieve high rate with two-stage analog combining

## Slide 69: ANALOG BEAMFORMING IN OFDM WITH LOW-RESOLUTION ADCS
Mutual Information for subcarrier n
Quantization noise covariance matrix
Quantization noise covariance matrix
Maximize gain by capturing frequency domain channel gain
Minimize quantization error by manipulating time domain delay channels
VS