## Slide 1: Channel Impairments

## Slide 2: Communication System Structure
Information sources
  Voice, music, images, video, and data (baseband signals)
Transmitter
  Signal processing block lowpass filters message signal
  Carrier circuits block upconverts baseband signal and bandpass filters to enforce transmission band
Review
baseband
baseband
bandpass
bandpass
baseband
baseband
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 3: Communication Channel
Transmission medium
  Wireline (twisted pair, coaxial, fiber optics)
  Wireless (indoor/air, outdoor/air, underwater, space)
Propagating signals degrade over distance
Repeaters can strengthen signal and reduce noise
  Simple repeater is a bandpass filter and power amplifier
Review
baseband
baseband
bandpass
bandpass
baseband
baseband
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Light painting Wi-Fi demo

## Slide 4: Impairment: Additive Thermal Noise
Models thermal noise in the analog/RF front end of a receiver

## Slide 5: Impairment: LTI Effects
Wired linear time-invariant (LTI) effects
  Resistor-inductor-capacitor (RLC) model of wired channel
  LTI system must be “at rest”– initial conditions must be zero (initial current across inductors and voltage across capacitors)
Second-order case
  Linear constant-coefficient differential equation (with zero initial conditions)
  Impulse response is a damped sinusoid
R
L
C
−
+
+
−
x(t)
y(t)
t = 0 : 0.001 : 1;
h = exp(-5*t) .* cos(2*pi*t);
plot(t, h);
xlabel('t'); ylabel('h(t)');
t
h(t)
Impulse Response Derivation

## Slide 6: Impairment: LTI Effects
Wireless LTI effects due to wave propagation
  Reflection, absorption, and scattering
Line of Sight
Two Bounces

## Slide 7: Impairment: LTI Effects
Linear time-invariant effects
  Distortion in frequency: due to channel frequency response
  Spreading in time: due to channel impulse response
Th
t
1
Tb
t
A
Model channel as LTI system; then approximate the infinite impulse response as finite; further approximate using rect. pulse for timing analysis
Communication Channel
input
output
x(t)
y(t)
Tb
-A
t
-A Th
t
Th+Tb
Th
Assume Th < Tb
t
Th+Tb
Th
A Th
Bit of ‘0’ or ‘1’

## Slide 8: Impairment: LTI Effects
Spreading Effect
Wired/wireless physical medium is IIR
t
h(t)
Model as FIR by truncating impulse response

## Slide 9: Impairment: Phase Jitter
Linear time-varying effects: Phase jitter
  Sinusoid at same fixed frequency experiences different phase shifts when passing through channel
  Visualize phase jitter in periodic waveform by plotting it over one period, superimposing second period on the first, etc.
fc = 1;
Tc = 1 / fc;
fs = 100*fc;
Ts = 1/fs;
t = Ts : Ts : Tc;
numPeriods = 10;
figure;
hold on;
for i = 1 : numPeriods
phase = 0.05*randn(1, length(t));
plot(t, cos(2*pi*fc*t + phase));
pause(1);
end
hold off;

## Slide 10: Impairment: Phase Jitter
Linear time-varying effects: Phase jitter
  Transmission of two-level sinusoidal amplitude modulation
    Bit of value ‘1’ becomes an amplitude of +1
    Bit of value ‘0’ becomes an amplitude of -1
  Visualize by superimposing each period on first (eye diagram)
fc = 1;
Tc = 1 / fc;
fs = 100*fc;
Ts = 1/fs;
t = Ts : Ts : Tc;
numPeriods = 10;
figure;
hold on;
for i = 1 : numPeriods
symAmp = round(2*(randn() > 0) - 1);
phase = 0.05*randn(1, length(t));
plot(t, symAmp*cos(2*pi*fc*t + phase));
pause(1);
end
hold off;

## Slide 11: Impairment: Additive Interference
Nonlinear effects
  Harmonics: due to quantization, voltage rectifiers, squaring devices, power amplifiers, etc.
  Additive noise: arises from many sources in transmitter, channel, and receiver (e.g. thermal noise)
  Additive interference: arises from other systems operating in transmission band
Spectrogram of emissions from a microwave oven in unlicensed 2.4 GHz band sweeping across IEEE 802.11g channels 1, 6, 11
[Nassar, Lin & Evans, 2011]
Keysight Wi-Fi demo

## Slide 12
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011
Impairment: Additive Interference
Home Powerline

## Slide 13
Spectrally-Shaped Background Noise
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011
Impairment: Additive Interference
Home Powerline

## Slide 14
Spectrally-Shaped Background Noise
Narrowband Interference
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011
Impairment: Additive Interference
Home Powerline

## Slide 15
Spectrally-Shaped Background Noise
Narrowband Interference
Periodic and
Asynchronous Interference
Measurement taken on a wall power plug in an apartment in Austin, Texas, on March 20, 2011
Impairment: Additive Interference
Home Powerline

## Slide 16: Impairment: Fading
Same as wireline channel impairments plus others
Fading: multiplicative noise
  Talking on a mobile phone and reception fades in and out
  Represented as time-varying gain that follows a particular probability distribution
Model #4: fading, LTI effects additive noise, and additive interference
FIR
+
noise
+
interference
fading