## Slide 1: INTRODUCTION TO THE TMS320C6000 VLIW DSP
Prof. Brian L. Evans
in collaboration with Dr. Niranjan Damera-Venkata and Mr. Magesh Valliappan
Embedded Signal Processing Laboratory The University of Texas at Austin Austin, TX 78712-1084
http://signal.ece.utexas.edu/
Accumulator architecture
Load-store architecture
Memory-register architecture

## Slide 2: Outline
C6000 instruction set architecture review
Vector dot product example
Pipelining
Finite impulse response filtering
Vector dot product example
Conclusion

## Slide 3: TI TMS320C6000 DSP Architecture (Review)
Program RAM
Data RAM
or Cache
Internal Buses
Control Regs
Regs (B0-B15)
Regs (A0-A15)
.D1
.M1
.L1
.S1
.D2
.M2
.L2
.S2
CPU
Addr
Data
External
Memory
-Sync
-Async
DMA
Serial Port
Host Port
Boot Load
Timers
Pwr Down
Simplified Architecture
C6200 fixed point C6400 fixed point C6700 floating point

## Slide 4: TI TMS320C6000 DSP Architecture (Review)
Address 8/16/32 bit data + 64-bit data on C67x
Load-store RISC architecture with 2 data paths
  16 32-bit registers per data path (A0-A15 and B0-B15)
  48 instructions (C6200) and 79 instructions (C6700)
Two parallel data paths with 32-bit RISC units
  Data unit - 32-bit address calculations (modulo, linear)
  Multiplier unit - 16 bit x 16 bit with 32-bit result
  Logical unit - 40-bit (saturation) arithmetic & compares
  Shifter unit - 32-bit integer ALU and 40-bit shifter
  Conditionally executed based on registers A1-2 & B0-2
  Can work with two 16-bit halfwords packed into 32 bits

## Slide 5: TI TMS320C6000 DSP Architecture (Review)
.M multiplication unit
  16 bit x 16 bit signed/unsigned packed/unpacked
.L arithmetic logic unit
  Comparisons and logic operations (and, or, and xor)
  Saturation arithmetic and absolute value calculation
.S shifter unit
  Bit manipulation (set, get, shift, rotate) and branching
  Addition and packed addition
.D data unit
  Load/store to memory
  Addition and pointer arithmetic

## Slide 6: C6000 Restrictions on Register Accesses
Function unit access to register files
  Data path 1 (2) units read/write A (B) registers
  Data path 2 (1) can read one A (B) register per instruction cycle with one-cycle latency
  Two simultaneous memory accesses cannot use registers of same register file as address pointers
  Limit of four 32-bit reads per register per inst. cycle
40-bit longs stored in adjacent even/odd registers
  Extended precision accumulation of 32-bit numbers
  Only one 40-bit result can be written per cycle
  40-bit read cannot occur in same cycle as 40-bit write
  4:1 performance penalty using 40-bit mode

## Slide 7: Other C6000 Disadvantages
No ALU acceleration for bit stream manipulation
  50% computation in MPEG-2 decoder spent on variable length decoding on C6200 in C
  C6400 direct memory access controllers shred bit streams (for video conferencing & wireless basestations)
Branch in pipeline disables interrupts: Avoid branches by using conditional execution
No hardware protection against pipeline hazards: Programmer and tools must guard against it
Must emulate many conventional DSP features
  No hardware looping: use register/conditional branch
  No bit-reversed addressing: use fast algorithm by Elster
  No status register: only saturation bit given by .L units

## Slide 8: FIR Filter
Difference equation (vector dot product)
y(n) = 2 x(n) + 3 x(n - 1) + 4 x(n - 2) + 5 x(n - 3)
y(n)
x(n)
3
4
2
5
Dot product of inputs vector and coefficient vector
Store input in circular buffer, coefficients in array
Tapped delay line
Signal flow graph
z-1
z-1
z-1

## Slide 9: FIR Filter
Each tap requires
  Fetching data sample
  Fetching coefficient
  Fetching operand
  Multiplying two numbers
  Accumulating multiplication result
  Possibly updating delay line (see below)
Computing an FIR tap in one instruction cycle
  Two data memory and one program memory accesses
  Auto-increment or auto-decrement addressing modes
  Modulo addressing to implement delay line as circular buffer
z-1
z-1
z-1
One tap

## Slide 10: Example: Vector Dot Product (Unoptimized)
A vector dot product is common in filtering
  Store a(n) and x(n) into an array of N elements
C6000 peaks at 8 RISC instructions/cycle
  For 300-MHz C6000, RISC instructions per sample
    300,000 for speech (sampling rate 8 kHz)
    54,421 for audio CD (sampling rate 44.1 kHz)
    230 for luminance NTSC digital video (sampling rate 10,368 kHz)
  Generally requires hand coding for peak performance

## Slide 11: Example: Vector Dot Product (Unoptimized)
Prologue
  Initialize pointers: A5 for a(n), A6 for x(n), and A7 for Y
  Move number of times to loop (N) into A2
  Set accumulator (A4) to zero
Inner loop
  Put a(n) into A0 and x(n) into A1
  Multiply a(n) and x(n)
  Accumulate multiplication result into A4
  Decrement loop counter (A2)
  Continue inner loop if counter is not zero
Epilogue
  Store the result into Y
Assuming coefficients & data are 16 bits wide

## Slide 12: Example: Vector Dot Product (Unoptimized)
; clear A4 and initialize pointers A5, A6, and A7
MVK .S1 40,A2 ; A2 = 40 (loop counter)
loop LDH .D1 *A5++,A0 ; A0 = a(n), H = halfword
LDH .D1 *A6++,A1 ; A1 = x(n), H = halfword
MPY .M1 A0,A1,A3 ; A3 = a(n) * x(n)
ADD .L1 A3,A4,A4 ; Y = Y + A3
SUB .L1 A2,1,A2 ; decrement loop counter
[A2] B .S1 loop ; if A2 != 0, then branch
STH .D1 A4,*A7 ; *A7 = Y
Coefficients a(n)
Data x(n)
Using A data path only

## Slide 13
Example: Vector Dot Product (Unoptimized)
MoVeKonstant
  MVK .S 40,A2 ; A2 = 40
  Lower 16 bits of A2 are loaded
Conditional branch
  [condition] B .S loop
  [A2] means to execute instruction if A2 != 0 (same as C language)
  Only A1, A2, B0, B1, and B2 can be used (not symmetric)
Loading registers
  LDH .D *A5, A0 ;Loads half-word into A0 from memory
Registers may be used as pointers (*A1++)
Implementation not efficient due to pipeline effects

## Slide 14: Pipelining
CPU operations
  Fetch instruction from (on-chip) program memory
  Decode instruction
  Execute instruction including reading data values
Overlap operations to increase performance
  Pipeline CPU operations to increase clock speed over a sequential implementation
  Separate parallel functional units
  Peripheral interfaces for I/O do not burden CPU

## Slide 15: Pipelining
Managing Pipelines
compiler or programmer (TMS320C6000)
pipeline interlocking in processor (TMS320C30)
hardware instruction scheduling
Sequential (Motorola 56000)
Pipelined (Most conventional DSP processors)
Superscalar (Pentium, MIPS)
Superpipelined (TMS320C6000)
Fetch
Read
Execute
Decode
Fetch
Decode
Execute
Fetch
Read
Execute
Decode
Fetch
Read
Execute
Decode

## Slide 16: TMS320C6000 Pipeline
One instruction cycle every clock cycle
Deep pipeline
  7-11 stages in C62x: fetch 4, decode 2, execute 1-5
  7-16 stages in C67x: fetch 4, decode 2, execute 1-10
  If a branch is in the pipeline, interrupts are disabled
  Avoid branches by using conditional execution
No hardware protection against pipeline hazards
  Compiler and assembler must prevent pipeline hazards
Dispatches instructions in packets

## Slide 17: Program Fetch (F)
Program fetching consists of 4 phases
  Generate fetch address (FG)
  Send address to memory (FS)
  Wait for data ready (FW)
  Read opcode (FR)
Fetch packet consists of 8 32-bit instructions
C6000
Memory
FG
FS
FW
FR

## Slide 18: Decode Stage (D)
Decode stage consists of two phases
  Dispatch instruction to functional unit (DP)
  Instruction decoded at functional unit (DC)
C6000
Memory
FG
FS
FW
FR
DC
DP

## Slide 19: Execute Stage (E)

## Slide 20: Vector Dot Product with Pipeline Effects
pipeline
; clear A4 and initialize pointers A5, A6, and A7
MVK .S1 40,A2 ; A2 = 40 (loop counter)
loop LDH .D1 *A5++,A0 ; A0 = a(n), H = halfword
LDH .D1 *A6++,A1 ; A1 = x(n), H = halfword
MPY .M1 A0,A1,A3 ; A3 = a(n) * x(n)
ADD .L1 A3,A4,A4 ; Y = Y + A3
SUB .L1 A2,1,A2 ; decrement loop counter
[A2] B .S1 loop ; if A2 != 0, then branch
STH .D1 A4,*A7 ; *A7 = Y
Load has a delay of four cycles
Multiplication has a delay of 1 cycle

## Slide 21: Fetch packet
MVK
LDH
LDH
MPY
ADD
SUB
B
STH
(F1-4)
F
DP
E1
DC
E2
E3
E4
E5
E6
Time (t) = 4 clock cycles

## Slide 22: Dispatch
F(2-5)
F
DP
E1
MVK
LDH
LDH
MPY
ADD
SUB
B
STH
DC
E2
E3
E4
E5
E6
Time (t) = 5 clock cycles

## Slide 23: Decode
F(2-5)
F
DP
E1
LDH
LDH
MPY
ADD
SUB
B
STH
DC
MVK
E2
E3
E4
E5
E6
Time (t) = 6 clock cycles

## Slide 24: Execute (E1)
F(2-5)
F
DP
E1
LDH
MPY
ADD
SUB
B
STH
DC
LDH
E2
E3
E4
E5
E6
MVK
Time (t) = 7 clock cycles

## Slide 25: Execute (MVK done LDH in E1)
F(2-5)
F
DP
E1
MPY
ADD
SUB
B
STH
DC
LDH
E2
E3
E4
E5
E6
LDH
Time (t) = 8 clock cycles
MVK Done

## Slide 26: Vector Dot Product with Pipeline Effects
; clear A4 and initialize pointers A5, A6, and A7
MVK .S1 40,A2 ; A2 = 40 (loop counter)
loop LDH .D1 *A5++,A0 ; A0 = a(n)
LDH .D1 *A6++,A1 ; A1 = x(n)
NOP 4
MPY .M1 A0,A1,A3 ; A3 = a(n) * x(n)
NOP
ADD .L1 A3,A4,A4 ; Y = Y + A3
SUB .L1 A2,1,A2 ; decrement loop counter
[A2] B .S1 loop ; if A2 != 0, then branch
NOP 5
STH .D1 A4,*A7 ; *A7 = Y
Assembler will automatically insert NOP instructions
Assembler can also make sequential code parallel

## Slide 27: Optimized Vector Dot Product on the C6000
Split summation into two summations
Prologue
  Initialize pointers: A5 for a(n), B6 for x(n), A7 for y(n)
  Move number of times to loop (N) divided by 2 into A2
Inner loop
  Put a(n) and a(n+1) in A0 and x(n) and x(n+1) in A1 (packed data)
  Multiply a(n) x(n) and a(n+1) x(n+1)
  Accumulate even (odd) indexed terms in A4 (B4)
  Decrement loop counter (A2)
Store result
16-bit data/ coefficients

## Slide 28: FIR Filter Implementation on the C6000
MVK .S1 0x0001,AMR ; modulo block size 2^2
MVKH .S1 0x4000,AMR ; modulo addr register B6
MVK .S2 2,A2 ; A2 = 2 (four-tap filter)
ZERO .L1 A4 ; initialize accumulators
ZERO .L2 B4
; initialize pointers A5, B6, and A7
fir LDW .D1 *A5++,A0 ; load a(n) and a(n+1)
LDW .D2 *B6++,B1 ; load x(n) and x(n+1)
MPY .M1X A0,B1,A3 ; A3 = a(n) * x(n)
MPYH .M2X A0,B1,B3 ; B3 = a(n+1) * x(n+1)
ADD .L1 A3,A4,A4 ; yeven(n) += A3
ADD .L2 B3,B4,B4 ; yodd(n) += B3
[A2] SUB .S1 A2,1,A2 ; decrement loop counter
[A2] B .S2 fir ; if A2 != 0, then branch
ADD .L1 A4,B4,A4 ; Y = Yodd + Yeven
STH .D1 A4,*A7 ; *A7 = Y
Throughput of two multiply-accumulates per instruction cycle

## Slide 29: Conclusion
Conventional digital signal processors
  High performance vs. power consumption/cost/volume
  Excel at one-dimensional processing
  Have instructions tailored to specific applications
TMS320C6000 VLIW DSP
  High performance vs. cost/volume
  Excel at multidimensional signal processing
  Maximum of 8 RISC instructions per cycle

## Slide 30: Conclusion
Web resources
  comp.dsp news group: FAQ www.bdti.com/faq/dsp_faq.html
  embedded processors and systems: www.eg3.com
  on-line courses and DSP boards: www.techonline.com
References
  R. Bhargava, R. Radhakrishnan, B. L. Evans, and L. K. John, “Evaluating MMX Technology Using DSP and Multimedia Applications,” Proc. IEEE Sym. Microarchitecture, pp. 37-46, 1998.http://www.ece.utexas.edu/~ravib/mmxdsp/
  B. L. Evans, “EE345S Real-Time DSP Laboratory,” UT Austin. http://www.ece.utexas.edu/~bevans/courses/realtime/
  B. L. Evans, “EE382C Embedded Software Systems,” UT Austin.http://www.ece.utexas.edu/~bevans/courses/ee382c/

## Slide 31
FIR Filter on a TMS320C5000
COEFFP .set 02000h ; Program mem address
X .set 037Fh ; Newest data sample
LASTAP .set 037FH ; Oldest data sample
…
LAR AR3, #LASTAP ; Point to oldest sample
RPT #127 ; Repeat next inst. 126 times
MACD COEFFP, *- ; Compute one tap of FIR
APAC
SACH Y,1 ; Store result -- note shift
Coefficients
Data
Supplemental Slides

## Slide 32: TMS320C6200 vs. StarCore S140
* Does not count equivalent RISC operations for modulo addressing ** On the C6200, there is a performance penalty for 40-bit accumulation
Supplemental Slides