## Slide 1: Matched Filtering and Digital Pulse Amplitude Modulation (PAM)

## Slide 2: Outline
Transmitting one bit at a time
Tb
t
A
‘1’ bit
t
Tb
‘1’ bit
‘0’ bit
Th+Tb
Matched filtering
PAM system
Intersymbol interference
Communication performance
  Bit error probability for binary signals
  Symbol error probability
Eye diagram (in lab)

## Slide 3: Transmitting One Bit
Transmission on communication channels is analog
Two-level digital pulse amplitude modulation (PAM)
Tb
t
A
‘1’ bit
Additive Noise Channel
input
output
x(t)
y(t)
Tb
-A
‘0’ bit
t
How does the receiver decide which bit was sent?
receive‘1’ bit
Tb
t
A
receive ‘0’ bit
Tb
-A
t
14 - 3

## Slide 4: Transmitting One Bit
Two-level digital pulse amplitude modulation over channel that has memory but does not add noise
Th
t
1
Tb
t
A
Tb
-A
t
-A Th
t
Th+Tb
Th
Assume Th < Tb
t
Th+Tb
Th
A Th
Bit of ‘0’ or ‘1’
Communication Channel
input
output
x(t)
y(t)
Model channel as LTI system
Approximate infinite impulse response as a rectangular pulse for timing analysis
t

## Slide 5: Transmitting Two Bits (Interference)
Transmitting two bits (pulses) back-to-back will cause overlap (interference) at the receiver
Th
t
1
Assume that Th < Tb
t
Tb
A
‘1’ bit
‘0’ bit
2Tb
*
=
Intersymbol interference
-A Th
t
Tb
‘1’ bit
‘0’ bit
Th+Tb
Sample y(t) at Tb, 2 Tb, …, and threshold with threshold of zero
How do we prevent intersymbol interference (ISI) at the receiver?
14 - 5

## Slide 6: Preventing ISI at Receiver
Option #1: wait Th seconds between pulses in transmitter (called guard period or guard interval)
Assume that Th < Tb
*
Th
t
1
=
t
Tb
A
‘1’ bit
‘0’ bit
Th+Tb
t
-A Th
Tb
‘1’ bit
‘0’ bit
Th+Tb
Th
Option #2: use channel equalizer in receiver
  FIR filter designed via training sequences sent by transmitter
  Design goal: cascade of channel memory and channel equalizer should give all-pass frequency response
14 - 6

## Slide 7: Digital 2-level PAM System
Transmitter
Receiver
Transmitted signal
Reliable communication requires synchronization of symbol clocks between transmitter and receiver
Serial/ Parallel
1
J
bits
Map
an
symbol amplitude
s*(t)
baseband waveform
Interpolation
symbol of bits
Sample at
y(ti)
t = i Tsym
y(t)
h(t)
matched filter
1
0
DecisionBlock
bits
x(t)
Channel
  Interpolation pulse shape g(t) with g(0) = 1 and g(k Tsym) = 0 for and with lowpass frequency content
14 - 7

## Slide 8: Matched Filter
Detection of pulse in presence of additive noise
  Receiver knows what pulse shape it is looking for
  Channel memory ignored (assumed compensated by other means, e.g. channel equalizer in receiver)
Additive white Gaussian noise (AWGN) with zero mean and variance N0 /2
g(t)
Pulse shape
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
T is the symbol period
14 - 8

## Slide 9: Matched Filter Derivation
Design of matched filter
  Maximize signal power i.e. power of at t = T
  Minimize noise i.e. power of
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
T is the symbol period
Combine design criteria
14 - 9
Maximize , where is peak pulse SNR

## Slide 10: Power Spectra
Deterministic signal x(t) w/ Fourier transform X(f)
  Power spectrum is square of absolute value of magnitude response (phase is ignored)
t
1
x(t)
0
Ts
t
Rx(t)
-Ts
Ts
Ts
  Multiplication in Fourier domain is convolution in time domain
Autocorrelation of x(t)
  Maximum value (when it exists) is at Rx(0)
  Rx(t) is even symmetric, i.e. Rx(t) = Rx(-t)
  Conjugation in Fourier domain is reversal & conjugation in time

## Slide 11: Power Spectra
Two-sided random signal n(t)
  Fourier transform may not exist, but power spectrum exists
N = 16384; % finite no. of samples gaussianNoise = randn(N,1); plot( abs(fft(gaussianNoise)) .^ 2 );
approximate noise floor
time-averaged
Estimate noise power spectrum in Matlab
  For zero-mean Gaussian random process n(t) with variance s2
14 - 11

## Slide 12: Matched Filter Derivation
Noise
f
Noise power spectrum SW(f)
g(t)
Pulse signal
w(t)
x(t)
h(t)
y(t)
t = T
y(T)
Matched filter
AWGN
Matched filter
T is the symbol period
Signal
14 - 12

## Slide 13: Matched Filter Derivation
Find h(t) that maximizes pulse peak SNR h

a
b
Schwartz’s inequality
  For vectors:
  For functions:
  upper bound reached iff
14 - 13

## Slide 14: Matched Filter Derivation
T is the symbol period
14 - 14

## Slide 15: Matched Filter
Impulse response is hopt(t) = k g*(T - t)
  Symbol period T, transmitter pulse shape g(t) and gain k
  Scaled, conjugated, time-reversed, and shifted version of g(t)
  Duration and shape determined by pulse shape g(t)
Maximizes peak pulse SNR
  Does not depend on pulse shape g(t)
  Proportional to signal energy (energy per bit) Eb
  Inversely proportional to power spectral density of noise
14 - 15

## Slide 16: Matched Filter for Rectangular Pulse
Matched filter for causal rectangular pulse shape
  Impulse response is causal rectangular pulse of same duration
Convolve input with rectangular pulse of duration T sec and sample result at T sec is same as
  First, integrate for T sec
  Second, sample at symbol period T sec
  Third, reset integration for next time period
Integrate and dump circuit
T
Sample and dump
t=nT
h(t) = ___
14 - 16

## Slide 17: Matched Filter for Rectangular Pulse
14 - 17

## Slide 18: Bit Error Probability for 2-PAM
Tb is bit period (bit rate is fb = 1/Tb)
  w(t) is spectrally flat noise that follows a Gaussian distribution with zero mean and variance 2
h(t)
s(t)
Sample at
t = nTb
Matched filter
w(t)
r(t)
r(t)
rn
r(t) = h(t) * r(t)
Lowpass filtering a Gaussian random process produces another Gaussian random process
  Mean scaled by H(0)
  Variance scaled by twice lowpass filter’s bandwidth
Matched filter’s bandwidth is ½ fb
14 - 18

## Slide 19: Bit Error Probability for 2-PAM
Noise power at matched filter output
Noise power
T = Tsym
Filtered noise
s2 d(t1–t2)
14 - 19

## Slide 20: Bit Error Probability for 2-PAM
Symbol amplitudes of +A and -A
Rectangular pulse shape with amplitude 1
Bit duration (Tb) of 1 second
Matched filtering with gain of one (see slide 14-15)
  Integrate received signal over nth bit period and sample
0
-
Probability density function (PDF)
14 - 20

## Slide 21: Bit Error Probability for 2-PAM
Probability of error given that transmitted pulse has amplitude –A
Q function is on next slide
PDF for N(0, 1)
0
Tb = 1
Random variable is Gaussian with zero mean and variance of one
14 - 21

## Slide 22: Q Function
Q function
Erfc[x] in Mathematica
erfc(x) in Matlab
Relationship
Complementary error function erfc
14 - 22

## Slide 23: Bit Error Probability for 2-PAM
Probability of error given that transmitted pulse has amplitude A
Tb = 1
Probability of error exponentially decreases with SNR (see slide 8-16)
Assume that 0 and 1 are equally likely bits
14 - 23

## Slide 24: PAM Symbol Error Probability
Set symbol time (Tsym) to 1 second
Constellation points with receiver decision boundaries
2-PAM
d
-d
4-PAM
d
d
3 d
3 d
M-level PAM symbol amplitudes
With each symbol equally likely
Average transmitted signal power
  GT(w) square root raised cosine spectrum
14 - 24

## Slide 25: PAM Symbol Error Probability
Noise power and SNR
two-sided power spectral density of AWGN
channel noise after matched filtering and sampling
Assume ideal channel, i.e. one without ISI
Consider two outer levels in constellation
Consider M-2 inner levels in constellation
  Error only if
  where
  Probability of error is
14 - 25

## Slide 26: PAM Symbol Error Probability
Assuming that each symbol is equally likely, symbol error probability for M-level PAM
M-2 interior points
2 exterior points
Symbol error probability in terms of SNR
14 - 26

## Slide 27: Eye Diagram for 2-PAM
Useful for PAM transmitter and receiver analysis and troubleshooting
M=2
Sampling instant
Slope indicates sensitivity to timing error
Distortion over zero crossing
Margin over noise
The more open the eye, the better the reception
t - Tsym
Interval over which it can be sampled
t + Tsym
t
14 - 27

## Slide 28: Eye Diagram for 4-PAM
3d
d
-d
-3d
Due to startup transients.
Fix is to discard first few symbols equal to number of symbol periods in pulse shape.
14 - 28

## Slide 29: Symbol Clock Recovery
Transmitter and receiver normally have different oscillator circuits
Critical for receiver to sample at correct time instances to have max signal power and min ISI
Receiver should try to synchronize with transmitter clock (symbol frequency and phase)
  First extract clock information from received signal
  Then either adjust analog-to-digital converter or interpolate
Next slides develop adjustment to A/D converter
Also, see Handout M in the reader
Optional
14 - 29

## Slide 30: Symbol Clock Recovery
g1(t) is impulse response of LTI composite channel of pulse shaper, noise-free channel, receive filter
Optional
Receive
B(w)
Squarer
BPF
H(w)
PLL
x(t)
q(t)
q2(t)
p(t)
z(t)
E{ak am} = a2 d[k-m]
g1(t) is deterministic
s*(t) is transmitted signal
Periodic with period Tsym
14 - 30

## Slide 31: Symbol Clock Recovery
Fourier series representation of E{ p(t) }
In terms of g1(t) and using Parseval’s relation
Fourier series representation of E{ z(t) }
where
Optional
Receive
B(w)
Squarer
BPF
H(w)
PLL
x(t)
q(t)
q2(t)
p(t)
z(t)
14 - 31

## Slide 32: Symbol Clock Recovery
With G1(w) = X(w) B(w)
  Choose B(w) to pass  ½wsym  pk = 0 except k = -1, 0, 1
  Choose H(w) to pass wsym  Zk = 0 except k = -1, 1
B(w) is lowpass filter with wpassband = ½ wsym
H(w) is bandpass filter with center frequency wsym
Optional
Receive
B(w)
Squarer
BPF
H(w)
PLL
x(t)
q(t)
q2(t)
p(t)
z(t)
14 - 32