## Slide 1: Data Conversion
Slides by Prof. Brian L. Evans, Dept. of ECE, UT Austin, and Dr. Thomas D. Kite, Audio Precision, Beaverton, OR tomk@audioprecision.com
Dr. Ming Ding, when he was at the Dept. of ECE, UT Austin, converted slides by Dr. Kite to PowerPoint format
Some figures are from Ken C. Pohlmann, Principles of Digital Audio, McGraw-Hill, 1995.

## Slide 2: Image Halftoning
Handout J on noise-shaped feedback coding
  Different ways to perform one-bit quantization (halftoning)
  Original image has 8 bits per pixel original image (pixel values range from 0 to 255 inclusive)
No noise shaping
No noise shaping
Pixel thresholding: Same threshold at each pixel
  Gray levels from 128-255 become 1 (white)
  Gray levels from 0-127 become 0 (black)
Ordered dither: Periodic space-varying thresholding
  Equivalent to adding spatially-varying dither (noise) at input to threshold operation (quantizer)
  Example uses 16 different thresholds in a 4  4 mask
  Periodic artifacts appear as if screen has been overlaid

## Slide 3: Image Halftoning
Error diffusion: Noise-shaping feedback coding
  Contains sharpened original plus high-frequency noise
  Human visual system less sensitive to high-frequency noise (as is the auditory system)
  Example uses four-tap Floyd-Steinberg noise-shaping (i.e. a four-tap IIR filter)
Image quality of halftones
  Thresholding (low): error spread equally over all freq.
  Ordered dither (medium): resampling causes aliasing
  Error diffusion (high): error placed into higher frequencies
Noise-shaped feedback coding is a key principle in modern A/D and D/A converters

## Slide 4: Digital Halftoning Methods
Clustered Dot Screening
AM Halftoning
Blue-noise Mask FM Halftoning 1993
Dispersed Dot Screening
FM Halftoning
Green-noise Halftoning
AM-FM Halftoning 1992
Error Diffusion
FM Halftoning 1975
Direct Binary Search
FM Halftoning 1992

## Slide 5: Screening (Masking) Methods
Periodic array of thresholds smaller than image
  Spatial resampling leads to aliasing (gridding effect)
  Clustered dot screening produces a coarse image that is more resistant to printer defects such as ink spread
  Dispersed dot screening has higher spatial resolution

## Slide 6: Grayscale Error Diffusion
Error Diffusion Halftone
Shapes quantization error (noise) into high frequencies
Type of sigma-delta modulation
Error filter h(m) is lowpass
b(m)
+
_
_
+
e(m)
x(m)
difference
threshold
compute error (noise)
shape error (noise)
u(m)
current pixel
weights
3/16
7/16
5/16
1/16
Floyd-Steinberg filter h(m)
Spectrum

## Slide 7: Old-Style A/D and D/A Converters
Used discrete components (before mid-1980s)
Analog Lowpass Filter
Quantizer
Sampler at sampling rate of fs
Analog Lowpass Filter
Discrete to Continuous Conversion
fs
A/D Converter
  Lowpass filter has stopband frequency of ½ fs or less
D/A Converter
  Lowpass filter has stopband frequency of ½ fs or less
  Discrete-to-continuous conversion could be as simple as sample and hold

## Slide 8: Cost of Multibit Conversion Part I: Brickwall Analog Filters
A
B
C
D
Pohlmann Fig. 3-5 Two examples of passive Chebyshev lowpass filters and their frequency responses. A. A passive low-order filter schematic. B. Low-order filter frequency response. C. Attenuation to -90 dB is obtained by adding sections to increase the filter’s order. D. Steepness of slope and depth of attenuation are improved.

## Slide 9: Cost of Multibit Conversion Part II: Low- Level Linearity
Pohlmann Fig. 4-3 An example of a low-level linearity measurement of a D/A converter showing increasing non-linearity with decreasing amplitude.

## Slide 10: Solutions
Oversampling eases analog filter design
  Also creates spectrum to put noise at inaudible frequencies
Add dither (noise) at quantizer input
  Breaks up harmonics (idle tones) caused by quantization
Shape quantization noise into high frequencies
  Auditory system is less sensitive at higher frequencies
State-of-the-art in 20-bit/24-bit audio converters
  Oversampling 64x 256x 512x
  Quantization 8 bits 6 bits 5 bits
  Additive dither 2-bit  PDF 2-bit  PDF 2-bit  PDF
  Noise shaping 5th / 7th order 5th / 7th order 5th / 7th order
  Dynamic range 110 dB 120 dB 120 dB

## Slide 11: Solution 1: Oversampling
A. A brick-wall filter must sharply bandlimit the output spectra.
B. With four-times oversampling, images appear only at the oversampling frequency.
C. The output sample/hold (S/H) circuit can be used to further suppress the oversampling spectra.
Pohlmann Fig. 4-15 Image spectra of nonoversampled and oversampled reconstruction. Four times oversampling simplifies reconstruction filter.

## Slide 12: Solution 2: Add Dither
Pohlmann Fig. 2-8 Adding dither at quantizer input alleviates effects of quantization error. A. An undithered input signal with amplitude on the order of one LSB. B. Quantization results in a coarse coding over two levels. C. Dithered input signal. D. Quantization yields a PWM waveform that codes information below the LSB.

## Slide 13: Time Domain Effect of Dither
A A 1 kHz sinewave with amplitude of one-half LSB without dither produces a square wave.
C Modulation carries the encoded sinewave information, as can be seen after 32 averagings.
B Dither of one-third LSB rms amplitude is added to the sinewave before quantization, resulting in a PWM waveform.
D Modulation carries the encoded sinewave information, as can be seen after 960 averagings.
Pohlmann Fig. 2-9 Dither permits encoding of information below the least significant bit. Vanderkooy and Lipshitz.

## Slide 14: Frequency Domain Effect of Dither
undithered
dithered
undithered
dithered
Pohlmann Fig. 2-10 Computer-simulated quantization of a low-level 1- kHz sinewave without, and with dither. A. Input signal. B. Output signal (no dither). C. Total error signal (no dither). D. Power spectrum of output signal (no dither). E. Input signal. F. Output signal (triangualr pdf dither). G. Total error signal (triangular pdf dither). H. Power spectrum of output signal (triangular pdf dither) Lipshitz, Wannamaker, and Vanderkooy

## Slide 15: Solution 3: Noise Shaping
We have a two-bit DAC and four-bit input signal words. Both are unsigned.
1 sample
delay
Input signal
words
To DAC
4
2
2
2
Assume input = 1001 constant
Adder Inputs Output Time Upper Lower Sum to DAC
1 1001 00 1001 10
2 1001 01 1010 10
3 1001 10 1011 10
4 1001 11 1100 11
Periodic
Average output = 1/4(10+10+10+11)=1001
4-bit resolution at DC!
Going from 4 bits down to 2 bits increases noise by ~ 12 dB. However, the shaping eliminates noise at DC at the expense of increased noise at high frequency.
added
noise
f
12 dB
(2 bits)
If signal is in
this band, you are
better off!
Let’s hope this is
above the passband!
(oversample)

## Slide 16: Putting It All Together
A/D converter samples at fs and quantizes to B bits
Sigma delta modulator implementation
  Internal clock runs at M fs
  FIR filter expands wordlength of b[m] to B bits
b[m]
+
_
_
+
e[m]
v[m]
dither
quantizer
x[m]
x(t)
Sample and hold
M fs
FIR Filter
M