## Slide 1: Finite Impulse Response Filters

## Slide 2: Outline
Many Roles for Filters
Convolution
Z-transforms
Linear time-invariant systems
  Transfer functions
  Frequency responses
Finite impulse response (FIR) filters
  Filter design
  Cascading FIR filters demonstration
  Linear phase

## Slide 3: Many Roles for Filters
Noise removal
  Bandpass filtering to suppress out-of-band noise (slide 1-5)
w
wc
- wc
Bandpass Spectrum In Noise
LPF
HPF
x0[m]
x1[m]
x[m]
r[m]
x[m]
System Model (Filter)
Equalizer
Goal is to make cascade all-pass
Spectral analysis
  Two-channel filter bank on right
  Used in interpolation (slide 13-9)
Spectral shaping
  Data conversion (lectures 10/11)
  Equalization (slides 6-15 & 16-7)
  Carrier frequency/phase recovery
  Timing recovery (slide 13-17 & 16-10)

## Slide 4: Spectral Analysis
Analysis: decompose signal into frequency bands
  Graphic equalizer: apply separate gain to each band
  Compression: spend more bits on more important bands
Synthesis: combine bands into one signal
Example: Two-band filter bank / wavelet
  LPF – averaging: x0[m] = ½ x[m] + ½ x[m-1]
  HPF – first-order difference: x1[m] = ½ x[m] - ½ x[m-1]
  Exact reconstruction of x[m] is possible through synthesis
LPF
HPF
x0[m]
x1[m]
x[m]
Analysis
x0[m]
x1[m]
x[m]
+
Synthesis

## Slide 5: Finite Impulse Response (FIR) Filter
Same as discrete-time tapped delay line (slide 3-22)
Discrete-time convolution
z-1
z-1
z-1
…
…
x[n]
S
y[n]
h[0]
h[1]
h[2]
h[M-1]
x[n-1]
Impulse response h[n] has finite extent n = 0,…, M-1

## Slide 6: Discrete-time Convolution Derivation
Output y[n] for input x[n]
y[n] = h[0] x[n] + h[1] x[n-1]
= ( x[n] + x[n-1] ) / 2
n
h[n]
Averaging filter impulse response
0
1
2
3
Review
Any signal can be decomposed into sum of discrete impulses
Apply linearity properties
Apply shift-invariance
Apply change of variables

## Slide 7: Convolution Comparison
Continuous-time convolution of x(t) and h(t)
  For each t, compute different (possibly) infinite integral
Review
In discrete-time, replace integral with summation
  For each n, compute different (possibly) infinite summation
LTI system
  Characterized uniquely by its impulse response
  Its output is convolution of the input and its impulse response

## Slide 8: Convolution Demos
Signal Processing First Matlab Demonstrations
  Continuous-Time http://dspfirst.gatech.edu/matlab/#cconvdemo
  Discrete-Time http://dspfirst.gatech.edu/matlab/#dconvdemo
t
1
x(t)
0
Ts
2Ts
Ts
t
1
h(t)
0
Ts
*
=
y(t)
Ts
t
What about convolving two pulses of different lengths? See Appendix E
Convolving two signals of finite lengths
  Continuous-Time y(t) = x(t) * h(t) Ly = Lx + Lh
  Discrete-Time y[n] = x[n] * h[n] Ly = Lx + Lh − 1
Convolving two causal signals?

## Slide 9: Z-transform Definition
For discrete-time systems, z-transforms play same role as Laplace transforms do in continuous-time
Bilateral Forward z-transform
Bilateral Inverse z-transform
Review
  Inverse transform requires contour integration over closed contour (region) R
  Contour integration covered in a Complex Analysis course
Compute forward and inverse transforms using transform pairs and properties

## Slide 10: Three Common Z-transform Pairs
Finite extent sequences
Infinite extent sequence
Review
  Region of convergence: entire z-plane
h[n] = d[n-1]
  Region of convergence: entire z-plane except z = 0
  h[n-1]  z-1 H(z)
  Region of convergence for summation: |z| > |a|
  |z| > |a| is the complement of a disk (see next slide)
h[n] = an u[n]
h[n] = d[n]

## Slide 11: Region of Convergence
Region of the complex z-plane for which forward z-transform converges
Im{z}
Re{z}
Entire plane
Im{z}
Re{z}
Complement of a disk
Im{z}
Re{z}
Disk
Im{z}
Re{z}
Intersection of a disk and complement of a disk
Four possibilities (z = 0 is special case that may or may not be included)
Review

## Slide 12: System Transfer Function
Z-transform of system’s impulse response
  Impulse response uniquely represents an LTI system
Review
Example: FIR filter with M coefficients (slide 5-5)
  Transfer function H(z) is polynomial in powers of z -1
  Region of convergence (ROC) is entire z-plane except z = 0
Since ROC includes unit circle, substitute z = e j w into transfer function to obtain frequency response

## Slide 13: Example: Ideal Delay
Continuous Time
Discrete Time
x(t)
y(t)
x[n]
y[n]
Linear Phase
Allpass Filter
w = W T
  LTI delay by T seconds
  Impulse response
  Frequency response
  LTI delay by 1 sample
  Impulse response
  Frequency response

## Slide 14: Phase Shift in Time Domain
Continuous Time
Discrete Time
x(t)
y(t)
  LTI delay by T seconds
  Sinusoidal input signal
  Sinusoidal output signal
  LTI delay by N samples
  Sinusoidal input signal
  Sinusoidal output signal
x[n]
y[n]
Phase shift

## Slide 15: Linear Time-Invariant Systems
Fundamental Theorem of Linear Systems
  If a complex sinusoid were input into an LTI system, then output would be input scaled by frequency response of LTI system (evaluated at complex sinusoidal frequency)
  Scaling may attenuate complex sinusoid and shift it in phase (complex sinusoids are eigenfunctions of LTI systems)
  Continuous-time example: see handout F (lowpass RC filter)
  Discrete-time derivation: Input x[n] = e j w n into LTI system
H(w)
x[n] * h[n]
  H(w) is frequency response (DT Fourier transform of h[n])

## Slide 16: Frequency Response
Continuous-time LTI system
Discrete-time LTI system
For real-valued impulse response H(e -j ω) = H*(e j ω)
  Input
  Output

## Slide 17: Frequency Response
System response to complex sinusoid e j w n for all possible frequencies w in radians per sample:
w
|H(w)|
wp
wstop
-wstop
-wp
passband
stopband
stopband
w
|H(w)|
Linear phase
  Lowpass filter: passes low and attenuates high frequencies
  Linear phase / constant group delay: FIR filter whose impulse response is symmetric or anti-symmetric about its midpoint
Not all FIR filters exhibit linear phase

## Slide 18: FIR Filter Design
Specify desired piecewise constant magnitude resp.
Apass passband tolerance (dB) Astop stopband attenuation (dB) AdB = 20 log10(A)
0
Astop
Apass/2
w
wpass
wstop
Passband
Stopband
Transition band
p
Lowpass Specification
forbidden
forbidden
forbidden
Achtung!
-Apass/2
dB
Lowpass filter example
  w  [0, wpass], magdB  [-Apass/2, Apass/2]
  w  [wstop, p], magdB ≤ Astop
  Transition band unspecified but should not amplify
Symmetric (linear phase) FIR filter design methods
  Windowing
  Least squares
  Remez (Parks-McClellan)

## Slide 19: Example: Two-Tap Averaging Filter
Input-output relationship
n
h[n]
Two-tap averaging filter
½
2
3
1
z-1
x[n]
S
y[n]
h[0]
h[1]
x[n-1]
Impulse response
Frequency response
magnitude
linear phase

## Slide 20: Example: First-Order Difference
n
h[n]
First-order difference
½
2
3
- ½
Input-output relationship
Impulse response
Frequency response
amplitude
generalized linear phase

## Slide 21: Complementary Frequency Responses
Averaging filter (lowpass) in white First-order difference filter (highpass) in yellow/blue First-order difference has p phase shift at zero mag response frequency
Magnitude response
Phase response

## Slide 22: Cascading FIR Filters Demo
Five-tap discrete-time averaging FIR filter with input x[n] and output y[n]
  Standard averaging filtering scaled by 5
  Lowpass filter (smooth/blur input signal)
  Impulse response of {1, 1, 1, 1, 1} removes multiplications
n
h[n]
First-order difference impulse response
1
-1
2
3
First-order difference FIR filter
  Highpass filter (sharpens input signal)
  Impulse response is {1, -1} removes multiplications

## Slide 23: Cascading FIR Filters Demo
Apply 1-D five-tap filter across each row to produce 256 x 260 image
and then apply the same 1-D five-tap filter down each column of 256 x 260 image to produce a 260 x 260 image

## Slide 24: Cascading FIR Filters Demo
DSP First, 2nd ed, ch. 6, cascading FIR Filters
  http://dspfirst.gatech.edu/chapters/06firfreq/demos/blockd/index.html
  From lowpass filter to highpass filter:
  original image  blurred image  sharpened/blurred image
  From highpass to lowpass filter:
  original image  sharpened image  blurred/sharpened image
Frequencies that are zeroed out can never be recovered (e.g. DC is zeroed out by highpass filter)
Order of two LTI systems in cascade can be switched under the assumption that computations are performed in exact precision

## Slide 25: Cascading FIR Filters Demo
Input image is 256 x 256 matrix
  Each pixel represented by eight-bit number in [0, 255]
  0 is black and 255 is white for monitor display
Each filter applied along row then column
  Averaging filter adds five numbers to create output pixel which requires 3 extra bits (worst case) for each pass
  Difference filter subtracts two numbers to create output pixel which requires 1 extra bit (worst case) for each pass
Full output precision 16 bits/pixel is maintained
  Demonstration uses double-precision floating-point data and arithmetic (53 bits of mantissa + sign; 11 bits for exponent)

## Slide 26: Cascading FIR Filters Demo
How to compare images pixel by pixel?
  Input image is 256 x 256 and output image is 261 x 261
Unit sample delay example
  If observing output y[n], how to recover input x[n] exactly?
x[n]
y[n]
n
x[n]
1
2
1
2
3
…
0
n
y[n]
1
3
1
2
3
…
0
2
FIR filters in demo have constant group delay
  Remove first 2 rows/columns and last 3 rows/columns

## Slide 27: Importance of Linear Phase
Speech signals
  Use phase differences in arrival to locate speaker
  Once speaker is located, ears are relatively insensitive to phase distortion in speech from that speaker
  Used in speech compression (in cell phones)
Linear phase crucial
  Audio
  Images
  Communication systems
Linear phase response
  Need FIR filters
  Realizable IIR filters cannot achieve linear phase response over all frequencies
d = c t

## Slide 28: Importance of Linear Phase
For images, vital visual information in phase
Take FFT of image
Set phase to zero
Take inverse FFT (which is real-valued)
Take FFT of image
Set magnitude to one
Take inverse FFT
Keep imaginary part
Take FFT of image
Set magnitude to one
Take inverse FFT
Keep real part
code
http://users.ece.utexas.edu/~bevans/courses/realtime/lectures/05_FIR_Filters/Original%20Image.tif
Original image is from Matlab
Notes: %%% ImagePhaseDemo.m
%%%
%%% Programmer: Prof. Brian L. Evans
%%% Organization: The University of Texas at Austin
%%% Created: February 21, 2008
%%%
%%% Requires the image processing toolbox in Matlab
aerialview = imread('westconcordorthophoto.png', 'PNG');
grayramp = 0 : 1/255 : 1;
graymap = [grayramp; grayramp; grayramp]';
figure(1);
imshow(aerialview);
colormap(graymap);
title('Original image');
aerialviewfft = fft2(single(aerialview));
aerialviewfftmag = abs(aerialviewfft);
aerialview2fp = ifft2(aerialviewfftmag);
%%% Show the contribution in the spatial domain of the magnitude of the FFT
%%% of the original image
figure(2);

## Slide 29: Takeaways
Linear time-invariant systems
  Uniquely defined by its impulse response
  Do not create new frequencies
  System must be initially “at rest” (zero initial conditions)
Some FIR filters have linear phase
  FIR coefficients (impulse response) must be either even symmetric or odd symmetric about its midpoint
  Constant group delay in samples for all input frequencies
Useful discrete-time FIR filters
  Averaging: Lowpass, linear phase
  Make all coefficients 1 for efficient multiplier-free version
  First-order difference: highpass, linear phase