## Slide 1: Advanced Data Conversion
Slides by Prof. Brian L. Evans, Dept. of ECE, UT Austin, and Dr. Thomas D. Kite (Audio Precision, Beaverton, OR tomk@audioprecision.com)
Dr. Ming Ding, when he was at the Dept. of ECE, UT Austin, converted slides by Dr. Kite to PowerPoint format
Some figures are from Ken C. Pohlmann, Principles of Digital Audio, McGraw-Hill, 1995.

## Slide 2: Solutions
11 - <number>
Oversampling eases analog filter design
  Also creates spectrum to put noise at inaudible frequencies
Add dither (noise) at quantizer input
  Breaks up harmonics (idle tones) caused by quantization
Shape quantization noise into high frequencies
  Auditory system is less sensitive at higher frequencies
State-of-the-art in 20-bit/24-bit audio converters
  Oversampling 64x 256x 512x
  Quantization 8 bits 6 bits 5 bits
  Additive dither 2-bit  PDF 2-bit  PDF 2-bit  PDF
  Noise shaping 5th / 7th order 5th / 7th order 5th / 7th order
  Dynamic range 110 dB 120 dB 120 dB

## Slide 3: Digital 4x Oversampling Filter
11 - <number>
Upsampling by 4 (denoted by 4)
  For each input sample, output the input sample followed by three zeros
  Four times the samples on output as input
  Increases sampling rate by factor of 4
FIR filter performs interpolation
  Multiplying 16-bit data and 8-bit coefficient: 24-bit result
  Adding two 24-bit numbers: 25-bit result
  Adding 16 24-bit numbers: 28-bit result
Digital 4x Oversampling Filter
16 bits 44.1 kHz
28 bits 176.4 kHz
4
FIR Filter
16 bits 176.4 kHz
1
2
Input to Upsampler by 4
n
n’
Output of Upsampler by 4
1
2
3
4
5
6
7
8
1
2
Output of FIR Filter
3
4
5
6
7
8
n’

## Slide 4: Oversampling Plus Noise Shaping
11 - <number>
Pohlmann Fig. 4-17 Noise shaping following oversampling decreases in-band quantization error. A. Simple noise-shaping loop. B. Noise shaping suppresses noise in the audio band; boosted noise outside the audio band is filtered out.
176 kHz

## Slide 5: Oversampling and Noise Shaping
11 - <number>
Pohlmann Fig. 16-4 With 1-bit conversion, quantization noise is quite high. In-band noise is reduced with oversampling. With noise shaping, quantization noise is shifted away from the audio band, further reducing in-band noise.

## Slide 6: Oversampling and Noise Shaping
11 - <number>
Pohlmann Fig. 16- 6 Higher orders of noise shaping result in more pronounced shifts in requantization noise.

## Slide 7: First-Order Delta-Sigma Modulator
11 - <number>
Discrete time:
+
_
+
x
y
Assume quantizer adds
uncorrelated white noise n (model nonlinearity as additive noise)
Higher-order modulators
Add more integrators
Stability is a major issue
Continuous time:
1
1
Lowpass
Highpass
Lowpass
Highpass
STF
NTF
signal transfer function (STF)
noise transfer function (NTF)
signal transfer function (STF)
noise transfer function (NTF)

## Slide 8: Noise-Shaped Feedback Coder
11 - <number>
Type of sigma-delta modulator (see slide 9-6)
Model quantizer as LTI [Ardalan & Paulos, 1988]
  Scales input signal by a gain by K (where K > 1)
  Adds uncorrelated noise n(m)
K
us(m)
Signal Path
K us(m)
un(m)
+
n(m)
un(m) + n(m)
Noise Path
Q[·]
u(m)
b(m)
{
NTF is highpass H(z) is lowpass STF passes low frequencies and amplifies high frequencies
Notes: <number>
Simple linear equalizers are easy to implement but enhance noise
Complex equalizers such as the DFE is required (how many taps has an DFE ?)
The computational complexity of DFE increases very fast with bit rate

## Slide 9: Third-order Noise Shaper Results
11 - <number>
Pohlmann Fig. 16-13 Reproduction of a 20 kHz waveform showing the effect of third-order noise shaping. Matsushita Electric

## Slide 10: 19-Bit Resolution from a CD: Part I
11 - <number>
Poh1man Fig. 6-27 An example of noise shaping showing a 1 kHz sinewave with -90 dB amplitude; measurements are made with a 16 kHz lowpass filter. A. Original 20 bit recording. B. Truncated 16 bit signal. C. Dithered 16 bit signal. D. Noise shaping preserves information in lower 4 bits.

## Slide 11: 19-Bit Resolution from a CD: Part II
11 - <number>
Pohlmann Fig. 16-28 An example of noise shaping showing the spectrum of a 1 kHz, -90 dB sinewave (from Fig. 16-27). A. Original 20-bit recording
B. Truncated 16-bit signal
C. Dithered 16-bit signal
D. Noise shaping reduces low and medium frequency noise.
Sony’s Super Bit Mapping uses psycho-acoustic noise shaping (instead of sigma-delta modulation) to convert studio masters recorded at 20-24 bits/sample into CD audio at 16 bits/sample. All Dire Straits albums are available in this format.

## Slide 12: Open Issues in Audio CD Converters
11 - <number>
Oversampling systems used in 44.1 kHz converters
  Digital anti-imaging filters (anti-aliasing filters in the case of A/D converters) can be improved (from paper by J. Dunn)
Ripple: Near-sinusoidal ripple of passband can be interpreted as due to sum of original signal and smaller pre- and post-echoes of original signal
  Ripple magnitude and no. of cycles in passband correspond to echoes up to 0.8 ms either side of direct signal and between -120 and -50 dB in amplitude relative to direct
  Post-echo masked by signal, but pre-echo is not masked
  Solution is to reduce passband ripple. Human hearing is no better than 0.1 dB at its most sensitive, but associated pre-echo from 0.1 dB passband ripple is audible.

## Slide 13: Open Issues in Audio CD Converters
11 - <number>
Stopband rejection (A/D Converter)
  Anti-aliasing filters are often half-band type with only 6 dB attenuation at 1/2 of sampling rate.
  Do not adequately reject frequencies that will alias.
  Ideal filter rolls off at 20 kHz and attenuates below the noise floor by 22.05 kHz, but many converter designs do not achieve this
Stopband rejection (D/A Converter)
  Same as for A/D converters
  Additional problem: intermodulation products in passband. Signal from the D/A converter fed to a (power) amplifier which may have nonlinearity, especially at high frequencies where the open loop gain is falling.

## Slide 14: Audio-Only DVDs
11 - <number>
Sampling rate of 96 kHz with resolution of 24 bits
  Dynamic range of 6.02 B + 1.17 = 145.17 dB
  Marketing ploy to get people to buy more disks
Cannot provide better performance than CD
  Hearing limited to 20 kHz: sampling rates > 40 kHz wasted
  Dynamic range in typical living room is 70 dB SPL
    Noise floor 40 dB Sound Pressure Level (SPL)
    Most loudspeakers will not produce even 110 dB SPL
  Dynamic range in a quiet room less than 80 dB SPL
  No audio A/D or D/A converter has true 24-bit performance
Why not release a tiny DVD with the same capacity as a CD, with CD format audio on it?

## Slide 15: Super Audio CD (SACD) Format
11 - <number>
One-bit digital audio bitstream
  Being promoted by Sony and Philips (CD patents expired)
  SACD player uses a green laser (rather than CD's infrared)
  Dual-layer format for play on an ordinary CD player
Direct Stream Digital (DSD) bitstream
  Produced by 1-bit 5th-order sigma-delta converter operating at 2.8224 MHz (oversampling ratio of 64 vs. CD sampling)
  Problems with 1-bit converters: distortion, noise modulation, and high out-of-band noise power.
Problems with 1-bit stream (S. Lipshitz, AES 2000)
  Cannot properly add dither without overloading quantizer
  Suffers from distortion, noise modulation, and idle tones

## Slide 16: Conclusion on Audio Formats
11 - <number>
Audio CD format
  Fine as a delivery format
  Converters have some room for improvement
Audio DVD format
  Not justified from audio perspective
  Appears to be a marketing ploy
Super Audio CD format
  Good specifications on paper
  Not needed: conventional audio CD is more than adequate
  1-bit quantization cannot be made to work correctly
  Another marketing ploy (17-year patents expiring)