## Slide 1: Digital Pulse Amplitude Modulation (PAM)

## Slide 2: Outline
Introduction
FIR 0
FIR 1
FIR L-1
Pulse shaping
Pulse shaping filter bank
Design tradeoffs
Symbol clock recovery

## Slide 3: Introduction
Convert bit stream into pulse stream
4-level PAM Constellation Map
d
d
3d
3d
00
01
10
11
symbol of bits
symbol ampl.
Serial/ Parallel
1
J
bit stream
J bits per symbol
Map to PAM
constellation
an
symbol amplitude
s*(t)
baseband waveform
Discrete-to-Continuous Time Conversion (Interpolation)
M-level PAM or simply M-PAM (M = 2J)
  Symbol period is Tsym and bit rate is J fsym
  Interpolation pulse shape gTsym(t) per slide 7-6
d is a voltage
  Group stream of bits into symbols of J bits
  Map symbol of bits to unique amplitude
  Convert from discrete-time to continuous-time

## Slide 4: 2-PAM Transmission
2-PAM example (right)
  Truncated raised cosine pulse gTsym(t) with peak of 1
  What are d and Tsym ?
  Max amplitude depends on d?
Highest frequency ½ fsym
  Alternating symbol amplitudes +d, -d, +d, … which is d cos(p n)
Serial/ Parallel
1
J
bit stream
J bits per symbol
Map to PAM
constellation
an
symbol amplitude
s*(t)
baseband waveform
Discrete-to-Continuous Time Conversion (Interpolation)

## Slide 5: Baseband PAM Transmission Code
% Baseband PAM Signal Generation
% by Prof. Brian L. Evans
% The University of Texas at Austin
% Spring 2018
%
% m is sample index
% n is symbol index
% Simulation parameters
N = 25; % Number symbol periods
% Pulse shape g[m]
Ng = 4; % Number symbol periods
L = 20; % Samples/symbol period
f0 = 1/L;
midpt = Ng*L/2;
m = (-midpt) : (midpt-1);
g = sinc(f0*m);
% Adjust for group delay
N = N + (Ng/2);
% M-level PAM symbol amplitudes
d = 1;
M = 2;
ioffset = M + 1;
symAmp = (2*randi(M,[1,N]) - ioffset)*d;
% Discrete-time baseband PAM signal
mmax = N*L;
v = zeros(1,mmax);
v(1:L:end) = symAmp; % interpolation
s = conv(v, g); % pulse shaping
slength = length(s); % trim result
s = s(midpt+1:slength-midpt+1);
% Interpretation in continuous time
Tsym = 4; % Symbol period in sec
fsym = 1/Tsym; % Symbol rate in Hz
fs = L*fsym; % Sampling rate in Hz
Ts = 1/fs; % Sampling time in sec
% Plots
Mmax = length(s);
m = 0 : (Mmax-1);
t = m*Ts;
Nmax = Mmax / L;
n = 0 : (Nmax-1);
figure;
plot(t,s);
hold on;
stem(n*Tsym,symAmp);
hold off;
xlim( [0 (Nmax-(Ng/2))*Tsym-Ts] );
ymax = Ng * (M-1) * d / 2;
ylim( [-ymax ymax] );
xlabel('Time (ms)');
title('Baseband PAM Signal s(t)');

## Slide 6: 4-PAM Transmission
4-PAM example (right)
  Truncated raised cosine pulse gTsym(t) with peak of 1
  What are d and Tsym ?
  Max amplitude depends on d?
Highest frequency ½ fsym
  Alternating symbol amplitudes +d, -d, +d, ... or +3d, -3d, +3d, ...
Serial/ Parallel
1
J
bit stream
J bits per symbol
Map to PAM
constellation
an
symbol amplitude
s*(t)
baseband waveform
Discrete-to-Continuous Time Conversion (Interpolation)

## Slide 7: PAM Transmission
Convert baseband processing to discrete time
Pulse shaper gTsym[m]
L
Sample at sampling time Ts : let t = (n L + m) Ts
  L samples per symbol period Tsym i.e. Tsym = L Ts
  n is the index of the current symbol period being transmitted
  m is a sample index within nth symbol (i.e., m = 0, 1, …, L-1)
Serial/ Parallel
1
J
bit stream
J bits per symbol
Map to PAM
constellation
an
symbol amplitude
s*(t)
baseband waveform
D/A
fs
s*[i]
@fs
@fs
@fsym
@fsym
fs = L fsym

## Slide 8: PAM Transmission
Derivation of s*[Ln + m] expression on previous slide

## Slide 9: Digital Interpolation Example
Upsampling by 4 (denoted by L)
  Output input sample followed by 3 zeros
  Four times samples on output as input
  Increases sampling rate by factor of 4
Digital Audio 4x Oversampling Filter
16 bits 44.1 kHz
28 bits 176.4 kHz
4
FIR Filter
16 bits 176.4 kHz
1
2
Input to Upsampler by 4
n
0
n’
Output of Upsampler by 4
1
2
3
4
5
6
7
8
0
1
2
Output of FIR Filter
3
4
5
6
7
8
n’
0
FIR fills in zero values
FIR interpolation filter (lowpass)
  Prior to upsampling, fmax is 22.05 kHz
  At filter input, wmax = 2 p fmax / fs = p / 4 = p / L
  Filter specifications: wstop < p / 4 and wpass = 0.9 wstop

## Slide 10: PAM Transmission Example
Fall 2021 Midterm #2

## Slide 11: Filter Bank Example #1
Avoid multiplying by and storing inserted 0 samples
Pulse shape g[m] lasts 2 symbols (8 samples; L = 4)
s[m] = x[m] * g[m]
s[0] = a0 g[0] s[1] = a0 g[1] s[2] = a0 g[2] s[3] = a0 g[3]
s[4] = a0 g[4] + a1 g[0] s[5] = a0 g[5] + a1 g[1] s[6] = a0 g[6] + a1 g[2] s[7] = a0 g[7] + a1 g[3]
L polyphase filters operating at symbol rate
Filter Bank
encoding
↑4
g[m]
bits
…a2a1a0
…000a1000a0
s[m]
x[m]
{g[0],g[4]}
{g[1],g[5]}
{g[2],g[6]}
{g[3],g[7]}
s[m]
…,s[4],s[0]
…,s[5],s[1]
…,s[6],s[2]
…,s[7],s[3]
…a2a1a0
m=0
Commutator (Periodic)

## Slide 12: Filter Bank Example #2
24 samples in pulse
L = 4 samples per symbol
Polyphase filter 0 impulse response is first sample of the pulse shape and every Lth sample after that
Polyphase filter 0 has only one non-zero sample.
Ng = 6 symbol periods/pulse

## Slide 13: Filter Bank Example #2
Polyphase filter 1 impulse response is second sample of the pulse shape and every Lth sample after that
24 samples in pulse
L = 4 samples per symbol
Ng = 6 symbol periods/pulse

## Slide 14: Filter Bank Example #2
Polyphase filter 2 impulse response is third sample of the pulse shape and every Lth sample after that
24 samples in pulse
L = 4 samples per symbol
Ng = 6 symbol periods/pulse

## Slide 15: Filter Bank Example #2
Polyphase filter 3 impulse response is fourth sample of the pulse shape and every Lth sample after that
24 samples in pulse
L = 4 samples per symbol
Ng = 6 symbol periods/pulse

## Slide 16: Pulse Shaping Design Tradeoffs
 | Computation in MACs/s | Memory size in words | Memory reads in words/s | Memory writes in words/s
Direct structure (slide 13-9) | (L Ng)(L fsym) |  |  | 
Filter bank structure (slide 13-12) | L Ng fsym |  |  | 
fsym symbol rate L samples/symbol Ng duration of pulse shape in symbol periods

## Slide 17: Pulse Shaping Design Tradeoffs
FIR filter with N coefficients to compute output
  Read current input value x[n]
  Read pointer to newest input sample in circular buffer
  Read previous N-1 input values
  Read N filter coefficients h
  Compute the output value y[n]
  Write current input value to circular buffer to oldest sample
  Write (update) the newest pointer in circular buffer
  Write output value
N multiplications-additions, 2N + 1 reads, 3 writes

## Slide 18: Pulse Shaping Design Tradeoffs
Direct structure (slide 13-9)
  FIR filter has L Ng coefficients (N = L Ng)
  FIR filter: N multiplications-additions, 2N + 1 reads, 3 writes
  FIR filter runs at sampling rate L fsym
  Upsampler reads at symbol rate and writes at sampling rate
Filter bank structure (slide 13-9)
  L polyphase FIR filters with Ng coefficients each
  FIR filter: Ng multiplications-additions, 2Ng + 1 reads, 3 writes
  Each polyphase FIR filter runs at symbol rate fsym
  Commutator reads and writes at sampling rate L fsym