## Slide 1: Review for Midterm #2
Prof. Brian L. Evans
EE 445S Real-Time Digital Signal Processing Laboratory

## Slide 2: Outline
Course objectives
Design flow
Signal processing
Communication systems
Communication system tradeoffs
Symbol timing recovery

## Slide 3: Course Overview
Objectives
  Build intuition for signal processing concepts
  Explore design tradeoffs in signal quality vs. run-time implementation complexity
Asymmetric Digital Subscriber Line (ADSL) Receiver Design
  FIR channel equalizer gives up to 10x increase in bit rate vs. not having one
  ADSL transmitter sends training data
  Eight adaptive channel equalizer design methods shown on right
  Three have best tradeoffs in bit rate vs. run-time computational complexity
Receiver design: bit rate in Mbps vs. multiplications for eight channel equalizer training methods
[Data from Figs. 6 & 7 in B. L. Evans et al., “Unification and Evaluation of Equalization Structures…”, IEEE Trans. Sig. Proc., 2005]
105
106
107
6.6
6.5
6.4
6.3
6.2
6.1
6.0
5.9
5.8
5.7

## Slide 4: Signal Quality Measures
Signal-to-noise ratio:
  Thermal noise (modeled as Gaussian) in Rx analog/RF front end
  Quantization noise (modeled as uniform) in data converters
Communication Systems
  PAM/QAM Bit rate:
  PAM Bit error rate
  PAM Error vector magnitude squared
Data Converters
  Signal-to-noise ratio
  Total harmonic distortion plus noise (lecture slide 8-14)
Estimated Rx symbol amplitude
Nearest Tx Constellation Point or Training Symbol

## Slide 5: Design Flow
Matrices
Fourier series
Difference & differential equations
Fourier transforms
Probability
Sampling Filtering
Modulation Adaptation
Speech & audio
Image & video
Communications
Builds on courses in programming, embedded systems, and signals & systems
Feedback run-time complexity analysis
Feedback run-time complexity analysis

## Slide 6: Signal Processing Building Blocks
Signals
  Impulse
  Sinusoids
  Exponentials
  Rectangular Pulse
  Triangular Pulse
  Sinc & Raised Cosine
  Chirp
  Pseudo-noise
  Impulse train
  Noise
Systems
  Adder & gain/multiplier
  Ideal delay
  FIR & IIR filters
  Pointwise nonlinearities (squarer, absolute value, etc.)
  Signal generation (sinusoidal)
  Samplers & up/downsampling
  Quantizers
  Modulators/demodulators
  Adaptation (steepest descent)
  Fast Fourier transform

## Slide 7: Increasing Sampling Rate
7
Upsampling by L denoted as L
  Outputs input sample followed by L-1 zeros
  Increases sampling rate by factor of L
Finite impulse response (FIR) filter g[m]
  Fills in zero values generated by upsampler
  Bandwidth p / L
  Every Lth sample of g[m] is zero
  Multiplies by zero L-1 out of every L times
Represented as rate changing FIR block
m
Output of Upsampler by 4
1
2
3
4
5
6
7
8
0
1
2
Output of FIR Filter
3
4
5
6
7
8
m
0
1
2
Input to Upsampler by 4
n
0
g[m]
4
1
4
1
1
FIR
1
4
1 input sample produces 4 output samples

## Slide 8: Polyphase Filter Bank
8
Filter bank (right) avoids multiplication by zero
  Split filter g[m] into L shorter polyphase filters operating at the lower sampling rate (no loss in output precision)
  Saves factor of L in multiplications and previous inputs stored and increases parallelism by factor of L
g[m]
L
Oversampling filter a.k.a. sampler + pulse shaper a.k.a. linear interpolator
Multiplies by zero (L-1)/L of the time
1
L
g0[n]
g1[n]
gL-1[n]
s(Ln)
s(Ln+1)
s(Ln+(L-1))
L
1

## Slide 9: Decreasing Sampling Rate
Finite impulse response (FIR) filter g[m]
  Lowpass filter to enforce sampling theorem
  Bandwidth is p / L
Downsampling by L denoted as L
  Inputs L samples
  Outputs first sample and discards L-1 samples
  Decreases sampling rate by factor of L
Represented as rate changing FIR block
4
4
1
g[m]
1
1
1
2
Input to Downsampler
3
4
5
6
7
8
m
0
1
2
Output of Downsampler
n
0
FIR
4
1
4 input samples produce 1 output sample

## Slide 10: Polyphase Filter Bank Form
10
  y[1] = v[L] = h[0] s[L] + h[1] s[L-1] + … + h[L-1] s[1] + h[L] s[0]
Filter bank only computes values output by downsampler
  Split filter h[m] into L shorter polyphase filters operating at the lower sampling rate (no loss in output precision)
  Reduces multiplications and increases parallelism by factor of L
Undersampling filter a.k.a. Matched filter + sampling a.k.a. linear decimator
Outputs discarded (L-1)/L of the time
h0[n]
h1[n]
hL-1[n]
s(Ln)
s(Ln+1)
s(Ln+(L-1))
1
M
s[m]
y[n]
h[m]
L
1
L
s[m]
y[n]
v[m]

## Slide 11: Communication Systems
11
Message signal is information to be sent
  Information may be voice, music, images, video, data
  Low frequency (baseband) signal centered at DC
Transmitter baseband processing includes lowpass filtering to enforce transmission band
Transmitter analog/RF front end includes digital-to-analog converter, analog/RF upconverter, and transmit filter
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 12: Communication Systems
12
Propagating signals experience attenuation & spreading w/ distance
Receiver analog/RF front end includes receive filter, carrier recovery, analog/RF downconverter, automatic gain control and analog-to-digital converter
Receiver baseband processing extracts/enhances baseband signal
Model the environment
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 13: Quadrature Amplitude Modulation
13
Transmitter Baseband Processing
i[n]
gT[m]
L
+
cos(0 m)
q[n]
gT[m]
L
sin(0 m)
Serial/ parallel converter
1
Bits
Map to 2-D
constellation
J
L samples per symbol (upsampling)
Pulse shaper (FIR filter)
Index
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
In-phase i[n] and quadrature q[n] symbol amplitudes each come from PAM constellation

## Slide 14: Transmitter Analog/RF Front End
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Mixer: Reduce circuit complexity by replacing multiplication by cosine with sampling device (single transistor)
cos(2 p fc t)
D/A
fs
LPF
LNA
BPF
BPF selects replica of baseband spectrum at fc
LNA Low-Noise Amplifier
Wavelength l = c / fc
Antenna Length?

## Slide 15: Communication Channel Modeling
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Line of sight
Propagation Paths
One bounce
Two bounces
Channel Impairments
Each path has its own attenuation & delay
Frequency distortion due to multiple paths
Additive thermal noise & interference
More in Lecture 12
15

## Slide 16: Receiver Analog/RF Front End
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
cos(2 p fc t)
A/D
fs
BPF
LNA
LPF
Mixer: Reduce circuit complexity by replacing multiplication by cosine with sampling device (single transistor)
LPF selects replica of bandpass spectrum at baseband
LNA Low-Noise Amplifier
16

## Slide 17: Baseband Equivalent Channel
Baseband discrete-time channel model
  Combines transmitter carrier circuits, physical channel and receiver carrier circuits
  One model uses cascade of gain, FIR filter, and additive noise
  Fast simulation
FIR
+
noise
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 18: Quad. Amplitude Demodulation
18
iest[n]
hopt[m]
L
cos(0 m)
hopt[m]
L
sin(0 m)
L samples per symbol (downsampling)
Matched filter (FIR filter)
qest[n]
Parallel/ serial converter
J
Bits
Decision Device
1
Symbol
heq[m]
Channel equalizer (FIR filter)
Receiver Baseband Processing
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 19: QAM Signal Quality
Assumptions
  Each symbol is equally likely
  Channel only consists of additive noise
    White Gaussian noise with zero mean and variance 2 in in-phase and quadrature components
    Total noise power of 22
  Carrier frequency and phase recovery
  Symbol timing recovery
Probability of symbol error
  Constellation spacing of 2d
  Symbol duration of Tsym
3
3
3
3
2
2
2
2
2
2
2
2
1
1
1
1
I
Q
16-QAM

## Slide 20: Communication System Tradeoffs
What happens to signal quality and run-time implementation complexity if PAM system parameter in first column increases?
  Indicate increase, decrease, or blank to mean no effect
  Assume other parameters in first column are not changing
Parameter | Transmission Bandwidth | Bit Rate | Symbol Error Rate | Tx Power Consumption | Run-Time Complexity
B bits in A/D output & D/A input |  | ? | ? |  | increase
2d constellation spacing in Volts |  |  | decrease | increase | 
fsym symbol rate in Hz | increase | increase | increase |  | increase
J bits/symbol |  | increase | increase | increase | increase
L samples/symbol |  |  | decrease |  | increase
symbol periods in pulse shape |  |  | decrease |  | increase
Parameter | Transmission Bandwidth | Bit Rate | Symbol Error Rate | Tx Power Consumption | Run-Time Complexity
B bits in A/D output & D/A input |  | ? | ? |  | increase
2d constellation spacing in Volts |  |  | decrease | increase | 
fsym symbol rate in Hz | increase | increase | increase |  | increase
J bits/symbol |  | increase | increase | increase | increase
L samples/symbol |  |  | decrease |  | increase
 |  |  | decrease |  | increase
Fall 2020 Midterm #2.4

## Slide 21: Symbol Timing Recovery
Consider a baseband PAM system using a rect. pulse shape
Matched filter impulse response is also a rectangular pulse
Receiver needs to find the symbol timing offset t
Develop adaptive method to update t in nth symbol period
Spring 2021 Midterm #2.1
when there is no noise
k can be negative

## Slide 22: Symbol Timing Recovery
Maximize power at received symbol amplitude
Objective function:
  is Gaussian random signal with 0 mean and variance
  Average noise power is constant regardless of sampling time
Spring 2021 Midterm #2.1
?

## Slide 23: Symbol Timing Recovery
A differentiator circuit can be as implemented as an
  RC circuit where the output is tapped across the resistor
  RL circuit where the output is tapped across the inductor
For h(t) being a rectangular pulse, we simplify derivative of y(t) by using a linear time-invariant model of differentiation with impulse response v(t) per JSK Appendix G.2:
)
How to handle many symbols?
  Send bits 11
  What is y2(t)?
Spring 2021 Midterm #2.1
Tsym
t
kTsym
2Tsym
3Tsym

## Slide 24: Data Conversion
Analog-to-Digital
Quantize to B bits
  Quantization error = noise
  SNRdB  C0 + 6.02 B
  Dynamic range  SNR
Digital-to-Analog
A/D and D/A lowpass filter
  fstop < ½ fs
  fpass  0.9 fstop
  Astop = SNRdB
  Apass = 20 log10(1-) where
   is quantizer step size:
  mmax is max quantizer voltage
Analog Lowpass Filter
Discrete to Continuous Conversion
fs
Analog Lowpass Filter
Quantizer
Sample at rate of fs
B
B