## Slide 1: INTRODUCTION TO DIGITAL SIGNAL PROCESSORS
Prof. Brian L. Evans
Contributions by Dr. Niranjan Damera-Venkata and Mr. Magesh Valliappan
Embedded Signal Processing Laboratory The University of Texas at Austin
http://signal.ece.utexas.edu/
Accumulator architecture
Load-store architecture
Memory-register architecture
register file
on-chip memory

## Slide 2: Outline
Embedded processors and systems
Signal processing applications
TI TMS320C6000 digital signal processor
Conventional digital signal processors
Pipelining
RISC vs. DSP processor architectures
Conclusion

## Slide 3: Embedded Processors and Systems
Embedded system works
  On application-specific tasks
  “Behind the scenes” (little/no direct user interaction)
Units of consumer products shipped worldwide 2017
  1472M smart phones 72M DVD/Blu-ray players
  259M PCs/laptops 55M digital media streamers
  164M tablets 47M game consoles
  138M smart TVs 25M digital still cameras
  79M cars/lt trucks
  1B/year smart phones since 2014 and connected TVs since 2018
How many embedded processors are in each?
How much should an embedded processor cost?
  2015: iPhone6 $676 (16GB) $942 (128GB) w/o contract
9%
10%
24%
3%
0.3%
0.1%
6%
2%
20%

## Slide 4: Smart Phone Application Processors
Standalone app processors (Apple, Samsung)
Integrated baseband-app processors (Qualcomm)
iPhone5 (10+ cores)
Touchscreen: Broadcom (probably 2 ARM cores)
Apps: Samsung (2 ARM + 3 GPU cores)
Audio: Cirrus Logic (1 DSP core + 1 codec)
Wi-Fi: Broadcom
Baseband: Qualcomm
Inertial sensors: STMicroelectronics
Source: Statista and Strategy Analytics
42% Qualcomm, 22% Apple, 15% MediaTek, 21% Others.
Samsung LSI and Spreadtrum had next two largest shares.
Others incude Broadcom (Avago), HiSilicon (Huawei), Intel.
40% have eight cores and 14% in 10nm CMOS process
“iPhone 5 Tear Down”
Chart: 2017 Smartphone AP Market
| Qualcomm | Apple | MediaTek | Others
1H2017 Smartphone AP Market | 0.42 | 0.22 | 0.15 | 0.21

## Slide 5: Market for Application Processors
Tablets $ 4.2B ‘14, $ 2.7B ’15, $ 2.1B ’16, $ 2.0B ‘17
Phones $20.9B ‘14, $20.1B ’15, $21.5B ’16, $20.2B ’17
10% revenue of all microprocessors in 2017 (est.) $400B in revenue for microprocessors in 2017
Tablet App Processor Market
Statista and Strategy Analytics
(1) Apple 36%, (2) Intel 18%,
(3) Qualcomm 17%, (4) Others 29%. MediaTek and Samsung LSI had next two largest market shares.
Apple, HiSilicon (Huawei), Intel and Qualcomm had increase in shipments
Decline in 2015 and 2016 due to strong competition from large screen smartphones
Chart: 2017 Tablet AP Market
| Apple | Intel | Qualcomm | Others
1H2017 Tablet AP Market | 0.36 | 0.18 | 0.17 | 0.29

## Slide 6: Signal Processing Applications
Embedded system cost & input/output rates
  Low-cost, low-throughput: sound cards, 2G cell phones, MP3 players, car audio, guitar effects
  Medium-cost, medium-throughput: printers, disk drives, 3G cell phones, ADSL modems, digital cameras, video conferencing
  High-cost, high-throughput: high-end printers, audio mixing boards, wireless basestations, 3-D medical reconstruction from 2-D X-rays
Embedded processor requirements
  Inexpensive with small area and volume
  Predictable input/output (I/O) rates to/from processor
  Low power (e.g. smart phone uses 200mW average for voice and 500mW for video; battery gives 5 W-hours)
Single DSP
Multiple multicore DSPs
Multiple DSP chips or cores + accelerators

## Slide 7: Type of Digital Signal Processor?
 | Fixed-Point | Floating-Point
Per unit cost | $2 and up | $2 and up
Prototyping time | Long | Short
Power consumption | 10 mw - 1 W | 1-3 W
Battery-powered products | Cell phones Digital cameras | Very few
Other products | DSL modems Cellular basestations | Pro & car audio Medical imaging
Sales volume | High | Low
Prototyping | Convert floating- to fixed-point; use non-standard C extensions; redesign algorithms | Reuse desktop simulations; feasibility check before investing in fixed-point design

## Slide 8: Modern Digital Signal Processor Example
Program RAM
Data RAM
or Cache
Internal Buses
Control Regs
Regs (B0-B15)
Regs (A0-A15)
.D1
.M1
.L1
.S1
.D2
.M2
.L2
.S2
CPU
Addr
Data
External
Memory
-Sync
-Async
DMA
Serial Port
Host Port
Boot Load
Timers
Pwr Down
TI TMS320C6000 Family, Simplified Architecture

## Slide 9: Modern DSP: TI TMS320C6000 Architecture
Very long instruction word (VLIW) of 256 bits
  Eight 32-bit functional units with one cycle throughput
  One instruction cycle per clock cycle
Data word size and register size are 32 bits
  16 (32 on C6400) registers in each of two data paths
  40 bits can be stored in adjacent even/odd registers
Two parallel data paths
  Data unit - 32-bit address calculations (modulo, linear)
  Multiplier unit - 16 bit  16 bit with 32-bit result
  Logical unit - 40-bit (saturation) arithmetic/compares
  Shifter unit - 32-bit integer ALU and 40-bit shifter

## Slide 10: Modern DSP: TI TMS320C6000 Architecture
Families: All support same C6000 instruction set
  C6200 fixed-pt. 150- 300 MHz printers, DSL (obsolete)
  C6400 fixed pt. 500-1200 MHz video, DSL
  C6600 floating 1000-1250 MHz basestations (8 cores)
  C6700 floating 150-1,000 MHz medical imaging, audio
TMS320C6748 OMAP-L138 Experimenter Kit
  375-MHz CPU (750 million MACs/s, 3000 RISC MIPS)
  On-chip: 8 kword program, 8 kword data, 64 kword L2
  On-board memory: 32 Mword SDRAM, 2 Mword ROM

## Slide 11: Modern DSP: TMS320C6000 Instruction Set
.S Unit
ADD NEG ADDK NOT ADD2 OR AND SET B SHL CLR SHR EXT SSHL MV SUB MVC SUB2 MVK XOR MVKH ZERO
.L Unit
ABS NOT ADD OR AND SADD CMPEQ SAT CMPGT SSUB CMPLT SUB LMBD SUBC MV XOR NEG ZERO NORM
.M Unit
MPY SMPY MPYH SMPYH
.D Unit
ADD ST ADDA SUB LD SUBA MV ZERO NEG
Other
NOP IDLE
C6000 Instruction Set by Functional Unit
Six of the eight functional units can perform integer add, subtract, and move operations

## Slide 12: Modern DSP: TMS320C6000 Instruction Set
Arithmetic ABS ADD ADDA ADDK ADD2 MPY MPYH NEG SMPY SMPYH SADD SAT SSUB SUB SUBA SUBC SUB2 ZERO
Logical AND CMPEQ CMPGT CMPLT NOT OR SHL SHR SSHL XOR
Bit Management CLR EXT LMBD NORM SET
Data Management LD MV MVC MVK MVKH ST
Program Control B IDLE NOP
C6000 Instruction Set by Category
(un)signed multiplication saturation/packed arithmetic

## Slide 13: C5000 vs. C6000 Addressing Modes
ADD #0Fh mvk .D1 15, A1
add .L1 A1, A6, A6
TI C5000
TI C6000
(implied) add .L1 A7, A6, A7
ADD 010h not supported
ADD * ldw .D1 *A5++[8],A1
Immediate
  Operand part of instruction
Register
  Operand specified in a register
Direct
  Address of operand is part of the instruction (added to imply memory page)
Indirect
  Address of operand is stored in a register

## Slide 14: C6700 Extensions
.S Unit
ABSDP CMPLTSP ABSSP RCPDP CMPEQDP RCPSP CMPEQSP RSARDP CMPGTDP RSQRSP CMPGTSP SPDP CMPLTDP
.L Unit
ADDDP INTSP ADDSP SPINT DPINT SPTRUNC DPSP SUBDP DPTRUNC SUBSP INTDP
.M Unit
MPYDP MPYID MPYI MPYSP
.D Unit
ADDAD LDDW
C6700 Floating Point Extensions by Unit
Four functional units perform IEEE single-precision (SP) and double-precision (DP) floating-point add, subtract, and move.
Operations beginning with R are reciprocal (i.e. 1/x) calculations.

## Slide 15: Selected TMS320C6700 Floating-Point DSPs
For more information: http://www.ti.com
Unit price for 100 units. Prices effective February 1, 2009.
DSK: DSP Starter Kit. EVM: Evaluation Module.

## Slide 16: Selected TMS320C6000 Fixed-Point DSPs
For more information: http://www.ti.com
Unit price is for 100 units. Prices effective February 1, 2009.
C6416 has Viterbi and Turbo decoder coprocessors.

## Slide 17: C6000 Reference Information for Lab Work
Code Composer Studio v5
  http://processors.wiki.ti.com/index.php/CCSv4
C6000 Optimizing C Compiler 7.4
  http://focus.ti.com/lit/ug/spru187u/spru187u.pdf
C6000 Programmer's Guide
  http://www.ti.com/lit/ug/spru198k/spru198k.pdf
C674x DSP CPU & Instruction Set Ref. Guide
  http://focus.ti.com/lit/ug/sprufe8b/sprufe8b.pdf
C6748 Board
  Logic PD’s ZOOM OMAP-L138 Experimenter Kit
  http://www.logicpd.com/products/development-kits/zoom-omap-l138-experimenter-kit
Download them for reference
TI software development environment

## Slide 18: Conventional Digital Signal Processors
Low cost: as low as $2/processor in volume
Deterministic interrupt service routine latency guarantees predictable input/output rates
  On-chip direct memory access (DMA) controllers
    Processes streaming input/output separately from CPU
    Sends interrupt to CPU when frame read/written
  Ping-pong buffering
    CPU reads/writes buffer 1 as DMA reads/writes buffer 2
    After DMA finishes buffer 2, roles of buffers switch
Low power consumption: 10-100 mW
  TI TMS320C54: 0.48 mW/MHz  76.8 mW at 160 MHz
  TI TMS320C5504: 0.15 mW/MHz  45.0 mW at 300 MHz
Based on conventional (pre-1996) architecture

## Slide 19: Conventional Digital Signal Processors
Multiply-accumulate in one instruction cycle
Harvard architecture for fast on-chip I/O
  Separate data memory/bus and program memory/bus
  1 read from program memory per instruction cycle
  2 reads/writes from/to data memory per inst. cycle
Instructions to keep pipeline (3-6 stages) full
  Zero-overhead looping (one pipeline flush to set up)
  Delayed branches
Special addressing modes in hardware
  Bit-reversed addressing (fast Fourier transforms)
  Modulo addressing for circular buffers (e.g. filters)

## Slide 20
Conventional Digital Signal Processors
xN-K+1
xN-K+2
xN-1
xN
Data Shifting Using a Linear Buffer
Time
Buffer contents
Next sample
xN+1
xN+3
xN+2
n=N
n=N+1
n=N+2
xN-K+3
xN-K+4
xN+1
xN+2
xN-K+2
xN-K+3
xN
xN+1
Modulo Addressing Using a Circular Buffer
Time
Buffer contents
Next sample
n=N
n=N+1
n=N+2
xN-2
xN-1
xN-K+1
xN-K+2
xN-K+4
xN+1
xN+2
xN+3
xN-2
xN-1
xN+1
xN-K+2
xN
xN-2
xN-1
xN+1
xN+2
xN
xN
xN
xN
xN-K+3
xN-K+3
xN-K+4
Buffers
  Used in processing streaming data
Linear buffer
  Sort by time index
  Update: discard oldest data, copy old data left, insert new data
Circular buffer
  Oldest data index
  Update: insert new data at oldest index, update oldest index

## Slide 21: Conventional Digital Signal Processors

## Slide 22: Conventional Digital Signal Processors
Different on-chip configurations in each family
  Size and map of data and program memory
  A/D, input/output buffers, interfaces, timers, and D/A
Drawbacks to conventional digital signal processors
  No byte addressing (needed for images and video)
  Limited on-chip memory
  Limited addressable memory on fixed-point DSPs (exceptions include Freescale 56300 and TI C5409)
  Non-standard C extensions for fixed-point data type

## Slide 23: Pipelining
Pipelining
Process instruction stream in stages (as stages of assembly in manufacturing line)
Increase throughput
Managing Pipelines
Compiler or programmer
Pipeline interlocking
Sequential (Freescale 56000)
Pipelined (Most conventional DSPs)
Superscalar (Pentium)
Superpipelined (TI C6000)
Fetch
Read
Execute
Decode
Fetch
Decode
Read
Execute
Fetch
Read
Execute
Decode
Fetch
Read
Execute
Decode

## Slide 24: Pipelining: Operation
Time-stationary pipeline model
  Programmer controls each cycle
  Example: Freescale DSP56001 (has X/Y data memories/registers)
Data-stationary pipeline model
  Programmer specifies data operations
  Example: TI TMS320C30
Interlocked pipeline
  “Protection” from pipeline effects
  May not be reported by simulators: inner loops may take extra cycles
MAC X0,Y0,A X:(R0)+,X0 Y:(R4)-,Y0
MPYF *++AR0(1),*++AR1(IR0),R0
D
E
F
G
H
I
J
K
L
L
C
D
E
F
G
H
I
J
K
-
L
B
C
D
E
F
G
H
I
J
K
-
L
A
B
C
D
E
F
G
H
I
J
K
-
L
F
D
R
E
Execute
Read
Decode
Fetch
MAC means multiplication-accumulation.

## Slide 25: Pipelining: Control and Data Hazards
A control hazard occurs when a branch instruction is decoded
  Processor “flushes” the pipeline, or
  Delayed branch (expose pipeline)
A data hazard occurs because an operand cannot be read yet
  Intended by programmer, or
  Interlock hardware inserts “bubble”
  TI TMS320C5000 (20 CPU & 16 I/O registers, one accumulator, and one address pointer ARP implied by *)
LAR AR2, ADDR ; load address reg.
LACC *- ; load accumulator w/ ; contents of AR2
D
E
F
br
G
-
-
X
Y
Y
Z
F
D
R
E
Execute
Read
Decode
Fetch
CD
E
F
br
-
-
-
X
-
Y
Z
BCD
E
F
br
-
-
-
X
-
Y
Z
ABCD
E
F
br
-
-
-
X
-
Y
Z
LAR: 2 cycles to update AR2 & ARP; need NOP after it

## Slide 26: Pipelining: Avoiding Control Hazards
A repeat instruction repeats one instruction or block of instructions after repeat
The pipeline is filled with repeated instruction (or block of instructions)
Cost: one pipeline flush only
; repeat TBLR inst. COUNT-1 times
RPT COUNT
TBLR *+
High throughput performance of DSPs is helped by on-chip dedicated logic for looping (downcounters/looping registers)
D
E
F
rpt
X
X
X
X
X
X
X
X
F
D
R
E
Execute
Read
Decode
Fetch
C
D
E
F
rpt
-
-
X
X
X
X
X
B
CD
E
F
rpt
-
-
X
X
X
X
AB CD
E
F
rpt
-
-
X
X
X

## Slide 27: Pipelining: TI TMS320C6000 DSP
C6000 has deep pipeline
  7-11 stages in C6200: fetch 4, decode 2, execute 1-5
  7-16 stages in C6700: fetch 4, decode 2, execute 1-10
  Compiler and assembler must prevent pipeline hazards
Only branch instruction: delayed unconditional
  Processor executes next 5 instructions after branch
  Conditional branch via conditional execution: [A2] B loop
  Branch instruction in pipeline disables interrupts
  Undefined if both shifters take branch on same cycle
  Avoid branches by conditionally executing instructions
Pentium IV pipeline has more than 20 stages
Contributions by Sundararajan Sriram (TI)

## Slide 28: RISC vs. DSP: Instruction Encoding
RISC: Superscalar, out-of-order execution
DSP: Horizontal microcode, in-order execution
Reorder
Load/store
Integer Unit
Floating-Point Unit
Load/store
Load/store
Address
Multiplier
ALU
Memory
Memory

## Slide 29: RISC vs. DSP: Memory Hierarchy
RISC
DSP
Registers
Out of
order
I/D Cache
Physical
memory
TLB
Registers
DMA Controller
I Cache
Internal
memories
External
memories
TLB: Translation Lookaside Buffer
DMA: Direct Memory Access

## Slide 30: Concluding Remarks
Conventional digital signal processors
  High performance vs. power consumption/cost/volume
  Excel at one-dimensional processing
  Per cycle: 1 16  16 MAC & 4 16-bit RISC instructions
TMS320C6000 VLIW DSP family
  High performance vs. cost/volume
  Excel at multidimensional signal processing
  Per cycle: 2 1616 MACs & 4 32-bit RISC instructions
Get the best of both worlds
  Assembly language for computational kernels (possibly wrapped in C callable functions)
  C for main program (control code, interrupt definition)

## Slide 31: References
Unit shipments worldwide (2017)
  Blu-ray & DVD players: https://www.prnewswire.com/news-releases/global-blu-ray-media-and-players-market-2018-2023---a-dying-market-300602693.html
  Cars & light trucks: https://www.scotiabank.com/content/dam/scotiabank/sub-brands/scotiabank-economics/english/documents/GAR_2018-03-29.pdf
  Digital media streamers: https://www.broadbandtvnews.com/2018/08/14/research-globally-more-than-one-billion-connected-tv-devices/
  Digital still cameras: https://www.businessinsider.com/digital-camera-shipments-15-years-decline-and-rise-2018-2
  iPhone5: http://www.ifixit.com/Teardown/iPhone-5-Teardown/10525/
  PCs/laptops: https://www.statista.com/statistics/272595/global-shipments-forecast-for-tablets-laptops-and-desktop-pcs/
  Smart phones: https://www.idc.com/getdoc.jsp?containerId=prUS43548018
  Smart TVs: https://technology.ihs.com/604804/smart-tv-share-jumps-to-70-percent-of-tv-shipments-in-2018-from-less-than-50-percent-in-2015-ihs-markit-says
  Tablets: https://venturebeat.com/2018/02/05/idc-tablet-shipments-decline-for-13th-straight-quarter-amazon-overtakes-samsung-for-second-place/
  Video game consoles: https://www.statista.com/statistics/276768/global-unit-sales-of-video-game-consoles/

## Slide 32: References
Unit shipments worldwide (2016)
  Blu-ray & DVD players: https://www.futuresource-consulting.com/reports/report/ r/futuresource-worldwide-home-video-market-report/i/412362
  Cars: http://www.gbm.scotiabank.com/scpt/gbm/scotiaeconomics63/GAR_2017-02-07.pdf
  Digital media streamers: https://www.strategyanalytics.com/access-services/devices/connected-home/consumer-electronics/reports/report-detail/global-connected-tv-device-vendor-share-q3-2016
  Digital still cameras: http://promuser.com/markets/2017/global-digital-camera-market-report-january-2017
  iPhone5: http://www.ifixit.com/Teardown/iPhone-5-Teardown/10525/
  PCs/laptops: https://www.gartner.com/newsroom/id/3568420
  Smart phones: http://www.gartner.com/newsroom/id/3609817
  Tablets: https://www.idc.com/getdoc.jsp?containerId=prUS42272117
  Video game consoles: https://www.statista.com/statistics/276768/global-unit-sales-of-video-game-consoles/
Embedded processor resources
  Embedded Microproc. Benchmark Consortium: http://www.eembc.org
  Embedded processing comparison: http://www.embeddedinsights.com/directory.php